## Slide 1
Reconstruction of energy and collision point of heavy ions with Forward Hadron Calorimeter at MPD setup
А. Strizhak
MIPT, Moscow
Institute for Nuclear Research RAS, Moscow

## Slide 2
Phase diagram of QCD
- research of phase transition
- research of mixed phase
- search for a critical point
- help in deriving equation of state
Goals of MPD/NICA project
2/18

## Slide 3
FHCal
Position and design of FHCal
Left - FHCal in MPD(green), right – transversal cut of FHCal arm
FHCal will consist of two arms;
Each arm will be positioned at 3,2 m from collision point;
Transversal size of FHCal ~1.1x1.1 m2;
Expected energy resolution
3/18
(FHCal)

## Slide 4
Design of FHCal module
Scintillator plate
A module will consist of 42 pairs of lead/scintillator plates (16mm/4mm) having total length of 84cm
Transversal size of FHCal module: 15x15cm2 ;
Module length ~ 4 λint;
Each module consists of 7 equal cells, connected(SiPM) ;
4/18
FHCal module

## Slide 5
Main aim of FHCal
Impact parameter – distance named b in the left picture (experimental estimate – centrality, that is fraction of nuclear inelastic cross-section);
Reaction plane is determined by impact parameter vector and beam axis (experimental estimate – Event plane)
5/18

## Slide 6
Determination of centrality
6/18
Determination of average impact parameter using deposited in calorimeter energies for
Error in centrality determination for
peripheral
central
Asymmetry of deposited energies in inner and outer zones of calorimeter

## Slide 7
Event Plane determination
i
7/18
Spectators
Participants
ejected particles
Reaction Plane
Impact parameter
colliding nuclei
Beam line
- coordinates of centre of module i;
- energy that is released in module i;
- Event plane at one of the calorimeter arms
- Event plane at the other calorimeter arm
Full event plane

## Slide 8
Test stand
Traits of Hamamatsu MPPC S12572-010C/P
+ high dynamic range
+ relatively low noise
+ low relaxation time
+ high count rate
- low photon detection efficiency
LED
8/18
Test stand of 12 modules
Front End Electronics (FEE)
Photodetector (SiPM)
Hamamatsu MPPC S12572-010C/P

## Slide 9
Energy calibration on cosmic muons from all directions
- At first, a coordinate of charge center needs to be found:
- Then distance between centers of fired cells and possible muon track needs to be minimized in order to find right muon track:
Finally, corrected charge spectrum (as if all muons go along the axis of FHCal module) can be found
Real charge spectrum of muon and corrected charge spectrum
9/18
Experimental setup consisting of 4x3 modules (longitudinal cut)
Position of peak corresponds to released energy of muon

## Slide 10
Determination of ion interaction point.
Energy method.

## Slide 11
Determination of ion interaction point for different event classes
peripheral
semi-peripheral
central
10/18
Three different event classes can be distinguished: central, peripheral, semi-peripheral
- Monte-Carlo modeling was carried out for ion interaction points 0, 30 and 60 cm from center of MPD detector along the axis of MPD.
- 50000 events were processed for each point
- Dependence is not monotonous due to the beam hole at the center of FHCal
= deposited Energy

## Slide 12
Determination of ion interaction point for different event classes
- energy deposited in left(right) arm of FHCal for class event class. class - central, semi-peripheral and peripheral events
for different event classes
11/18
To determine ion interaction point energy distribution in FHCal modules can be used.
Asymmetry of deposited energy in left and right arms of FHCal was used as we should expect its dependence on ion interaction point
spectra for different event classes
Left FHCal arm
Right FHCal arm

## Slide 13
External ring of modules
Middle ring of modules
Internal ring of modules
for different rings
The picture shows that internal modules react more to change in collision point than others
12/18
Determination of ion interaction point for different calorimeter zones
The same procedure as in the previous slide for different calorimeter zones (instead of event classes) was used

## Slide 14
Without errors
With errors
13/18
In this slide lines are shown for central, semi-peripheral and peripheral centrality classes only for internal ring of modules
Determination of ion interaction point. Combination of methods.

## Slide 15
14/18
Determination of ion interaction point. Accuracy.
for different event classes
Spatial resolution obtained from the combination of methods is worse than the resolution obtained from the first method.
The accuracy of reconstruction of the collision point using the first method is 21-23 cm.

## Slide 16
Determination of ion interaction point.
Time method.

## Slide 17
1
2
3
4
Module №
ADC
PC
Discriminator
Discriminator
Coincidence scheme
In order to increase the accuracy of determination of ion interaction point time resolution should be determined
Experimental setup for determination of time resolution
15/18
Time method of ion interaction point determination
Left FHCal arm
Right FHCal arm
Left FHCal arm
Right FHCal arm
Time method of determination of ion interaction point
Collision point
Muons that pass through modules 1 and 4 are selected and are used as input signals for coincidence scheme.
Coincidence scheme yields trigger signal.
Time and amplitude spectra from modules 2 and 3 are written.

## Slide 18
Correlation between muon amplitude spectra of modules 2 and 3
In order to increase the accuracy of determination of ion interaction point time resolution was explored
Spectrum of difference in time pulses of modules 2 and 3
Spectrum of difference in time pulses of modules 2 and 3 for mentioned range of amplitudes
cut
Time resolution of FHCal modules
All events were divided as shown above.
Time spectra for all event cuts were fitted with gauss distribution in order to get time resolutions of corresponding energy regions.
Amplitude from module 3
Amplitude from module 2
16/18

## Slide 19
Accuracy of ion interaction point reconstruction by the time method
Time resolution can be obtained from time spectra, acquired from energy cuts (they are shown as green rectangles at the previous slide)
If released energy
If time resolution accuracy of reconstruction
Dependence of time resolution on energy
17/18
Spectrum of difference in time pulses of modules 2 and 3 for mentioned range of amplitudes
In order to get energy in MeVs energy calibration results were used

## Slide 20
Thank you for your attention

## Slide 21
Determination of ion interaction point
Energy method

## Slide 22
Determination of ion interaction point for different event classes
peripheral
semi-peripheral
central
- energy deposited in left(right) arm of FHCal for class event class. class - central, semi-peripheral and peripheral events
for different event classes
8/28

## Slide 23
External module ring
Middle module ring
Internal module ring
for different rings
The picture shows that internal modules react more to change in collision point than others
9/28
Determination of ion interaction point for different calorimeter zones

## Slide 24
Without errors
With errors
10/28
In this slide lines are shown for central, semi-peripheral and peripheral centrality classes only for internal ring of modules
Determination of ion interaction point. Combination of methods.

## Slide 25
Energy calibration of FHCal modules

## Slide 26
Experimental setup scheme
Absolute calibration
LEDs amplitude spectrum for a module
=>
These spectra have Poisson distribution. Poisson distribution has following parameters: ,

## Slide 27
Energy calibration on cosmic muons
Different muon tracks that are taken into account:
- when two neighbor cells signals
- three neighbor cells signals
- all cells signals
are compared
Cosmic muon amplitude spectra of all cells in one of FHCal modules
Light yield of module cells that was received after fitting amplitude spectra of cosmic muons with langaus distribution
FHCal module design

## Slide 28
Калибровка на космических мюонах всех направлений
Калибровка на космических мюонах
Recently a method of simultaneous calibration of all modules was invented
When compared to previously used method the new one has following advantages:
- more statistics
- grater signal/noise ratio
- possibility of simultaneous calibration of all modules
Test stand scheme (longitudinal cut)
11/28
Energy calibration on cosmic muons from all directions

## Slide 29
Energy calibration on cosmic muons from all directions
Average light yield of 9 modules (old SiPMs)
Using corrected amplitude spectrum it is possible to find light yield like it was done before
13/28
Average light yield of 9 modules (new SiPMs)

## Slide 30
Determination of ion interaction point
Time method