## Slide 1: Simulation of the drift chambers for the BM@N experiment
Dubna State University
ENU named after L.N. Gumilyov
Student:
Gulfairuz Serikbayeva
Thesis supervisor:
Maria Patsyuk, PhD, JINR LHEP

## Slide 2
Purpose of the thesis
Tasks of the thesis research were following:
Study of basic principles of drift chambers
Explore and learn to use the BmnRoot software framework
Master the object-oriented environment ROOT
Develop the simulation programming code
To improve the existing simulation of the drift chambers for the BM@N experimental setup

## Slide 3
The subject of the thesis
Event generator
(UrQMD, LAQGSM, Pythia...)
Detector simulation
(Geant3, Geant4)
Digitization
Reconstruction/Analysis
Software of the experiment
(BmnRoot, FairRoot...)
Fig. 1. The layout of the BM@N experiment [1]. Drift chambers are labeled by 8.

## Slide 4: Drift chambers (DCH) at the BM@N setup
DCH-2
DCH-1
DCH-2

## Slide 5
The following steps were done:
1. The accurate shape of background noise was accomplished by fitting XY distribution of DCH hits from 12C ion beam with applied magnetic field of 2.7 Tm.
2. The precise positioning of 8 wire planes of each drift chamber was reconstructed with ROOT macro.
3. Physical and background hits are separated according to reference index.
4. Individual hits were plotted for each wire plane to illustrate the wires' orientation.

## Slide 6: Geometry of the DCH
Octagonal shape
8 wire planes in each DCH
Fig. 2. Four different directions of wires in each DCH, orthogonal to the beam axis (Z axis) [3].

## Slide 7: Positioning of wire planes in the DCH based on simulation
Fig. 3. Z coordinates of wire planes in drift chambers.
V-oriented wire plane
U-oriented wire plane
Y-oriented wire plane
X-oriented wire plane

## Slide 8: X-profile distribution of experimental hits
Charged particles are bent to the side of chambers because of magnetic field influence.
Fig. 4. Distribution of experimental hits in the DCHs according to X coordinate.

## Slide 9: X-profile fitting
The fitting function was chosen as sum of several functions at different intervals of X axis to achieve adequate fitting parameters.
Fig. 5 . Fitting of hits distribution according to X coordinate.
pol4
Gaussian
Gaussian
pol6

## Slide 10: Y-profile distribution of experimental hits
Fig. 6. Distribution of experimental hits in drift chambers according to Y coordinate.

## Slide 11: Y-profile fitting
Gaussian
The fitting function was chosen as sum of several functions at different intervals of Y axis to achieve adequate fitting parameters.
Fig. 7. Fitting of hits distribution according to Y coordinate.
pol4
pol4

## Slide 12: Simulated background hits
1000 events
10 background hits per wire plane in each event
Fig. 8. Distribution of simulated background hits in drift chambers.

## Slide 13: The geometry of the DCH for simulated background hits
1000 events
10 background hits per wire plane in each event
Fig. 9. Geometry for simulated background hits distribution. Green lines are circles of beam hole and outer sides of drift chambers. Black line - octagon fitted into circle.

## Slide 14: Separation of the simulated physical and background hits
For testing purposes reference index for background hits starts with 1000.
Simulated physical hits
Background hits
Fig. 10. Reference indices of simulated physical and background hits.

## Slide 15: Simulated physical and background hits
100 events
5 protons per event
10 background hits per wire plane in each event
Momentum of protons: 5 GeV/c
Azimuth angle range: (0; 360)
Polar angle in lab system range: (0; 5)
Fig. 11. Simulated physical and background hits in drift chambers.

## Slide 16: Simulated hits in the 1st DCH
Fig. 12. Simulated hits on the 1st-4th wire planes in the 1st drift chamber.
Simulated physical and background hits are duplicated in the same way.

## Slide 17: Simulated hits in the 1st DCH
Fig. 13. Simulated hits on the 5th-8th wire planes in the first drift chamber.
Simulated physical and background hits are duplicated in the same way.

## Slide 18
The XY-profile of background noise was added into hit producing class for DCH of BM@N software.
The exact Z coordinates of planes are added into background generation algorithm of BM@N software.
The distribution of background hits is verified to be match the XY geometry of DCH.
A method of addition of background hits to simulation macro was developed.
A macro code for testing and visualization of the hits was developed.
Results
The results of improved simulation will be used to determine the efficiency of drift chambers and improve the track reconstruction.

## Slide 19: Thank you for your attention!

## Slide 20: Backup slides

## Slide 21
References
1. Official BM@N collaboration web-site: https://bmn.jinr.ru
2. The BM@N experiment at JINR: status and physics program / Baranov D., Kapishin M., Mamontova T., Pokatashkin G., Rufanov I., Vasendina V., Zinchenko A. - Dubna: JINR, 2018.
https://knepublishing.com/index.php/KnE-Energy/article/view/1757
3. Ján Fedorišin. Calibration, autocalibration and alignement of drift chambers in BMN experiment - Dubna: JINR, 2015.
http://bmnshift.jinr.ru/wiki/lib/exe/fetch.php?media=bmn_dch_oct2015_fedorishin.pdf
4. BM@N collaboration. BmnRoot: simulation and analysis framework for BM@N experiment - Dubna: JINR, 2016.
https://bmn.jinr.ru/wp-content/uploads/2019/07/BmnRoot_Start_Guide.pdf

## Slide 22: NICA experiment
Fig. 14. NICA facility [4].

## Slide 23: Operation of the drift chamber
sensitive wires
resistive wires
4 double coordinate planes: 2x; 2y, 2u, 2v;
wire angles 0°,90°,±45°;
radius of central hole = 10 cm;
2048 wires per chamber.
Trigger
Fig. 15. Efficiency per layer in the 1st drift chamber.

## Slide 24: Table 1. Fitting functions for X-profile distribution of experimental hits

## Slide 25: Table 1. Fitting functions for X-profile distribution of experimental hits

## Slide 26
Table 2. Fitting functions for Y-profile distribution of experimental hits

## Slide 27
Table 2. Fitting functions for Y-profile distribution of experimental hits

## Slide 28: Simulated physical hits in the 1st DCH
Fig. 16. Simulated physical hits on the 1st-4th wire planes in the first drift chamber.
V
V
U
U

## Slide 29: Simulated physical hits in the 1st DCH
Fig. 17. Simulated physical hits on the 5th-8th wire planes in the first drift chamber.
Y
X
X
Y

## Slide 30: Simulated physical hits in the 2nd DCH
Fig. 18. Simulated physical hysical hits on the 1st-4th wire planes in the second drift chamber.
V
V
U
U

## Slide 31: Simulated physical hits in the 2nd DCH
Fig. 19. Simulated physical hits on the 5th-8th wire planes in the second drift chamber.
Y
Y
X
X

## Slide 32: Simulated background hits in the 1st DCH
Fig. 20. Simulated background hits on the 1st-4th wire planes in the first drift chamber.
V
V
U
U

## Slide 33: Simulated background hits in the 1st DCH
Fig. 21. Simulated background hits on the 5th-8th wire planes in the first drift chamber.
Y
Y
X
X

## Slide 34: Simulated hits in drift chambers
1000 events
1 proton per event
Momentum of particles:
5 GeV/c
Azimuth angle range:
(0; 360)
Polar angle in lab system range:
(0; 5)
Charged particles are bent to the side of chambers because of magnetic field influence.
Fig. 22. Hits, generated with a single proton events in drift chambers.