## Slide 1: Control and readout electronics of the time-of-flight system of the MPD
A. Dmitriev on behalf of the TOF MPD group
Notes: Hello…I am Alexandr Dmitriev. I represent the TOF group of the MPD. I'm going to show in this presentation our progress in control and readout electronics of the TOF system.

## Slide 2: Contents
The MPD Time of Flight system design
Triple-stack MRPC
Cabling in The TOF modules
FEE based on the NINO chips
Differential Amplifier
Methodical studies and modeling:
  Crosstalk;
  Efficiency;
Cosmic test setup
2/14
Control and readout electronics of the time-of-flight system of the MPD, NEC’2017

## Slide 3: The MPD Time of Flight system design
Advantages of the design: ~94% estimated geometrical efficiency
Convience of integration (28 sec. ECal)
645x12.5 mm strip: 280х24 = 6720 strips → 13440 el.ch
Z-direction detectors layout
 | Number of detectors | Number of readout strips | Sensitive area, m2 | Number of FEE cards | Number of FEE channels
MRPC | 1 | 24 | 0.2 | 2 | 48
Module | 10 | 240 | 1.85 | 20 | 480
Sector | 20 | 480 | 3.7 | 40 | 960
Barrel | 280 | 6720 | 51.8 | 560 | 13440 (1680 chips)
φ-direction TOF modules layout
For TPC rail
3/14
Control and readout electronics of the time-of-flight system of the MPD, NEC’2017
Notes: At first, let me tell you about the current design of the barrel TOF. It is look like cylinder made of 14 sectors. It is convenient for integration of Ecal as it consists of 28 modules. The radius of the TOF cylinder is about one and half meters. Detectors are arranged inside module with small angle to the beam line for better registration and geometrical efficiency. In this table I show the quantity of the main parts of the barrel TOF.

## Slide 4: Triple-stack MRPC
Inner readout board with strips
Triple-stack MRPC cut view
4/14
Control and readout electronics of the time-of-flight system of the MPD, NEC’2017
Read-out twisted pair
Notes: The TOF system is based on the multigap resistive plate cameras (MRPC). We use a three-stack design with two-side differential readout. Differential readout is carried out by double twisted couple. It is a sectional view of three-stack MRPC with strip reading. Each stack consists of 5 gas gaps of 200 microns. Gaps are formed of usual sheet glasses with thickness of 280 microns. Width of strips is 10 mm. Distance between them is 2,5 mm. Quantity of strip is 24. Testing showed that such MRPC has time resolution better than 50 пс (the best time resolution which we achieved is 41 пс.)

## Slide 5: Cabling in The TOF modules
VMEx64 crate
LV Distribution board
Fixing of Molex InfiniBand cables
Air cooling
The output of trigger
Total cabling:
14 VME crates
196 TDC72VHL => 14 per crate
560 cables Molex CXP => 40 per crate
Cable lengths: 4 - 8 m
5/14
Control and readout electronics of the time-of-flight system of the MPD, NEC’2017
Notes: Next is the TOF modules. It is look like aluminum box. It is one of difficult parts of technical design because the module must be easy and strong, compact and spacious inside to place all detectors, electronics and cables. The correct cabling is very important part of creation of the TOF modules. It is example of module with communications. Front-end electronics must be as close as possible to the detector to achieve the best time resolution. And every crate radiates heat to 300 W. So, it was decided to arrange them directly on a yoke. And all cables come out the TOF sector and pass through special openings in a yoke.

## Slide 6: FEE based on the NINO chips
3 V to 6 V power supply range
stabilized of the voltage (+2.5V);
differential input signal; ( Zdiff = 55 Ohm)
overload protection for input channels;
capacitors on the inputs for double-end strip readout;
CPX (InfiniBand) output transmitting line;
the possibility to use as trigger (series “or” output);
controlling and monitoring of the thresholds.
The time distribution between two channels of the NINO FE board
6/14
Control and readout electronics of the time-of-flight system of the MPD, NEC’2017
Notes: For the front-end electronics we use the preamplifier-discriminator based on ASIC NINO developed for the TOF ALICE. Preamplifier have a 24-channel amplifier. The differential input was designed to have 55 Ω impedance that is equal to the MRPC output. In order to protect the channels of ASIC when the high voltage is applied to the detector, we put 1 MΩ resistors on each input. The Molex CXP (InfiniBand) connector system as an output provides 100 Ω transmission line with good electrical characteristics. The board can operate with the voltage in the range from 3.3 to 6 V.

## Slide 7: Differential Amplifier. modeling Crosstalk in mRpc
#1+
#2+
#1-
#2-
24%
19%
Mutual Inductance, Lm
Zo
Zo
Zo
Zo
Lm
near
far
Zo
Zo
Zo
Zo
Mutual Capacitance, Cm
Cm
near
far
ADA4960
ADA4937
Modeling in Comsol Multiphysics
7/14
Control and readout electronics of the time-of-flight system of the MPD, NEC’2017
Notes: Another front-end electronics is the differential amplifier. It was developed for methodical research. Differential amplifier is based on two chips: ADA4960 and ADA4937. You can see the single-channel test example of the differential amplifier and the full-fledged 12-channel differential amplifier. One of methodical research is assessment of crosstalks in the detector between strips. Simulation of formation and distribution of a signal in the detector was carried out. The simulation was performed in Comsol Multiphysics.

## Slide 8: Crosstalk in mRpc obtained experimentally
S2
S3
S4
S5
S6
S7
S8
S1
S9
Strip MRPC
8/14
Control and readout electronics of the time-of-flight system of the MPD, NEC’2017
Termination
Differential Amplifiers
Strips
Notes: And also the experiment with the differential amplifiers was made.

## Slide 9
Voltage(mV)
Voltage(mV)
Time(ns)
Time(ns)
160 mV
40 mV
25% crosstalk from strip #3
Voltage(mV)
Voltage(mV)
Time(ns)
Time(ns)
20 mV
90 mV
22% crosstalk from strip #2
#1
#2
#3
#4
9/14
Control and readout electronics of the time-of-flight system of the MPD, NEC’2017
Notes: The simulation and the experiment showed similar results.

## Slide 10: The calculation of the efficiency MRPc
0.579 steradian
S1
S2
S3
S4
S5
S6
S7
S8
One gap
the value of the
gas gap 175 µm
NA61 #1
S9
99% efficiency is expected with 14 gaps
The probability of the detector response
The number of gaps
The probability of operation several gaps
The number of gaps
10/14
Control and readout electronics of the time-of-flight system of the MPD, NEC’2017
Notes: Calculation of efficiency of the detector with the reduced gap was the another work performed on differential amplifiers. Results of this research showed that 99% efficiency with fourteen gas gaps is expected.

## Slide 11: Cosmic test setup
11/14
Control and readout electronics of the time-of-flight system of the MPD, NEC’2017
Notes: Another area of works is a mass production the time-of-flight of detectors. One of tasks is mass testing of new detectors. For this purpose test setup on cosmic rays was developed. Test setup allows testing up to 12 modules. It consists of the bearing design, racks of electronics, gas system, etc.

## Slide 12: Trigger system of test stand
Programmable
logic
Two operating modes:
selection of vertical tracks of the particles;
selection of the inclined tracks of the particles.
12/14
Control and readout electronics of the time-of-flight system of the MPD, NEC’2017
Notes: An opportunity to use each module as the trigger by means of special logic is the interesting feature of the detector. Front-end electronics has the general OR exit in the LVDS format. The signal is transmitted to FPGA on twisted couple and FPGA allows to select cosmic rays under different corners.

## Slide 13: Testing of the Trigger system
13/14
Control and readout electronics of the time-of-flight system of the MPD, NEC’2017
Notes: Testing of programmable logic showed that the efficiency is about 95%

## Slide 14
14/14
Control and readout electronics of the time-of-flight system of the MPD, NEC’2017
Notes: And as a conclusion I put our time chart

## Slide 15
Thank you for your attention

## Slide 16: Control and readout electronics of the time-of-flight system of the MPD
A. Dmitriev on behalf of the TOF MPD group

## Slide 17
Backup
Что положить в бэкап???
Какие могут возникнуть вопросы?

## Slide 18: MRPC

## Slide 19: Scheme of analog

## Slide 20: Time of flight system of multi-purpose detector
FEEs
560 pieces
(13440 channels)
TDCs
187 pieces
Modules
28 pieces
MRPCs
280 pieces