## Slide 1
Software-Defined Networks (SDN)
Fedor Pavlov
Storage Technology Consultant,
Modern Infrastructure Team, Dell EMC, Russia & eCIS

## Slide 2: 3 approaches to SDN
Control plane
Network overlay
Open networking
?

## Slide 3: 1. Control plane
Controller
Southband API (OpenFlow)
Northband API
Open source (OpenDaylight, Floodlight, RUNOS) and commercial (NEC, Big Switch, HPE, Brocade, Brain4Net) controllers
Data plane
Data plane
Data plane
Control plane
Control plane
Control plane
Control plane

## Slide 4: Pros and cons
Centralized management and simplicity
Open standards-based and vendor-neutral
Network abstraction
Vulnerability and scalability of single brain approach
Hardware dependency
Greenfield environment

## Slide 5: 2. Network Overlay
Overlay protocol (VXLAN, NVGRE, STT)
Controller
Gateway to communicate with physical environment
Commercial (VMware, Microsoft, Nuage) and open source (Midokura) products
Physical
network
Virtual switch
VM
Virtual switch
Virtual switch
VM
VM
VM
VM
VM
Controller

## Slide 6: Pros and cons
Fits to almost any physical network
16M virtual networks, distributed network services
Crossing Layer 3 boundaries
Overhead
Scalability limitation
Virtualized environment only

## Slide 7: 3. Open Networking
Disaggregation with ONIE
Hardware agnostic with SAI (Switch Abstraction Interface)
Linux OS: Cumulus, Pica8, OpenSwitch, Dell EMC OS10 Open Edition
White-box switches or brite-box (Dell EMC, HPE, Juniper, Mellanox)
Programming API
Open Networking Hardware
Open Networking Software

## Slide 8: Pros and cons
Switch becomes like a server
Reduced vendor lock-in
Well known Linux OS and tools for automation
Support for software and hardware
Programming and Linux skills of network admins
Distributed control plane

## Slide 9: Use-Case – IoX project in University of Pisa
IoT gateway
JSON
IoT gateway
Dell EMC OS10 Open Edition

## Slide 10: How Dell EMC drives SDN?
Operating environment: Dell EMC OS 10 Open Edition
Support and contribution to OpenSwitch
Brite-Box hardware

## Slide 11: How Dell EMC drives SDN?
Open Networking Install Environment (ONIE)
Switch Abstraction Interface (SAI)
SONiC
OpenSwitch
OS10 Open Edition
OS10
Enterprise Edition
Linux/Open
Source Apps
3d-Party
Software

## Slide 12: Dell EMC open networks concept
Open Switch Platforms
Standard Switch
Hardware
Open Network –
Choice of switch OS
Software Control Plane
Automatisation and Orchestration
1GE | 10GE | 40GE | 100GE
S3048-ON | S4100-ON S4000-ON | S6010-ON | S6100-ON Z9100-ON