## Slide 1: NICA injection complex status
A. Martynov on behalf of NICA team

## Slide 2: Table of Contents
Structure and layout of the injection complex
LU-20 injector:
  Source of polarized Ions
  Modernized foreinjector
  Transportation channel overview
  Obtained results during Nuclotron runs 52-54
Heavy ions linear accelerator (HILAc)
  Design & parameters
  Commissioning

## Slide 3: Structure of the complex
SPI
LU-20
Nuclotron
ESIS
Booster
Transfer to collider rings
LIS
RFQ
RFQ
IH1
IH2
HILAc
Au31+ 3.2 MeV/u
p↑, d↑, ions z/A>0.3 5 MeV/u
Polarized p and d beams, protons and light ions
are planned to be accelerated with existing Linac LU-20,
Heavy ions: HILac + Booster

## Slide 4: Source of polarized ions (SPIon)
The main purpose of the SPI-project is to produce the intensity of the accelerated polarized beams (D+,H+) at the JINR Accelerator Complex up to 1010 p/pulse

## Slide 5: SPIon
 | Polarized deutrons | Polarized protons
Obtained beam current in 2017 (source) | 2 mA | 0.4 mA
Project beam current (source) | 5-6 mA | 5-6 mA
Obtained beam intensity in 2017 (Nuclotron) | 2.2x109 ppc | 1.8x108 ppc
Project beam intensity (Nuclotron) | 1-2x1010 ppc | 1-2x1010 ppc
Plans:
1) Measure and match beam emittance from SPI to LEBT
2) Install buncher in front of DTL (int. x3)
3 runs in 2016-2017 (#52-54) with d↑, 1 run (#54) with stable p↑ beam.

## Slide 6: LU-20 injection line
LEBT
MEBT
QT + (Bu) +QT
LU-20 (DTL)
RFQ
Source
10 keV/u(SPI)
0.5 keV/u (LIS)
31 keV/u
156 keV/u
5 MeV/u
Ion source output
LEBT output
RFQ output
Lu-20 output

## Slide 7: RFQ
q/A | 1.0 | 0.5 |  0.3
Injection energy, [keV] | 31 | 61.8 | 103
Max current, [mА] | 10 | 20 | 10
Output energy [keV/u] | 156 |  | 
Norm emittance (output) [π·cm·mrad] | ≤ 0.5 |  | 
RFQ length, [m] | 2.2 |  | 
Transmission, % | > 85% | > 89% | > 93%
In LU-20 acceptance with buncher | 70 % | 71 % | 80 %
In LU-20 acceptance without buncher | 15 % | 15 % | 20 %
In collaboration with ITEP, VNIITF (Snezhinsk), MEPHi (2016)

## Slide 8: Transportation channel to Nuclotron
CF-1
Protons acceleration: I = 500 μA. For polarized protons I = 38 μA.
CF-4
Protons acceleration: I = 300 μA.
For polarized protons I = 30 μA.
Beam current
RF of LU-20
RF of RFQ
Accelerating
voltage
Beam loss in channel:
Protons: 40%
Polarized protons: 21%

## Slide 9: p↑ beam at Nuclotron
Beam intensity, particles/sec.
Time, ms
Magnetic field, Gs
Beam voltage ,U
1650
1.8 E8

## Slide 10: d↑ beam at Nuclotron
Beam intensity, particles/sec.
Magnetic field, Gs
Beam voltage ,U
Time, ms
2.0 E9
2500

## Slide 11: Beam loss overview
 | d | d↑ | p(H+) | p↑ | Li3+ | C5+/C6+
IRFQ, μA | 3000 | 2000 | 3600 | 520 | 10000 | 12000
ICF-1, μA | 500 | 500 | 500 | 38 | 430 | 400
ICF-4, μA | 400 | 100 | 420 | 30 | 340 | 320
Intensity, ppc | 8x108 | 2.2x109 | 2x109 | 1.8x108 | 2x109 | 3.5x108
SPI
LEBT
RFQ
MEBT
LU-20
100%
80%
70%
16%
8-12%
Measured parameters of accelerated beam
HEBT
Nuclotron
3-10%
SPI
LEBT
RFQ
MEBT+ Buncher
LU-20
100%
80%
70%
50%
25-38%
HEBT
Nuclotron
10-32%
Obtained results (run 54)
Theoretical beam loss (with buncher)

## Slide 12: Next steps
Buncher installation in front of LU-20 and MEBT (ITEP)
Replacement of debuncher at transportation channel from LU-20 to Nuclotron (INR RAS).
Beam diagnostics.
Replacement of power supplies for elements of transportation channel.
Channel optics optimization.
Buncher tuning and installation (april 2017)

## Slide 13: Heavy ions linac (HILAc)
Heavy Ions Linear Accelerator
NICA Injector for Au31+ 3.2 MeV/u
to Booster & Nuclotron
In collaboration with
“BEVATECH OHG”(Germany),
JINR, INR, ITEP(Russia).

## Slide 14: HILAc design parameters

## Slide 15: RF Amplifiers
RFQ
IH2
IH1
Three solid state amplifiers,
100MHz, 10Hz rate:
140 kW, 340 kW, 340 kW
Operational vacuum @ 5,5*10-7 mbar
Achieved vacuum conditions @ 7*10-8 mbar
Max. pulse length RF: 200 μs

## Slide 16: Krion-6T ESIS
 | Project | At test bench | At Nuclotron run #50 (2014)
Element | Au31+ | Tu50+ | Ar16+
Ion intensity, ppp | 1.4x109 | 3x107 | 4x108
Magnetic field, T | 6 | 5.4 | 4.6
Extraction time from ESIS, μs | 8 - 30 | 8 | 8
Energy of electron string, keV | 25 | 9-10 | 5-6
RMS emittance | 0.6 π mm mrad (for 8 μs extraction time) 0.15 π mm mrad (for 30 μs extraction time) |  | 
Plans:
1) Preparation for Ar16+ and Kr26+ injection in 2017.
2) Improvement of internal Au and Bi injection.
3) Experiments in Au production in magnetic field up to 6Т.

## Slide 17: Laser ion source and LEBT
LEBT: Ein=3 keV/u Eout=17 keV/u

## Slide 18: RFQ

## Slide 19: Buncher+IH1+IH2
DTL structure «KONUS» (KOmbinierte NUll grad Struktur) – combined structure with zero synchronous phase.

## Slide 20: Test bench for HILAc comissioning
D1
T1
S2v, S2h
D2
T2
CT1
PP1
CT2
PP3
PP2
FC-Faraday cup, S-steerer, CT-current transformer, PP-phase probe,
D-doublet, T-triplet, B-buncher.
Experimental Eout= 3.2 MeV
FC
Analyzing
magnet
Source
RFQ
IH 1
IH 2
B

## Slide 21: C3+ ions from Laser Ion Source
Phase probe’s signals
MEBT (red), IH1(blue), IH2(green)
Current transformer’s
and Faraday cup signals

## Slide 22: C3+ ions from Laser Ion Source
Energy spectrum after HILAc
Experimentally found energy ≈ 3.2 MeV
RFQ at nominal energy of 300 AKeV
Experimental energy matches with design parameters of HILAc

## Slide 23: Next steps
Development of transportation channel from HILAc to Booster.
Debuncher installation (already manufactured and delivered by Bevatech).
ESIS source installation.
HILAc’s LEBT optimization (drift space should be shorter due to beam dynamics calculations).
Beam diagnostics.
Thank you for attention!