## Slide 1
Optimization of the Collider rings’ optics
O.S. Kozlov, S.A. Kostromin
LHEP, JINR, Dubna
Machine Advisory Committee, JINR, Dubna, May 22-23, 2017

## Slide 2
Collider project parameters
Composition of the rings
Dynamic Aperture calculations
Contents
Collider optics, MAC 2017

## Slide 3
Circumference, m | 503.04 |  | 
Number of bunches | 22 |  | 
Rms bunch length, m | 0.6 |  | 
Beta-function at IP, m | 0.35 |  | 
Betatron tunes, Qx / Qy | 9.44 / 9.44 |  | 
Chromaticity, Q’x / Q’y | -33 / -28 |  | 
Ring acceptance, mmmrad | 40 |  | 
Long. acceptance, p/p | 0.010 |  | 
Gamma-transition, tr | 7.088 |  | 
Ion energy, GeV/u | 1.0 | 3.0 | 4.5
Ion number per bunch | 2.0∙108 | 2.4∙109 | 2.3∙109
Rms p/p, 10-3 | 0.55 | 1.15 | 1.5
Rms beam emittance, hor/vert, (unnormalized), mmmrad | 1.1/ 0.95 | 1.1/ 0.85 | 1.1/ 0.75
Luminosity, cm2s1 | 0.6∙1025 | 1.0∙1027 | 1.0∙1027
IBS growth time, sec | 160 | 460 | 1800
Tune shift, Qtotal =QSC +2 | -0.050 | -0.037 | -0.011
1. Collider project parameters
Collider optics, MAC 2017

## Slide 4
1. Collider ring composition
M: horizontal dipole magnet, L=1940mm oq: space QF/QD-CP, L=100mm
QF, QD: regular quadrupole magnet, L=470mm odd: space Dipole-Dipole, L=300mm
MC: multipole corrector, L=300mm od: space Dipole-MC, L=265mm
CP: X,Y dipole corrector+Beam PickUp, L=300mm
Arc: FODO periodic Cell
Collider optics, MAC 2017

## Slide 5
1. Collider ring composition
Arc, missing dipole Cells: – Injection, Dump, Dispersion suppressor.
Lower Ring 1, Upper Ring 2 - Arc North-East side
Collider optics, MAC 2017

## Slide 6
1. Collider ring composition
Arc, missing dipole Cells: – Injection, Dump, Dispersion suppressor.
Lower Ring 1, Upper Ring 2 Arc South-East side
Collider optics, MAC 2017

## Slide 7
1. Collider ring composition
Straight sections South: SPD
Collider optics, MAC 2017
Straight sections North: MPD

## Slide 8
2. Nonlinearities of the magnetic field in Collider
1. Dipole/Quadrupole harmonics
Collider optics, MAC 2017
2. Chromaticity correction Sextupoles
3. Fringe Fields, Final Focus Quads in particular
(ΔB/B) n ~ 10-4 expected values at Rbeam
Tune spread over the momentum acceptance ±4p before (1) and after (2) correction
Natural chromaticities: Q’x=-33, Q’y=-28 (Q’x,y~20 from 2 IPs)
Corrected chromaticities: Q’x,y=0
Ncorr=24, G’max=150T/m2
Gradient in QFF1 vs. Longitudinal coor. @ I=10.3kA

## Slide 9
2. Nonlinearities: Fringe Fields
Fringe Field effect in quadrupole:
Collider optics, MAC 2017
Δθ/θ ~ β2 ·k2 · L·ε
=> To decrease Fringe Field effect:
- Increase Quadrupole length  Decrease Quadrupole strength k;
Decrease beta-function in Lense β (or Decrease IP-QFF1 distance) or Increase β* in IP ;
Decrease Emittance ε.
Fringe Fields in ALL elements are taken into account in MADX

## Slide 10
Collider optics, MAC 2017
Q-diagram and Resonances
Resonance diagram up to 5th order.
Collider Working points and sp. ch. Tune Shifts at 1 / 4.5 GeV/u
Betatron tunes Qx/Qy regulation: 1. Quadrupole correctors (trim-quads) in long straight sections (tune regulation and matching conditions); 2. Arc quadrupoles (strong change of tune, Q=89.5 ), Imax=11kA;
Nominal Betatron Tunes x=y=0.420.44 require for effective Stochastic Cooling in Energy range 34.5 GeV/u;
Qx/Qy=9.10 – second possible working point: ECool up to 3GeV/u, larger DA

## Slide 11
Collider optics, MAC 2017
Original Lattice: Qx,y =9.44/9.44, β* =0.35m
3. Dynamic Aperture calculations

## Slide 12
Collider optics, MAC 2017
3. Dynamic Aperture calculations
X plane
Y plane
Chrom. Corr. ON
Fringe Field OFF
Chrom. Corr. ON
Fringe Field ON

## Slide 13
Collider optics, MAC 2017
Lattice: Qx,y =9.44/9.44, β* =0.5, 0.6, 0.7, 1.0m
3. Dynamic Aperture calculations
β* = 1.0m

## Slide 14
Collider optics, MAC 2017
Lattice: Qx,y =9.44/9.44, intermediate β* = 0.6m
3. Dynamic Aperture calculations

## Slide 15
Collider optics, MAC 2017
3. Dynamic Aperture calculations
X plane
Y plane
Chrom. Corr. ON
Fringe Field OFF
Chrom. Corr. ON
Fringe Field ON

## Slide 16
Collider optics, MAC 2017
3. Dynamic Aperture calculations
X plane
Y plane
Chrom. Corr. ON
Fringe Field OFF
Chrom. Corr. ON
Fringe Field ON
Qx,y =8.10/10.10

## Slide 17
Collider optics, MAC 2017
Conclusions 1
Increase β* at IP increase DA: 0.35m DA<GA, 0.6m DA≥GA ;
For β*=0.6m the required luminosity at Ek =3÷4.5 GeV/u of L=1•1027 cm-2s-1 will be achieved with ~15% higher bunch intensity;
Ring tunes Qx,y =9.44/9.44 chosen as a project base option due to S-Cooling reasons ;
Tunes qx,y =0.10/0.10 (Qx,y =8.10/10.10) show a largest aperture DA>GA

## Slide 18
Collider optics, MAC 2017
3. Dynamic Aperture calculations (continued)
- Optics for two beams optimization
- Nominal Working point Qx,y =9.44/9.44
Qx,y =9.44/9.44, β* =0.60m

## Slide 19
Collider optics, MAC 2017
3. Dynamic Aperture calculations (continued)
- Optics for two beams
- Working point Qx,y =9.44/9.44
Quadrupoles in straight sections A and B

## Slide 20
Collider optics, MAC 2017
3. Dynamic Aperture calculations (continued)
Qx,y =9.10/9.10, β* =0.60m
- Move to Working point Qx,y =9.10/9.10 by qF, qD Quads strength adjustment

## Slide 21
Collider optics, MAC 2017
3. Dynamic Aperture calculations
X plane
Y plane
Chrom. Corr. ON
Fringe Field OFF
Chrom. Corr. ON
Fringe Field ON
Qx,y =9.12/9.12

## Slide 22
Collider optics, MAC 2017
3. Dynamic Aperture calculations
“Artificial” Tune Scan (by the phase advance adjusting matrix) along the coupling resonance.
JINR
BINP

## Slide 23
Collider optics, MAC 2017
Conclusions 2
Anti-symmetric optics suitable for both rings compiled;
Half-Ring-A differs from Half-Ring-B in Straight Sections Quads strength ;
Tunes Qx,y =9.10/9.10 produced by 4% decrease of main Quads qF, qD strenght;
Point 9.10/9.10 has largest DA›GA, will be used at StartUp;
Point 9.44/9.44 preferable for S-cooling has a smaller DA

## Slide 24
Collider optics, MAC 2017
Conclusions 3: Tasks to Do

## Slide 25
Thank you for your attention !