## Slide 1: Stochastic cooling system: Start-up and project modes
NICA MAC 2017
I.Gorelyshev, N.Shurkhno, A.Sidorin

## Slide 2: Nuclotron-based Ion Collider fAcility
Tasks:
Beam accumulation(at low intensities)
Longitudinal emittance reduction during the bunching
Luminosity preservation(IBS counteration)
Stochastic cooling system – one of the crucial elements of NICA project

## Slide 3
Start-up mode | Project mode
RMS bunch length 1,2 m | RMS bunch length 0,6 m
URF = 50 kV | URF < 1000 kV
h = 22 | h = 66
Ions 179Au97+ | 
ε⫠max= 1,1 π mm mrad | 
Energy range 3-4,5 GeV/u | 
Bandwidth 2-4 GHz | 
Only longitudinal cooling | 3-D cooling

## Slide 4
Project mode
IBS calculations: BETACOOL
σs = 60 cm
Structures compared:
3-D cooling
IBS simulation condition

## Slide 5: Luminosity
ΔQ = 0,05
Lmax = 1027сm-2s-1
βIP, m | 0,35 | 0,7 | 1,0
E, GeV/u | 3.0 | 3.2 | 3.4
N, 109 | 2.3 | 2.85 | 3.25
Project luminosity attainment

## Slide 6: Intrabeam scattering
In the range from 3,3 to 4,5 GeV/u IBS times for compared structures does not significantly depend on βIP and are about (700-1800 s)
Requirement: cooling rates has to exceed IBS rates

## Slide 7: Bandwidth & Working Point
Bandwidth 2-4 GHz
Having bandwidth 2 – 4 GHz we have the absence of overlapping 1.5 – 4.6 σp
Preferable working point is

## Slide 8: Cooling Acceptance
At energies below 3.9 GeV/u cooling by the filter method does not cover the whole separatrix, which leads to additional beam loss.
The Filter method is rejected for the project mode due to the low acceptance

## Slide 9: Cooling times(at optimal gain)
Time-of-Flight method does not provide faster cooling tempo than tempo of IBS heating.
Only Palmer method satisfied the requirements and it is chosen for the project mode.

## Slide 10
Drift force is not linear
The core is cooled faster than the tail

## Slide 11
E=3Gev/u | β*=35cm | β*=70cm | β*=100cm
IBS/CoolRMS | 2,034 | 2,543 | 2,464
IBS/CoolFWHM | 5,110 | 5,584 | 5,302
For the project mode the Palmer cooling rates 2-5 times exceed the IBS rates at any discussing choice of β–function in the interaction point

## Slide 12
Start-up mode
σs ≤ 120 см
Longitudinal cooling only
IBS simulation condition

## Slide 13: Intrabeam scattering
Required luminosity for start-up mode L = 5∙1025cm-2s-1

## Slide 14: Bandwidth & Cooling Acceptance
Separatrix covered:
Palmer: >1,7 GeV/u
Filter: >2,5 GeV/u
Absence of band overlapping > 6σp
Palmer and Filter methods are allowed to be implemented by acceptance criterion.
Filter method provides faster cooling rates therefore it is chosen for the start-up mode.

## Slide 15: Luminosity (at equal IBS/Cooling rates)
for project luminosity
For the core of the distribution the stochastic cooling system provides the required cooling rates

## Slide 17
Power & Gain
Output peak power is chosen
500 Watt/channel
Mode | Start-up | Project
Long. cool. method | Filter | Palmer
Optimal gain, dB | 69 | 91
Equipment losses, dB | 67 | 37
Total gain, dB | 136 | 128
Gain is chosen 140 dB

## Slide 18
List of Equipment
Low power(<–30dBm): Pickups, Low noise Preamplifiers, Couplers
Medium power: Preamplifiers, Feeder Cable, Optical Comb Filter,
Attenuators, Phase Shifters
High power(>30dBm): Main Amplifiers, Dividers, Kickers

## Slide 19
Placement & Delay
Variable delay:
Range 32 ns
Precision 1 ps
Min. constant delay:
Channel 1 – 595 ns
Channel 2 – 490ns
Channel 1
Channel 1’
Channel 2
Start-up mode:
Longitudinal channel 1
(Equipment own delay 452 ns)
Project mode:
Longitudinal channel 2 (473 ns)
Transverse channels 1, 1’ with combined kicker
(405 ns, 418 ns)
There is a reserve in delay for all channels and modes
+

## Slide 20
Pickups, Kickers & Main Amplifiers
FZJ Ring-slot couplers are chosen as Pickups & Kickers
Basic structure – 16 rings
High Impedance
Purchase list:
Pickup – 2 basic structures
Kicker – 4 basic structures
6 pickups & 4 kickers in total
16 amplifiers per kicker
100 amplifiers in total
Negotiations with FZJ concerning pickups & kickers are on the way
Main 30W Amplifiers R&D is in progress (OKB TSP, Minsk)
30W amplifier
per each pair of
combiner boards
Kicker dissipates ~ 120 Watt

## Slide 21
Diagnostics
Schottky diagnostics
BTF measurements
Power meter
Signal Spectrum Analyzer
4-channel Vector Network Analyzer
Equipment
is being purchased

## Slide 22
Status & Plans
Equipment | Status |  | Plans | 
Diagnostics | Being Purchased |  | Finished by the end of 2017 | 
Optical Comb Filter | Components being purchased |  | Purchased (III 2017) | Assembled (I 2018)
4 Kickers | Test bench Production | Negotiations (FZJ) | First Tests (III-IV 2017) | Production + Assembly 1 unit/year starting 2018
6 Pickups | Negotiations (FZJ) |  | Production + Assembly 1 unit/year starting 2018 | 
Main amplifiers | R&D |  | R&D finished (end 2017) | 16 units/yr starting 2018
Electronics | Being purchased |  | Purchase + Assembly 1 channel/year starting 2018 | 
More detailed plan is in the database

## Slide 23
Beam Transfer Function:
Nyquist diagrams of
41 harmonics measured
Recent results

## Slide 24
BTF measurements at FZJ

## Slide 25
Conclusions
Stochastic cooling system can provide the required luminosity at any discussing beta-function in the interaction point for both Start-up and Project modes.
For longitudinal cooling in the Start-up mode the Filter method is chosen, Palmer method is chosen in the Project mode. Also main parameters are defined.
For the Start-up mode the stochastic cooling system provides the required cooling rates for the core of the distribution. Evolution of the distribution function tails has to be investigated numerically.
Equipment purchasing is started, main amplifiers R&D is in progress, negotiations with FZJ concerning pickups and kickers are on the way.

## Slide 26
Thank you for attention