## Slide 1
Lattice and Dynamic Aperture
of the NICA Collider
O.S. Kozlov, S.A. Kostromin
LHEP, JINR, Dubna
XII Международный семинар по проблемам ускорителей заряженных частиц, г.Алушта, 4 сентября, 2017

## Slide 2
Collider project parameters
Composition of the rings
Dynamic Aperture calculations
Contents

## Slide 3
Beams – p,d(h)..197Au79+
Collision energy √s= 4-11 GeV/n (Au), 12-27 (p)
Beam energy (fixed target) - 1-6 GeV/n
Luminosity: 1027 cm-2s-1(Au), 1032 (p)
Experiments:
2 Interaction points – MPD and SPD
Fixed target experiment BM@N
NICA Complex

## Slide 4
Nuclotron (45 Tm)
injection of one bunch
of  2×109 ions,
acceleration up to
1 - 4.5 GeV/u max.
Linac LU-20
Ion sources
Fixed Target Area
Booster (25 Tm)
1(2-3) single-turn injection,
storage of (2  4)×109 ions,
acceleration up to 100 MeV/u,
electron cooling, acceleration
up to 578 MeV/u
Two SC
collider rings
Linac HILac
KRION
IP-1
IP-2
~ 2 x 22 injection cycles
22 bunches per ring
Facility operation scenario
Stripping (80%) 197Au31+ => 197Au79+
NICA structure and operation regimes. (Heavy Ion Mode)

## Slide 5
Circumference, m | 503.04 |  | 
Number of bunches | 22 |  | 
Rms bunch length, m | 0.6 |  | 
Beta-function at IP, m | 0.35 |  | 
Betatron tunes, Qx / Qy | 9.44 / 9.44 |  | 
Chromaticity, Q’x / Q’y | -33 / -28 |  | 
Ring acceptance, mmmrad | 40 |  | 
Long. acceptance, p/p | 0.010 |  | 
Gamma-transition, tr | 7.088 |  | 
Ion energy, GeV/u | 1.0 | 3.0 | 4.5
Ion number per bunch | 2.0∙108 | 2.4∙109 | 2.3∙109
Rms p/p, 10-3 | 0.55 | 1.15 | 1.5
Rms beam emittance, hor/vert, (unnormalized), mmmrad | 1.1/ 0.95 | 1.1/ 0.85 | 1.1/ 0.75
Luminosity, cm2s1 | 0.6∙1025 | 1.0∙1027 | 1.0∙1027
IBS growth time, sec | 160 | 460 | 1800
Tune shift, Qtotal =QSC +2 | -0.050 | -0.037 | -0.011
1. Collider project parameters

## Slide 6
Designations and numbering of the Collider elements
1) 1st collider ring - “Red", lower, direction of beam movement - counter-clockwise
2) 2nd collider ring - "blue", the upper, the direction of the beam - clockwise.
Designations and numbering of structural elements:
The collider consists of the eastern (E) and western (W) superperiods. They begin and end at the collision points (MPD-SPD). The super period includes a corresponding arch and two halves of Long Straight sections.
2) The Interaction Region MPD is the "northern“ straight section, the Interaction Region SPD is the "southern“ one.
3) The sequence numbering of the elements starts from the Interaction Points in MPD or SPD in the direction of the beam movement in the corresponding ring.
4) The designation of an element consists of:
a) type designations:
Q is the quadrupole magnet
QT - tuning quadrupole magnet
QFF - quadrupole magnet of final focusing of beams
M - dipole magnet
BV - dipole magnet of the system of vertical reduction / separation of beams
MS - correcting magnet (multipole)
CP - correcting magnet (dipole) + beam position monitor
b) the sequence number of the element
c) an index giving an accessory to the superperiod (W or E)
d) an index giving an accessory to the ring (1 or 2)
For example, Q20E2 is a regular quadrupole magnet in the eastern arch, 20th from the collision point of the beams in the MPD.
The index of the ring (1 or 2) is absent for the elements in the sections common to both beams.
List of elements of the collider (without indexes belonging to the super period and the ring):
Q1 - Q39 - quadrupole magnets (Q8 - Q32 - in the arches)
QT1 - QT10 - Trim Quadrupole Magnets in Straight Gaps
QFF1 - QFF6 - quadrupole magnets of the final focusing of beams
BV1 - BV4 - dipole magnets of vertical reduction / separation of beams
MC1-MC33 - multipole correcting magnets (MC6 - MC28 - in arches)

## Slide 7
1. Collider rings composition

## Slide 8
1. Collider ring composition
Arc: FODO periodic Cell
M: horizontal dipole magnet, L=1940mm, Bmax=1.8T oq: space QF/QD-CP, L=100mm
QF, QD: regular quadrupole magnet, L=470mm, Gmax=23T/m odd: space Dipole-Dipole, L=300mm
MC: multipole corrector, L=300mm od: space Dipole-MC, L=265mm
CP: X,Y dipole corrector+Beam PickUp, L=300mm

## Slide 9
1. Collider rings composition
Arc, missing dipole Cells: – Injection, Dump, Dispersion suppressor.
Lower Ring 1, Upper Ring 2 - East Arc - North side

## Slide 10
1. Collider rings composition
Arc, missing dipole Cells: – Injection, Dump, Dispersion suppressor.
Lower Ring 1, Upper Ring 2 - East Arc - South side

## Slide 11
1. Collider rings composition
Straight sections North: MPD

## Slide 12
1. Collider rings composition
Straight sections South: SPD

## Slide 13
1. Collider ring composition
Beta-functions in Straight section. β* @ IP = 0.6m.

## Slide 14
1. Collider ring composition
Twiss-functions in Half of the Ring. Qx,y =9.44/9.44, β*=0.6m.
No coupling correction. Bs_MPD=0.6T, Bs_Ecool=0.2T

## Slide 15
1. Collider ring composition
Beta-functions of the Ring. X/Y-Coupling correction.
4 Families of Skew Quads in Drifts. Gmax=1.8 T/m

## Slide 16
1. Collider ring composition
Dy-Dispertion correction.
2 Families of Skew Quads in arcs. Gmax=4T/m

## Slide 17
2. Nonlinearities of the magnetic field in Collider
1. Dipole/Quadrupole harmonics
2. Chromaticity correction Sextupoles
3. Fringe Fields, Final Focus Quads in particular
(ΔB/B) n ~ 10-4 expected values at Rbeam
Tune spread over the momentum acceptance ±4p before (1) and after (2) correction
Natural chromaticities: Q’x=-33, Q’y=-28 (Q’x,y~20 from 2 IPs)
Corrected chromaticities: Q’x,y=0
Ncorr=24, G’max=150T/m2
Gradient in QFF1 vs. Longitudinal coor. @ I=10.3kA

## Slide 18
2. Nonlinearities: Fringe Fields
Fringe Field effect in quadrupole:
Δθ/θ ~ β2 ·k2 · L·ε
=> To decrease Fringe Field effect:
- Increase Quadrupole length  Decrease Quadrupole strength k;
Decrease beta-function in Lense β (or Decrease IP-QFF1 distance) or Increase β* in IP ;
Decrease Emittance ε.
Fringe Fields in ALL elements are taken into account in MADX code

## Slide 19
Q-diagram and Resonances
Resonance diagram up to 5th order.
Collider Working points and Space Charge Tune Shifts at 1/4.5 GeV/u
Betatron tunes Qx/Qy regulation: 1. Quadrupole correctors (trim-quads) in long straight sections (tune regulation and matching conditions); 2. Arc quadrupoles (strong change of tune, Q=89.5 ), Imax=11kA;
Nominal Betatron Tunes x=y=0.420.44 require for effective Stochastic Cooling in Energy range 34.5 GeV/u;
Qx/Qy=9.10 – second possible working point: ECool up to 3GeV/u, larger DA

## Slide 20
3. Dynamic Aperture calculations
Dynamic Aperture: A(x,y)= Ax,y(s,Nturn )
in optimal collider lattice: Ax,y(s)>Mx,y(s), Mx,y(s) – vacuum chamber
good reserve: Ax,y(s)=2Mx,y(s);
DA calculation methods:
PTC - Polymorphic Tracking Code, (MAD-X):
Symplectic tracking;
Nonlinearities of magnetic elements (chromaticity sextupoles, systematic/random errors in dipoles/quadrupoles);
Fringe fields of all magnetic elements;
2. Thin-lens tracking, (MAD-X): Symplectic tracking;
Beam-beam interactions in IPs;
Space charge forces.

## Slide 21
Original Lattice: Qx,y =9.44/9.44, β* =0.35m
3. Dynamic Aperture calculations

## Slide 22
3. Dynamic Aperture calculations
X plane
Y plane
Chrom. Corr. ON
Fringe Field OFF
Chrom. Corr. ON
Fringe Field ON

## Slide 23
Lattice: Qx,y =9.44/9.44, β* =0.5, 0.6, 0.7, 1.0m
3. Dynamic Aperture calculations
β* = 1.0m

## Slide 24
Lattice: Qx,y =9.44/9.44, intermediate β* = 0.6m
3. Dynamic Aperture calculations

## Slide 25
3. Dynamic Aperture calculations
X plane
Y plane
Chrom. Corr. ON
Fringe Field OFF
Chrom. Corr. ON
Fringe Field ON

## Slide 26
3. Dynamic Aperture calculations
X plane
Y plane
Chrom. Corr. ON
Fringe Field OFF
Chrom. Corr. ON
Fringe Field ON
Qx,y =8.10/10.10

## Slide 27
Conclusions 1
Increase β* at IP increase DA: 0.35m DA<GA, 0.6m DA≥GA ;
For β*=0.6m the required luminosity at Ek =3÷4.5 GeV/u of L=1•1027 cm-2s-1 will be achieved with ~15% higher bunch intensity;
Ring tunes Qx,y =9.44/9.44 chosen as a project base option due to S-Cooling reasons ;
Tunes qx,y =0.10/0.10 (Qx,y =8.10/10.10) show a largest aperture DA>GA

## Slide 28
3. Dynamic Aperture calculations (continued)
- Optics for two beams optimization
- Nominal Working point Qx,y =9.44/9.44
Qx,y =9.44/9.44, β* =0.60m

## Slide 29
Collider optics, MAC 2017
3. Dynamic Aperture calculations (continued)
- Optics for two beams
- Working point Qx,y =9.44/9.44
Quadrupoles in straight sections A and B

## Slide 30
3. Dynamic Aperture calculations (continued)
Qx,y =9.10/9.10, β* =0.60m
- Move to Working point Qx,y =9.10/9.10 by qF, qD Quads strength adjustment

## Slide 31
3. Dynamic Aperture calculations
X plane
Y plane
Chrom. Corr. ON
Fringe Field OFF
Chrom. Corr. ON
Fringe Field ON
Qx,y =9.12/9.12

## Slide 32
3. Dynamic Aperture calculations
“Artificial” Tune Scan (by the phase advance adjusting matrix) along the coupling resonance.

## Slide 33
Conclusions 2
Anti-symmetric optics suitable for both rings compiled;
Designations and numbering of elements of the collider Rings have been introduced;
Half-Ring-A differs from Half-Ring-B in Straight Sections Quads strength ;
Tunes Qx,y =9.10/9.10 produced by 4% decrease of main Quads qF, qD strenght;
Point 9.10/9.10 has largest DA›GA, will be used at StartUp;
Point 9.44/9.44 preferable for S-cooling has a smaller DA

## Slide 34
Conclusions 3: Tasks

## Slide 35
Thank you for your attention !