## Slide 1: Ion storage, bunch formation and parasitic collisions in collider NICA О.Brovko1, A. Eliseev1, O.Kozlov1, N.Mitjanina2, V.Petrov2, A.Sidorin1, A.Smirnov1, E.Syresin1, A.Tribendis2 1) JINR, Dubna, Russia, 2) BINP, Novosibirsk, Russia
The RF barrier buckets provide the ion storage in collider NICA. Parasitic collisions take place in the interaction point for the ion stacks. To compensate these parasitic collisions the ion orbit bump and an increase of betta function up 2.5 m in collision point will be realized. The RF2 system provides bunching on 22 harmonics at adiabatic RF voltage increase. Rebucketing in RF3 system is realized when longitudinal bunch size is reduced to value smaller separatrix of 66 harmonics. Cooling and further adiabatic increase of RF voltage provide requered for colliding experiments bunch length.

## Slide 2: Longitudinal Bunch parameters after Nuclotron
After stripping foil - εrms = 3.2 eV·s (Au+79).
 | 1 GeV/u | 1.5 GeV/u | 2.5 GeV/u | 3.5 GeV/u | 4.5 GeV/u
σs (m) | 4.5 ÷ 9 | 3.7÷ 7.4 | 2.8 ÷ 5.6 | 2.1 ÷ 4.2 | 1.7 ÷ 3.4
σp | 1.4·10-4 ÷ 0.7·10-4 | 1.3·10-4 ÷ 0.65·10-4 | 1.2·10-4 ÷ 0.6·10-4 | 1.2·10-4 ÷ 0.6·10-4 | 1.2·10-4 ÷ 0.6·10-4
Number of ions - 1÷1.5 109
Maximum possible rms bunch length is 9 m
Rms momentum spread is below 1.4·10-4 in the total energy range
Rms horizontal emittance 0.5 mmmrad, r.m.s. vertical emittance
0.25 mmmrad at ion energy 1GeV/n

## Slide 3: NICA collider parameters
Ring circumference, m | 503,04 |  | 
Number of bunches | 22 |  | 
Rms bunch length, m | 0.6 |  | 
Beta-function in the IP, m | 0.35 |  | 
Betatron tunes, Qx/Qy | 9.44/9.44 |  | 
Ring acceptance | 40 mmmrad |  | 
Long. acceptance, p/p | ±0.010 |  | 
Gamma-transition, tr | 7.088 |  | 
Ion energy, GeV/u | 1.0 | 3.0 | 4.5
Ion number per bunch | 2∙108 | 2.4∙109 | 2.3∙109
Rms dp/p, 10-3 | 0.55 | 1.15 | 1.5
Rms beam emittance, h/v, (unnormalized), mmmrad | 1.1/ 0.95 | 1.1/ 0.85 | 1.1/ 0.75
Luminosity, cm2s1 | 0.66e25 | 1e27 | 1e27
IBS growthe time, sec | 160 | 460 | 2000
R.m.s momentum spread
at equilibrium between IBS and
electron or stochastic cooling

## Slide 4: Beam preparation scheme
Beam storage at the experiment energy
RF barrier bucket system (RF1)
Allowing storage of the required beam intensity at half ring circumference Cring/2. Accumulation efficiency ~ 95%, about 44 - 100 injection pulses (22-50 to each ring) every 5 sec. Total accumulation time is about 6 min. RF1 can be used for acceleration ions if injection energy is less then energy of experiment RF1 generates accelerating voltage 250-300 V.
1st narrow-band RF system (RF2)
Operating at 22 harmonics of revolution frequency; it provides the beam bunching.
2nd narrow-band RF system (RF3)
Operating at harmonics number 66, that provides the bunch length necessary for collision experiments.

## Slide 5
Barrier RF system (1-st RF)
accumulation
barriers are switched off
coasting beam
2-nd RF system (h=C/23m=22)
1/3
bunching with adiabatic RF increase
Stop at length of 1/3 of bucket
3-d RF system (h=h2x3=66)
rebucketing adiabatic RF increase
bunch has final parameters
Scheme of RF cycle in collider

## Slide 6: Main parameters of RF systems
RF2
RF3
RF1
RF3
RF3
RF3
Parameters | RF1 | RF2 | RF3
Frequency, MHz | BB | 11.48-12.9 | 34.4-38.7
Total voltage amplitude, kV | 5 | 100 | 1000
Voltage per resonator, kV | 5 | 25 | 125
Number of resonators (per ring) | 1 | 4 | 8
RF1
IP
ECOOL

## Slide 7: Maximum luminosity
Betta function in collision point is minimal
=0.35 m and =0.6 m
2. Collision frequency is maximal, Number of bunches nb =22
to avoid parasitic collisions in IP region with length 23 m
3. Bunch length is minimal b=0.6 m to reduce hour-glass effect
in collision point, further reduction of bunch length
became to increase of peak current and betatron tune shift
4. Phase density in bunch is maximal Nb/
5. Bunch intensity is maximal Nb

## Slide 8: Incoherent betatron tune shift
Qtot=Qsp+2
tune shift of bunched beam at experiment parameters
Qsp-bunch=-(
Qsp-bunch= - 0.035/0.014 at ion energy 1/4.5 GeV/n
Beam- beam parameter of bunched beam at experiment parameters
bunch=
bunch= 0.004/0.0014 at ion energy 1/4.5 GeV/n
Stack beam at maximal storage ion intensity
stack= 0.004/0.0014 at ion energy 1/4.5 GeV/n
Qsp-stack= -0.013/0.005 at ion energy 1/4.5 GeV/n
Qsp-bunch N/(nb
Stack beam at maximal storage ion intensity
Qsp-stackN/(Cring /2)
Qsp-bunch/Qsp-stack=(Cring/2)/(nb
bunchN/nb
stackNlcol/(Cring /2)
bunch/stack=(Cring/2lcol)/nb=1

## Slide 9: 5 order sum resonances

## Slide 10: Bumps of ion orbits in collision region at storage of ion beams
Four correctors from each side of colliding region in two rings will be used for correction of ion orbit in colliding region.
At storage of ion beams in collider rings these correctors are planed to used for bump of ion orbits of counter propagating beams in collision region. The correctors provide 1 mrad deflection angle (magnetic field is 0.1 T, corrector length is 30 cm) and vertical displacement of centers gravity of ion beams on distance =10 mm.
Bump of ion orbit in collision region
Ion trajectories at bump of orbits
O. Kozlov simulations,
β*=0.6m, sigma_x,y, =0.8 mm
Counter propagating beams are separated only In collision point.

## Slide 11: β* variation at storage of ion beams
Twiss-parameters for a quarter of the ring, β* variation (O. Kozlov)
β*=0.6m
β*=2.5m
sigma_x,y, =0.8 mm
sigma_x,y, =1.65 mm

## Slide 12: Bump orbit at IP beta function 2.5 m
The correctors provide 0.5 mrad deflection angle (magnetic field is 0.075 T, corrector length is 30 cm) and vertical displacement of centers gravity of ion beams on distance =10 mm.
Beam envelope 6  in colliding region at bump orbit

## Slide 13: Reduction of parasitic collisions of stored ion beams
x,y, =1.65 mm
IP
This aperture permits to store two counter propagating ion beams with sizes of 6. Each beam center gravity is displaced in vertical direction on a distance 3=5 mm relatively to axis. The distance between beam center gravities is =6=10 mm
Lenses of final focus
=10-4.5 mm
x,y, =3.8-5.1 mm
In the lenses of final focus the counter propagating ion beams
with sizes of 6 are overlapping. However the centers of gravities for two counter propagating ion beams are displaced in vertical direction on distance of =2.5 - .
It permits to reduce beam-beam parameter  by a factor of 4-5 in regime of parasitic collisions, caused by collisions by ion tails, where number of colliding ions is reduced, and reduction of collision length.
β*=2.5m

## Slide 14: Parameters of Barrier Bucket (RF1)
Maximal voltage – 5 kV
Rectangular barrier with phase length – π/12
Stack phase zone – π (Nuclotron perimeter 251.5 м).
Kicker pulse = kicker forward front – 100 ns +
plateau – 200 ns +
back front- 410 ns =
710 ns = π-2π/12 = 5/6π
Injection zone = kicker plateau = 200 ns = 0.23 π (59 m>6)
Ion storage is realized with four moving barriers. Barriers with voltage 5kV and phase length π/12 capture ions with momentum spread p/p=0.01, corresponding to collider acceptance.
E=4.5 GeV/n

## Slide 15: RF Barrier Buckets scheme operation (BETACOOL simulation)
Particle distribution and
BB positions at ion storage
Ion injection
Injection zone=0.23 (59 m)
Stack zone= (251.5 m)
b)BB position at bunches merging
Barriers 2 and 3 moved adiabatically in counter directions
to provide equal momentum spread in injection and stack zones Barriers 3and 4 than switch off and injection portion merging with stack.
c)BB start to prepare space
for new injection
d)BB are displaced to initial
injection position, BB 2-3 should be appeared at injection
RF1 generates four pulses of RF voltage during one revolution period. Pulses 1 and 4 are used for stored ions, pulses 2 and 3 -for injected particles.
a)
b)
c)
d)

## Slide 16
Influence of pulse shape of barrier bucket RF voltage on ion phase motion in separatrix at ion storage
N. Mitjanina
At conservation of depth of potential well or square of pulse of RF voltage the results obtained for rectangular pulses are valid if the front duration less than 1/5 of pulse duration.

## Slide 17
Momentum spread evolution during accumulation

## Slide 18
Last injection cycle (t=233 sec)

## Slide 19
Evolution of particle number (black) and accumulation efficiency (green)
without beam cooling
0 50 100
Efficiency, %

## Slide 20: Increasing of accumulated particle number with cooling
Accumulation process and its efficiency
1.5 Gev/u
3.5 Gev/u
E > 3 GeV/u:
stacking with Stochastic cooling
E < 3 GeV/u:
Stacking with Electron cooling
Storage time corresponds to 200 s
at ion energy 1-2.5 GeV/n.
BETACOOL simulation with e – cooling.
E=1.5 GeV/u. (A.Smirnov)
Simulation with stochastic cooling.
E= 3.5 GeV/u. (T. Katayama)

## Slide 21
Ion energy, GeV/u | 1.5 | 2.5 | 4.5
Barrier height,(p/p)×10-3 | 0.87 | 1.08 | 2
Electron cooling rates, s-1 | 1.0 | 0.25 | 0.03
Without cooling, % | 68 | 70 | 74
With electron cooling, % | 93 | 91 | 93
Stacking efficiency (%) with moving barriers
Ion Energy, GeV/u | 1.0 | 4.5
Particle number, 109 | 1 | 1
RMS bunch length, m | 5.9÷17.5 | 2.5÷6.2
Momentum spread, 10-4 | 2.8÷0.95 | 2.1÷0.85
Parameters of the injected bunch

## Slide 22: RF2 for beam bunching
  RF2 voltage of 100 kV corresponds to case when longitudinal acceptance is larger than emittance of captured coasting ion beam
  Number of bunches nb =22 to avoid parasitic collisions in IP region with length 23 m
Final emittance is less than starting one (after accumulation) due to cooling.
Preparation of beam for collision occurs in two stages:
1. Adiabatic voltage increase in RF2 (h=22) until time when bunch is placed inside separatrix of 66 harmonic. (Under cooling the bunch shrinks not only in its length but in emittance as well)
  2. Then the bunch length becomes short enough it is intercepted into RF3 (h=66). Adiabatic voltage increase is going on.
The lowest possible RF2 voltage can be limited by 50 kV.

## Slide 23: Choice of the RF3 harmonics number
h3/h2 | L bucket in σs | V rf (kV) | Hbucket in σp
1 | ±18 | 1723 | ±11.5
2 | ±9 | 861 | ±5.7
3 | ±6 | 574 | ±3.82
4 | ±4.5 | 431 | ±2.9
5 | ±3.6 | 344 | ±2.29
4.5 GeV/u, σp = 1.710-3
RF3 voltage
Height of bucket in p at harmonic number more than h3/h2= 3 is less than 3p. RF voltage is enough large at h3/h2<3. Optimal value h3/h2=3.
Bunching + cooling
RF3 provides formation of required bunch length and momentum

## Slide 24: Thanks for your RF attention!