## Slide 1
NICA
Heavy Ion Linear Accelerator (HILAC)
commissioning
Levterov К. on behalf of Acceleration Department,
DUBNA, JINR LHEP
In collaboration with
“BEVATECH OHG”(Germany), Tomco (Australia)
JINR, INR(Russia).

## Slide 2
HILAC
(Heavy Ion Linear Accelerator)
3.2 MeV/u
Z/Amin=0.16
LINAC
LU-20
5 MeV/u
Z/Amin=0.33
Injection facility NICA

## Slide 3: TOPICS
RFQ commissioning results.
Total commissioning RFQ+IH1+IH2.

## Slide 4
4-rod RFQ
Au31+, Ein=17 keV/u Eout=300 keV/u
Estimation of output energy and transmission is Goal of RFQ commissioning

## Slide 5: EXPERIMENTAL SETUP
RFQ
LEBT
MEBT
ANALISING MAGNET
Electrodes
Accelerating tube
Buncher
D1
D2
Focusing
lenses
Osciloscope

## Slide 6
RFQ input
LEBT
Low Energy Beam Transport
Ein=3 keV/u Eout=17 keV/u
Electrodes
Accelerating
tube
Focusing magnet lenses
Steer

## Slide 7
LEBT
Low Energy Beam Transport
Ein=3 keV/u Eout=17 keV/u

## Slide 8
OUTPUT ENERGY
E=300 keV/u => β = 0.0253
STEPS :
Experimental searching for R at the given energy
Calculating βacc at the found R
β = [2(e/ mp с2) (Z/A) U]1/2
R= (mpс/e) β (A/Z) 1/B
R= 3,13 β A/Z 1/B

## Slide 9: OUTPUT ENERGY searching for R
Chart: No acceleration in RFQ
U=51 kV | Z/A | β | B, G | R, m
C2+ | 1/6 | 0,00430 | 484 | 1,665
C3+ | 1/4 | 0,00520 | 394 | 1,652
C4+ | 1/3 | 0,00603 | 340 | 1,669
<R>=1.662 m (+/-0.5%)
β = [2(e/ mpс2) (Z/A) U]1/2
R= (mpс/e) β (A/Z) 1/B
R= 3,13 β A/Z 1/B

## Slide 10: OUTPUT ENERGY
 | I magnet, A | B, kG | Urf p-p, mV | Uinj, kV | β +/_0.5%
C2+ | 88,60 | 2,88 | 823 | 102 | 0,0254
C3+ | 59,50 | 1,95 | 565 | 65 | 0,0258
C4+ | 44,00 | 1,45 | 442 | 49 | 0,0255
C5+ | 35,70 | 1,18 | 340 | 41 | 0,0261
C6+ | 29,70 | 0,97 | 283 | 34 | 0,0257
D+ | 29,70 | 0,97 | 283 | 34 | 0,0257
H+ | 14,50 | 0,48 | 144 | 17 | 0,0256
βуск = (e/mpC) (Z/A) BR
βуск = 0,319 Z/A BR

## Slide 11: RESULTS OF RFQ COMMISSIONING
OUTPUT ENERGY E~ 300 keV/u, experimentally approved for C6+, C5+, C4+, C3+, C2+, C1+, D+, H+
Transmission for C2+ ~ 80%, C2+ ~ 90% (desirable to be defined more exactly)

## Slide 12: Total commissioning RFQ+IH1+IH2

## Slide 13
- asynchronous beam injection with a surplus energy into structure with ‘fictional’ 0° synchronous particle, which defines only the drift tube structure
- Each accelerating section is followed by a transversal
focusing element
- At the entrance of each 0° synchronous particle
section the bunch must be longitudinally focused -35º.
DTL structure IH1 + IH2
Ein=300 keV/u Eout=3.2 MeV/u
«KONUS» (KOmbinierte NUll grad Struktur–нем.) – combined structure with zero synchronus phase.
IH, βλ/2 , TEM110.

## Slide 18
D1
T1
S2v, S2h
D2
T2
CT1
PP1
CT2
PP3
PP2
Experimental setup
S- steerer, CT-current transformer, PP-phase probe,
D- doublet, T- triplet, FC- Faraday cup
Experimental Eout= 3.2 MeV
Analizing
magnet
FC
FC

## Slide 19
OUTPUT ENERGY
E=3.2 MeV/u => β = 0.0826
STEPS :
Experimental searching for R at the given energy
Calculating βacc at the found R
β = [2(e/ mp с2) (Z/A) U]1/2
R= (mpс/e) β (A/Z) 1/B
R= 3,13 β A/Z 1/B

## Slide 20: OUTPUT ENERGY searching for R
U=51 kV | Z/A | β | B, G | R, m
C2+ | 1/6 | 0,00495 | 494 | 1,91
C3+ | 1/4 | 0,00606 | 392 | 1,92
C4+ | 1/3 | 0,00700 | 338 | 1,91
<R>=2.00 m (+/-0.5%)
β = [2(e/ mpс2) (Z/A) U]1/2
R= (mpс/e) β (A/Z) 1/B
R= 3,13 β A/Z 1/B
Uinj=69 kV

## Slide 21
Three stages of C3+ beam acceleration in HILAC

## Slide 22: ?OUTPUT ENERGY?
βуск = (e/mpC) (Z/A) BR
βуск = 0,319 Z/A BR
Acceleration | E, Mev/n | βexp | βth
RFQ | 0.282 | 0.0245 | 0.0253
RFQ+IH1 | 1.666 | 0.0596 | 0.0626
RFQ+IH+IH2 | 2.698 | 0.0758 | 0.0826

## Slide 23
Measurement of transmission.
RF control system.
Beam test with ESIS.
NEXT STEPS

## Slide 24: THANKS