## Slide 1: THE NEW DC-280 CYCLOTRON. STATUS AND ROAD MAP
G.G. Gulbekian, S.N. Dmitriev, Yu.Ts. Oganessian, B.N. Gikal, I.V. Kalagin, V.A.Semin, S.L. Bogomolov, I.A.Ivanenko, N.Yu.Kazarinov, G.N. Ivanov, N.F.Osipov
ALUSHTA, SARANTSEV 2017
FLEROV LABORATORY of NUCLEAR REACTIONS
JOINT INSTITUTE FOR NUCLEAR RESEARCH
Igor Kalagin

## Slide 2: Factory of Superheavy Elements – the main Goals
The Factory will be based on the new DC-280 cyclotron. The cyclotron will produce high intensity ion beams.
The cyclotron is being created in the new experimental building of the FLNR.
Synthesis of SHE and studying of their properties;
Search for new reactions for SHE-synthesis;
Study of chemical properties of SHE;
Because of extremely low (σ<50 fb) cross sections of reactions the experiments require high intensities of primary beams for the best statistics.

## Slide 3
PLAN OF THE FLEROV LABORATORY OF NUCLEAR REACTIONS
The project of the SHEF experimental building
The FLNR main building

## Slide 4
To satisfy the Goals, the DC-280 must have the following parameters of the ion beams:
Ion energy 4÷8 MeV/n
Ion masses 10÷238
Intensities (A~50) >10 pµA
Beam emittance less than 30 π mm·mrad
Efficiency of beam transfer >50%
THE NEW FLNR ACCELERATOR –
THE DC-280 CYCLOTRON
Ion energies correspond to total accelerating potential up to 40 MV

## Slide 5
 | Principles | Expected results
1. | High injection energy of ions (>50 keV/Z) | Decreasing of ion beam emittance (typical injection energy of 15÷20 keV/Z). Effective transportation of ions through injection. Better efficiency of capture into acceleration.
2. | Low magnetic field (<1.5 Т) | Larger beam starting radius. Lower power of the main magnet.
3. | High accelerating voltage (>100 kV) | Higher turns separation. Lower vacuum losses of ions.
4. | Beam extraction by the electrostatic deflector together with the flat-top system | Effective ion extraction. Better beam quality.
Basic principles of the DC-280 design

## Slide 6
Main RF-resonator
Magnet yoke
HV platform N1
(Umax=60 kV)
Electrostatic deflector
(Bender)
Separating magnet
DECRIS-PM
ECR-source
(Umax=20 kV)
Magnet coils
Ion beam extraction
Flat –top resonator
Vacuum pump
Accelerating tube
Actual configuration of the DC-280

## Slide 7
Ion sources | DECRIS-PM - 14 GHz on the 1-st HV platform Superconducting ECR on the 2-nd HV platform (developing stage)
Injection energy | Up to 80 keV/Z
A/Z range | 4÷7.5
Energy | 4÷8 MeV/n
Magnetic field level | 0.6÷1.3 T
K factor | 280
Dee voltage | 2x130 kV
RF power consumption | 2x30 kW
Flat-top dee voltage | 2x13 kV
Flat-top power consumption | 2x2 kW
Main design parameters of the DC-280

## Slide 8
ION | Z | Beam Intensity from ECR |  | HV platform N | Efficiency of acceleration | Expected beam intensities of (4÷8) MeV/n ions on targets pps
 |  | eA | pps |  |  | 
20Ne | 3 | 150 | 3.1014 | 1 | 50% | 1.5·1014
40Ar | 7 | 300 | 3.1014 | 1 | 50% | 1.5·1014
48Са | 7/8 | 160 | 1.3.1014 | 1 | 50% | 6.2·1013
50Ti | 8/9 | 80 | 6.2.1013 | 1 | 50% | 3.1.1013
54Cr | 9 | 125 | 8.1013 | 1 | 50% | 4.1013
58Fe | 9/10 | 125 | 8.1013 | 1 | 50% | 4·1013
64Ni | 10/11 | 125 | 8.1013 | 1 | 50% | 4·1013
70Zn | 11/12 | 100 | 5.1013 | 1 | 50% | 2,5.1013
136Хе | 22/23 | 150 | 4.1013 | 1 | 50% | 2·1013
209Bi | 34/35 | 15 | 2,2.1012 | 2 | 60% | 1·1012
238U | 39/40 | 1 | 1,5.1011 | 2 | 60% | 1.1011
Expected beam parameters of the DC-280

## Slide 9
N | Item
1 | Magnetic system
2 | RF system
3 | Beam injection system
4 | Beam extraction system
5 | Beam transport system
6 | Diagnostic system
7 | Vacuum system
8 | Water cooling system
9 | Control system
Main systems of the DC-280

## Slide 10: Magnetic system of ДЦ-280
Size of magnet yoke LхWхH | 8.76х4.08х4.84 m3
Pole diameter | 4 m
Gap between central plugs | 400 mm
Valley/hill gap | 500/208 mm/mm
Magnet weight | 1100 t
Magnet power | 300 kW
Maximal current | 1000 A
Magnetic field level | 0.6÷1.3 T
DC-280 magnet at the FLNR, February 2017
Magnet at the NKMZ, Ukraine (2014)
Magnet assembling (November 2016)
DC-280- isochronous cyclotron
Main coils made in N&V, Romania (2016)

## Slide 11
Magnet trimming coils
Number of radial trimming coils | 11
Number of azimuthal trimming coils | 8
Block of radial trimming coils
(EVPU, Slovakia)
Blocks of azimuthal trimming coils (GKMP, Bryansk, Russia)
Radial trimming coils
Azimuthal trimming coils
The radial trimming coils have been installed in the main magnet and are being used in magnetic measurements. The azimuthal trimming coils will be installed on magnet sectors after the end of the measurements in September 2017.

## Slide 12
Vacuum chamber of the DC-280 magnet
Vacuum chamber has been manufactured at the NKMZ plant.
Vacuum tests have been made at the FLNR (2016)
Working vacuum is 10-7 mBar

## Slide 13
Magnetic field measurements
The magnetometer with 14 Hall probes has been developed at the FLNR and was manufactured at the SPA “ATOM”, Dubna. Radial and azimuthal motions are carried by thepneumatic engines with using toothed belt for azimuthal stepping. Measuring accuracy of 10-4. At present, magnetic field measurements are being carrying out.
Magnetometer
Bottom sectors
Top sectors
Toothed belt
3D field map of the DC-280,
coil current of 750 A, average magnetic field induction of 1.05 T
Comparative radial distributions of calculated and measured average magnetic field at the main coil current of 750A
Calculated behavior of beam phase (Fi) for ions with A/Z=6 at acceleration with using trimming coils (I coil)

## Slide 14
3Frf
Frf
RF system
Frf=7.32÷10.38 MHz
Fft=21.96÷31.14 MHz
The main dee (EVPU, Slovakia)
The RF resonator at the FLNR
Details of the resonator
(ZAVKOM, Tambov, Russia)
Configuration of the DC-280
In June 2017, resonance frequencies of the N1 resonator have been measured at minimal RF power. The experimental frequency range is 7.17÷10.8 MHz, which covers the designed one.

## Slide 15
The RF generators made in the QEI Corporation, NJ, USA
RF generators
Frf=7.32÷10.38 MHz
Fft=21.96÷31.14 MHz
Dee voltage | 2x130 kV
RF Power consumption | 2x30 kW
Generator RF Power | 2x50 kW
Flat-top dee voltage | 2x13 kV
RF Power consumption | 2x2 kW
Generator RF Power | 2x3 kW

## Slide 16
Ion beam
Magnet yoke
Bender
±15 kV
HV platform
Umax=60 kV
Beam injection system
Focussing solenoids
Working vacuum in injection is 5·10-8 mBar
Vacuum volumes made by “Vacuum Praha”, Czech Republic
NEC,USA
Median plane
Inflector
“Vacuum Praha”
Buncher

## Slide 17: Beam injection system
The HV platform N1 (August 2017)
Internal focusing solenoids have been installed to the cyclotron center (May 2017)
The magnet with the base platform for injection
Magnetic elements for the injection made in EVPU, Slovakia

## Slide 18
ECR-ion sources
Experimental spectrums of Ar and Ca ions extracted from the DECRIS-PM
The new ECR-ion source DECRIS-PM (14 GHz)
for the 1-st HV platform .
(FLNR and “ITT-Group”, Moscow).
The FLNR has experience in developing and creation of DECRIS-SC and DECRIS-SC2 (18 GHz). The experience will be used for developing the new superconducting ECR for the 2-nd HV platform.

## Slide 19
Beam extraction system
Electrostatic deflector
Focusing magnetic channel
Extraction radius of Rext=1.79 m

## Slide 20
Electrostatic deflector
Magnetic channel
Length of electrostatic deflector | 1.3 m
Deflector voltage | 80 kV
Length of the magnetic channel | 0.9 m
Gradient of the magnetic channel | 4.6÷8.4 T/m
The magnetic channel has been produced at the Institute for Nuclear Research and Nuclear Energy of the Bulgarian Academy of Science.
Electrostatic deflector is being produced in the INR&NE too.

## Slide 21
Bending magnet ±50
Quadrupole lenses
MAX beam power ~2.5 kW
Beam transport system
Area of
experimental setups
Vacuum volumes of channels: “Vacuum Praha”, Czech Republic
Working vacuum is 10-7 mBar
Beam diagnostics: INR&NE of the Bulgarian Academy of Science
Ion beam

## Slide 22
TM±50 bending magnet
(NKMZ, Ukraine)
The triplet of quadrupole lenses 11К30-700
(N&V, Romania)
Magnetic optics
Beam channel N3 at the DC-280 hall

## Slide 23
Water cooling system
The water cooling system was developed at the FLNR (equipment suppliers: Russia, Italy, Germany)

## Slide 24
Control system
The control system based on FLNR developments and LabVIEW

## Slide 25
Experimental area ~1000 m2 (3 halls)
Plan of the 1-st floor of the SHEF
GFS-2
Sigma Phi
Notes: 25

## Slide 26
Schedule

## Slide 27
THANKS FOR YOUR ATTENTION!
The building of the SHEF
August 2017
The outline sketch of the building (2012)

## Slide 28
Working diagram of the DC-280