## Slide 1: Status VEPP-2000
Yuri Shatunov
BINP, Novosibirsk
on behalf of IC,VEPP-2000 teams
Sept 2017
Alushta

## Slide 2: VEPP-2000
VEPP-2000 main design parameters @ 1 GeV |  |  | 
Circumference | 24.388 m | Energy range | 150  1000 MeV
Number of bunches | 1 | Number of particles | 11011
Betatron tunes | 4.1/2.1 | Beta-functions @ IP | 8.5 cm
Beam-beam parameter | 0.1 | Luminosity | 11032 cm-2s-1
13 T final focusing
solenoids
max. production rate:
2×107 e+/s

## Slide 3: VEPP-2000 collider
06/21

## Slide 4: Experimental program
Precision measurement of
    exclusive approach, up to <1% for major modes
Study of hadronic final states:
Study of vector mesons and theirs excitations:
Comparison of cross-sections with spectral functions of -decays
Study of nucleon electromagnetic formfactor at threshold
Measurement of the cross-sections using ISR
Study of higher order QED processes
Target luminosity integral is 1 fb-1

## Slide 5
Hadronic contribution to muon g-2
VEPP-2M, BaBar, KLOE reduced errors Δ≈3.6 σ
contribution
error2
< 1% systematic error for most of the channels is needed
Absolute energy calibration ≃10-4 must be done in whole energy range
VEPP-2000 task!
BNL measurements

## Slide 6: Data collection 2010-2013
Delivered integral luminosity L = 60 pb-1/detector
PLB 723 (2013) 82
PRD 90 (2014) 112007
arXiv:1607.00371
14/21

## Slide 7: Программа модернизации
Получение пучков e+, e из ИК:
высокая интенсивность (20100 мА);
высокая частота повторения (1  100с);
высокая энергия (400 МэВ);
качество пучка (!);
надёжность (?)
Модернизация бустера БЭП до 1 ГэВ.
Модернизация канала БЭП  ВЭПП до 1 ГэВ.
Модификация кольца ВЭПП-2000.

## Slide 8: VEPP-2000 upgrade: 2013 >> 2016
BINP Injection complex
K-500 beam transfer channel
VEPP-2000 complex
e+, e beams from new BINP Injection Complex (IC):
high intensity
higher energy (400 MeV);
high quality (!);
Booster BEP upgrade to 1 GeV.
Transfer channels BEP  VEPP to 1 GeV.
VEPP-2000 ring modifications.

## Slide 9: New injecton beam commissioning (2016)
Stacking rate of 2×108 e+/sec @ 390 MeV is obtained (gain factor of 10 in comparison to old production system)
BEP operates stable up to E = 1 GeV
I+,mA
First beam SR @ BEP
Image current BPMs @ K-500 transfer channel
K-500 tunnel and beam @ scintillator screen
Positrons stacking @ BEP

## Slide 10: BEP reconstruction
New pulsed injection septum
New RF-system (110 kV, 174.382 MHz, q = 13)
Magnets yokes reprofiling (gap reduction, etc.). Fed in series all magnets has to follow single saturation curve. As well as chromatic sextupoles embedded into quads profile.
New correction coils
Vacuum chamber local deformation within reduced gaps
New pulse “bump” magnets (COD @ extraction)
New SR outlet
Dipoles excitation curve
Booster BEP
RF cavity
@ 1 GeV:
H = 26 kGs,
I = 10.2 kA
P = 2.4 MW

## Slide 11: BEP vacuum chamber
Press for dipoles (40 mm 32 mm) and quads

## Slide 12: БЭП: 17.02.2016

## Slide 13: VEPP-2000 modifications
New vacuum chambers in two dipoles with additional kicker electrodes (injection @ 1 GeV)
Original kicker electrodes
Additional
kicker electrodes
Scraper 2
Scraper 1
New SR mirrors for beam diagnostics:
17/21
KMD
SND

## Slide 14: ВЭПП-2000 with new magnets of transfer canal
BPMs @ BEP-VEPP transfer channel (510 MeV)

## Slide 15: Beam size measurement by CCD cameras
07/21

## Slide 16: Luminosity with new injector (2017)

## Slide 17
VEPP-2000 luminosity
CMD-3 luminosity, averaged over 10% of best runs
Achieved peak luminosity 4×1031 cm-2s-1
Best day integral 1.2 pb-1

## Slide 18: The concept of Round Colliding Beams
Head-on collisions!
Small and equal β-functions at IP:
Equal beam emittances:
Equal fractional parts of betatron tunes:
Transversal force is 1D
Axial symmetry of counter beam force together with x-y symmetry of transfer matrix should provide additional integral of motion (angular momentum Mz = xy - xy). Particle dynamics remains nonlinear, but becomes 1D.
Mx = My
Lattice requirements:
03/19
Round beam
“hour glass effect”
y
s
x

## Slide 19: Beam-beam parameter
Е = 392.5 MeV
Urf = 35 kV (purple)
Urf = 17 kV (blue)
 = 0.175   = 0.125/IP
Coherent oscillations spectrum
BB-threshold improvement with beam lengthening:
Beam-beam parameter extracted from luminosity monitor data



## Slide 20: “Flip-flop” effect
E = 240 MeV,
Ibeam ~ 55 mA
0.17
0.2
0.25
0.17
0.2
0.17
0.2
Pickup spectrum of the coherent oscillations
Coherent beam-beam -mode interaction with machine nonlinear resonances?
13/19
TV
e+
e


regular
blown-up e
blown-up e+

## Slide 21: Collected data in 2017
,

̍
D*0
Lowest energy ever obtained in e+e− colliders

## Slide 22
BaBar
CMD-3
CMD-3 (2017)
at systematic precision 1.8%
at systematic precision 2.5%
at threshold
Recent result from CMD-3

## Slide 23: Summary
New BINP injection complex started to serve both colliders.
Round beams concept gives the luminosity enhancement of VEPP-2000.
Th achieved beam-beam parameter value at middle energies amounts to  ~ 0.1–0.12 during regular operation.
VEPP-2000 resumed data taking after injection chain upgrade. During first run 100 pb-1 already collected.
DData processing in the progress
Thank you for your attention