## Slide 1
12th International Scientific Workshop
in Memory of Professor V.P.Sarantsev
«Problems of Colliders and Charged Particle Accelerators»
Forming of An Ordered Positron Flux
Формирование упорядоченного потока позитронов
I.N. Meshkov
3-8 September 2017
Alushta, Crimea

## Slide 2
Introduction: What is Positron Annihilation Spectroscopy (PAS)
Examples of defect structure
I.Meshkov Forming of an OPF Sarantsev Seminar September 4, 2015
Three kinds of PAS
1. Angular correlation of annihilation gamma-quanta (ACAG)
2. Doppler Broadening Annihilation Line (DBAL) Spectroscopy => “Yes” or “No”
method regularly used for PAS studies at the LEPTA facility (JINR) since 2015
3. Positron Annihilation Lifetime Spectroscopy (PALS) => detection of defect kinds
by measurement of positron lifetime in the sample

ppPs
=
The annihilation gamma line is naturally broadened, but in defect free structure positron annihilates mainly with valence electrons, which have larger momenta. Therefore broadening from non-defected area is larger.
Single vacancy
  175 ps
Divacancy
  183 ps
Three vacancy
  195 ps
Interstitial atom
  110 ps
Defect free structure
  110 ps
Edge dislocation
  113 ps
Vacancy near dislocation line
110 ps    175 ps
The ACAG method brings the same information as DBAL spectroscopy, however it requires
much longer time for data acquisition. Therefore its application is very rare presently .

## Slide 3
DBAL Spectroscopy:
“Yes” or “No” method
I.Meshkov Forming of an OPF Sarantsev Seminar September 4, 2015
Introduction: What is Positron Annihilation Spectroscopy (PAS)
Single vacancy
  175 ps
Divacancy
  183 ps
Three vacancy
  195 ps
Intertitial atom
  110 ps
Defect free structure
  110 ps
Edge dislocation
  113 ps
Vacancy near dislocation line
110 ps    175 ps
Why do we need PALS:
Two groups and one lonely “rebellious”
… and three kinds of short lived states.
PALS application:
Possibility to distinguish between long-lived state of positron inside a defect (vacancy)…
Only exclusion: wide range of probable lifetime values!
Conclusions from the introduction:
DBAL and PALS are complimentary
Resolution of PaLS method should be better than 30 ps

## Slide 4
3. Positron Annihilation Lifetime Spectroscopy (Ordinary Version)
Introduction: What is Positron Annihilation Spectroscopy (PAS)
22Na T1/2 = 2.6 years
22Ne
Nuclear transition -quant
1.274 MeV Start signal
Annihilitation -quant
511 keV Stop signal
Table-top set up
Dr. Pawel Horodek – leader of this activity at LEPTA

## Slide 5
STM – Scanning Tunnel Microscopy
AFM – Atomic Force Spectroscopy
TEM – Transmission Electron Microscopy
The place of PAS in The Methods of Solid State Physics and Materials Science
Introduction: What is Positron Annihilation Spectroscopy (PAS)
Positron 0.5 2.0 7.8 30.6 119 465 1.81 7.1 27.6
energy (Fe) keV MeV
Defect size and positron penetration depth vs energy
PAS at LEPTA => 0.1 – 100 keV (0.1 – 700 nm)

## Slide 6
Generation of Positron Flux of Wide Spectrum
Na22-based Positron Source
A gift from iThemba LABS (Cape Town, RSA)
2008 => 25 mCi
2015 => 30 mCi
Emax = 545 keV
Traditionally PAS studies are performed using of a positron source of the wide spectrum that gives great problems for analysis of experiment results!

## Slide 7
2015 => 30 mCi
Chart: 
| 10 | 20 | 30 | 35 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 60
 | 120 | 205 | 400 | 690 | 1100 | 1200 | 1800 | 2000 | 1800 | 2300 | 2700 | 3000 | 3350 | 4650 | 7500 | 3550 | 950 | 450 | 200 | 150 | 50
e+ spectrum of the source
FWHM 2.5 eV
Ne  1%
Generation of Slow Monochromatic Positron Flux
Na22-based Cryogenic Source of Slow Monochromatic Positrons (CSSMP)
and its creator Valentin N.Pavlov
7 K
Frozen Ne

## Slide 8
Scheme of forming of Ordered Positron Flux (OPF)
Forming of The Ordered Positron Flux
U0  0
UA  0
I
Channel-2
Target
Target chamber
e+ source
Channel-1
Cryo-cooler
LHe
URF
LRF
LA
dA
Lt
LU
Utarget  0
Solenoidal magnetic field
-detector
e+ - cryogenic source of slow positrons based on the 22Na isotope,
Channels 1, 2 — the positron transfer channels,
U0 > 0 - the potential between the source and the Channel-1,
UA > 0 — potential difference between Channels 1 and 2,
LRF — RF system with URF voltage of special form, LA — 1st drift section of the PAS channel, dA — accelerating gap with the static electric field UA, I — vacuum insulator,
Lt — 2nd drift section of the PAS channel, LU — the gap between the entrance
to the target chamber and the target with the sample to be studied,
Utarget — negative potential of the target.
Fig.1

## Slide 9
Forming of The Ordered Positron Flux
Here E0 = eU0 , e, m – positron charge and mass,
LA – see Fig.1, t2 – see details in Ref. 1.
Generation of an OPF from continuous flux of monochromatic positrons is performed by using the periodic pulsed voltage URF(t) of the special form (Fig. 2). Positrons from CSSMP come to the entrance of the RF gap from channel 1 at some random time tinj (injection):
(1)
T0 is pulse period, n = 0, 1… - integer number.
The criterion of the choice of the pulse form URF(t) is independence of time of positron flight from RF gap exit to the target on injection time tinj :
, (2)
tinj is defined in (1). The calculation gives us the following Formula:
URF(tinj), V
(3)
1. I. Meshkov, Forming of OPF, Preprint JINR P13-2017-49
tinj / T0
Fig.2. Functions URF(tinj) at T0 = 10 ns (100 MHz),
E0 = 150 V, LA = 20 (1), 15 (2), 12 (3) cm
1 2
3

## Slide 10
Forming of The Ordered Positron Flux
Here E0 = eU0 , e, m – positron charge and mass,
LA – see Fig.1, t2 – see details in Ref. 1.
Influence of positron energy spread
Positron energy spread E leads to a spread of time of positron flight from RF gap
exit to the target
ttarget(tinj),
ns
(4)
tinj / T0
Fig.3. Functions ttarget(tinj) at E0 = 150 V,
LA = 20 (1), 15 (2), 12 (3), cm
1
2
3
It is the main characteristics of the positron flux ordering!
For the LEPTA CSSMP positron energy spread E  1 eV (see slide 5).
Calculating ttarget (4) allows one to optimize the set up parameters, i.e.
E0 and U0 , URF(t) amplitude, LA, UA, Lt .
As calculation shows, a choice of values of these parameters is very critical.
The gap LRF should be as short as possible, optimization of the gap dA is “included”
in optimization of the gap LA, as well as LU is included in Lt .
Results of optimization (Fig.3) show

## Slide 11
I.Meshkov Forming of an OPF Sarantsev Seminar September 4, 2015
(5)
Synthesis of URF(t) pulses with harmonic voltage
To perform the Fourier analysis of URF(t) periodic pulses we add
to the URF(t) pulse (Formula 3) a smooth (linear) rear front
(Formula 5 and Fig.4):
Fig.4. Functions FU(x) (red solid line) and sum of its three Fourier harmonics (blue dot-and-dash curve)
FU(x), V
FF(x), V
Fourier transformation of the periodic function FUF(x) gives us
x
m | Am, [V] | φm , [rad]
0 | 213.76 | -
1 | 85.44 | π + 0.265
2 | 36.54 | π + 0.667
3 | 21.43 | π + 0.978
4 | 13.93 | π + 1.281
5 | 9.23 | π + 1.556

## Slide 12
I.Meshkov Forming of an OPF Sarantsev Seminar September 4, 2015
Synthesis of URF(t) pulses with harmonic voltage
Comparison of application of the calculated URF(t) (Formula 3)
and its Fourier synthesis
x
Fig.6. Functions ttarget(tinj) calculated for URF(t) (Formula 3) – solid curves
and for “Fourier synthesized” (dashed curves)
E0 = 150 V, LA = 15 (1) and 12 (2) cm
1
2
ttarget(tinj),
ns
tinj / T0

## Slide 13
Thank you for your attention!
Спасибо за Ваше внимательное внимание!
Author takes the opportunity to thank the colleagues and friends
Valery Kobets, Andrey Kobets, Pawel Horodek and Krzistof Siemek
for many fruitful discussions and proposals of technical solution of the system.
Problems to be solved
1. Design and construction of 3-cavities RF system
2. Construction of synchronization (start-stop) system
3. Construction of detection system
All these problems are under development presently – see
Ref. 2. Poster report #79, Orlov et al., Development of Positron Annihilation
Spectroscopy at JINR.
Conclusion
1. The proposed method forming of the ordered positron flux is an advanced version of well known method bunching continuous particle flux with a system of harmonic RF voltage. Nevertheless, the method promises significant increase of ordering efficiency and higher precision of positron life time measurement – below 30 ps.
2. Design and construction of the PaLS-OPF system is in progress at LEPTA facility at JINR – see Ref. 2 above.