## Slide 1: Tests of the electron cooling system for the NICA booster
Bryzgunov Maxim
Budker Institute of Nuclear Physics
Siberian Branch of the Russian Academy of Sciences

## Slide 2
Parameter | Value
Ion type | 197Au31+
Electron energy, E | 1.5÷60 keV
Electron beam current, I | 0.2÷1.0 A
Energy stability, ΔE/E | <10-5
Electron current stability, ΔI/I | <10-4
Longitudinal magnetic field, B | 0.1÷0.2 T
Electron current loses, Ileak/I | <3∙10-5
Inhomogeneity of magnetic field, ΔB/B | <3∙10-5
Transverse electron temperature, T | <0.3 eV
Vacuum pressure, P | ≈10-11 mbar
Main parameters of the system

## Slide 3
December of 2016
Budker INP
Cooler without gun and collector solenoids.
The cooler built with classical scheme.
On the way from gun to collector electrons move in longitudinal magnetic field.

## Slide 4
Cooling section
Solenoid consists of separate coils. Each coil can be rotated in two direction
Hiogenity of magnetic field is very important for cooling force.

## Slide 5
Toroids
Electrostatic plates are used in toroid. Recuperation efficiency increases to
E=0 magnet bending B=pc/eR
B=0 electrostatic bending E=pV/eR

## Slide 6
Electron gun
The gun is based on construction from HV COSY cooler.

## Slide 7
4-sector control electrode
Voltage is applied to one sector
Different values of magnetic field
Different regimes of gun work

## Slide 8
Electron collector

## Slide 9
Collector power supply
The PS gives up to 5 kV, 3 A (DC).
The PS is based on isolation transformer. Each of 5 identical windings after rectifiers give 1 kV. Using HV relays we can get from 0 to 5 kV.

## Slide 10
Collector power supply
The transformer is based on UNICORE core.
The transformer also contains winding to feed power supplies which control gun and collector.

## Slide 11
Transformer: 5 kV, 15 kW.
power supply: 60 kV 10 mA
High voltage system

## Slide 12
60 kV power supply and oil cooling system
High voltage system

## Slide 13
High voltage system
The crate contains power supplies for anode, grid, suppressor and filament.

## Slide 14
Diagram of the measuring device: (1) magnetic sensor, (2) conductors of the compensating circuits, (3) beam splitter, (4) photo-detector, (I-IV) photo-detector quadrants, and (X, Y) output current amplifiers.
Compass like system for measuring of the transverse component of the magnetic field

## Slide 15
Inhomogeneity of longitudinal magnetic field in the cooling section B/B≈10-5.
Correction of field line straightness

## Slide 16
BPMs
2 electrostatic bends shift beam in horizontal direction 2 times.

## Slide 17
Magnetic correctors

## Slide 18
Current–voltage characteristic of the gun
The rescale allows to compare measures with different Uanode .
Because of problems with cathode activation, emission ability is not anough for high current.
Comparison with COSY gun shows, that there is small difference in gun construction.

## Slide 19
Investigation of recuperation
Scan with Ugrid for different values of collector voltage.
Dependence of electron current on Ugrid. Hysteresis related with problems of cathode.
Current on anode electrode increases with increase of collector voltage that limits beam current

## Slide 20: Additional potential barrier in collector
The supressor electrode produces barrier in the entrance. Increase of collector voltage decreases the barrier.
Beam space charge in the collector entrance produces additional barrier that increase collector efficiency.

## Slide 21
Investigation of recuperation
Dependence of leakage current on Ugrid.
Similar shape but different height.
Dependence of recuperation efficiency on electron beam current. The value is ≈10-6.

## Slide 22
Work on different energies
For different energies only voltage on electrostatic plates was changed.
For every energy value current ≈130 mA was reached with appropriate leakage current.

## Slide 23
Influence of electron beam on vacuum
Vacuum conditions are important for ion beam lifetime.
Electron beam improves vacuum in the cooler.
- 1 electron ionizes all molecules in volume V1.
- Number of electrons in 1 second
- Formula for estimation of pumping speed
(1) - Turn off vacuum pump
1

## Slide 24
Influence of electron beam on vacuum
Ϭ≈6.5∙10-18 cm2 (H2)
7
L=6 m (trajectory length from gun to collector)
I=300 mA
Ileak, mA

## Slide 25
Correction of field line straightness in Dubna

## Slide 26
Vacuum baking in Dubna
Assembling of vacuum chamber
Cathode activation after baking

## Slide 27
Thank you for your attention!