## Slide 1
MAGNETIC FIELD CORRECTION
AT NICA BOOSTER
V. Altsybeev1), A. Butenko2), V. Emelianenko2),
O. Kazinova2), V. Kozynchenko1), S. Kostromin2), V. Mikhaylov2),
D. Ovsyannikov1), A. Tuzikov2), H. Khodzhibagiyan2)
1) Saint Petersburg University, Saint Petersburg
2) Joint Institute for Nuclear Research, Dubna

## Slide 2
Booster
Goals
Accumulation of required intensity of ions by means of several methods of beam injection.
Acceleration of ions up to energy required for effective stripping.
Forming of the required beam emittance with electron cooling system.
Main parameters
Alushta 2017
Ions | 197Au31+
Energy at injection | 3.2 MeV/amu
Maximum energy | 578 MeV/amu
Magnetic rigidity: at injection maximal | 1.6 T∙m 25 T∙m
Betatron tunes: Qx Qz | 4.8 4.85
Chromaticity: ΔQx/(Δp/p) ΔQz/(Δp/p) | −5.1 −5.5
Momentum compaction | 0.05
Amplitude of corrected C.O. | 5 mm
Acceptance: horizontal vertical | 150 ∙mm∙mrad 55 ∙mm∙mrad
Emittance: at injection εx,z at extraction εx at extraction εz | 15 ∙mm∙mrad < 3 ∙mm∙mrad < 1.5 ∙mm∙mrad
Momentum spread: at injection maximal at extraction | ±10−3 ±2.310–3 ±2.210–4
Revolution period: at injection at extraction | 8.5 μs 0.89 μs

## Slide 3
Booster
Booster layout inside Synchrophasotron yoke
Alushta 2017

## Slide 4
Booster
DFO cells
4 large straight sections
Injection system
Two RF cavities
Single-turn extraction system
E-cooler
Alushta 2017

## Slide 5
Booster composition
Alushta 2017

## Slide 6
Correction system
Alushta 2017
Multipole corrector magnets
 |  | Nonlinearity | mm | mm | Turns
Dipole | 1 | 0.08 T | 0.6 | 97 | 115
Quadrupole | 2 | 0.6 T/m | 0.6 | 95 | 92
Sextupole normal | 3 | 50 T/m2 | 0.6 | 94 | 67
Sextupole skew | 3 | 50 T/m2 | 0.6 | 96 | 68
 |  | Nonlinearity |  |  | Turns
Dipole | 1 | 0.08 T | 0.6 | 97 | 115
Quadrupole | 2 | 0.6 T/m | 0.6 | 95 | 92
Sextupole normal | 3 | 50 T/m2 | 0.6 | 94 | 67
Sextupole skew | 3 | 50 T/m2 | 0.6 | 96 | 68
Parameters of corrector magnets

## Slide 7
Magnet tolerances
Tolerances
Alushta 2017
Errors | Dipole | Quadrupole
Relative effective length spread | 5*10-4 | 5*10-4
Transverse shifts relative to longitudinal axis | - | ±0.1 mm
Rotation along longitudinal axis | 5*10-4 rad | 5*10-4 rad
Closed orbit perturbations

## Slide 8
Magnetic measurements
Effective lengths of dipoles
Alushta 2017
2nd harmonics of dipoles

## Slide 9
Magnetic measurements
3rd harmonics of dipoles
Alushta 2017
4th harmonics of dipoles

## Slide 10
Closed orbit correction
Alushta 2017
Example of closed orbit correction
Before correction
After correction (LSQ)

## Slide 11
Closed orbit correction
Alushta 2017
Distributions of maximal C.O. deviations on X-plane
Before correction
After correction (SVD)

## Slide 12
Closed orbit correction
Alushta 2017
Distributions of maximal C.O. deviations on Y-plane
Before correction
After correction (SVD)

## Slide 13
Closed orbit correction
Alushta 2017
C.O. correction quality
Dipole component and adjustment errors for lattice magnets are normally distributed.
Maximal deviations of the closed orbit on both transverse planes are calculated.
Closed orbit is corrected by SVD method.
Maximal deviations of the corrected orbit on both transverse planes are also calculated.
Closed orbit correction quality is defined as a ratio of maximums of the corrected and initial orbits.
X-plane
Y-plane

## Slide 14
Closed orbit correction
Alushta 2017
Local C.O. correction
1st straight section pulsed bump (for beam injection)
3rd straight section bump (for beam extraction)

## Slide 15
THANK YOU FOR ATTENTION