## Slide 1: The Unified Database as offline storage of the BM@N experiment at NICA
Gertsenberger K.
VBLHEP, Joint Institute for Nuclear Research
4 October 2017
The XXI International Scientific Conference of
Young Scientists and Specialists (AYSS-2017)
for the BM@N collaboration

## Slide 2
Gertsenberger K.
Nuclotron based Ion Collider fAcility
Collision energy: = 2 – 6 AGeV
Fixed target experiment: BM@N (2017)
Beams: from to
Baryonic Matter at Nuclotron (BM@N)

## Slide 3
Gertsenberger K.
Baryonic Matter @ Nuclotron
Nuclotron
~160 m
BM@N physics program:
strange / multi-strange hyperon and hypernuclei production at the threshold
hadron femtoscopy
short range correlations
event-by event fluctuations
in-medium modifications of strange & vector mesons in dense nuclear matter
electromagnetic probes, states decaying into γ, e (with ECAL)…

## Slide 4
Gertsenberger K.
Run – 51 (d,C) 22 Feb. - 15 Mar., 2015
Run – 52 (d) June 29 –June 30, 2016
Run – 53 (d) Dec. 9 – Dec. 23 , 2016
Run – 54 (C) Mar. 7 – Mar. 18 , 2017
Run – 55 will be conducted Nov. 2017
BM@N in Nuclotron runs (2015 - 2017)
deutron and beams with T = 3.5 – 5.14 AGeV targets: C, Cu, Pb, Al, or empty
Trace beams, measure beam profile and time structure
Test detector response T0+Trigger, MWPC, Si, GEM, ToF-400, DCH-1, DCH-2, ToF-700 and ZDC, ECAL modules, beam monitors
Test integrated DAQ and trigger system
Technical

## Slide 5: Multiple data of the BM@N experiment
~1000 raw files, ~2000 *.root files, various parameter data
Gertsenberger K.
e.g. noise channels
HTML
Text
Excel

## Slide 6: The main problems of BM@N data storing
the data of the experiment is distributed between many subdivisions – it’s difficult to find necessary absent information for the other subdivisions
required information is stored in a lot of files of different types (binary, xml, html, excel, text)
detector mapping (text files) can be corrected but you won’t know about changes and will continue to work with old data
BM@N geometry schemes are hand-drawn and can be varied from run to run
Gertsenberger K.

## Slide 7: Why should a database system be used?
The lacks of the file storing approach:
the usage of multiple files and arbitrary formats, duplication of information in different files lead to data isolation, redundancy and inconsistency
sequential, non-indexed access and search (not efficient)
no mechanism exists for relating data between these files
it’s difficult to access and manipulate the data: one needs some dedicated programs
uncontrolled concurrent access by many users often leads to inconsistencies
Gertsenberger K.

## Slide 8: The purposes of the Unified Database
Gertsenberger K.
central data storage for offline data analysis in the high-energy physics experiments
unified access and data management for all collaboration members
correct multi-user data processing
ensuring the actuality of the information being accessed (run parameters, detector geometries and positions, technical and calibration data, etc.), data consistency and integrity
excluding the multiple duplication and use of outdated data
automatic backup of the stored data
merged the existing databases to simplify access and administration

## Slide 9: The Unified Database diagram
Gertsenberger K.
PostgreSQL DBMS
pointer to
SIM storage level
pointer to
RAW storage level

## Slide 10: The data being stored in the parameter part
Gertsenberger K.
Configuration data is concerned with detector running mode, i.e. voltage settings as well as some programmable parameters for frontends electronics.
Calibration data describes the calibration and the alignment of different subdetectors. Usually quantities are evaluated by running dedicated offline algorithms.
Parameter data presents the state of detector subsystems. They include a variety of detector settings including the geometry and material definitions.
Algorithm data is used to control the way offline algorithms operate. It includes, for example, cuts for selection and production file paths.

## Slide 11
BmnRoot software
The software BmnRoot is developed for the BM@N event simulation, reconstruction of experimental or simulated data and following physical analysis of collisions of elementary particles and ions with a fixed target at the NICA collider.
C++ classes, Linux OS support,
based on ROOT and FairRoot
BmnRoot has a runtime parameter manager which writes and initializes parameters from ASCII or ROOT files
Gertsenberger K.
Notes: TOF-400, TOF-700

## Slide 12: C++ database interface
Gertsenberger K.
Class wrappers for all database tables with many specific functions allow to access and manage the data without SQL statements in experiment software
UniDbRunPeriod – describes run periods (a set of runs) of the experiment
UniDbRun – run parameters (number, time, energy, beam, target, magnet field, file path, etc.)
UniDbRunGeometry – contains whole detector geometry in the ROOT format
UniDbDetector – detectors of the experiment (detector dictionary)
UniDbParameter – common information about detectors’ parameters presented on the previous slides and stored in the database (parameter dictionary)
UniDbDetectorParameter – values of detector parameters for experiment runs
UniDbSimulationFile – describes a set of generated simulation files
The main functions:
for data objects (static): Create, Delete, Get, Search, PrintAll.
for attributes (non-static): Getters and Setters functions, Print.

## Slide 13: «Noise channels» parameter (example)
Gertsenberger K.
slot
channel
run
IIStructure* pValues = new IIStructure[32];
AssignIIStructure(pValues, 0, 15, 33, 48); // slot:15, channel:33-48
AssignIIStructure(pValues, 16, 16, 49, 64); // slot:16, channel:49-64
DbDetectorParameter::CreateDetectorParameter(run_number, "DCH", "noise", pValues, 32);
DbDetectorParameter* pDetectorParameter = DbDetectorParameter::GetDetectorParameter(run_number, "DCH1", "noise");
if (pDetectorParameter != NULL)
{
IIStructure* pValues; int element_count = 0;
pDetectorParameter->GetIIArray(pValues, element_count);
// e.g. print values (slot:channel)
for (int i = 0; i < element_count; i++)
cout<<pValues[i].int_1<<":"<<pValues[i].int_2<<endl;
}

## Slide 14: Additional classes of the database interface
Gertsenberger K.
UniDbConnection serves to open and close connections to the database
UniDbSearchCondition forms criteria for selection of runs and detector parameters
UniDbParser parses existing data of the experiment from HTML, Excel and text files, and writes them to the Unified Database
UniDbGenerateClasses generates skeleton classes for all tables of the database
UniDbGeoConverter converts ROOT files with full geometry to the alternative database view
UniDbTangoData gets hardware data from the “slow” control system (Tango) for selected time range (run number), detector and parameter defined by name
It includes the following directories:
macros/ - ROOT macros for executing the tasks presented by the classes above
examples/ - numerous examples (ROOT macros) of using C++ interface to work with the BM@N database
docs/ - Unified Database documentation: Reference Manual, User’s Guide

## Slide 15: Getting Tango (hardware) data
Gertsenberger K.
UniDbTangoData class gets hardware data from the Tango control system
Main functions of the class:
Tango_Data* GetTangoParameter(char* detector_name, char* parameter_name, char* date_start, char* date_end);
void PrintData(Tango_Data* parameter, bool isGraphicPresentation = false);
(“ZDC”, “PosY”, “2015.03.12 18:20”, “2015.03.12 19:40”);
(“ZDC”, “Vset”, “2015.03.13 23:40”, “2015.03.13 24:00”);
time
coordinate
time counter
ZDC tower number
voltage
GetTangoParameter

## Slide 16: The Unified Database in offline processing
Gertsenberger K.
Unified
Database
ROOT
C++ database interface w/o SQL
(connect, SQL I/O)
Web-interface is under development
PHP
Slow Control System
Tango
UniDbTango class
users
PostgreSQL
detector simulation
raw data processing
event reconstruction
physics analysis
reading and changing data
BmnRoot
configuration
calibration
parameter and
algorithm data

## Slide 17: Web-interface of the simulation part
It contains paths to all simulated data files for different event generators
Easy search by many parameters
event generators:
UrQMD
QGSM
Hybrid UrQMD
vHLLE_UrQMD
3FD(Theseus)
…
1,2TB
~ 34 000 files
~ events/file
Gertsenberger K.

## Slide 18: Web-interface of the experimental part
for exp. data ~ 12TB count of rows ~ 50k
Web-interface by Slepov I.
Gertsenberger K.

## Slide 19
The «Databases» section on mpd.jinr.ru
Information
News
Forum
Mail-lists (updates, errors…)
Software repositories
Software tests dashboard
etc.
Gertsenberger K.

## Slide 20: Conclusions
The BM@N database was developed based on PostgreSQL and deployed in the cloud of the Laboratory of Information Technologies.
The Unified Database merged the existing databases and included existing data of all BM@N runs from multiple files (HTML, Excel, text).
The developed database is comprehensive data storage of the BM@N experiment allowing unified access and data management for all BM@N members.
C++ database interface was implemented as a part of the BmnRoot environment to use it for offline raw data processing, reconstruction and physical analysis tasks. It provides the classes and tools to store and access data without SQL statements.
C++ Tango interface was developed to get hardware data from the BM@N slow control system.
Web interface is under development now to simplify reading and changing the data by users over the Web.
A future version of the Unified Database can be used for the MPD/NICA experiment
Gertsenberger K.

## Slide 21
The XXI International Scientific Conference of
Young Scientists and Specialists (AYSS-2017)
Thank you for your attention!
More information: mpd.jinr.ru
email: gertsen@jinr.ru
4 October 2017
Gertsenberger K.

## Slide 22
Backup slides

## Slide 23: BM@N Geometry and Material definition
ASCII .GEO format
Creation of a volume
  Volume name
  Shape
  Shape parameters
  Medium
Positioning of the volume in a mother (Node)
  Mother
  Transformation (position and rotation matrix)
TUBE
input formats
for geometry
ASCII
.GEO
FairGeoInterface
TGeo Geometry
& Material
TGeoVolume
TGeoNode
TGeoMaterial
RootBuilder
G3Builder
G3 Geometry
& Material
ROOT
files
GDML*
GDMLBuilder
*supported but not used