## Slide 1
ELCHEM_NS
M.V. Avdeev, I.A. Bobrikov, I.V. Gapon, A.I. Ivankov, V.I. Petrenko, D.V. Soloviev, S.V. Sumnikov, A.V. Tomchuk (FLNP JINR)
D.M. Itkis (MSU)
F.S. Napolsky (Dubna University)
Leader: Mikhail V. Avdeev
Leader’s assistants: Ivan A. Bobrikov, Viktor I. Petrenko
A system for neutron operando monitoring and diagnostics of materials and interfaces for electrochemical energy storage devices at the IBR-2 reactor
Proposal for opening a new project

## Slide 2
Motivation
Objectives
Physical background
Methodical background
Expected results
General scheme
Costs
Conclusions
Outline

## Slide 3
Electrochemical energy storage devices: current challenges
Samsung Galaxy Note 7 banned on all U.S. flights due to fire hazard!
Oct. 14, 2016
High Specific Energy Accumulated
and
Safety
Volta’s pile, 1800
1900
???
2000

## Slide 4
Electrochemical energy storage devices: current research interests
Electrode structure evolution
Interface evolution

## Slide 5
Negative
Electrode
Electrochemical energy storage devices: current research interests
Electrode structure evolution
Interface evolution
Lithium intercalation

## Slide 6
Negative
Electrode
Formation of solid electrolyte intephase
Lithium intercalation
Electrochemical energy storage devices: current research interests
Electrode structure evolution
Interface evolution

## Slide 7
Growth of dendrites
Negative
Electrode
Formation of solid electrolyte intephase
Lithium intercalation
Electrochemical energy storage devices: current research interests
Electrode structure evolution
Interface evolution

## Slide 8
Study of operating electrodes and interfaces (operando mode)
Important task
Growth of dendrites
Negative
Electrode
Formation of solid electrolyte intephase
Lithium intercalation
Electrochemical energy storage devices: current research interests
Electrode structure evolution
Interface evolution

## Slide 9
Electrochemical energy storage devices:
useful properties of thermal neutrons
High penetrating power (weak interaction with atoms)
Scattering sensitivity to light elements (lithium)
Possibilities for contrasting wide range of materials (isotope substitution)
Scattering length distribution

## Slide 10
A.M.Balagurov, I.A.Bobrikov, N.Y.Samoylova, O.A.Drozhzhin, E.V.Antipov, Neutron scattering for analysis of processes in lithium-ion batteries, Russ. Chem. Rev. 2014, 83, 1120
D.M. Itkis, J.J. Velasco-Velez, A. Knop-Gericke, A. Vyalikh, M.V. Avdeev, L.V. Yashina, Probing of electrochemical interfaces by photons and neutrons in operando. Review ChemElectroChem 2 (2015) 1427
Scattering of thermal neutrons allows one to investigate the "hidden" structures of electrode materials and interfaces for electrochemical energy storage devices
Important, from a practical point of view, feature of neutron scattering is that "averaged" information on the volume or surface of electrodes is obtained, which avoids artifacts often related with the locality of information and influenced by numerous factors
The organization and conduct of high-quality operando experiments with electrode materials and interfaces for electrochemical energy storage devices require an appropriate "electrochemical infrastructure“
Electrochemical energy storage devices:
neutron scattering and other methods

## Slide 11
Project objectives
Development of common approaches to the effective use of neutron scattering methods (diffraction, reflectometry, small-angle scattering) in the analysis of the structural evolution of various types of electrodes and interfaces for electrochemical energy storage devices during operation (operando mode).
Design and development of specialized electrochemical cells and sample environment systems for operando research in neutron scattering experiments.

## Slide 12
Neutron Difftraction (ND):
HRFD, RTD
Small-Angle Neutron Scattering (SANS):
YuMO
Neutron Reflectometry (NR):
GRAINS
YuMO (SANS)
HRFD, RTD (ND)
GRAINS (NR)
Involved methods and instruments
IBR-2 pulsed reactor, FLNP JINR

## Slide 13
Physical background: Neutron Diffraction
Research projects: RFBR 14-02-31506 mol_а, RFBR 14-29-04091 ofi-m, RSF, Rosnauka ‘SYNESTESia’
Evolution of neutron diffraction patterns from lithium-based electrical current source during charge/discharge cycles
graphite
HRFD diffractometer, IBR-2 (Dubna)
olivine
Bulk structure of electrodes
I.A.Bobrikov, A.M.Balagurov, Chih-Wei Hu, Chih-Hao Lee, Sangaa Deleg, D.A.Balagurov J. Power Sources 258 (2014) 356

## Slide 14
Tasks of current interest
Intercalation/deintercalation of lithium into electrodes based on new advanced materials for increasing discharge capacity, including nanostructured silicon and silicon-based metal alloys, vanadium oxide, etc.
Evolution and degradation of the electrode crystalline structure after short- and long-period operation.
Fundamental problems like phase transitions in materials during electrochemical cycling.
Physical background: Neutron Diffraction

## Slide 15
Intensity
Cathode
Anode
Interplanar distance, Å
Voltage, V
Current, A
Time, h
Optimization of electrochemical cells for diffraction experiments
Installation of a specialized collimation system for incoming and scattered neutron beams
Development of a sample environment system, including the electrode preparation line, for electrochemical studies
PTFE case
V or Si window
Stack of electrodes : (cathodes, separators, anodes, current collectors)
n
Remote control
Methodical tasks: Neutron Diffraction
back scattering

## Slide 16
M.V.Avdeev, A.A.Rulev, V.I.Bodnarchuk, E.E.Ushakova, V.I.Petrenko, I.V.Gapon, O.V.Tomchuk, V.A.Matveev, N.K.Pleshanov, E.Yu.Kataev, L.V.Yashina, D.M.Itkis, Applied Surface Science (2017) in press
Monitoring of Li plating on metal electrode
GRAINS reflectometer, IBR-2 (Dubna)
Physical background: Neutron Reflectometry
Research projects: Rosnauka ‘SYNESTESia’ , RSF
with TBAP

## Slide 17
Design and approbation of complex heterogeneous thin-film interfaces based on metals and silicon for increasing the discharge capacity. Analysis of the formation and development of a transitional layer of solid-electrolyte interphase (SEI) in such interfaces.
Analysis of the appearance and growth of heterogeneities, including needle-like ‘moss’ formations (dendrites), on interfaces with various electrolytes. Development for this purpose of the techniques of specular reflection, diffuse scattering and grazing incidence small-angle scattering.
Development of contrast variation technique based on the use of electrolytes with deuterated solvents.
Tasks of current interest
Physical background: Neutron Reflectometry

## Slide 18
Optimization of reflectometry cells and sample environment system
Synthesis of complex heterogeneous film electrodes
Complimentary diagnostics of electrode surfaces after neutron scattering experiments
Processing of crystalline substrates after neutron scattering experiments
Remote control
Principal scheme of experiment
Methodical tasks: Neutron Reflectometry

## Slide 19
Study of Li2O2 particle formation in porous carbon cathodes for Li-air batteries
D.M. Itkis, V.A. Vizgalov, T.K. Zakharchenko, E.Yu. Kataev, M.V.Avdeev , SANS investigation of Li2O2 particles formation in Li-air battery cathodes, Proposal 2015-10-15-22-43-07.
D.M.Itkis, V.A. Vizgalov, A.V. Sergeev, M.V.Avdeev, Study of Li-air battery carbon electrode porosity by SANS, Proposal 2015-10-15-19-38-34
D.M.Itkis, V.A. Vizgalov, M.V.Avdeev, SANS investigation of the influence of solvent on Li2O2 growth in lithium-oxygen batteries, Proposal 2016-04-15-21-13-55
D.M.Itkis, V.A. Vizgalov, M.V.Avdeev, Study of Li-air battery recharge process by SANS, Proposal 2016-04-15-21-17-55
YuMO spectrometer, IBR-2 (Dubna)
No electrolyte
Discharged in MeCN
Discharged in DMSO
Physical background: Small-Angle Neutron Scattering

## Slide 20
Study of deposition of discharge products in porous positive electrodes for lithium-air and lithium-sulfur batteries in operando mode
Development of methods for analysis of pore filling in an electrode by products of electrochemical processes
Development of the contrast variation technique based on the use of electrolytes with deuterated solvents
Physical background: Small-Angle Neutron Scattering
Tasks of current interest

## Slide 21
Development of an electrochemical cell for neutron experiments
Development of a sample environment system for in situ neutron experiments
Specialized electrochemical Li-Air cell,
Department of Chemistry, Moscow State University
Methodical tasks: Small-angle Neutron Scattering
O2
O2
Lithium
Separator
+
-
Carbon electrode
n
Requirements to SANS cell
low coherent scattering from separators;
sufficiently thick carbon electrode;
sufficiently thin separator, electrolyte region and lithium electrode;
low incoherent background from all components;
air-tight construction;
Electrolyte
1 cm

## Slide 22
 |  | Year 1 | Year 2 | Year 3
ND | Specialized Li-ion cells for multiple charge/discharge (~ 10 pcs.) |  |  | 
 | Sample environment system for operando experiments |  |  | 
 | Multichannel cell charge/discharge line |  |  | 
NR | Specialized Li-ion cells with heterogeneous electrodes (~ 10 pcs.) |  |  | 
 | Sample environment system for operando experiments |  |  | 
 | System for post experiment sample diagnostics, storage and treatment |  |  | 
SANS | Specialized Li-air cells for multiple charge/discharge (~ 10 pcs.) |  |  | 
 | Sample environment system for ex-situ experiments |  |  | 
 | Sample environment system for operando experiments |  |  | 
Expected results

## Slide 23
Diffraction
Reflectometry
Small-angle
scattering
Creation at IBR-2 of Extended Sample Environment System
for complex operando studies of electrochemical processes
Si1-yMy
Сu/Ni/Ti
Si
n
Si1-yMy
Сu/Ni/Ti
Si
n
Si1-yMy
Si
n
Сu/Ni/Ti
Electrolyte
Electrolyte
Electrolyte
Expected results

## Slide 24
General scheme
Dubna University/ Engineering Center
Test assembly and electrochemical measurements of the cells and sample environment systems for neutron scattering experiments;
Electrochemical support of neutron scattering experiments.
MSU
Design and draft projects:
Electrochemical cells for neutron scattering experiments;
Sample environment systems for in situ neutron scattering experiments.
Scientific support.
FLNP JINR
Manufacturing:
Electrochemical cells for neutron scattering experiments;
Sample environment systems for in situ neutron scattering experiments.
Organization and support of R&D line for deposition and polishing of crystalline substrates;
Preparation and conduct of neutron scattering experiments at IBR-2;
Diagnostics and special treatment of samples after neutron scattering experiments.

## Slide 25
Manpower
FLNP JINR
M.V. Avdeev, V.I. Petrenko, A.V. Tomchuk, I.V. Gapon, I.A. Bobrykov, S.V. Sumnikov, A.M. Balagurov, O.Yu. Ivanshina, N.Yu. Samoylova, D.V. Soloviev, A.I. Ivankov
MSU, Moscow
D.M. Itkis, E.B. Kataev, A.A. Rulev, T.K. Zakharchenko, O. Kapitanova, L.V. Yashina
Dubna University, Dubna
F.S. Napolsky, E.E. Ushakova, M. Erdaulethov, V.A. Krivchenko

## Slide 26
Costs
Description | Cost, k$ | Year 1, k$ | Year 2, k$ | Year 3, k$
Equipment | 240 | 80 | 80 | 80
Development and manufacturing of electrochemical cells for neutron diffraction, neutron reflectometry and small-angle neutron scattering (~ 30 pcs.) | 100 | 30 | 30 | 40
Sample environment systems including in situ experiments | 100 | 30 | 30 | 40
Portable programmable potentiostat with safety control (2 pcs.) | 40 | 20 | 20 | -
Outside contracts | 100 | 30 | 30 | 40
Sputtering and processing of crystalline substrates | 100 | 30 | 30 | 40
Materials | 80 | 30 | 30 | 20
Crystalline substrates | 10 | 5 | 5 | -
Targets for sputtering electrodes | 10 | 5 | 5 | -
Consumables | 10 | 5 | 5 | -
Deuterated electrolytes | 25 | 5 | 10 | 10
7Li salts | 25 | 5 | 10 | 10
Software | 15 | 5 | 5 | 5
Travel expenses | 15 | 5 | 5 | 5
Total: | 450 | 150 | 150 | 150

## Slide 27
Conclusions
Suggestion to PAC solutions
The PAC supports the opening of the project "A system for neutron operando monitoring and diagnostics of materials and interfaces for electrochemical energy storage devices at the IBR-2 reactor” (headed by M.V.Avdeev) for the period of 2018-2020. The PAC notes the high importance of the implementation of this project for the development of the broad experimental support of the User Policy at the IBR-2 reactor.
Natural extension from crystalline structures to large-scale structures in electrochemical research at IBR-2
Increase in number of interested research centers and proposals on electrochemical studies under the User Policy at IBR-2
Project implementation will result in:
Widening of the possibilities for enhanced operando experiments in the field of electrochemistry at IBR-2