## Slide 1
Overview of the poster presentations
T.V. Tropin
47th Program Advisory Committee on Condensed Matter Physics, JINR, Dubna, 2018

## Slide 2
47th PAC CMP poster session
The poster session of the present PAC consisted of a total of 24 posters
presented by young scientists from several JINR laboratories
Notes: Armenia Azerbaijan Belarus Bulgaria Cuba Czech. Rep. Georgia Kazakhstan D.P.R. Korea
Moldov Mongolia Poland Romania Russia Slovakia Ukraine Uzbekistan Vietnam
Добавить
Egypt Germany Hungary Italy Serbia South Africa

## Slide 3
47th PAC CMP poster session
Notes: Armenia Azerbaijan Belarus Bulgaria Cuba Czech. Rep. Georgia Kazakhstan D.P.R. Korea
Moldov Mongolia Poland Romania Russia Slovakia Ukraine Uzbekistan Vietnam
Добавить
Egypt Germany Hungary Italy Serbia South Africa

## Slide 4
“Study of crystal and magnetic structures of complex ferrites
by neutron diffraction method” B.K. Argymbek, S.E. Kichanov, D.P. Kozlenko, E.V. Lukin, B.N. Savenko
The main aim was to study crystal and magnetic structures of a number of complex ferrites by means of neutron diffraction.
The structures and dependencies of characteristic sizes on granules sizes were also investigated.
1
Mn0.25Cu0.75Fe1.7Ga0.3O4 Mn0.5Cu0.5Fe1.7Ga0.3O4
Ni0.4Cu0.4Zn0.2Fe2O4
Ni1.2Zn0.1Ti0.3Fe1.4O4

## Slide 5
“Poly (ethylene glycol) addition influence on the structure and
interaction parameters of anionic surfactant micellar systems” O.P. Artykulnyi, V.I. Petrenko, M.V. Avdeev, L.A. Bulavin
The investigation of structure of sodium oleate (SO) and dodecylbenzene sulphonic acid (DBSA) micellar system after addition of poly(ethylene glycol) (PEG) via SANS together with surface tension study of the solution has been made.
2
The investigation via small angle neutron scattering (SANS) technique (left figure) allowed to determine structural and interaction parameters of micelle: number of aggregation (Nagg), degree of ionization (α), axial ratio of ellipsoid model (γ), inverse screen length (kd).

## Slide 6
“SFF analysis of the vesicular systems structure: MPI implementation of the fitting procedure and numerical results” M.V. Bashashin, E.V. Zemlyanaya, T.P. Sapozhnikova, M.A. Kiselev
3
Investigation of the structure and properties of phospholipid membranes is an actual problem due to the importance of understanding the basic principles of the organization and functioning of biological and artificial membranes, as well as the prospects for their use in biomedicine and pharmacology.
In biomedicine, a vesicle is a small structure within a cell, consisting of fluid enclosed by a lipid bilayer. Artificately prepared vesicles are used for transport of drugs.
The separated form factors method (SFF) is an effective approach of investigation of structure of polydispersed systems of phospholipid vesicles on the basis of the small angle neutron scattering (SANS) data analysis.
We use the parallel MPI-version of the SFF calculations for the SANS data analysis. Effectiveness of this parallel implementation is tested on the cluster HybriLIT.

## Slide 7: Investigation of crystal and magnetic structure of nanostructured complex oxides of transition metals in wide pressure and temperature range
4
N.M. Belozerova, S.E. Kichanov, E.V. Lukin, D.P. Kozlenko, Z. Jirak, B.N.Savenko
Apart from a great amount of applications in microelectronics, complex oxides of transition metals proved themselves as a promising material for biomedical applications: as biomarker in MRT and in magnetic hyperthermia procedure.
The ferrite spinel Zn0.3Cu0.7Fe1.5Ga0.5O4 exhibits ferrimagnetic state. Gradual suppression of the magnetic moments of iron ions on pressure increase observed.
Nanostructured manganite La0.53Sr0.47MnO3 exhibits ferromagnetic metallic state. Transition from ferromagnetic phase to paramagnetic at Tc=337K were found.
Notes: Apart from a great amount of applications in microelectronics, complex oxides of transition metals proved themselves as a promising material for biomedical applications: as biomarker in MRT and in magnetic hyperthermia procedure.
The experimental results of neutron diffraction studies shows that ferrite spinel Zn0.3Cu0.7Fe1.5Ga0.5O4 exhibit ferrimagnetic state. Upon temperature and pressure variation, a gradual suppression of the magnetic moments of iron ions in both A and B crystallographic sites was observed. This effect corresponds to magnetic phase transition from the ferrimagnetic state to paramagnetic one. (Главная мысль: обнаружили уменьшение магнитных моментов в обоих кристаллографических позициях, что свидетельствует о переходе из ферримагнитного в парамагнитное состояние.)
The neutron diffraction studies shows that nanostructured manganite La0.53Sr0.47MnO3 exhibit ferromagnetic metallic state as corresponding bulk samples, in contrast to nanostructured manganites (investigated earlier) which shows coexisting of 2 phases in magnetic structure: FM and AFM at ambient conditions. Transition from ferromagnetic phase to paramagnetic at Tc=337K were found. The lattice parameters, interatomic bond lengths and angles, magnetic moments of manganese as functions of temperature were calculated for both samples.
(Главная мысль: полученные результаты не совпадают с результатами для ранее исследованных образцов. Сейчас магнитная структура представлена только ферромагнитным состоянием, а тогда было сосуществование 2 фаз ФМ и АФМ. Тоже обнаружили уменьшение магнитных моментов, что свидетельствует о переходе из ферромагнитного в парамагнитное состояние.)

## Slide 8
“Detection of DNA molecules by SERS spectroscopy with silvered
porous silicon as an active substrate” N. Doroshkevich, K. Mamatkulov, G.M. Arzumanyan, H. Bandarenka
The effect of silvered porous silicon substrates on the spectra of the herring sperm DNA for choosing the optimal conditions of the SERS measurements for a reliable DNA study investigated.
The prospects for the DNA detection by the SERS spectroscopy with lasers of 473, 633, and 785 nm wavelengths demonstrated. The most promising result is in the detection of the DNA molecules at very low concentration (10-10 M) with the silvered PS.
5

## Slide 9
6
STRUCTURE OF MAGNETIC FLUIDS AT INTERFACE WITH SILICON BY NEUTRON REFLECTOMETRY
I.V.Gapon, V.I.Petrenko, M.V.Avdeev, M.Kubovcikova, V.Zavisova, P.Kopcansky, L.A. Bulavin
Structural organization of the nanoparticles at the interface with
Just one layer of magnetic nanoparticles is observed
Influence of the concentration of ferrofluid on the adsorption of magnetic particles
An increase concentration of particles leads to increase degree of filling of the adsorption layer with magnetic particles, but does not lead to the precipitation of new layers.
non-polar FF
polar FF
Impact of bulk structure of ferrofluids on adsorption of magnetic particles by silicon
Impact of the stabilization type and change magnetic material of the nanoparticles on ferrofluids adsorption properties

## Slide 10
Methodology of electrode manufacturing for
operando diffraction investigations in FLNP JINR
O. Yu. Ivanshina, S. V. Sumnikov, A.V. Ushakov, and I. A. Bobrikov
Special Li-ion electrochemical cells
designed in FLNP JINR for operando structural analysis
Cell for X-ray analysis
Cell for neutron analysis
Examples of investigations of cathode material NCA
Examples of operando neutron diffraction study of the commercial cathode material LiNi0.8Co0.15Al0.05O2
Electrolyte: LiPF6 dissolved in ethyl carbonate (EC) and dimethyl carbonate (DMC).
Current rate 0.1C. Anode: 7Li. Δt = 5 minutes.
The methodology of cathode manufacturing for special designed Li-ion electrochemical cells was developed.
Small reﬂection at ∼24° 2θ arises because of the excess Li cation ordering in the metal layer.
Second charge/discharge profiles, 0.1C: discharge capacity Li1.2Ni0.13Mn0.54Co0.13O2 (LNMC) 213 mAh/g; LiNi0.33Mn0.33Co0.33O2 (NMC) 165 mAh/g.
Successful synthesis of the perspective lithium-rich oxide cathode material Li1.2Ni0.13Mn0.54Co0.13O2 was carried out in FLNP JINR for the purpose of further structural studies.
Electrochemical study
X-ray diffraction study
7

## Slide 11
Optimization of neutron reflectometry experiments for planar interfaces
Ye.N. Kosiachkin, V.I. Petrenko, L.A. Bulavin, M.V. Avdeev
8

## Slide 12
Insulin fibrils
2:1
Fullerene-based complexes in solutions
for anticancer therapy and neurodegenerative diseases
Olena Kyzyma1,2
1Joint Institute for Nuclear Research, Dubna, Russia
2Taras Shevchenko Kyiv National University, Kyiv, Ukraine
C60 + Dox complex leads to significantly higher anticancer action compared with the effect of Dox alone!
Fullerenes are promising candidates for anti-amyloidogenic and antitumor agents!!!
Fullerenes destroy the amyloid fibrils!
Control
C60+Dox
+ fullerenes
Healthy brain
Advanced Alzheimer's
9
Notes: The next poster devoted to the problem of cancer and neurodegenerative diseases. It was shown that fullerene water solutions effectively destroy of amyloid fibrils and increased antitumor action in vivo on mice as compared with the effect of drug alone.

## Slide 13
“Raman, CARS and up-conversion luminescence imaging
of bio- and nonorganic samples on the multimodal optical platform”
K. Mamatkulov, N. Doroshkevich, G.M. Arzumanyan
A new extremely sensitive method of the imaging of protein crystals which is based on polarized coherent anti-Stokes Raman scattering (P-CARS) is described.
The successful results of measuring the bacteriorhodopsion crystals and of gold and silver NPs reported.
10
Fig.3 Panoramic and submicron sized images of bR crystals (scan area: top - 225x225 µm,
bottom - 8x8 µm)
P-CARS at 1529cm-1
P-CARS at 1529 cm-1

## Slide 14: “New ring detector for small-angle scattering of thermal neutrons for Real-Time Diffractometer (RTD)” (by V.M. Milkov)
The development of the detector is based on the design and experience of working with a one-dimensional coordinate-sensitive ring thermal neutron detector,
The new detector is designed to measure small-angle scattering of thermal neutrons at the IBR-2 reactor, Real-Time Neutron Diffractometer (RTD) (channel No. 6a).
11

## Slide 15
12
Сlusterization aspects of fullerene C60 and C70 in toluene / N-methyl-2-pyrrolidone mixture according to SANS, SAXS and DLS data.
T.V. Nagorna, O.A. Kyzyma, D. Chudoba, L.А. Bulavin
Spectra of the system ‘C70/toluene plus NMP’ for different contents of NMP.
The solvatochromic changes in the solutions as a response to the variation of the solvent composition depend strongly on the order of mixing.
Fullerenes transition into a state with a new electronic structure, presumably due to a fullerene complex formation with NMP.
Our results confirm presence of some aggregates in the solutions. It was noted that with a component of toluene more than 60%, the clusters are reorganized.
Spectra of the system ‘C70/NMP plus toluene’ for different contents of toluene.

## Slide 16
A.V. Nagornyi, M.V. Avdeev, L.A. Bulavin
A combined investigation of nanostructured powders of magnetite, cobalt-ferrite and their composite was investigated and compared with the studies of ferrofluids structure.
‘Core/shell’ structure revealed and investigated. The using of Polysorbate-80 to stabilize magnetic nanoparticles is very promising for preparing sustainable water-based ferrofluids and for providing SANS contrast variation.
13
On determination of the core-shell structure in magnetic nanoparticles by neutron and X-ray scattering

## Slide 17
“Simulation of interprocessor interactions for MPI-applications
in the cloud infrastructure” A.V. Nechaevskiy, D.I. Pryahina
As part of preparations for the new cloud center of parallel computing at the Laboratory of Information Technologies (LIT) of the JINR, a test problem - a parallel MPI algorithm for calculations of the long Josephson junctions for estimation of center’s performance at different hardware properties was considered.
14
The simulation program SyMSim can be successfully used to estimate the execution time of MPI algorithms in the cloud environment, taking into account interprocessor connections.
n>1, n – number of processors, Tv – the CPU time per one iteration without exchange time, t – buffer transfer time between CPU, I - iterations number.

## Slide 18
“Influence of high pressure on the crystal and magnetic
structure of La0.5Ba0.5CoO3” A.V. Rutkauskas, D.P. Kozlenko, I.O. Troyanchuk, S.E. Kichanov, E.V. Lukin, B.N. Savenko
15
The crystal and magnetic structures of cobaltite La0.5Ba0.5CoO3 have been investigated by the neutron diffraction method at high pressure up to 4.6 GPa in the temperature range from 10 to 290 K. Under normal pressure, the crystal structure of this compound has a cubic symmetry with the spatial group , which is kept throughout the investigated pressure range. Ferromagnetic ordering is observed when the temperature is reduced to T = Tc = 178 K. This magnetic ordering and Curie temperature do not change at high pressure up to 4.6 GPa. The results of our study show that the ferromagnetic ground state and the intermediate spin state of Co3+ ions remain stable in La0.5Ba0.5CoO3 under pressure up to 4.6 GPa.

## Slide 19
“Monte Carlo simulations of SESANS-TGF experiments” V.V. Sadilov, V.I. Bodnarchuk, S.A. Manoshin, R. V. Erhan, A.S. Doroshkevich, A. Ioffe
16
Results of virtual experiments with TGF-SESANS setup. Solid lines are the results of calculations.
First experimental results: spin-echo focusing, measured at 9th channel IBR-2. B=130 Gauss and pulses frequency f = 200 Hz
New opportunities, opened by the development and implementation of a new Spin-Echo SANS method based on the use of time-gradient magnetic fields (TGF NSE), considered.

## Slide 20
“Verification of the “XiO” TPS using Radiochromic Films” K. Shipulin, C. Oancea, D.M. Borowicz, G. Mytsin,
J. Vilimovsky, V. Vondracek
The objective was to verify all the stages of proton pencil beam scanning technique applied at the Proton Therapy Center (PTC), Prague, Czech Republic.
17
The 2D dose distributions of the imaginary target in the phantom calculated (TPS) and measured (EBT2) were obtained. The result is within the accuracy of the experiment.

## Slide 21
“Increasing Bandwidth of Data Acquisition Systems on
IBR-2 Reactor Spectrometers in FLNP” V.A. Drozdov, V.V. Shvetsov, S.M. Murashkevich
18
Due to new project design and modify for the new FLINK module with an USB 3.0 interface allows increasing the data acquisition bandwidth to 100 MB/s. (Fig. 1).
Fig. 1 Architecture of data acquisition system with FLINK USB 3.0
Fig. 2 New architecture of data acquisition system with USB 3.0 extender
The development of new modules with DAQ functions similar to MPD and De-Li-DAQ-2D and with the USB3.0 interface on the board with USB extender will allow increasing the bandwidth of data up to 375 MB/s (Fig. 2).
Fig. 3 The architecture of the data acquisition system based on MPD32 USB 3.0.
Today, the development of the architecture of the module MPD32 with USB 3.0 for the new wide-aperture backscattering detector on the High Resolution Fourier Diffractometer is completed and FLNP JINR is developing software for the discussed DAQ (Fig. 3).

## Slide 22
“Investigation of the magnetic and structural properties of nanosized simple oxides” S.V. Sumnikov, I.A. Bobrikov, A.M. Balagurov, N. Mironova-Ulmane
To establish the correlation between structure and magnetic properties of simple oxides the magnetic structural phase transitions in NiO and MnO have been studied by neutron diffraction.
In MnO structural and magnetic transitions occur at the same temperature. In NiO a noticeable difference between structural and magnetic phase transition is observed (ΔT=56 ± 9 K, TN = 539 ± 7 K, T = 483 ± 5 K).
19

## Slide 23
“Growth of the silicate clusters in basic
TEOS/ethanol/water solutions” O.V. Tomchuk, M.V. Avdeev, V.L. Aksenov, L.A. Bulavin
The small-angle neutron scattering with the inner and outer contrast variation (H/D substitution) was applied to clusters in hydrolyzed solutions of TEOS in ethanol.
The obtained data indicate that the structure of clusters does not contain closed hydroxyl groups. Thus, the overwhelming majority of the hydrolyzed bonds participate in the condensation reaction to form Si-O-Si structure units.
20

## Slide 24
21
HLIT-VDI - a new service of the HybriLIT ecosystem for work with applied software packages
1Matveev M., 1Podgainy D., 1Streltsova O., 1Torosyan Sh., 1Zrelov P., 1Zuev M.,
1LIT JINR, Dubna, Russia

## Slide 25
“Neutron reflectometry study of structure and glass transition in thin films of polystyrene-fullerene nanocomposites” T.V. Tropin, C. Schick, I.V. Gapon, M.V. Avdeev, V.L. Aksenov
At the GRAINS reflectometer at IBR-2 the measurements of the glass transition of thin films of polymer-fullerene nanocomposites were performed.
Tg dependence on composition investigated, perspectives of research discussed.
22
Tg~91°C

## Slide 26
23
DATA MANAGEMENT SYSTEM OF THE UNECE ICP Vegetation Program
Authors: Gennady Ososkov, Marina Frontasyeva, Alexander Uzhinskiy, Nikolay Kutovskiy, Andrey Nechaevsky
The aim of the UNECE International Cooperative Program (ICP) Vegetation in the framework of the United Nations Convention on Long-Range Transboundary Air Pollution (CLRTAP) is to identify the main polluted areas of Europe, produce regional maps and further develop the understanding of the long-range transboundary pollution. The program is realized in 39 countries of Europe and Asia. Since 2014 Frank Laboratory of Neutron Physics (FLNP) has been in charge of that part of the project which is related to the moss biomonitoring. The Data Management System (DMS, moss.jinr.ru) of the UNECE ICP Vegetation was developed at the Laboratory of Information Technologies (LIT). It consists of a set of interconnected services and tools deployed and hosted at the Joint Institute of Nuclear Research (JINR) cloud infrastructure. DMS is intended to provide its participants with modern unified system of collecting, analyzing and processing of biological monitoring data.
DMS allows organizing data collection quite flexible in respect to heterogeneity of raw data. Verification of imported data is done automatically and allows to find most of human made mistakes
Participants are able to generate maps, get historical reports and statistic parameters of their data, correlation between element concentration, contaminations factors, geo-indexes and so on.
More than 6000 sampling sites from 47 regions of different countries are presented at the DMS

## Slide 27
“Temperature resumption and correlation of inhomogeneous magnetic
states in the structure Nb(70nm)/Ni[65%]Cu[35%](7nm)//Si” V.D. Zhaketov, Yu.V. Nikitenko
24
Nb(70nm)
Ni65%Cu35%(6.5nm)
Substrate
(Si–1mm)
Fig.1. Investigated structure
1 – 25 Oe
2 – 25 Oe (sample is magnetized)
3 – 200 Oe
λ=1 Å
Fig.2. Neutron Intensity of the
reflection + refraction
Fig.3. Magnetic state of
the ferromagnetic layer
Magnetic properties of superconductor are antagonistic to the ferromagnetic ones. But in layered structures ferromagnetic/superconductor (FM/S), where thickness of layers are order of the superconductivity correlation length or magnetic order parameters, their coexistence is possible and it’s cause arising of different nontrivial effects. In this work we investigated structure Nb/NiCu (Fig.1). Tcurie of NiCu is rather low, so it’s possible to make FM-layer thicker (dFM~1/Tcurie – limit thickness for cryptoferromagnetism’s realization). In this work we found temperature resumption of ferromagnetic state at T=9K and 4K by neutron scattering (for example Fig.2). Nature of this phenomenon required further investigations. On pic.3 shown magnetic state of FM layer, which described experimental data. There are superparamagnetic clusters in the structure and magnetic media with magnetic domains. Magnetic moment’s alignment of domains and clusters depend on temperature and magnetic field.

## Slide 28
Conclusions
The total number of 24 poster reports have been prepared for the present PAC session;
The reported topics include investigation of “soft” and “hard” condensed matter using neutron scattering and complementary methods, current developments related to informational technologies at the JINR, methodological works and production of detectors for the IBR-2 instruments;
THANK YOU FOR YOUR ATTENTION