## Slide 1: Cooperation between JINR and the National Synchrotron Radiation Centre SOLARIS (Kraków, Poland)
47-th meeting of the PAC for Condensed Matter Physics
Speaker: V. Shvetsov

## Slide 2
8 at US
4 at China;
4 at Japan;
> 12 at Europe

## Slide 4
The end of 2013 visit of the JINR delegation to SOLARIS

## Slide 5
600 MeV Injector:
Thermionic RF Gun
6 accelerating structures
Transfer line with DC septum
Normalized emittance 10 mm mrad
Energy spread <0.2%
1.5 GeV Storage Ring
12 DBA magnet blocks
Natural emittance 5.598 mm mrad
100 MHz RF system
300 MHz Landau Cavities
Injection dipole kicker
Ramping

## Slide 7
May 2015

## Slide 8: SOLARIS ring orbit correction: 36 BPM
Without any correction the rms orbit at 1.5 GeV is 0.70 mm in the horizontal plane and 1.09 mm in the vertical plane
After a few BBA iterations the rms values were reduced to 97.67 μm and 88.81 μm, respectively

## Slide 11: SOLCRYS – new laboratory for structural research at Polish synchrotron SOLARIS
The SOLCRYS laboratory will be a part of the SOLARIS synchrotron in Cracow where the state of the art structural research will be performed. The Laboratory will comprise two beamlines:
  “classical” beamline called MX/BioSAXS/PD with three experimental endstations;
  second experimental line which will be equipped with a CryoTEM microscope;
In order to organize the SOLCRYS laboratory the extension of the existing experimental hall will be necessary. The extended part of the building will contain the endstations of the beamlines and Cryo TEM microscope room as well as the small lab for sample preparation;
Research methods available in these two parts of the laboratory will be complementary enabling complex structural characterization of various materials including the biological samples(proteins, protein complexes, nucleic acids etc);

## Slide 12: General idea of MX-SAXS beamline (initial project)
Fig. 3. M. Kozak, W. Rypniewski, M. Jaskólski (2012) Synchrotron Radiation in Natural Science 11, 5-10)

## Slide 13
PX/SAXS BL, NCPS Solaris, Kraków, Poland
Extended hall

## Slide 14: MX/SAXS/PD BL
High-energy beamline MX/BioSAXS/PD will use the monochromatized synchrotron radiation from the
superconducting wiggler. It will be equipped with 3 endstations enabling measurements in 4 experimental modes:
  single crystal diffraction (in particular protein crystallography - PX);
  small angle X-ray scattering (SAXS);
  powder diffraction (PD);
  X-ray absorption spectroscopy (XAS);

## Slide 15: MX/SAXS/PD BL
The Macromolecular Crystallography sector - tunable beamline (for Muliwavelength Anomalous Diffraction - MAD)
Wavelength range: 0.6 – 3.0 Å ;
Energy resolution ~ 1 x 10-4.
Main components
a) Vertically Collimating Mirror (Si and Rh)
b) Cryogenically-cooled DCM operating at 5-21 keV (~0.6 –3.0 Å)
c) Toroidal Focussing Mirror
d) Endstation
Expected spot size at the sample position ~ 50μm .

## Slide 16: MX/SAXS/PD BL
The Small angle X-ray scattering sector - tunable beamline (for anomalous SAXS)
Wavelength range: 0.75 – 2.0 Å ;
Energy resolution ~ 1-2 x 10-4.
Main components
a) Toroidal Collimating Mirror (Si and Rh)
b) Water-cooled DCM or Cryogenically-cooled DCM (preffered) (~0.75 –2.0 Å)
c) Endstation
Expected beam size ~100-150 μm

## Slide 17: MX/SAXS/PD BL - endstations
The Macromolecular Crystallography sector - tunable beamline (for MAD)
Detectors – Pilaus 3X 6M or EigerX 9M (Dectris),
cryocooling system,
robotic autosampler for remote access,
high pressure (HP) cell (mini HP cell).
The Small angle X-ray scattering sector - tunable beamline (for anomalous SAXS)
Detectors (for SAXS/WAXS) – Pilaus 3S 2M or EigerX 4M,
size exclusion chromatography system (SEC),
temperature attachments,
HP system (optional).

## Slide 18: SC wiggler for MX/SAXS beam line
Potential manufacturer – BINP Novosibirsk. An example – SC wiggler SCW30 produced for ALBA at Spain

## Slide 19: Scientific topics (examples) for MX outstation
The MX endstation will be used for routine collection of diffraction data for macromolecular crystallography including:
  Multiwavelength Anomalous Diffraction experiments
  (using Se – selenomethionine substituted proteins, Br – brominated oligonucleotides, …),
  Cryocrystallography,
  Remote access, high pressure (option).
Objects:
  Protein and peptides (crystals),
  Protein complexes, viruses (crystals),
  Nucleic acids (crystals),
  Protein fibrils (fiber diffraction - eg. amyloids).

## Slide 20: Scientific topics (examples) for SAXS outstation
SAXS studies at this station will include wide range of biological objects, new materials, nanoparticles and nanocomposites (in solution or in solid state):
  nanocomposites
  polymers and copolymers,
  nanoparticles,
  semiconductors and new materials for nanoelectronics
  nanomaterials for energy storage applications
  amphiphilic molecules (surfactants, lipids etc),
  drug delivery systems,
  intrinsically disordered proteins,
  globular and membrane proteins,
  macromolecular complexes,
  viruses and virus-like particles,
  liposomes, biological membranes, nucleic acids and their complexes with proteins.

## Slide 21: CryoTEM BL
The cryo electron microscopy has shown a burst like development during last years. The progress in development of instruments caused that cryo transmission electron microscopy became one of the main techniques used for determination of the structure of macromolecules with the resolution asgood as 0.2 nm.
The newest microscopes like the Titan Krios transmission electron microscope (TEM) with direct beam detector are ready for use in protein and cellular imaging. The instrument permits full range of semiautomated applications, including: 2D electron crystallography, single particle analysis, cryo electron microscopy, and dual-axis cellular tomography of frozen hydrated cell organelles and cells. Cryo techniques preserve sample integrity by maintaining the sample in its natural condition and state.

## Slide 22: Several slides, courtesy of P.Kuzhir from BSU, Minsk

## Slide 23
Our aim
Looking for new materials promising for
Optoelectronics, nanoelectronics, photovoltaic, and thermoelectric applications
Open questions, which could be solved
using synchrotron techniques
- What is crystalline structure of materials (phase composition, defectiveness, etc.)?
- How is it transformed with temperature and pressure?
- What is local atomic order?
What is electronic density of states?
Influence and presence of impurities, deffects on the electronic properties
- . . .

## Slide 24
Revealing peculiarities of electronic structure of different materials using X-ray absorption spectroscopy (MX experimental station)
Objects:
topological insulators,
2D crystals (graphene, MoS2, MoSe2, WS2, WSe2, silicene), as they are and modified (or defected) after ionizing radiation treatment;
chalcogenide semiconductors, bismuth semiconductor compounds (oxyhalides, oxysulfides)
Nanoscale Research Letters (2016)
Appl.Phys. Lett. 108, 123101 (2016)

## Slide 25
Revealing peculiarities of electronic structure of different materials using X-ray absorption spectroscopy (MX experimental station)
Journ. Chem. Phys. 138 (2013), 154706. DOI: 10.1063/1.4801501.
JPCC (2017). DOI: 10.1021/acs.jpcc.7b07840.
Objects:
topological insulators,
2D crystals (graphene, MoS2, MoSe2, WS2, WSe2, silicene), as they are and modified (or defected) after ionizing radiation treatment;
chalcogenide semiconductors, bismuth semiconductor compounds (oxyhalides, oxysulfides)

## Slide 26
Analysis of materials structure and its modification with temperature / pressure by small-angle X-ray scattering and powder diffraction (BioSAXS and PD experimental stations)
XRD patterns
of MoS2/rGO
Journal RSC Advances (2018). DOI: 10.1039/C7RA12455D
Electrochimica Acta 190 (2016), 612. DOI: 10.1016/j.electacta.2015.12.229.
Objects:
chalcogenide semiconductors, bismuth semiconductor compounds (oxyhalides, oxysulfides),
two-dimensional materials (graphene, MoS2, MoSe2, WS2, WSe2, silicene etc.)
BiOI on FTO

## Slide 27
Diffraction study of single crystals (MX experimental station)
Objects: metal halide perovskites
Sci. Chi. Mat. 60 (2017), 1063. DOI: 10.1007/s40843-017-9039-8.
Phys. Chem. Chem. Phys. 6 (2017). DOI: 10.1039/C6CP07182A.

## Slide 28: Conclusion
Year 2017 – only at ESRF and SPRING-8 we spent 228 man-days, didn’t check other sources;
Not all our requests for beamtime were fulfilled;
JINR lab at SOLARIS which is much closer and guaranties 50% of beam time available – very good synergy with our neutron scattering instruments at IBR-2;

## Slide 29
THANK YOU FOR YOUR ATTENTION