## Slide 1: CYCLOTRON DC-280 STATUS
PAC, DUBNA 2018
FLEROV LABORATORY of NUCLEAR REACTIONS
JOINT INSTITUTE FOR NUCLEAR RESEARCH
Vasiliy Semin

## Slide 2
Ion sources | DECRIS-PM - 14 GHz on the HV platform (Umax=60kV )
Injection energy | Up to 80 keV/Z
A/Z range | 4÷7.5
Energy | 4÷8 MeV/n
Ion mass (for DECRIS-PM) | 4-136
Intensities (A~50) | >10 pµA
Magnetic field level | 0.6÷1.3 T
K factor | 280
Dee voltage | 2x130 kV
RF power consumption | 2x30 kW
Flat-top dee voltage | 2x13 kV
Flat-top power consumption | 2x2 kW
Beam emittance | less than 30 π mm·mrad
Efficiency of beam transfer | >50%
Main design parameters of the DC-280

## Slide 3
N | Item
1 | Magnetic system
2 | RF system
3 | Beam injection system
4 | Beam extraction system
5 | Beam transport system
6 | Diagnostic system
7 | Vacuum system
8 | Water cooling system
9 | Control and power supply system
Main systems of the DC-280

## Slide 4
Magnetic system
guides of internal probe
Radial trimming coils
azimuthal trimmer coils
Shims after modifications

## Slide 5
Main chamber Vacuum equipment
Vacuum system
Vacuum tests in November 2017
The chamber was installed in November of 2017. Нelium leak tests were made in November at vacuum level of 4·10-3 mBar, revealed leaks were successfully eliminated.
Axial injection vacuum equipment

## Slide 6
3Frf
Frf
RF system
Frf=7.32÷10.38 MHz
Fft=21.96÷31.14 MHz
In June 2017, resonance frequencies of the N1 resonator have been measured at minimal RF power. The experimental frequency range is 7.17÷10.8 MHz, which covers the designed one.
Dee voltage | 2x130 kV
RF Power consumption | 2x30 kW
Generator RF Power | 2x50 kW
Flat-top dee voltage | 2x13 kV
RF Power consumption | 2x2 kW
Generator RF Power | 2x3 kW
Flat-top resonators and dees

## Slide 7
Axial injection system
View of ECR-platform equipment
Experimental spectrums of Ca and Ti ions extracted from the DECRIS-PM
ECR- sours DECRIS-PM
Ion currents, pµA |  |  |  |  |  |  |  |  |  |  |  |  | 
Q+ | 5+ | 7+ | 8+ | 9+ | 10+ | 11+ | 12+ | 15+ | 17+ | 19+ | 20+ | 23+ | 26+
Ar |  |  | 116 | 56 |  | 19 | 13 |  |  |  |  |  | 
Kr |  |  |  |  |  |  | 13 | 12 | 7,3 | 2,6 |  |  | 
Xe |  |  |  |  |  |  |  |  |  |  | 3,9 | 3 | 2
24Mg | 90 | 20 | 5 | 1,7 |  |  |  |  |  |  |  |  | 
40Ca |  | 16 | 22 | 24 |  | 14 | 4,8 |  |  |  |  |  | 
50Ti |  |  |  | 10 | 7,2 | 5,5 | 1,9 |  |  |  |  |  | 
56Fe |  |  |  | 9,4 | 8 | 5 |  |  |  |  |  |  | 
Results of bench test of DECRIS-PM

## Slide 8
Bending magnet ±50
Quadrupole lenses
Beam transport system
Vacuum volumes of channels: “Vacuum Praha”, Czech Republic
Beam diagnostics: INR&NE of the Bulgarian Academy of Science
The triplet of quadrupole lenses 11К30-700 (N&V, Romania)

## Slide 9
Water cooling system
The water cooling system was launched in the middle of 2017
Control and power supply systems
The control and power supply systems are being created. Power supply for the main magnet was tested in middle of 2017.

## Slide 10
Schedule of the creation and the launching the DC-280
THANKS FOR YOUR ATTENTION!

## Slide 11
ION | Z | Beam Intensity from ECR |  | Efficiency of acceleration | Expected beam intensities of (4÷8) MeV/n ions on targets pps
 |  | eA | pps |  | 
20Ne | 3 | 150 | 3.1014 | 50% | 1.5·1014
40Ar | 7 | 300 | 3.1014 | 50% | 1.5·1014
48Са | 7/8 | 160 | 1.3.1014 | 50% | 6.2·1013
50Ti | 8/9 | 80 | 6.2.1013 | 50% | 3.1.1013
54Cr | 9 | 125 | 8.1013 | 50% | 4.1013
58Fe | 9/10 | 125 | 8.1013 | 50% | 4·1013
64Ni | 10/11 | 125 | 8.1013 | 50% | 4·1013
70Zn | 11/12 | 100 | 5.1013 | 50% | 2,5.1013
136Хе | 22/23 | 150 | 4.1013 | 50% | 2·1013
Expected beam parameters of the DC-280

## Slide 12
Working diagram of the DC-280

## Slide 13
Electrostatic deflector
Focusing magnetic channel
Extraction radius of Rext=1.79 m
Extraction radius of Rext=1.79 m
Length of the magnetic channel | 0.9 m
Gradient of the magnetic channel | 4.6÷8.4 T/m
Length of electrostatic deflector | 1.3 m
Deflector voltage | 80 kV
Beam extraction system

## Slide 14
References:
Status of the DC-280 cyclotron project, G.G. Gulbekian, S.N. Dmitriev, Yu.Ts. Oganessian, B.N. Gikal, I.V. Kalagin, S.L. Bogomolov, I.A.Ivanenko, N.Yu.Kazarinov, G.N. Ivanov, N.F.Osipov, In. Proc. of Cyclotrons2016 Int. Conf, p.p. 363-365, Zurich, Switzerland, 2016.
http://accelconf.web.cern.ch/AccelConf/cyclotrons2016/papers/thp25.pdf
See also new: https://agenda.infn.it/getFile.py/access?contribId=1&sessionId=1&resId=0&materialId=slides&confId=12207
High-Frequency Acceleration System of the DC-280 Cyclotron, G.G.Gulbekyan, V.B.Zarubin,
G.A.Karmysheva, O.V.Karmyshev, J.Franko, Physics of Particles and Nuclei Letters, Vol. 9, N8, p.p. 637-642, 2012. https://link.springer.com/content/pdf/10.1134/S1547477112080067.pdf
DC-280 cyclotron central region with independent flat-top system, G. Gulbekian, B.Gikal, I.Ivanenko, N.Kazarinov, Proc. of IPAC-2011, San-Sebastian, Spain, p.p. 2703-2705, 2011.
http://accelconf.web.cern.ch/AccelConf/IPAC2011/papers/weps083.pdf
The project of the HV axial injection for the DC-280 cyclotron at the JINR FLNR G.G.Gulbekian, B.N.Gikal, V.V.Bekhterev, S.L.Bogomolov, A.A.Efremov, I.A.Ivanenko, N.Yu.Kazarinov, I.V.Kalagin, V.N.Melnikov, N.F.Osipov, S.V.Prokhorov, A.V.Tikhomirov, M.V.Khabarov, Physics of Particles and Nuclei Letters, 2014, Vol. 11, No. 6, pp. 763–773, 2014. https://inis.iaea.org/search/search.aspx?orig_q=RN:46024650
See also: Proc. of RUPAC-2014, Obninsk, Russia, p.p. 333-335, 2014. http://accelconf.web.cern.ch/AccelConf/rupac2014/papers/thpsc08.pdf
Development of the magnetic system for new DECRIS-PM ion source, V.Bekhterev, S.Bogomolov, A.Efremov, N.Konev, Proc. of ECRIS-14, Nijniy Novgorod, Russia, 2014. http://accelconf.web.cern.ch/AccelConf/ECRIS2014/papers/weommh03.pdf
See also new:
https://agenda.infn.it/getFile.py/access?contribId=2&sessionId=7&resId=0&materialId=slides&confId=12207
The project of the beam transportation lines for the DC-280 cyclotron at the JINR FLNR, G.G.Gulbekyan, B.N.Gikal, G.N. Ivanov, I.V.Kalagin*, V.I. Kazacha, N.Yu. Kazarinov, M.V. Khabarov, V.N. Melnikov, N.F. Osipov, A.V. Tikhomirov, Y.G. Teterev, In Proc. of RuPAC-2014 Int. Conf., p.p. 336-338, Obninsk, Russia, 2014. http://accelconf.web.cern.ch/AccelConf/rupac2014/papers/thpsc09.pdf