## Slide 1
1.-Introduction Physics topics: Excitation of Nucleons and Polarizabilities
2.-Experimental setup: g- beam and detector - Tagger + Crystal Ball@MAMI
Frozen Spin Target
3.-Active Target developement
Institut
für Kernphysik
New Trends in High energy Physics
Budva
September 24th - 30th , 2018
Andreas Thomas
for the A2 Collaboration
First use of an active polarized Frozen Spin Target in a 4 π detector - Detection of particles under cryogenic conditions below 1 Kelvin

## Slide 2
Introduction Physics:
Quark Model
Classification of Baryons
qqq; only uds
Oktett
Dekuplett
Simple Constituent quark picture:
Proton p(938): |uud> ~ |hhi> Spin 1/2
Delta D(1232): |uud> ~ |hhh> Spin 3/2
M1-Transition
(Small 2.5% E2)

## Slide 3
Löhrig, Metsch, Petry, Eur.Phys.J. A10 (2001) 395-446
Introduction: Excitation Spectrum of the Nucleon
H
The light baryon spectrum in a relativistic quark model
He
Hg
Atom
Nucleon

## Slide 4
Phys. Rev. Lett. 87, 022003 (2001)
Phys. Rev. Lett. 84, 5950 (2000)
Nucl. Phys. A642, 561 (1998)
Phys. Rev. C 53, 430 (1996); SP01
Nucl. Phys. A645, 145 (1999)
Unpolarised total photoabsorption cross section
What is the nature of the Nucleon Resonances?
-Excitation inner deg. of freedom
-Molecule
-Quark – Diquark Structure
-Dynamical Generation
- …….?

## Slide 5
Nature and Properties of nucleon resonances
Polarisation observables used to disentangle broad, overlapping resonances.
Beam
Target
s
p
p
p
g
g
g
g
E
G
P
P
T
P
F
H
P
d
d
P
P
P
P
z
y
x
unpol
circ
lin
lin
unpol
-
-
-
-
-
-
-
-
4
,
4
2
,
0
Target
Beam
S
÷
ø
ö
ç
è
æ
W
÷
ø
ö
ç
è
æ
-
+
÷
ø
ö
ç
è
æ

## Slide 6
Parameter
1604MeV, sE=0.100MeV
max. 40mA polarised
eh=9 nm rad, ev=0.5 nm rad
~6500h/year as MAMI B !

## Slide 7
Determination of the degree of polarization of
the electron beam (Moeller Polarimeter).
Circularly pol. photons.
2.
3.
Coherent production of linearly polarized
photons on a diamond radiator
Production and energy measurement of the Bremsstrahlung photons.
A2 Tagging system (Glasgow, Mainz)
1.
Glasgow Tagging Spectrometer
EPJ A 37, 129 (2008)

## Slide 8
4p photon Spectrometer @ MAMI
TAPS:
366 BaF2 detectors
72 PbWO4 detectors
Max. kin. energy:
p+- : 180 MeV
K+- : 280 MeV
P : 360 MeV
Crystal Ball:
672 NaJ detectors
Max. kin. energy:
m+- : 233MeV
p+- : 240 MeV
K+- : 341 MeV
P : 425 MeV
Vertex detector:
2 Cylindr. MWPCs
480 wires, 320stripes
PID detector:
24 thin plastic detectors
gp  S11  ph
p0p0p0
gggggg

## Slide 9
Polarized Target
Polarization = Orientation of Spins in a magnetic field
Ideally: All spins in field direction
P=100%
Complicated interplay between
Polarising force ~ magnetic field B
and
Depolarising force ~ thermal motion of spin particles
(temperature T – relaxation)

## Slide 10
Thermal equilibrium
Boltzmann distribution
Trick: Transfer of the high electron polarization to the nucleon via
m-wave irradiation (DNP)
electron
proton
Magnetic moment in magnetic field:
B=0T
B=0T
B=2.5T
B=2.5T
DE
B [Tesla] | T [mK] | e- [%] | p [%] | d [%]
2,5 | 100 | 99,8 | 0,51 | 0,10
 | 1000 | 93,3 | 0,25 | 0,05
5,0 | 100 | 100,0 | 5,09 | 1,05
 | 1000 | 99,8 | 1,28 | 0,11

## Slide 11
Mainz/Dubna Dilution refrigerator
Separator (4.2Kelvin)
Evaporator (1.5Kelvin)
Mixing chamber(25mK)
Still (0.7K)

## Slide 12
Free electrons
Radicals in material by
chemical or
radiative doping
Saturated electrons of target material not polarized (Pauli principle)
Butanol
Ammonia
LiD
30mm
N
H
H
H
N
O
CH3
CH3
CH3
CH3
Tempo
Target material
Dilution factor (e.g. fButanol=10/74)
determines quality of target material

## Slide 13
Additional challenges for the analysis of experiments with Frozen Spin Target  Dilution Factor.
Carbon
Hydrogen
Butanol

## Slide 14
Helicity Dependence E of Meson Photoproduction on the Proton and Neutron
Gerasimov-Drell-Hearn sum rule (GDH)
1998-
2003
Mainz and Bonn
2010-
2016
New
Mainz
Exp.
with CBall
New Measurement of transverse asymmetries at Bonn ELSA 2017-2019.

## Slide 15
New double polarization data from several facilities
CLAS, Jlab Crystal Barrel, ELSA Crystal Ball, MAMI
With a variety of new measurements of spin observables it comes to a convergence of the multipoles in the region of leading resonances using PWA.
R.Edwards et al.,
Phys. Rev. D84
(2011) 074508
Excited baryons
from Lattice QCD:

## Slide 16
p+
p+
p+
p+
p+
p+
p+
p+
Electric polarizability: proton between charged parallel plates
Pion
cloud
+ + + + + + + + + + + + +
- - - - - - - - - - - - -
Proton Polarizabilities

## Slide 17
d
u
u
p+
p+
p+
p+
Magnetic polarizability: proton between poles of a magnetic
Proton magnetic polarizability
Diamagnetic + Paramagnetic
pion cloud
Paramagnetic
D(1232)
N N N N N N N N N
S S S S S S S S S S S

## Slide 18
Proton Polarizabilities
New measurement of the Proton Scalar Polarisabilities via beamasymmetry in Compton process finished in July 2018.
[PhD E.Mornacchi]

## Slide 19
Spin Vector polarizabilities describe spin response to an incident photon
Four vector pol. (γE1E1 γM1M1 γE1M2 γM1E2) appear at 3rd order in eff. Hamiltonian
Only two linear combinations of vector polarizabilities measured:
Spin Polarizabilities
The Forward S.P. g0 was determined in GDH-Experiment at ELSA and MAMI (DAPHNE) :
The Backward S.P. gp was determined from dispersive analysis of backward angle Compton scattering. [B. Pasquini et al., Proton Spin Polarizabilities from Polarized Compton Scattering (2007).]

## Slide 20
Σ2x 300 hours measurement
Σ2x 300 hours measurement
Curves from:-
B. Pasquini, D. Drechsel, M. Vanderhaeghen,
Phys. Rev. C 76 015203 (2007)
B. Pasquini, D. Drechsel, M. Vanderhaeghen,
Phys. Rept. 378 99 (2003)
Pion photoproduction off of a proton is 75-100 times more likely than Compton (in the 240-280 MeV range) 
Kinematic overdetermination used for cuts (missing mass, proton angle, …).
Test with ‘substraction target’.
Main problems:
Low energetic recoil protons do not escape from the target and do not reach the detector.
Events are produced on the background nuclei (Carbon, coherent, incoherent, k~13%). ).
Measurements of the Proton Spin-Polarizabilities with Double-Polarized Compton Scattering
P.P.Martel et al., PRL 114 (2015) 112501

## Slide 21
New Developement:
Active Polarized Target

## Slide 22
Active Polarized Target
T=45mKelvin after 5 days by 3He/4He mixture  Vacuum in beampipe

## Slide 23
Measurement of P via NMR
[G.Reicherz, Bochum]

## Slide 24
Detector
Electronics
at 150Kelvin
SiPMs gain depends strongly from the temperature ~1% K-1. Therefore it is necessary to control the 25V bias voltage to ~10mV and to have a stable temperature. [PhD M.Biroth, Mainz]
[M.Biroth et al., IEEE Transaction on Nuclear Science,
Vol. 64, Issue 6, June 2017]

## Slide 25
QDC Spectra
at 150Kelvin
QDC Spectra
at 300Kelvin
Clear Separation:
Pedestal,
1 photon,
2 photon, ….

## Slide 26
TDC Spectra show the coincidence with Crystal Ball

## Slide 27
Run
June 2016

## Slide 28
First count rate asymmetries from June 2016
f distribution for p0 production
Target +
Target -

## Slide 29
Recoil proton
Coherent 𝜋0
Background reactions by scattering on 12C or heavy nuclei
Recoil proton
Proton 𝜋0 photo production
Recoil nucleus
Investigation of dilution factor for p0 production

## Slide 31
Recoil protons from scattering on H and
a broad distribution from incoherent scattering on 12C

## Slide 32
M. Biroth, P. Achenbach, E. Downie, and A. Thomas, “A low-noise
and fast pre-amplifier and readout system for SiPMs,” Nucl. Instrum.
Methods Phys. Res. A, vol. 787, pp. 185–188, Jul. 2015.
P. Achenbach, M. Biroth, E. Downie, and A. Thomas, “On the operation
of silicon photomultipliers at temperatures of 1–4 kelvin,” Nucl. Instrum.
Methods Phys. Res. A, vol. 824, pp. 74–75, Jul. 2016.
M. Biroth, P. Achenbach, E. Downie, and A. Thomas, “Silicon photomultiplier
properties at cryogenic temperatures,” Nucl. Instrum. Methods
Phys. Res. A, vol. 787, pp. 68–71, Jul. 2015.

## Slide 33
Data taking with CBall TAPS detector system started 2010 at MAMI C.
All directions of polarization were measured for protons and deuterons in Butanol. Analysis is ongoing.
Measurement of 4 Vector Spin Polarisabilities in Compton process.
Conclusions
Outlook
R&D for polarised active szintillator target for threshold production and Compton will continue. Analysis of first data is on the way.
New active target insert with better light transport system, fibers,
Scintillating target container with Butanol.
New Measurement of transverse asymmetries at Bonn ELSA 2017/19.
The active polarised proton target was in operation in our 4p detector system in 2016.
Neutron Scalar Polarisabilities with active helium gas target 2019.

## Slide 34
Thank You!

## Slide 35
Transverse (Saddle coil)
and
Longitudinal (Solenoid)
Internal
Holding Field (1.2K, 0.6T)
Magnet Technology
DNP at 200mK and 2.5T with 70GHz microwaves.
Frozen spin target (25mKelvin, 0.6T).
Secondary particles punch through holding coil.
All directions of polarization.

## Slide 36
Copper/scandium wire with 54 Nb-Ti filaments embedded in it.
Cu:Sc=1.35:1
Alloy composition: Nb47wt.%Ti
Diameter=0.222mm
It achieves currents up to 50A at 4.2K and 1T.
Internal holding coils

## Slide 37
150mm
4-layer dipole:
N1=N2=138
N3=N4=78