## Slide 1: Circular Hadron- Colliders and Beyond
Frank Zimmermann
CERN, BE Department
Helmholtz School CALC2018 Dubna
Work supported by the European Commission under Capacities 7th Framework Programme, Grant Agreement 312453
Geneva site
Qinghuangdao site

## Slide 2
collider history - technology & discovery
LHC and HL-LHC
FCC study and HE-LHC
FCC-hh and Nb3Sn magnet program
SPPC and Fe HTS magnet program
handling the synchrotron radiation
FCC-hh particle-physics examples
beyond FCC-hh – a staged approach
Outline

## Slide 3
Colliders constructed and operated
Colliders with
superconducting arc magnet system
Colliders with
superconducting RF system
Colliders with
superconducting magnet & RF
Notes: New slide from Davide.
Showing that conductor development is launched at international level, Russia, Japan, (Korea and Europe in preparation)
Underline importance of that development as main cost driver for the hadron collider machine.

## Slide 4
Discoveries by colliders
Standard Model
Particles and forces
Colliders are powerful instruments in High Energy physics
for particle discoveries and precision measurements
SPEAR:
charm quark
tau lepton
PETRA:
gluon
SppS:
Z-boson
W-boson
Tevatron:
top-quark
LHC:
Higgs-boson
Notes: New slide from Davide.
Showing that conductor development is launched at international level, Russia, Japan, (Korea and Europe in preparation)
Underline importance of that development as main cost driver for the hadron collider machine.

## Slide 5
LHC: present collider flagship
2012: Higgs boson discovery
    Completes standard model describing known matter, BUT this is only 5% of the universe!
    what is dark matter?
    what is dark energy?
    why is there more matter than antimatter?
    what about gravity?
    etc…
 Upgrade and full exploitation of LHC as first step
Notes: New slide from Davide.
Showing that conductor development is launched at international level, Russia, Japan, (Korea and Europe in preparation)
Underline importance of that development as main cost driver for the hadron collider machine.

## Slide 6
Goal of High Luminosity LHC (HL-LHC)
The main objective of HiLumi LHC Design Study is to determine a hardware configuration and a set of beam parameters that will allow the LHC to reach the
following targets:
Prepare machine for operation beyond 2025 and up to 2035
Devise beam parameters and operation scenarios for:
# enabling at total integrated luminosity of 3000 fb-1
# implying an integrated luminosity of 250 fb-1 per year,
# design oper. for m = 140 ( peak luminosity 5 1034 cm-2 s-1)
Operation with levelled luminosity! (beta*, crossing angle & crab cavity)
10x the luminosity reach of first 10 years of LHC operation!!
5 events
400
events

## Slide 7
High Luminosity LHC project scope
L. Rossi
More than100 new SC magnets 36 large magnets in Nb3Sn Powering via SC Links and HTS Current Leads
20 new RF cavities
New tunnel and surface infrastructures
New and upgraded cryo plants
Notes: New slide from Davide.
Showing that conductor development is launched at international level, Russia, Japan, (Korea and Europe in preparation)
Underline importance of that development as main cost driver for the hadron collider machine.

## Slide 8
HL-LHC upgrade – ongoing
    HL-LHC significantly increases data rate to improve statistics, measurement precision, and energy reach in search of new physics
    Gain of a factor 5 in rate, factor 10 in integral data wrt initial design
Notes: New slide from Davide.
Showing that conductor development is launched at international level, Russia, Japan, (Korea and Europe in preparation)
Underline importance of that development as main cost driver for the hadron collider machine.

## Slide 9
European Strategy Update 2013
“CERN should undertake design studies for accelerator projects in a global context, with emphasis on proton-proton and electron-positron high-energy frontier machines.”

## Slide 10
International FCC collaboration (CERN as host lab) to study:
pp-collider (FCC-hh)  main emphasis, defining infrastructure requirements
80-100 km tunnel infrastructure in Geneva area, site specific
e+e- collider (FCC-ee), as potential first step
p-e (FCC-he) option, integration one IP, FCC-hh & ERL
HE-LHC with FCC-hh technology
~16 T  100 TeV pp in 100 km
Future Circular Collider Study
GOAL: CDR and cost review for the next ESU (2019)
HE-LHC

## Slide 11
Tevatron (closed)
Circumference: 6.2 km
Energy: 2 TeV

## Slide 12
Large Hadron Collider
Circumference: 27 km
Energy:
- 14 TeV (pp)
- 209 GeV (e+e-)

## Slide 13
Future Circular Collider
Circumference: 80-100 km
Energy:
100 TeV (pp)
>350 GeV (e+e-)
hadron collider energy reach

## Slide 14
“Of course, it should not be the size of an accelerator, but its costs which must be minimized.”
G.-A. Voss,
builder of PETRA,
PAC 1995 Dallas
† 5. October 2013
is 100 km too big?

## Slide 15
FCC-hh: 100 TeV pp collider as long-term goal  defines infrastructure needs
FCC-ee: e+e- collider, potential intermediate step
HE-LHC: based on FCC-hh technology
Tunnel infrastructure in Geneva area, linked to CERN accelerator complex;
site-specific, as requested by European strategy
Launch R&D on key enabling technologies in dedicated R&D programmes, e.g.
16 Tesla magnet program, cryogenics,
SRF technologies and RF power sources
FCC Scope:
Accelerator and Infrastructure
M. Benedikt

## Slide 16
Elaborate and document
- Physics opportunities
- Discovery potentials
Experiment concepts for hh, ee and he
Machine Detector Interface studies
R&D needs for detector technologies
Overall cost model for collider scenarios
including infrastructure and injectors
Develop realization concepts Forge partnerships with industry
FCC Scope:
Physics & Experiments
M. Benedikt

## Slide 17
Role of CERN
Host the study
Prepare organisation frame
Setup collaboration
Identify R&D needs
Estimate costs

## Slide 18: A sustained decrease in specific cost
Will FCC pass below the specific cost of
100 kCHF/GeV c.m.?

## Slide 19
Constr.
Physics
LEP
Construction
Physics
Proto
Design
LHC – operation run 2
Construction
Physics
Design
HL-LHC - ongoing project
Physics
Construction
Proto
1980
1985
1990
1995
2000
2005
2010
2015
2020
2025
2030
2035
~20 years
Design
FCC – design study
Must advance fast now to be ready for the period 2035 – 2040
CDR by end 2018 for next update of European Strategy
CERN Circular Colliders & FCC

## Slide 20
parameter | FCC-hh |  | HE-LHC | HL-LHC | LHC
collision energy cms [TeV] | 100 |  | 27 | 14 | 14
dipole field [T] | 16 |  | 16 | 8.33 | 8.33
circumference [km] | 97.75 |  | 26.7 | 26.7 | 26.7
beam current [A] | 0.5 |  | 1.1 | 1.1 | 0.58
bunch intensity [1011] | 1 |  | 2.2 | 2.2 | 1.15
bunch spacing [ns] | 25 |  | 25 | 25 | 25
synchr. rad. power / ring [kW] | 2400 |  | 101 | 7.3 | 3.6
SR power / length [W/m/ap.] | 28.4 |  | 4.6 | 0.33 | 0.17
long. emit. damping time [h] | 0.54 |  | 1.8 | 12.9 | 12.9
beta* [m] | 1.1 | 0.3 | 0.45 | 0.15 (min.) | 0.55
normalized emittance [mm] | 2.2 |  | 2.5 | 2.5 | 3.75
peak luminosity [1034 cm-2s-1] | 5 | 30 | 16 | 5 (lev.) | 1
events/bunch crossing | 170 | 1000 | 460 | 132 | 27
stored energy/beam [GJ] | 8.4 |  | 1.3 | 0.7 | 0.36
FCC-pp Collider Parameters

## Slide 21
Integration & design strategy:
Development of optimized 16 T magnet, ompatible with HE LHC requirements
New cryogenic layout to limit QRL dimension
  Working hypothesis for HE-LHC :
  No major CE modifications on tunnel and caverns
  similar geometry and layout as LHC machine & experiments
  maximum magnet cryostat diameter ~1200 mm
  maximum QRL diameter ~830 mm
HE-LHC Integration Aspects
V. Mertens

## Slide 22
Half-sector cooling instead of full sector (as for LHC)
to limit cross section of cryogenic distribution line
higher heat load and integration limitations:
8 additional 1.8 K refrigeration units wrt. LHC
8 new higher-power 4.5 K cryoplants
Cryogenics Modification for HE-LHC
L. Tavian

## Slide 23
circumference 97.8 km
two high-luminosity experiments (A & G)
two other experiments (L & B) combined with injection upstream of experiments
two collimation insertions
  betatron cleaning (J)
  momentum cleaning (F)
extraction/dump insertion (D)
RF insertion (H)
integrated optics for full ring established, beam dynamics studies confirm design goals
FCC-hh layout and optics
D. Schulte, M. Benedikt

## Slide 24
phase 1:
b*=1.1 m, DQtot=0.01, tta=5 h
250 fb-1 / year
phase 2:
b*=0.3 m, DQtot=0.03, tta=4 h
1 ab-1 / year
radiation damping: t~1 h
total integrated luminosity over 25 years of operation O(20) ab-1/experiment - consistent with physics goals
phase 2: Interplay of radiation damping,
luminosity burn-off, controlled transverse blow-up
transition via operation experience,
no HW modification
FCC-hh operation phases

## Slide 25
Baseline:
LHC @ 3.3 TeV
Alternative:
scSPS @ 1.3 TeV
Total of O(5.5 km) superconducting bends in transfer lines from LHC, at 7.2 T
O(6.5 km) normal-conducting bends from SPS, at 1.8 T
FCC-hh injector options
Current baseline: Injection energy 3.3 TeV LHC  Field-swing FCC-hh like LHC
Alternative options: Injection from SPSupgrade around 1.3 TeV
SPSupgrade could be based on fast-cycling SC magnets, 6-7T, ~ 1T/s ramp, cf. SIS 300 design
SPSupgrade would also be an ideal injector for HE LHC (as alternative to the 450 GeV SPS)

## Slide 26
Main development goal is wire performance increase:
Jc (16T, 4.2K) > 1500 A/mm2 50% increase wrt HL-LHC wire
Reduction of coil & magnet cross-section
3150 mm2
~1.7 times less SC
~10% margin
HL-LHC
~10% margin
FCC ultimate
5400 mm2
After only one year development, prototype Nb3Sn wires from several new industrial FCC partners already achieve HL-LHC performance
Conductor activities for FCC started in 2017:
Bochvar Institute (production at TVEL), Russia
KEK (Jastec and Furukawa), Japan
KAT, Korea
Columbus, Italy
University of Geneva, Switzerland
Technical University of Vienna, Austria
SPIN, Italy
University of Freiberg, Germany
  In addition, agreements under preparation:
  Bruker, Germany
  Luvata Pori, Finland
worldwide FCC Nb3Sn program

## Slide 27
Short model magnets (1.5 m lengths) built from 2018 – 2022
Russian 16 T magnet program launched by BINP recently
16 T dipole design activities & options
M. Benedikt

## Slide 28
All coil parts, structural components and tooling are available at FNAL
Coil fabrication and the work with mechanical structure are in progress
First magnet test in September 2018
Iron Laminations
AL I-Clamps
Fillers
Axial Rods
End Plates
StSt Skin
15 T dipole demonstrator (US MDP)
A. Zlobin

## Slide 29
Coil fabrication
Winding of the first coil has been completed. Preparation for reaction on-going. All tooling for coil production ready
First ERMC coil winding
Coil Reaction Tool
Coil Impregnation Tool
Aluminum shell
Magnet yoke
Axial rods
Dummy coils
Magnet assembly
Components and tooling ready. Dummy assembly to characterize the structure behavior on-going.
16 T ERMC construction at CERN
D. Tommasini

## Slide 30
FCC 16 T magnet R&D schedule
total duration of magnet program: ~20 years
would follow HL-LHC Nb3Sn program with long models w industry from 2023/24
M. Benedikt, L. Bottura

## Slide 31
Parameter | Unit | SPPC |  |  | FCC |  | 
 |  | PreCDR | “CDR” | “Ultimate” |  |  | 
Circumference | km | 54.4 | 100 | 100 | 100 |  | 
c.m. energy | TeV | 70.6 | 75 | 125-150 | 100 |  | 
dipole field | T | 20 | 12 | 20-24 | 16 |  | 
injection energy | TeV | 2.1 | 2.1 | 4.2 | 3.3 |  | 
#IPs |  | 2 | 2 | 2 | 2 |  | 
luminosity per IP | 1035 cm-2s-1 | 1.2 | 1.0 | - | 0.5 |  | 3.0
norm. emittance | mm | 4.1 | 2.4 | ? | 2.2 (0.44) |  | 
IP beta function | m | 0.75 | 0.75 | - | 1.1 |  | 0.3
beam current | A | 1.0 | 0.7 | - | 0.5 |  | 
bunch separation | ns | 25 | 25 | - | 25 (5) | 25 (5) | 
bunch population | 1011 | 2.0 | 1.5 | - | 1.0 (0.2) | 1.0 (0.2 | 
SR power /beam | MW | 2.1 | 1.1 | - | 2.5 |  | 
SR heat load/ap | W/m | 45 | 13 | - | 30 |  | 
SPPC main parameters
J. Tang

## Slide 32
SppC layout 2017
coexistence ee, pp, ep
two high-luminosity pp experiments
two other experiments for AA & ep
one (combined) collimation insertion
one RF insertion
extraction insertion
injection insertion
greenfield injector chain
circumference: 100 km
J. Gao
J. Gao, X. Lou, J. Tang

## Slide 33
p-Linac: proton superconducting linac
p-RCS: proton rapid cycling synchrotron
MSS: Medium-Stage Synchrotron
SS: Super Synchrotron
ion beams: dedicated linac (I-Linac) and RCS (I-RCS)
SppC injector chain
J. Gao

## Slide 34
Chinese 10-year R&D target
for SPPC collider
wire from Fe-based HTS*
*discovered at TIT/Japan in 2008

## Slide 35
In October 2016, A consortium for High-temperature superconducting materials, industrialization and applications was formed in China, with participation of major research and production institutions on HTS.
China is actually leading the development of Fe-HTS technology in the world; world-first 100-m Fe-HTS wire was made by CAS-Institute of Electrical Engineering in the last year .
SppC: China-Domestic Collaboration on HTS
J. Gao,
J. Tang,
Q. Xu

## Slide 36
SppC Design of 12-T Fe-based Dipole Magnet
Yoke OD
500mm
Table 1: Main parameters of the cables
Table 2: Main parameters of the strand
Cable | Hight | Width-i | Width-o | Ns | Strand | Filament | Insulation
IRONBASED1 | 8 | 1.5 | 1.5 | 20 | IRON-BASED | FE-BASED | 0.15
IRONBASED2 | 5.6 | 1.5 | 1.5 | 14 | IRON-BASED | FE-BASED | 0.15
IRONBASED3 | 5 | 1.5 | 1.5 | 12 | IRON-BASED | FE-BASED | 0.15
Strand | diam. | cu/sc | RRR | Tref | Bref | Jc@ BrTr | dJc/dB
IRON-BASED | 0.802 | 1 | 200 | 4.2 | 10 | 4000 | 111
One meter of such magnet requires iron-based HTS strand length of 6.08 km
C. Wang, E. Kong (USTC), Q. Xu et al.

## Slide 37
synchrotron radiation (~ 30 W/m/beam) (cf. LHC <0.2W/m) ~ 5 MW total load in arcs
absorption of synchrotron radiation at higher temperature (> 1.8 K) for cryogenic efficiency
provision of beam vacuum, suppression of photo-electrons, electron cloud effect, impedance, …
ANKA e- photon spectrum = FCC–hh spectrum
FCC-hh cryogenic beam vacuum chamber

## Slide 38
BS temperature choice from overall optimisation of:
Cryoplant power consumption
Vacuum system performance
Impedance and beam stability
Optimum beam screen operation temperature 40 - 60 K
Electrical power for beam screen cooling ~100 MW .
cryoplants energy efficiency
P. Lebrun,
L. Tavian

## Slide 39
FCC tunnel integration in arcs
remember: LHC (HE-LHC) tunnel diameter only 3.8 m

## Slide 40
FCC-hh detector – reference design
4 T, 10 m bore solenoid, 4 T forward solenoids, no shielding coil
14 GJ stored energy
rotational symmetry for tracking!
20 m diameter (~ ATLAS)
15 m shaft
~1 billion project
W. Riegler et al.
latest l* = 40 m

## Slide 41
FCC-hh is a HUGE discovery machine (if nature …), but not only.
FCC-hh physics is dominated by three features:
- Highest center of mass energy –> a big step in high mass reach!
ex: strongly coupled new particles up to >30 TeV
Excited quarks, Z’, W’, up to ~tens of TeV
Give the final word on natural Supersymmetry, extra Higgs etc.. reach up to 5-20 TeV ; Sensitivity to high energy phenomena in e.g. WW scattering
- HUGE production rates for single & multiple production of SM bosons (H,W,Z) & quarks
-- Higgs precision tests using ratios to e.g. // /ZZ, ttH/ttZ @<% level
-- Precise determination of triple Higgs coupling (~3% level) and quartic Higgs coupling
-- detection of rare decays H V (V= ,,J/,,Z…)
-- search for invisibles (DM searches, RH neutrinos in W decays)
-- renewed interest for long lived (very weakly coupled) particles.
-- rich top and HF physics program
- Cleaner signals for high Pt physics
-- allows clean signals for channels presently difficult at LHC (e.g. H bb)
FCC-hh discovery potential highlights
A. Blondel, ICHEP 2018

## Slide 42
Physics at a 100 TeV pp collider: CERN Yellow Report (2017) no.3
1) Standard Model processes: https://arxiv.org/pdf/1607.01831v1.pdf
2) Higgs and EW symmetry breaking studies: https://arxiv.org/pdf/1606.09408v1.pdf
3) Βeyond the Standard Model phenomena: https://arxiv.org/abs/1606.00947
4) Heavy ions at the Future Circular Collider: https://arxiv.org/abs/1605.01389
Now proceeding to ascertain these cross-section calculations with real detector and simulations…
FCC-hh discovery potential
M. Mangano (ed.)

## Slide 43
FCC-hh Higgs production

## Slide 44
H at the few percent level
To reach a precision on H at the few percent level requires a linear collider of at least 3TeV
(ILC 500 GeV can obtain a 30% indication and CLIC 3TeV estimate is 10%)
Higgs studies at FCC-hh

## Slide 45
gHxx | FCC-ee | FCC-hh | FCC-eh
ZZ | 0.22 % | < 1% * | 
WW | 0.47% |  | 
H | 1.6% |  | 
 | 4.2% | <1% | 
Z | -- | 1% | 
ttH | 13% | 1% | 
bb | 0.7% |  | 0.5%
 | 0.8% |  | 
cc | 0.7% |  | 1.8%
gg | 1.0% |  | 
 | 8.6% | 1-2% | 
uu,dd | H ? | H ? | 
ss | H  ? | H  ? | 
ee | ee  H |  | 
HH | 40% | ~3-5% | 20%
inv, exo | <0.55% | 10-3 | 5%
HIGGS PHYSICS
hh, eh precisions assume
SM or ee measurements
Ffor FCC-hh : H ZZ to serve
as cross-normalization
(well measured at FCC-ee)
Higgs couplings gHxx precisions
for ttH, combination of
4% (model dependent)HL-LHC
with FCC-ee will lead to
ttH coupling to  3%...
model independent!
for gHHH investigating now : the possibility of reaching 5 observation at FCC-ee:
4 detectors
+ recast of running scenario
example synergy of FCC-ee/hh/eh

## Slide 46
how to go further?
muon collider* is back !
3 new ideas :
LEMMA m production by e+ annihilation
Gamma factory for e+ generation
full exploitation of FCC complex
*first proposed by Gersh Budker in 1969

## Slide 47
LHeC-class e+ source & e+ acceleration at 45 GeV
(circular/linear options)
e+ ring
100 KW target
m+
m-
isochronous rings
Positron Beam
key challenges
~1011 m / sec from e+e-gm+m-
key
R&D
1015 e+/sec, 100 kW class target, NON destructive process in e+ ring
key challenges
~1013-1014 m / sec
tertiary particle pgpgm:
fast cooling
(t=2ms)
by 106 (6D)
fast acceleration
mitigating m decay
background
from m decay
from US-MAP (2015) to LEMMA scheme (2017)
M. Antonelli, M. Boscolo, P. Raimondi et al.

## Slide 48
high photon energies,
high cross section
W. Krasny
FCC based Gamma Factory could provide >1017 e+/s
“Gamma Factory” based on “PSI”
Compton back scattering at LHC or FCC

## Slide 49
100 TeV m collider in C=100 km FCC tunnel with B=16 T → L>1034 cm-2s-1
Combining Gamma Factory, LEMMA,
FCC-ee and FCC-hh

## Slide 50
luminosity per wall-plug power vs c.m. energy
J.P. Delahaye, M. Palmer, et al., arXiv:1502.01647 (updated by A. Blondel, P. Janot, F.Z.)
“FCC-mm”-
a long-term
FCC upgrade
FCC-hh
collider efficiency – L per power

## Slide 51
a few conclusions
100 TeV hadron collider the only available path to directly produce new particles at energies of 10s of TeV; such machine also is the ultimate Higgs factory
complete design for FCC-hh, parallel effort in China for SppC
key technologies: SC wire and high field SC magnets; different approaches for FCC and SppC; worldwide R&D programme in place
FCC concept supports attractive staged long-term strategy for particle physics: FCC-ee → FCC-hh → FCC-mm
highest-luminosity collisions up to very high energies; collider program extending well into the 22nd century

## Slide 52
thank you for your attention!
Nima Arkani-Hamed during the
inauguration of the Center for
Future High Energy Physics
(CFHEP) IHEP Beijing, 17 Dec 2013

## Slide 53
High Energy Colliders under study
100 TeV pp  10-19 m
discovery of new particles at 10 TeV mass scale
100 TeV

## Slide 54: a few references
CAS Beam Dynamics and Technologies for Future Colliders, Zürich, 21 February – 6 March 2018
  https://indico.cern.ch/event/643268/ (esp. M. Benedikt)
ARIES muon collider workshop, 1-3 July 2018
https://indico.cern.ch/event/719240/ (esp. J.-P. Delahaye)
12th ICFA Seminar, Ottawa, 6-9 November 2017
https://meetings.triumf.ca/indico/event/9
A. Blondel, ‘’Physics at the FCCs – a story of synergy and complementarity,” ICHEP’18 Seoul
M. Mangano (ed.), “Physics at the FCC-hh, a 100 TeV pp collider,” arXiv:1710.06353 CERN-2017-003-M
FCC web site, http://cern.ch/fcc
CEPC/SppC CDR, just published
FCC CDR, to be published end of 2018