## Slide 1
Vadim Kolesnikov
(VBLHEP)
On behalf of the MPD team
Programme Advisory Committee for Particle Physics
49th Meeting
June 18-19, 2018
Within the JINR theme 02-0-1065-2007/2019
Progress towards the realization
of the MPD project

## Slide 2
Outline
Introduction
Progress in MPD project realization:
MPD TDR preparation
MPD mass-production: readiness status
Progress in MPD simulation
Summary

## Slide 3
NICA niche in heavy-ion collisions
QCD matter under extreme conditions (NICA niche – high mB)
arXiv:1605.07887
Highest net-baryon density – essential to probe deconfinement and CSR
Maximum of the strangeness/entropy ratio and hypernuclei production
Non-trivial excitation function for high moments of p-pbar and proton’s v1 slope
Increase of (anti)hyperon polarization  high vorticity QCD matter
Small contribution from correlated charm in dilepton spectra
arXiv:1701.06657

## Slide 4
NICA program (White Paper)
Physics targets for the exploration of the QCD phase diagram accessible to NICA & BMN and possible observables for a “mixed phase“ in the release of the “NICA White Paper” as a Topical Issue of the EPJ A (July 2016)
Bulk properties, EOS
hadron phase-space distributions, femtoscopy, flow
In-Medium modification of vector mesons
onset of low-mass dilepton enhancement, IMR dilepton slopes
Deconfinement (chiral) phase transition at high rB
enhanced strangeness production
CME, vorticity, L polarization
QCD Critical Point
event-by-event fluctuations and correlations
Hypermatter
single and double hypernuclei
Notes: 4

## Slide 5
MPD detector at NICA (Stage’1 setup)
h=1.2
TPC tracking: |h|<1.6 (Npoints>15)
PID: dE/dx+TOF+ECAL |h|<1.2, 0.1<pT<4 GeV/c
FHCAL: 2<|h|<5
Trigger&T0: FFD
FHCAL coverage and granularity provides good event plane resolution
5-10% resolution for the
wide centrality range

## Slide 6
MPD:
Net-protons
Au+Au @ 4 GeV
Net-protons
Au+Au @ 11 GeV
MPD detector provides a uniform midrapidity phase-space coverage
From 35 to 65 identified p-pbar (central Au+Au, |y|<0.5, pT<1.8 GeV/c)
MPD PID (hadrons) and CEP search prospects

## Slide 7
MPD PID performance: dileptons
Extra h-suppression
factor with EMC:
up to 30 for protons
up to 13 for pions
up to 12 for kaons
ECAL energy deposit
ECAL timing
ECAL E/p
Further hadron suppression with ECAL
Energy deposit and timing in ECAL
MPD Au+Au (TPC+TOF+ECAL)

## Slide 8
Status of MPD TDRs
MPD system | Date of recent evaluation | Comments
TPC | 30.01.2018 | Recent DAC recommendations and TDR status were discussed
TOF | 30.01.2018 | Recommendations from DAC implemented, ready for green light
FFD | 22.07.2017 | Got green light (22/06/2016)
ECAL | 30.01.2018 | Updated version of the ECAL TDR will be presented on 20.06.2018, still progressing
FHCAL | 22.07.2017 | All recommendations from DAC implemented, ready for green light
DAQ | 16.12.2015 | Version 6 (June’18), still under development
Computing | -- | VBLHEP+LIT project. Version 1.03. Still progressing
http://indico.jinr.ru/Projects/NICA/Detectors/DetectorAdvisoryCommitee
Next MPD DAC meeting – 20/06/2018
MPD DAC: H. Gutbrod, I. Tserruya, H.-R. Schmidt, N. Xu, L. Musa

## Slide 9
NICA/MPD infrastructure: progress
Working place inside/outside of the MPD Hall
Magnet elements placing
before assembling
MPD mobile
platform
Place & tooling for MPD assembling
Service & supply systems (cryo, cooling, power, etc.)
MPD Hall
MPD Hall will be soon ready for equipment installation!
Preparatory works: designing place, tooling and service systems for MPD assembling and maintenance
80/20 tons cranes for MPD.
Delivery to JINR – July 2018

## Slide 10
MPD superconducting solenoid: June’18 status
Vacuum vessel
Vacuum kiln & tooling
for coil compounding
Solenoid cylinder (all 3 ready)
N. Emelianov (VBLHEP)
Control assembling & tests (AGS) – August’18-March’19
Control assembling at JINR – May-August 2019
Winding of SC coil
Trim coils (ready)
Current up to 4.4 kA
Voltage up to 35 V
ASG superconductors (Genova, Italy):
Weight ~ 900 t
B0=0.5 T
B inhomogeneity ~3.10-4

## Slide 11
2 Poles: Ø 4.5 m, 47 tons each
Rings
Yoke assembly plans: 1) Control assembly at VHM - June 2018
2) Delivery to JINR - August-October 2018
Lodgment
MPD Magnet Yoke: construction status
Plates
N. Topilin (VBLHEP)

## Slide 12
MPD TPC: June’18 status
TPC TDR - minor corrections after recent evaluation
TPC elements & assembling tooling (field cage, rods, manipulators) – in production
Pad planes – in production, flatness issue under control (2 options)
FEE (SAMPA) – design optimization & tests
Service systems (gas, cooling, calibration) – under development
Integration - progressing
ROC chamber assembly facility
TPC pad plane tests
TPC gas system
S. Movchan (VBLHEP)
FEE mass-production
in 2019
ROC manipulator

## Slide 13
TOF TDR, few recommendations after recent evaluation
Production of TOF MRPC components
Renovation in the TOF workshop (ventilation)
Preparation of the MRPC test area
Construction of service systems (gas, etc.)
TOF integration, assembling tooling, etc.
MPD TOF: recent activity
TOF barrel status (readiness in %)
Ordered components (90%)
MRPC modules (25%)
FEE (35%), VME crates(45%), TDCs(10%)
Gas system (50%)
MRPC test area (80%)
LowVoltage (70%), HighVolatge (30%)
V. Golovatyuk, V.Babkin (VBLHEP)
TOF gas crate
MRPC test area
TOF module
Workshop renovation
(ventilation)
TOF module slipway

## Slide 14
MPD Electromagnetic Calorimeter (ECAL)
Pb+Scint. (14 X0 ,4x4 cm2)
WLS fibers + MAPD
I. Tiapkin (VBLHEP), Yi Wang (Tsinghua, China)
Finalizing ECAL geometry (design and simulation) – ITEP team
Mass-production technology testing – 3 workshops at JINR, IHEP, and Tsinghua
ECAL integration scenario – JINR and ProgressTech Ltd.
TDR preparation - All
Eg = 200 MeV
Projective geometry: response uniformity
ECAL module
assembling
FEE support
platform

## Slide 15
MPD FHCAL Calorimeter
2<|h|<5
FHCAL: 90 Lead/Scintillator modules
(15x15cm2 , L~4 λint,WLS+SiPM)
Beam tests: good linearity and sufficient
resolution at NICA energies
A. Ivashkin (INR,Troitsk), A.Taranenko (MEPhI)
Progress prior to June’18:
Successful beam tests in the NICA energy range
Advanced FHCAl simulation
Updated TDR (ready for green light)
Production of modules: ~1/3 ready

## Slide 16
Integration of the Multipurpose Detector
N. Topilin, S. Sukhovarov (VBVLHEP)
Installation of the
power skeleton
Installation of
ECAL "baskets"
Installation of
TOF modules
TPC Installation
MPD integration scenario
Mock-up & tooling

## Slide 17
Event plane with FHCAL, centrality with TPC estimator
TOF+TPC based PID, secondary vertex technique for L
Small difference between MC and reco results
MPD performance for event characterization & flow (QM’18 status)
P. Parfenov (MEPhI), N.Geraksiev (VBLHEP)

## Slide 18
MPD performance: multi-strangeness
Stage’1 MPD configuration (TPC+TOF)
Selection criteria dictated by the decay topology
Realistic tracking and PID (recent MPDRoot release)
MPD detector at NICA:
Large phase-space coverage for hyperons
Good reconstruction capability for multistrangeness
V. Vasendina, A. Zinchenko (VBVLHEP)

## Slide 19
First (kick-off) meeting of MPD and BM@N
JINR, Dubna, 11-13 April, 2018
https://indico.jinr.ru/conferenceDisplay.py?ovw=True&confId=385

## Slide 20
-CI NA Consortium
  Tsinghua University (THU)
  University of Science and Technology of China (USTC)
  Huzhou University (HU)
  Shandong University (SDU)
  Central China Normal University (CCNU)
  Shanghai Institute of Nuclear & Applied Physics (SINAP), Chinese Academy of Science
  Southern China University (SCU)
  Institute of High Energy Physics (IHEP), Chinese Academy of Science
MexNICA
Mexican consortium of six institutions:
BUAP, CINVESTAV, UAS, UNAM, UNISON, UCOL
MPD/NICA Collaboration (recent extension)

## Slide 21
Summary
Substantial progress in MPD project realization (Magnet, TPC, TOF, FFD, FHCAL)
Efficient MPD DAC evaluation process: Stage’1 sub-systems carry out regularly,
next meeting on 20/06/2018
The international collaboration around the NICA is growing.
New partners are invited to join NICA
MPD Collaboration first meeting in April, now waiting for Spokesperson/Boards voting..
Thank you for your attention!