## Slide 1
MAC 2018, JINR, Dubna
A.Butenko
on behalf of the Accelerator Division team
Nuclotron status
Last run’s results
40Ar
78Kr
124Xe

## Slide 2
Nuclotron – superconducting synchrotron
Circumference 251,2m, Br<45 Tm
The project approved
in 1986 year
Commissioning &
fist beam
March 1993 year
The last RUN #55
Feb. - April 2018
Slow extraction
2000 year
Accelerated:
Ions from p to Xe (C, Mg, Fe, Ar, Kr)
Polarized p & d beams
Proton energy max 12 GeV
Light ions max 6 GeV/u
Heavy ions max 4.5 GeV/u

## Slide 3
Nuclotron-N
Intensity >10^7 ppc
(with KRION-2)
Energy 6 Gev/n
(for Z/A = 1/2)
Field ~ 2T,
B’< 0,8 T/s
Heavy ions
Stable, safe,
long operation
Development of the
KRION ESIS
Vacuum improvement
Injector modernization
+
Energy evacuation system
Quench protection system
Slow extraction at HE
Control, diagnostics, RF
Power supply system modernization
Cryogenics modernization
Radiation safety
Nuclotron-N
preparation of the ring for NICA project
Nuclotron – superconducting synchrotron
Slide from 2010 year

## Slide 4
Run #48 11-12.2013 (1050 h, 73% beam time)
Carbon ions were accelerated and extracted at energy 5.8 GeV/u, 1*109
Run #49 02-03.2014 (650 h, 66% beam time)
good beam spill at low intensity (STRELA), double user mode.
Run #50 05-06.2014 (650 h, 31% beam time) Krion
Experiments “40Ar” 1.2 GeV/u, “7Li” 3 Gev/u,
Run #51 01-03.2015 (1150 h, 70% beam time)
Test of BM@N systems with deuteron and C+6 beams
Run #52 30-06.2016 (666 h, 57% beam time)
Technical run with SPI and laser source.
Run #53 25-12.2016 (1450 h, 78% beam time) * Longest Nuclotron run
Polarized deuterons 4,6 GeV/u, DSS, Alpom, Hyper NIS
Run #54 24-03.2017 (1150 h, 64% beam time)
Polarized protons & deuterons 4,6 GeV/u, DSS, Alpom, BM@N
Run #55 05-04.2018 (1018 h, 60% beam time) Krion6T
Physical run at BM@N, SRC with 12C, 40Ar, 78Kr beams
Statistics of operation

## Slide 5
Cooling, 7.3%
Tuning, 8.7%
Repairs, 4%
Unexpected losses, 2.5%
Experiments
77.6%
Run #53, 1450 h
Polarized, unpolarized deuterons,
maximum energy of extracted beam
4.6 GeV/u
Run #54, 1150 h
Nuclotron: statistics
Polarized program at Nuclotron,
SPI beams
Longest run

## Slide 6
Polarized beams, SPI
SPI “source of polarized ions” was transported, installed on the HV terminal and commissioned with the new fore-injector & LU-20 during 25 days preparation for the 52 technical RUN at the Nuclotron

## Slide 7
Nuclotron: adiabatic capture
8e8
6e8
RF Voltage
vs time
Capture
efficiency
70 – 80 %
RUN 54 & 55
routine regime
Routine operation during runs #54 & #55
with injection at magnetic field plateau
+ adiabatic capture

## Slide 8
Routine operation of SPI and new fore-injector
Polarized deuteron acceleration: Intensity 25*108 per cycle
Deuteron Spin Structure experiment, internal target of the Nuclotron
8E8
Nuclotron: polarized deuterons

## Slide 9
Run #54. Proton acceleration
LU-20 was designed for the proton acceleration to 20 MeV
Injection energy of about 625 keV was provided by HV transformer
The deuterons and light ions were accelerated at second harmonics
Injection energy – 156 keV, output energy 5 MeV/u
New RFQ fore-injector provides output energy of 156 keV for all ions:
the protons can be accelerated in LU-20 at the second harmonics only
the output proton energy after LU-20 is 5 MeV
the Nuclotron magnetic field at injection has to be about 150 G
(instead of 294 G for other ions with Z/A=1/2)
Because of high importance of the proton program 6 shifts were spent
for the tuning of the accelerator complex in the new regime:
Tuning of LU-20 and injection channel
Orbit correction at injection
Working point adjustment
Tuning of acceleration
Measurements of polarization of p+ at Int. Target and extracted beam.

## Slide 10
Beam intensity, particles
Time, ms
Magnetic field, G
1.8 E8
For effective acceleration of polarized proton beam at the Nuclotron
very accurate tuning of spin direction at the SPI and LU-20 is needed
Polarized protons

## Slide 11
New Light Ion Linac “LILac”
Injector for the Nuclotron ring (in 4 y.)
Lu-20 Hall
Meddle energy section
SC section
First Linac 7 MeV/u section
HILac
MAC’2017: «The improvement of the acceleration efficiency of polarized proton beam is urgently required.»
New linac – 3 sections:
1st sect. from BEVATECH
7MeV/u for ions Z/A>1/3
2nd sect. warm resonators
for p+ up to 13 MeV
3rd for SC res. testing & applied research up to 20MeV
Contract with BEVATECH signed in Dec. 2017 for 3.5 years.
July 2018: TDR
Summer 2021: commissioning at test bench with beam.

## Slide 12: Acceleration of 124Xe42+ beam RUN #41 (February 2010)
Xenon ions accelerated
up to the 1 GeV/u
and slow extracted with intensity ~103 ions/pulse
Photo of the 124Xe42+ extracted
beam (Е = 0,57 GeV/u)
Registration of 124Xe42+ beam during acceleration cycle by ionization profile monitor
Nuclotron: heavy ions acceleration

## Slide 13
Run #55 22.02 - 05.04.2018
Cooling, 9.9%
Tuning, 25.6%
Repairs, 4.2%
Unexpected losses, 1.1%
Experiments
59.2%
Nuclotron: RUN 55 statistics
1018 h
Heavy ion beams acceleration

## Slide 14
source
LEBT + Buncher
4 wane RFQ
(3 sections)
MEBT LU-20
QT + Bu +QT
The MEBT includes two triplets of quadrupole lenses and Buncher
At the first stage the Buncher was absent
(Theory transmission ~ 20%, achieved up to 10%)
The buncher is prepared to the run #55:
Expected gain in transmission is about 3 times
Nuclotron: injection chain

## Slide 15
KRION 6T – heavy ion source was used during Nuclotron RUN #55
for SRC & BM@N experiments
Usage of the buncher permitted to increase the Ar beam intensity
at the entrance of the Nuclotron by about 5 times

## Slide 16
Preparation for heavy ion run
Tuning of the injector complex
Results from 20.12.2017
Beam intensity at the entrance of the Nuclotron
 | Ar 14+ | Ar 15+ | Ar 16+ | C 4+ | C 5+ | C 6+ | Kr 26+
N e | 1.5 E8 | 4.4 E8 | 3.3 E8 | 2.1 E8 | 4.0 E8 | 1.1 E9 | 2.5 E8
N particle | 1.0 E7 | 3.0 E7 | 2.0 E7 | 5.3 E7 | 8.0 E7 | 1.7 E8 | 1.0 E7

## Slide 17
12C+6 beam acceleration (3,5 GeV/u) RUN #55
12C+6 Intensity 5*108
Nuclotron: ion acceleration
Run #54, carbon beam was accelerated up to 5.2 GeV/u, VESS = 145 kV

## Slide 18
Nuclotron: slow extraction
12C+6 beam extraction (3,5 Gev/u) RUN #55
Run #54, carbon beam, 5.2 GeV/u, VESS = 145 kV
12C+6 5*108 Tspill = 4s, kdc= 99,5%

## Slide 19
78Kr+26 beam acceleration (3,2 GeV/u) RUN #55
Nuclotron: ion acceleration

## Slide 20
Nuclotron: slow extraction beam spill
78Kr+26 beam extruction (2,8 Gev/u) RUN #55
78Kr 2*105 Tspill = 10s, kdc= 99,3%
RF kicker is Off | kicker is On

## Slide 21
Status of the Nuclotron 2018
Parameter | Project | Status (June 2018)
Max. magn. field, T | 2 | 2 (1.7 T routine)
B-field ramp, T/s | 1 | 0.8 (0.7 routine)
Accelerated particles | p–U, d | p, d, p – Xe
Max. energy, GeV/u | 12 (p), 5.8 (d) 4.5( 197Au79+) | 5.6 (d, 12C), 3.6 (40Ar16+)
Intensity, ions/cycle | 1E11(p,d), 2E9 (A > 100) | d 4*1010 (2*1010 routine), 7Li3+ 3*109 12C6+ 2*109 40Ar16+ 1*106 78Kr26+ 2*105 124Xe42+ 1*104

## Slide 22
Conclusion
During last beam runs of the superconducting ring Nuclorton was demonstrated:
High quality of the slowly extracted beam -
emittances, profiles, excellent spill structure;
Stable operation during long period;
Low beam losses for all stages of acceleration;
Real possibility for efficient acceleration of different ions:
    polarized protons and deuterons;
    light ions (d+, Li, C et. set.);
    heavy ions (Ar, Kr, earlier Xe…).
For operation of the Nuclotron as the main synchrotron of the NICA complex  new current lead-ins (high temp. SC),
 beam injection from the Booster
 fast extraction
systems are needed.

## Slide 23
Thank you for attention

## Slide 24: Cryogenic problems during the 55th Run
The reason for the forced stoppage of the 55th Run of the Nuclotron in November 2017 was the depletion of the resource of helium purification unit from the oil and water impurities.
The manufacturer of the refrigerator did not provide oil vapor monitoring in the helium stream after the purification unit, so it was impossible to determine when the unit's resource was spent.
Oil fumes after passing the purification device enter into the heat exchanger and freeze on its walls. After a power failure, the helium compressor stopped and the top part of the heat exchanger was warmed up. The oil on the walls of the upper part of the heat exchanger melted, flow down, accumulated, froze and blocked the channels of the lower cold part of the heat exchanger. Continuation of the Nuclotron operation without repairing its cryogenic system became impossible. The 55th Run of the Nuclotron was stopped on November 03th, 2017.