## Slide 1
2nd Collaboration meeting of the MPD and BM@N experiments at the NICA Facility,
October 29-30, 2018
F.Guber
INR, Moscow
on behalf of the FHCal group
New FHCAL for BM@N heavy ion experiments

## Slide 2
ZDC at BM@N
Main tasks of ZDC at BM@N:
Measurement of centrality and reaction plane
orientation in nucleus-nucleus collisions.
It is planned to replace existing ZDC by new forward hadron calorimeter FHCAL which should provide also selection of most central events on trigger level in nucleus-nucleus interactions .
ZDC already had been used at BM@N experiments with 6C, 18Ar and 36Kr beams.
C (T=3.5 GeV/n),

## Slide 3
Structure of ZDC and motivation of use new FHCAL
High radiation doses are expected in ZDC central modules in future experiments with heavy ion beams which will lead to degradation of ZDC performance.
Significant hadron shower leakage is expected in ZDC due to the use of small modules in the ZDC center and use WLS plates for the light collection in modules.
Central part – 36 nodules (7.5x7.5cm2).
Outer part 68 modules (15x15cm2).
64 layers (5mm (scint.) + 10mm (Pb)

## Slide 4
New FHCAL for heavy ions beam runs at BM@N
PSD CBM module - 60 Pb/scint layers (4mm (scint.) + 16mm (Pb), 4:1 sampling ratio.
Light readout - by 10 MPPCs from 10 longitudinal sections.
FHCAL MPD module - 42 layers of Pb/scint, the same sampling ratio.
Light readout - by 7 MPPCs from 7 longitudinal sections.
1650
Longitudinal segmentation (about ~0.6λint of each section) provides:
information about longitudinal shower profile;
possibility to use cosmic muons for calibration without any additional trigger detectors.
The use of the CBM and MPD modules in FHCAL BM@N will give the possibility to study Its response in real experiment before the CBM and the MPD experiments starts their operation.
FHCAL – new forward hadron calorimeter calorimeter with transverse and longitudinal segmentation;
- would assembled from existing 20 PSD CBM modules, 200 x 200 x 1650 mm and
35 FHCAL MPD modules (16_BM@N+19_MPD), 150 x 150 x 1000 mm.
- Total weight- 17 tons.

## Slide 5
Results of Fluka simulations of the ZDC and the FHCAL irradiation
radiation doses from ionizing and non-ionizing particles in the FHCal expected for 2 month of continues operation with gold beam at beam energy 4 AGeV and beam rate 2x106 ions per second.
- activation of calorimeter after 1 month of beam shutdown.
- Neutron fluence on the MPPCs position
Ionizing doses (Gy)
Activation (μSv/h)
Non ionizing fluence (neq /cm2)
ZDC
FHCAL
A.Senger. GSI

## Slide 6
Reaction Au+Au@4.5 AGeV was generated with LAQGSM code,
bmnroot framework with FTFP_BERT physics list.
FHCAL - 9 m from the target.
Beam smearing on the target was applied (σx = σy = 0.3cm).
FHCAL BM@N simulation
14 % of particles energy
goes through the hole
2 % of particles energy
goes through the hole
min. bias events
10% most central events
Distribution of all particles on the entrance surface of the FHCAL

## Slide 7
Protons Neutrons
Fragments (A<=4) Fragments (A>4)
Particle distributions for minimum bias events on the FHCAL entrance surface
(Calorimeter is shifted at 217 mm in X direction to have beam axis in the center of the beam hole)
Percentage of particles in the hole:
Protons 3%
Neutrons 4%
Fragments
A<=4 14%
A>4 92%

## Slide 8
How to measure centrality with FHCAL?
Calorimeter with beam hole.
Pb+Pb@29 AGeV Au+Au@4.5 AGeV
QGSM (SHIELD code), FTFP_BERT LAQGSM, FTFP_BERT
4775 ev. 99199 ev.
Non monotonic Edep vs centrality due to beam hole in FHCAL
Centrality selection on trigger level can not be done by use only Edep
Degradation of centrality resolution in the centrality range 30-60%
Black curve –centrality resolution simulated
for particles which hits entrance surface of
the FHCAL without the beam hole.

## Slide 9
New FHCAL observable
to resolve ambiguities in the centrality measurements
- Cut on the asymmetry gives the possibility to select about 40% of the most central events on the trigger level.
- Independent determination of the centrality can be done by use the AE in FHCAL.
- AE can not improve the centrality resolution.
Transverse FHCAL segmentation Energy deposition asymmetry in FHCAL:
Edep (blue) – Edep (yeloow)
AE =
Edep (blue) + Edep (yeloow)

## Slide 10
NA61 used Quartz Detector (QD) with a quartz (GE214P) plate 160x40x2.5 mm3 as the radiator equipped with two photomultipliers (X2020Q) attached to both sides of the quartz plate.
Is it possible to improve FHCAL centrality resolution
by use additional detector in the beam hole?
Use quartz detector to measure charge of fragments?
Estimation of ionizing dose for
quartz plate with thickness 4 mm.
The dose doesn’t exceed 1 Grad
In vey central part of QD
Charge distribution
of QD in NA61
fragmented beam
The position of the Pb
peak vs Dmax absorbed by
the ZDC detector
(ALICE ZDC TDR).
Degradation of signal due to radiation
dose can be recovered increasing the gain
of the PMT (MPPCs).

## Slide 11
Estimation of FH occupancy
(hits of p, pi+, pi-, fragments)
Occupancies for plates 10x75 mm are very small.
The size of quartz plates can be increased to reduce
numbers of detectors.
Optimization is needed.
150 mm
150 mm

## Slide 12
FHCAL with quartz hodoscope
in front of beam hole.
Comparison of centrality determination with FHCAL
and FHCAL plus quartz hodoscope in the beam hole
With quartz hodoscope in the beam hole
W/o quartz hodoscope in the beam hole
Monotonic dependence of the asymmetry vs centrality.
Improvement of centrality resolution for central and semi-peripheral events.
Additional tuning is needed for very peripheral events

## Slide 13
Study of PSD СВМ supermodule performance on Т9/Т10 beams at CERN
PSD СВМ supermodule on T10 test beam at CERN
Energy resolution and linearity response

## Slide 14
The readout electronics: FPGA based 64 channel ADC64 board, 62.5MS/s (AFI Electronics, JINR, Dubna).
7 channels for FHCal MPD nodules and 10 channels for PSD CBM modules:
two-stage amplifiers; HV channels;
LED calibration source.
Photodiodes, FEE and readout electronics.
A first samples of FEE with MPPC photodetectors were developed and tested.
Hamamatsu MPPC: size – 3x3 mm2;
pixel -10x10 µm2;
PDE~12%.
Photodetectors:
Full readout chain was tested with cosmic muons and at beam!
MPPC
Integrator
ADC
τ ~ 20ns
Amp
FEE
Dt ~ 50 ns
Dt ~ 200 ns
Front-End-Electronics:

## Slide 15
Estimation of energy resolution
for carbon 3.17 GeV/n - 10%
Comparison of measured energy resolution
by ZDC BM@N and by new forward hadron calorimeter
ZDC: energy resolution measured with carbon beam at 3.17 GeV/n
Energy resolution 24.5%
(preliminary)
=
FHCAL: results of PSD supermodule test at CERN proton beams
Energy resolution

## Slide 16
Comparison of PSD CBM single module energy resolution measured
on Ar beam (3.3 Gev/n) at BM@N and on proton beam at CERN
BM@N, Ar,
March 2018
CERN, protons,
May 2018
=
Energy resolution
– 7%
Energy resolution – 12%
(Preliminary)
Energy resolution

## Slide 17
Nearest plans of FHCAL (I)
Transportation of PSD CBM modules (20 pcs),
FHCAL BM@N modules (16 pcs) and FHCal MPD
modules (19 pcs) from INR at JINR.
- April 2019
Delivery of the FHCAL support structure at BM@N.
- Beginning of 2019
20 PSD CBM modules
35 FHCAL MPD modules (16_BM@N+19_MPD)

## Slide 18
Nearest plans of FHCAL (II)
FHCAL assembly
- April 2019
FEE and readout electronics
should be available at the middle of 2019. Not ordered up to now.
Integration in BM@N DAQ, cosmic tests and calibration
- up to the end of 2019
Simulations :
optimization of final FHCAL geometry to get
the best centrality and reaction plane angle resolutions,
- Development of methods for FHCAL cosmic muons calibrations
Centrality classification of existing ZDC data
Application for RFBR grant.
Participants:
INR, NEPHI, JINR

## Slide 19
Thank you for attention!

## Slide 20
160 cm
100 cm
Alternative geometry of FHCAL
105 cm
155 cm
P = 16.8 t.
P = 16.2 t.

## Slide 21
These observables taken into account transverse and longitudinal FHCAL segmentation
Another new observables calculated from
transverse and longitudinal segmentation of FHCAL modules.
ET and EL –sums of deposited energies in all i-sections in given event multiplied by sin(θi ) or cos(θi ).
θi is the angle between beam axis and line connected the center of corresponding section with the target.

## Slide 22
Damages in different materials as function of the applied
ionizing and non-ionizing dose.

## Slide 23
Kinetic energy spectra
of particles on the entrance surface of the FHCAL
Protons
Neutrons
Pions
Fragments (A<=4)
Fragments (A>4)