## Slide 1
V. Golovatyuk
Status of the MPD project

## Slide 2
MPD 1st stage
Powerful PID (TPC, TOF, ECAL)
- p/K up to 1.5 GeV/c,
- K/p up to 3 GeV/c,
- g, e : 0.1<p<3 GeV/c
3-D tracking (TPC, ECT)
Low material budget
High event rate (up to ~ 6 kHz)

## Slide 3
Charged
b<11 fm
dN/dh
Forward Tracker
Au+Au collisions at NICA (model predictions)
h
TPC
FFD
FHCal
TOF

## Slide 4
The Status of the main subsystems of the MPD

## Slide 5
Magnet fabrication: ASG (Genova) & Vitkovice HM
yoke control assembly at HM Vitkovice
trim coil
winding machune
cryostat
End of 2018 – SC coils are ready
March 2019 – Solenoid is ready
May 2019 – Transportation to Dubna
Oct 2019 – Assembling of Magnet Yoke and Solenoid at JINR

## Slide 6
MPD Time Projection Chamber
Item | Dimension
Length of the TPC | 340cm
Outer radius of vessel | 140cm
Inner radius of vessel | 27 cm
Outer radius of the drift volume | 133cm
Inner radius of the drift volume | 34cm
Length of the drift volume | 170cm (of each half)
HV electrode | Membrane at the center of the TPC
Electric field strength | ~140V/cm;
Drift gas | 90% Ar+10% Methane, Atmospheric pres. + 2 mbar
Gas amplification factor | ~ 104
Drift velocity | 5.45 cm/µs;
Drift time | < 30µs;
Temperature stability | < 0.5°C
Number of readout chambers | 24 (12 per each end-plate)
Segmentation in φ | 30°
Pad size | 5x12mm2 and 5x18mm2
Number of pads | 95232
Pad raw numbers | 53
Maximal event rate | < 7 kHz ( Lum. 1027 )
Electronics shaping time | ~180 ns (FWHM)
Signal-to-noise ratio | 30:1
Signal dynamical range | 10 bits
Sampling rate | 10 MHz
Sampling depth | 310 time buckets

## Slide 7
7
TPC cylinders: C1-C4
Length: 3.4 m
Diameter: 0.54 m
C1
C3
C4
C2
Length: 3.4 m
Diameter: 0.676 m
Length: 3.4 m
Diameter: 2.66 m
Length: 3.4 m
Diameter: 2.814 m

## Slide 8
8
TPC summary
TPC assembly preparation:
clean room – ready
C1-C4 cylinders – ready
flanges (2pc) - ready
field cage rods (30pc+30 pc) – Nov-Dec 2018
serial HV electrode – Oct -> Nov 2018
TPC ass tooling: adjust. and align. – Nov-Dec 2018
mylar strips manufacture – Dec 2018
start TPC assembly - Dec 2018
FE electronics:
512 ch system – tests ongoing
test with ROC chamber. – Dec 2018
SAMPA chips (4500 pc) – payment in progress
ROC chambers:
frames (26 pc) - ready
serial pad planes (30 pc) – ordering started
HV for ROC gate electrode – design started
test chamber with 512 ch r/o system – Dec 2018

## Slide 9
Forward tracker based on thin gap MWPC with pad (strip) readout.
Technical University of Santa Maria in Valparaiso, Chile (S.Kuleshov)
and Petersburg Nuclear Physics Institute, Gatchina (O.Fedin)

## Slide 10
MPD TOF
Dimensions of sensitive area
600 x300 mm2
 | Number of detectors | Number of readout strips | Sensitive area, m2 | Number of FEE cards | Number of FEE channels
MRPC | 1 | 24 | 0.192 | 2 | 48
Module | 10 | 240 | 1.848 | 20 | 480
Barrel | 280 | 6720 | 51.8 | 560 | 13440 (1680 chips)
Main parameters of the TOF system.

## Slide 11
Fast Trigger L0 for MPD
The vertex resolution for Au-Au collisions at √s=5GeV/n for three distances from interaction point
FFD efficiency for peripheral collisions
FFD provides information on
- fast triggering of Au-Au collision
- start signal for TOF
- bunch crossing region position
15 mm quartz radiator
10 mm Lead converter
The FFD sub-detector consists of
20 modules based on
Planacon MCP-PMTs
80 independent channels
The delay of charged particle arrival in FFD modules in comparison with arrival time
of photons for Au + Au collisions at sNN = 5 (red) and 11 (blue) GeV and FFD position of 140 cm.

## Slide 12
Beam-Beam Monitor (MexNICA Collaboration )
Fast timing scintillation hodoscope with APD readout. Required resolution –better 30 ps)
The main purpose of the Be-Be detector is to provide a fast signal T0 with resolution better than 30 ps for TOF system in low energy range of beams collision (⎷s= 4-11 GeV/n) and low mass of colliding particles (down to Carbon-Carbon and proton-proton collisions) where existing Forward Detector is not efficient)

## Slide 14: FHCal Forward Hadron Calorimeter
Two-arms at ~3.2 m from the interaction point.
Each arm consists of 45 individual modules.
Module size 150x150x1100cm3 (55 layers)
Pb(16mm)+Scint.(4mm) sandwich
7 longitudinal sections
6 WLS-fiber/MAPD per section
7 MAPDs/module

## Slide 15
Reaction plane and impact parameter resolution
The accuracy of reaction plane reconstruction is In range 26-31 degrees

## Slide 16
Electromagnetic Calorimeter (ECAL) for Multi Purpose Detector (MPD)
Barrel ECAL ~ 43000 ECAL modules
Prototype of one module
THU – Tsinghua University., Yi Wang
SDU –Shandong University
HU- Huzhou University Fuqing Wang

## Slide 17
two scenarios of ECal integration
scenario A
scenario B
~ 90 tons
184 towers
5 tons
5520 mm
Insertion of the sectors into
the Carbon fiber shell

## Slide 18
MCORD - MPD Cosmic Ray Detector for NICA
Polish Consortium NICA-PL
The Cosmic Ray Detector is needed for:
- discrimination signals induced by cosmic showers (mainly muons).
- off- beam calibration of the MPD response to muons,
- provide the opportunity for the early tests of the integration of
the Subsystems, Triggering, Experiment Control Systems and others.
Plastic scintillators with light readout as most suitable candidates for a detector module. In the initial stage one need to choose the optimum shape of scintillators, the configuration of photo-detectors and readout electronics.
TH barrel part consists of little bit more than 500 scintillator modules and about 1000 channels of readout electronics (see presentation of Marcin Bielewicz on October 30th)

## Slide 19
Stage I: 62 mm in diameter

## Slide 20
MPD with platforms for electronics and cryogenics
WUT, Warsaw (Coordinator -Marek Peryt) – Rack organization on the MPD platforms
Figure 17; PLATFORM, LEVEL 1-4

## Slide 21
Detector positions in the pit
Detector in assembling dock
Detector on the beam
Beam line

## Slide 22
Beam pipe
Final focus lenses
Detectors for Luminosity tuning
Positions of MPD in the experimental zone
Position 1 - Working position, Detector on the beam
Position 2 - Endcaps roll away zone
Position 3 – Detector Assembling area

## Slide 23
Summary
Substantial progress in MPD project realization in 2018
(Magnet, Solenoid, TPC, TOF, FFD, FHCal)
The mass production of the detectors elements is under way.
MPD Collaboration  toward the formal foundation
Thank you for your attention!

## Slide 24
The start signal resolution for Au + Au collisions at sNN = 5 and 11GeV for the real FFD detector as a function of the impact parameter.
The trigger efficiency as a function of the impact parameter of Au + Au collisions for two energies sNN = 5 and 11 GeV and two thresholds of 500 and 1000 Cherenkov photons.
The vertex uncertainty as a function of the impact parameter of Au + Au collisions, the blue points correspond to sNN = 5 GeV, the red points – to sNN = 11 GeV
FFD performance
The time-of-flight resolution for Au + Au collisions at real FFD and TOF detectors as a function of the impact parameter.
sNN = 5 and 11 GeV for the real FFD and TOF detectors as a function of the impact parameter

## Slide 25: ITS for MPD Experimen
MPD ITS based on ALICE type staves
.
Consortium includes JINR, NICA (BM@N & MPD) , FAIR, Russian, Poland and Ukrine Insitutes + CCNU Central China Normal Univ – Wu Han and Feng Liu
IMP- Institute of Modern Physics - Lan Zhou and Nu Xu
USTC – Hefei - Zebo Tang
Λ0 → p + π –
Ξ¯ → Λ + π –
└→ p + π –
Ω¯ → Λ + K¯
└→ p + π –
D0 → K¯ + π +