## Slide 1: Status of Forward Hadron Calorimeter (FHCal) at MPD
A.Ivashkin
Institute for Nuclear Researches RAS, Moscow
on behalf of the FHCal group (INR, MEPhI, JINR…)
2nd MPD/BM@N collaboration meeting, October 29-30, 2018.
FHCal in MPD/NICA setup;
Tasks of FHCal ;
Approaches in measurement of centrality;
Status of FHCal production;
Tests of FHCal modules;
Open issues.

## Slide 2
Tasks: detection of spectators to measure:
The centrality of the collision;
The reaction plane orientation.
Physics with spectators.
FHCAL
Two arms of hadron calorimeters at opposite sides in forward regions.
At the distance 3.2 meters from the interaction point.
Available acceptance corresponds to pseudorapidity 2.0< <5.0
FHCAL consists of 2x44 modules of ~1.1x1.1 m2 each part.
The forward hadron calorimeter in MPD setup

## Slide 3
FHCal will detect the spectators to measure the geometry of ion collisions.
FHCAL
FHCal will detect the energy of spectators ;
FHCal will detect the space distribution of the spectators .
FHCal will detect the energy of pions in forward region ;
Event plane
Spectator spot
By using the spectators energy and space distribution one can determine the centrality and the event plane of collisions.

## Slide 4
Structure of FHCal – two left/right arms.
Each arm:
44 modules;
Beam hole;
Weight – 9 tons.
Modular Lead/Scintillator sandwich compensating calorimeter. Sampling ratio Pb:Scint=4:1.
Light from scintillator tiles is captured by WLS-fibers and transported to SiPM.
Each module:
Transverse size - 15x15cm2 ;
Total length - 106 cm.
Interaction length ~4 λint;
Longitudinal segmentation – 7 sections;
1 section ~ 0.56λint;
7 photodetectors/module;
Photodetectors – silicon photomultipliers (SiPM).

## Slide 5: Event plane resolution with FHCal.
The detection of all types of the spectators (protons, neutrons) for both colliding nuclei would ensure nice angular resolution of the event plane!
spectators
Event plane in first FHCal arm.
Event plane in full FHCal.

## Slide 6
Energy deposition in FHCal isn’t monotonic and can’t resolve the central and peripheral events.
Centrality. Problem with energy depositions in FHCAL.
Ambiguity in the centrality measurements might be resolved by using the TPC multiplicity.
But other approaches are preffered.
Resolution of impact parameter for different FHCal energy (centrality) bins.
Effect of beam hole and escape of heavy fragments.
Other approaches are requested!

## Slide 7: Spectators spots at FHCal surface have different sizes for different centralities.
Occupancy of particles at front of FHCal
R, cm
R, cm
Cone for peripheral
events
Cone for central events
The energy deposition in inner and outer parts of calorimeter must be different for different centralities.
b>6 fm
b<6 fm
Ein
Eout
Let’s introduce energy asymmetry:

## Slide 8
Centrality measurements with two FHCal observables (Edep and AE).
Central events
Peripheral events
0.1
Central events
Peripheral events
With only FHCal the centrality resolution is below 10% excepting the most central, where the fluctuations of spectator energies dominate.

## Slide 9: Construction of other observables in FHCal for the centrality measurement.
Cone of spectators
Transverse energy:
and
Longitudinal energy:
A bagel structure in ET, EL correlations.

## Slide 10
Centrality measurements with ET and EL.
Central events
Peripheral events
With only FHCal the centrality resolution is below 10% excepting the most central, where the fluctuations of spectator energies dominate.
Central events
Peripheral events
Each color bin is 10% of centrality.
Each color bin is 10% of centrality.

## Slide 11: FHCal: Physics case.
These observables would depend on centrality;
These observables would reflect the recoil momenta of the spectators;
These observables would be different in different physics models;
Can spectators probe the fireball ?
Fine transverse/longitudinal segmentation of FHCal allows the construction of many experimental observables for spectators:
Asymmetry of energy deposition AE ;
Transverse energy: ;
Longitudinal energy:
Spread (compactness) of spectator spots;
And others….
Central events
Peripheral events

## Slide 12
Status of FHCal modules production.
At present, about 2/3 of FHCal modules are ready for the tests.
All FHCal modules will be ready next year.
Tests of modules with cosmic muons are done in parallel with the development of Front-End-Electronics and readout.

## Slide 13
The readout electronics: FPGA based 64 channel ADC64 board, 62.5MS/s (AFI Electronics, JINR, Dubna).
7 channels:
two-stage amplifiers; HV channels;
LED calibration source.
Photodiodes, FEE and readout electronics.
Front-End-Electronics:
A first samples of FEE with MPPC photodetectors were developed and produced.
MPPC
Integrator
ADC
τ ~ 20ns
Amp
FEE
Dt ~ 50 ns
Hamamatsu MPPC: size – 3x3 mm2;
pixel -10x10 µm2;
PDE~12%.
Photodetectors:
Full readout chain was tested with cosmic muons and at beam!
Dt ~ 200 ns

## Slide 14
Test of calorimeter modules with cosmic muons.
Geometries of muon tracks in FHCal module.
Tracks passed through 2, 3 or all of 7 sections were studied.
Light yield [ph.e.]
Section #
Light yield depends on WLS-fiber length.
After assembling each module was tested.
Average light yield for 50 modules.

## Slide 15
Test of calorimeter supermodule at CERN T9/T10 line.
Each module has 10 longitudinal sections with 10 SiPMs at the end (CBM option).
Full size 60x60x160 cm3.
Readout electronics – for FHCal.
Sect. 1
Sect. 2
Muons deposit
~5 MeV
in each section
Calibration of longitudinal sections with beam muons, 6 GeV/c
Identification of muons – equal energy deposition in first and last half of modules.
E2 [MeV]
E2 [MeV]
E1 [MeV]
E1 [MeV]
A [ch]
A [ch]
Proton momentum range: 2-10 GeV/c

## Slide 16
Dependence of energy resolution on supermodule length.
Length of 4λI or 7 longitudinal sections is optimum for momentum range 2-6 GeV/c
p= 6 GeV/c
Longitudinal profile of hadron shower.
Dependence of resolution on module length.
The stochastic term of ~56% is in good agreement with MC results.

## Slide 17
Open issues.
Magnet pole with FHCal.
Mechanical support. The concept only.
Mass-production of FEE and readout.
Simulations: detector performance and physics performance.
Calibration with cosmic muons in real setup.
Software for FHCal data analysis.
Beam quality study with FHCal.
Power supplies. Mounting of readout elements. Full integration to MPD.
Operation manpower.

## Slide 18
Thank you!

## Slide 19
Permanent quality control of scintillator tiles,
WLS-fibers and gluing is performing with 90Sr β-source.
Stages of FHCal production: scintillators.
Tests of different grooves and reflectors
Scintillator tiles with WLS-fibers.
Scintillator tiles in TYVEC reflector.
FHCal scintillator tiles and modules are assembled in workshop of INR, Moscow.

## Slide 20
Occupancy.

## Slide 21
Energy spectra.

## Slide 22: Other FHCal observable for the centrality measurement.
Let’s introduce energy asymmetry:
AE is experimental observable and has clear dependence on centrality. Let’s combine it with energy deposition in FHCal.
Dependence of AE on impact parameter.
Ein
Eout