## Slide 1
Nanobeacon: A time calibration device for the KM3NeT
David Calvo, Diego Real
1
VLVNT 2018, Dubna

## Slide 2
KM3NeT Time calibration: Nanobeacon
VLVNT-18 10-2018
2
The angular resolution is critical in a N.T. to resolve cosmic neutrino sources from the atmospheric background.
The angular resolution relies on a good positioning and time calibration.
Working within the specifications the attainable angular resolution of KM3NeT is better than 0.1º
Nanobeacon
  Electronic circuit controlled by I2C
  Integrated into the Digital Optical Module
  LED emits an ultra-short light pulses
Relative time resolution (among DOMs) depends on:
  Transit time spread (TTS), typically s~1-1.5 ns.
  Optical properties of the sea water: light scattering + chromatic dispersion (s~1-1.5 ns) for light coming from a distance of 50 m.
  Electronics (s<0.5 ns).
Therefore, an overall unavoidable uncertainty of ~2 ns will always be present.

## Slide 3
KM3NeT Time calibration: Nanobeacon
VLVNT-18 10-2018
3
The main use of this system is to measure PMT time offsets through intra-line calibration with LED beacons along the same detector line
Experience has shown that a system of external light sources with a well-know emission time is very useful to ensure the timing calibration of the detector and measure water optical parameters
Synchronizing timing offsets between beacon elements is cumbersome and time consuming. An
d time consuming
Providing trigger signals introduces unwanted electrical noise to system

## Slide 4
KM3NeT Time calibration: Nanobeacon
VLVNT-18 10-2018
4
Calibration:
  One Nanobeacon per DOM
  Not expensive and high redundancy
  Not triggered by the clock to avoid electronic noise
  Frequency of several kHz depending on the DAQ system
  Avoid cumbersome synchronization process, only one LED per Nanobeacon

## Slide 5
KM3NeT Nanobeacon: Electronics
VLVNT-18 10-2018
5
DC voltage charges a capacitor
Two ultra-fast transistors discharge the capacitor over the LED
Select the intensity of flashing (Booster 2.5 V - 30 V)
Select the frequency of the internal trigger (up to 8 kHz)
CLB

## Slide 6
KM3NeT Nanobeacon: Configuration
VLVNT-18 10-2018
6

## Slide 7
Nanobeacon: Photoelectron setup
Led Optical Pulse reproduced with the photoelectron method:
Dark Box
Oscilloscope with histrogram capability
2 PMTS: H6780-03 and H6156-50
Optical Filter
VLVNT-18 10-2018
7
H6156-50
H6780-03
FILTERS
PULSER + LED
DARK BOX
OSCILOSCOPE
LECROY
Δt
Nanobeacon property | Performance
Optical rise-time | ~ 2.7 ns
Optical FWHM | ~ 4.5 ns
Wavelength | 470 nm (blue)
Angular distribution | 15º
Intensity | ~150 pJ
Power consumption | < 0.12 W

## Slide 8
Nanobeacon optical pulse
Led Optical Pulse reproduced with the photoelectron method
Gaussian and Weibull fits – Weibull provides a better fit:
VLVNT-18 10-2018
8

## Slide 9
Rise time and FWHM of nanobeacon pulse
9
VLVNT-18 10-2018
 | RISE TIME (ns) |  | FWHM (ns) | 
 | Gaussian | Weibull | Gaussian | Weibull
Mean | 3.14 | 2.69 | 4.39 | 4.51
Std. Dev | 0.27 | 0.21 | 0.38 | 0.41
Results for 24 LEDs (Model: HLMP-CB1A-XY0DD)
24 V and 1 kHz:
Weibull data should be considered as more accurate:
Rise Time around 2.69 ns
FWHM around 4.51 ns

## Slide 10
Effects of frequency and voltage
10
VLVNT-18 10-2018

## Slide 11
Wavelength distribution (LED:HLMP CBLA-XY)
11
VLVNT-18 10-2018

## Slide 12
Effects of voltage on wavelength
12
VLVNT-18 10-2018
The wavelength decreases when the voltage is increased

## Slide 13
Effects of voltage on wavelength
13
VLVNT-18 10-2018

## Slide 14
Summary
14
VLVNT-18 10-2018
Nanobeacon: important calibration device
Characterization of the Pulse shape by photoelectron technique
Frequency has no impact on the pulse of light
Voltage affects:
  Wavelenght
  Rise time
  FWHM

## Slide 15
Nanobeacon: A time calibration device for the KM3NeT
David Calvo, Diego Real
15
VLVNT 2018, Dubna