## Slide 1
The Italian Site for KM3NeT ARCA
VLVNT 2018
Giorgio Riccobene
INFN –LNS

## Slide 2: Cabled infrastructures in Sicily
Two deep sea infrastructures built by INFN-LNS in Sicily
Capo Passero Site (KM3NeT-ARCA):
90 km South East offshore Capo Passero, 3500 m depth
Catania Test Site (deep Sea laboratory, first node of EMSO):
25 km East offshore the port of Catania, 2100 m depth
Catania Test Site (with INGV, first cabled node of EMSO):
Coastal Site, Close to ports and shipping lanes
East flank of the Etna Volcano, On the Sicilan-Maltese shelf break
Gate to the Messina Strait
Capo Passero Site:
Abyssal Site
Oligotrophic environment
Gate to the Sicilian Channel
10 fibers
20 fibers (Phase1)
48 fibers (Phase 2)
Now updated to 10 Gbit

## Slide 3: The Capo Passero Site for KM3NeT
Depth >3500 m, 90 km distance from the shore
Excellent water optical properties (La ≈ 70 m @ = 440 nm)
Optical background from bioluminescence extremely low
Deep sea water currents are low and stable (3 cm/s, 10 cm/s max)
Wide abyssal plain: large extension of the detector
More than 30 naval campaigns seeking deep sea sites in the Mediterranean Sea. Capo Passero is an optimal site.
The site selected for the km3 detector lies on a flat and wide plateau far from the shelf break (reduced risks)
CP Site
Shore Laboratory in Capo Passero harbour
Shore Laboratory:
Electronics Labs
Data Acquisition Room, Control Room
Guest House
Power Feeding Equipment (UPS protected)
10 Gbps direct Optical-fibre link GARR-X
Submarine cable and infrastructure:
96 km - 20 fibres ITU655-NZDSF
Single conductor with DC-sea return
Cable Termination Frame (5 hybrid outputs to JBs)
Medium Voltage Converter: 10kV to 375V
Second cable for ARCA Phase 2: tender assigned

## Slide 4: Construction of KM3NeT: Phase 1
Prototype
Prototype
CTF
MEOC
DU-ARCA 001
DU-ARCA 002
Junction Box
Junction Box
Junction Box
EMSO
Junction Box
Access to “Associated science”:
1 acoustic sensor per DOM
1 hydrophone at the base
1 Instrumentation Line
(2 CTD, 2CM, 2SV)
EMSO JB
CTF
JB
ARCA DU002
ARCA DU001
24 KM3NeT DUs (Phase 1)
115 DUs in 2020 (Phase 2)

## Slide 5: Capo Passero: deep Sea site monitoring
Study of deep seawater optical and oceanographic properties. More than 30 marine campaigns
Mooring lines: current meters, sediment traps, CTDs, biofouling and bioluminescence devices
Profiler (CTD +AC9), Niskins bottles + DNA analysis
In Collaboration with INOGS, CNR and Univ. of Messina
Astroparticle Physics 27 (2007) 1–9
Ligth transmission (absorption, attenuation) vs depth

## Slide 6: Optical background studies
Data collected since 2000 with different instruments and methods
Bioluminescent bacteria concentration and optical background rate (measured with 8’ PMTs, 0.5 s.p.e)
Stand alone device: 2 x 8’’ PMTs
Bioluminescent Bacteria concentration
NATURE, March 23, 2017
Bioluminescence rate
1 day, tidal frequency 20.5 h
KM3NeT prototype NEMO mini Tower: 32 Oms (10’’ PMTs)
rate of floor displacement
proxy for current speed
PMT rates [kHz]

## Slide 7: Optical background studies
150 Cherenkov photons/decay
stable 40K concentration
KM3NeT DUs (since 2015): multi PMT DOM
Data collected since 2000 with different instruments and methods
40K
40Ca
e
light
light
2 4 6 8 10 12 14 16 18 20 [kHz]
DU2 - PMT single rate distribution

## Slide 8: KM3NeT visitors
Marine Biology
M. Priede et al, 2018

## Slide 9: An Earthquake event observed with ARCA
Earthquake M 3.4 31/01 10:49 UTC
The DU starts to move (rotate, and tilt) and continue for about 10 hours.
The higher the DOM, the larger the swing.
Just connected to sea-floor displacement (string mechanics) or also a submarine wave?

## Slide 10: The Catania node
5 km
20 km
5 km
NEMO-SN1
2005-2008: Geophysics sensors
2012-2013:
Multidisciplinary node
2 CTDs, CM, seismic hydrophones, LF hydrophones, 4 HF hydrophones, magnetometers
2018 –
New deployment
LNS Test Site Laboratory
at the port of Catania
LNS-INFN Catania
1 Gbps fiber link
OnDE
2005-2006:
4 High Frequency Hydros
OnDE 2-SMO
2013-today
4 High Frequency Hydros
Test Site North
Test Site South
2018: CREEP (UCL) long term creeping of rocks at high pressure and a real time camera (CSIC)

## Slide 11: The Ocean noise Detection Experiment
Thetrahedral antenna (1m size):
4 Reson TC4042 hydrophones (special production for 2500 m depth).
Low cost professional audio electronics (96 kHz, 24 bit sampling, )
Hydrophones synchronised and phased.
On-line monitoring and recording on shore. Recording 5’ every hour
Data taking from Jan. 2005 to Nov. 2006 (when NEMO Phase 1 was deployed).
Sea Noise measurement and modelling (presently under study)
Bioacoustics: study of sperm whales population in the East Med Sea
2005-2006: First experiment to perform long-term measurement and monitoring of the acoustic background @ 2000 m depth
CIBRA
Average noise spectrum
Nature (2009)

## Slide 12: Sperm whale detection
On-line monitoring of acoustic signals with OnDE allowed identification of sperm whales, determination of the population, size and tracking
Adult males
Females or young males
Youngs
Dive of 2 sperm-whales

## Slide 13: Dolphins’ predation cycle
Automatic identification of dolphins’ echolocation clicks (hunting)
day/nigh cycle assessed with 2 years of data

## Slide 14: The Submarine Network 1 EMSO Node
Low frequency hydrophone
INFN – LNS shore lab
June 2012
May 2013
NEMO – SN1
24/24 h recordings, 11 months
First Cabled node of EMSO
Monitoring of volcanic and seismic activity in Sicily: thanks to reduced noise SN1 has improved sensitivity with respect to inland observatories.
Prototype of a Tsunami early warning system

## Slide 15: Geophysics and Volcanology
Real-time data acquisition
Sensor Sampling rate
Three-component broad-band seismometer 100 Hz
Hydrophone (geophysics) 100 Hz
Gravity meter 1 Hz
Scalar magnetometer 1 sample / 10 min
Three-axes single-point current meter 2 Hz
CTD 1 sample / 12 min
SN1 Connection
Seismic activity map reconstructed by NEMO-SN1

## Slide 16: Fin whale presence
Low frequency hydrophone on SN1
bio-acustics (mysticetes)
acoustic noise monitoring (Marine Strategy Directive)
18-20 Hz Calls
Target Species IUCN
Identification and monitoring
First data on effect of anthropogenic noise

## Slide 17: Airgun Signals
Noise level increase: 10 dB
Identified source, offshore Greece
Need of transnational policies !
Fin whale
Airgun
Anticoincidence between airgun shoots and fin whale presence
Real-time identification of “airguns” (compressed-air cannoons) used for geophysics studies
Italian Ministry for the environment

## Slide 18: Noise pollution measurements (MSFD)
MMSI: 247323100
(CARGO)
Real-time monitoring of man-made acoustic pollution in the Central Mediterranean Sea
Ship identification with AIS and acoustic sign signature
100 dB
1kHz
Noise maps
Noise Spectra

## Slide 19: The Smo-OnDE detector (running)
Data available for the implementation of the Marine Strategy Directive in Italy
Real time data acquisition and analyisis (24h/7d)
Improved senitivity and sampling rate, GPS synchronisation

## Slide 20
Thanks for your attention