## Slide 1
Moss monitoring manual
29th ICP Vegetation TFM, 1 – 3 March, 2016, Dubna
Science of the Total Environment 517 (2015): 132-150
Responses:
Harmens, H., Schröder, W., Zechmeister, H.G., Steinnes, E., M. Frontasyeva. Science of the Total Environment 538 (2015): 1024-1026.
Fernández, J.A. et al. Science of the Total Environment 538 (2015): 1027-1028

## Slide 2
Recommendations Fernández et al.
Variable | Manual | Recommendation
No. sampling sites | 1.5 or 0.8 samples/1000 km2 | 1 sample/1000 km2 (4, 16, 62)
Sampling design | Sites evenly distributed | Regular sampling
Frequency | Every 5 years | As frequent as possible (economic limitations)
Moss species | Interspecies calibration | No interspecies calibration; if more than one species - quantitative interpretation
Distance to vegetation | 3 m from tree canopy | 2 x height of tree (y = 23.6 ln(x) – 31.5)
Elevation, coast | No recommendation | Caution interpretation of results
Representation site | Original site or within 2 km | Original site or within 1 km
Area site | 50 x 50 m (2500 m2) | Between 201 and 2500 m2
Subsample | 5 – 10 (10 for POPs) | Minimum of 30 subsamples
Period | April – October (short period) | 2 samplings separated by 6-7 months
Amount and storage | 1 L, paper bags, air dried/frozen | 30 g dw, plastic bags, fridge (<2 weeks)
Selected material | Green, green-brown shoots (3 y) | Green
Drying and milling | 40 oC | 40 oC + aliquot 105 oC (dw), metal free mill

## Slide 3
Moss survey 2015/16
Time schedule preparation report 2015/16 survey:
  2015 sampling: data submission 1 October 2016
  2016 sampling: data submission 1 April 2017
  Draft maps: 1 October 2017
  Final approval at TFM Jan-Feb 2018
  Final report: 1 April 2018
Content moss survey report (to be translated into Russian too):
  Spatial patterns and temporal trends (where feasible) of concentrations of heavy metals, nitrogen and persistent organic pollutants in mosses;
  Country reports (maximum of 2 page) on a voluntary basis;
  A separate reports will be produced for radionuclides.
Preparation of additional standard for next surveys – working group:
Eero Kubin (Finland), Eiliv Steinnes (Norway), Stefan Fränzle (Germany) and Sebastien Leblond (France)
29th ICP Vegetation TFM, 1 – 3 March, 2016, Dubna
Notes: Contribution to WGE report on impacts of air pollution on biodiversity and ecosystem services

## Slide 4
Moss survey: other issues
Submission MossMet data (voluntary) and linking with previous MossMet
Data M2 and M3: every laboratory should report data to Marina!
Sampling at sites other monitoring networks: ICP Forests, EMEP etc.
Formal agreement between the new Moss Survey Coordination Centre (Joint Institute for Nuclear Research, Russian Federation) and national data providers regarding storage and use of data.
How to make more use of moss data?
Opportunities for monitoring air pollution in urban areas.
Opportunities for further enhancement participation EECCA countries and outreach beyond.
29th ICP Vegetation TFM, 1 – 3 March, 2016, Dubna
Notes: Contribution to WGE report on impacts of air pollution on biodiversity and ecosystem services

## Slide 5
Update publications 2010/11 data
Publications group Schröder, Germany:
Schröder W, Nickel S, et al. Spatially valid data of atmospheric deposition of heavy metals and nitrogen derived by moss surveys for pollution risk assessments of ecosystems. Environmental Science and Pollution Research Special Issue ContaSed (in press).
Schröder W, Nickel S, et al. Moss surveys as potential data source for forest monitoring. Annals of Forest Science. Special Issue ICP Forests (submitted).
Nickel S, Schröder W, et al. Modelling and mapping heavy metal and nitrogen concentrations in moss in 2010 throughout Europe by applying Random Forests models (planned to be submitted to Atmospheric Environment).
Other two planned papers partially included in submitted paper. Further analyses on hold due to workload 2016 moss survey in Germany.
Why lack of response to Winfried’s draft papers?
29th ICP Vegetation TFM, 1 – 3 March, 2016, Dubna