## Slide 1
49th PAC for Nuclear Physics
January, 22, 2019, JINR, Dubna
Status of the Factory of Superheavy Elements
Separators
A. Popeko
Flerov Laboratory of Nuclear Reactions,
Joint Institute for Nuclear Research

## Slide 2: Proposed Separators:
Velocity selector,
Gas-filled separator QDQQD,
Gas-filled pre-separator.

## Slide 3
Air-free separator:
complete fusion reactions;
multi-nucleon transfer reactions;
nuclear spectroscopy @ target & focal plane.

## Slide 4
SHELS + GABRIELA
Running @ U400

## Slide 5: Gas-filled separator Synthesis of SHE in complete fusion reactions

## Slide 6: Dubna Gas Filled Recoil Separator GFS-1
In operation since 1989,
Ist JINR price 1990 in instrumentation

## Slide 7: Gas-filled separator GFS-II
Assembled on 12.06.2018,
vacuum chamber tested.

## Slide 8
Gas-filled separator GFS-II: assembling

## Slide 9: Optical elements of GFS-2
Effective length | 460 mm
Bore diameter | 150 mm
Maximum field gradient | 13.2 T/m
Effective length | 600
Bore diameter | 300 mm
Maximum field gradient | 5.5 T/m
Gap | 132 mm
Deflection angle | 300
Radius of curvature | 1.8 m
Maximum field | 1.8 T
Face pole rotation angle | -70
Rear pole rotation angle | 43.50
Gap | 132 mm
Deflection angle | 100
Radius of curvature | 1.8 m
Maximum field | 1.8 T
Face pole rotation angle | 00
Rear pole rotation angle | 100
Magnetic quadrupole 1
Magnetic quadrupole 2 & 3
Magnetic dipole 1
Magnetic dipole 2

## Slide 10: Power supply units & cables
Cooling water;
Pressed air;
Power and control cables underlaid;
Tested with magnets.

## Slide 11: GFS-II systems
Will be delivered in February
Beam line lenses
Target block Ø240
Detector chamber
Are ready
Rotating window
Target block Ø150
Signal cables

## Slide 12: Detectors & Data Taking Systems under testing
New, digital
data taking system
48 × 128 strips
6144 pixels

## Slide 13
Preseparator & gas-catcher, RS-chamber:
chemistry;
fusion and multi-nucleon transfer reactions;
mass-spectrometry and nuclear spectroscopy;
laser spectroscopy of heavy atoms.

## Slide 14
available for
mass separation
Gas-filled Pre-Separator
(initial idea)
He – 100 tor
He – 1 tor

## Slide 15
Superconducting Gas-filled pre-separators (Dvh - variants)
Iron free concept
Superferric magnet concept
Deviation radius 900 mm
Maximum Field 3,5T
Total gap: 120 mm
Deviation angle 30°
Front pole face rotation: 68.4o
Rear pole face rotation : -62.5o

## Slide 16: Gas-Filled Pre-separator QVDH
Dipole D1 |  | 
 | warm | super
Bending angle | 40o | 40o
Bending radius | 1.8 m | 1.0 m
Maximum field | 1.8 T | 3.3 T
Field inhomogeneity factor n1 | -1.262 | -1.249
Front & rear pole face rotation angles | -35o | -20o
Quadrupole Q1 (vertical) | 
Effective length | 600 mm
Bore diameter | 200 mm
Maximum field gradient | 13.5 T/m

## Slide 17: Gas-filled pre-separator GFS-3 (QVDHQHQVD)

## Slide 18
Gas-filled pre-separator GFS-3
(at the ΣΦ’s site)
17 December 2018

## Slide 19
Gas-filled separators GFS-2 & GFS-3 @ DC280
GFS-3:
installation – Mai 2019
launching - 2020

## Slide 20: Focal plane detectors

## Slide 21: Focal plane DSS-Detectors (Micron Semiconductors, UK)
48 × 128 strips
6144 pixels
128 × 128 strips
16384 pixels

## Slide 22
GABRIELA - Gamma Alpha Beta Recoil Investigation with the Electromagnetic Analyser
New focal plane detector GABRIELA

## Slide 23: Comparison of the γ’s detection efficiency

## Slide 24: 50Ti beam intensity – 3×1012 pps. 50Ti + 208Pb = 256Rf + 2n
3He – neutron detector system
ε(252Cf) = 40%
Neutron multiplicity measured for spontaneous fission of 256Rf
TKE spectra for S.F. of 256Rf isotope
Notes: For the synthesis of elements heavier than 118, the beams of ions heavier than Ca-48 are needed. In cooperation with our colleagues from France the Ti-50 ions were accelerated at the U400. First experiments were dedicated to the measurement of the average number of prompt neutrons from spontaneous fission of Rf, produced in 50Ti+208Pb reaction using the modernized VASSILISSA separator He-3 neutron detector. These set-ups were developed in accordance with the DRIBS-III project. The average number of neutrons was found to be 4.47 n/SF. These measurements are of special interest for understanding properties of SHE and for their search in nature.

## Slide 25
Conclusion
The realization of the SHE-factory project will provide the quantitative increase of the efficiency of experiments as a whole by at least one order of magnitude.

## Slide 26
Thank you for your attention!
SHE-Factory building, January 2019