## Slide 1: Status of the GALS Setup Gas Cell Based Laser Ionization & Separation Setup Sergey Zemlyanoy Flerov Laboratory of Nuclear Reactions Joint Institute for Nuclear Research Dubna 49th meeting of the JINR PAC for Nuclear Physics Jan.22-23, 2019, Dubna.

## Slide 2: GALS Gas Cell Based Laser Ionization & Separation Setup
R E C O M M E N D A T I O N S 34th meeting, PAC for Nuclear Physics, 16-17 June, 2011
Possibility for the production and study of heavy neutron-rich nuclei formed in multi-nucleon transfer reactions
The PAC discussed the proposal of the Flerov Laboratory, presented by V. Zagrebaev, on the synthesis of heavy neutron rich nuclei formed in low-energy multi-nucleon transfer reactions. The use of this method opens a new field of research in low-energy heavy-ion physics, namely, the production and study of new neutron rich heavy nuclei playing a key role in the r-process of nucleosynthesis. The development of an experimental set-up based on the method of stopping reaction fragments in gas and on their subsequent selective resonance laser ionization is proposed. With such a method atoms of required elements can be selected. The method is already used in several laboratories for separation and study of light exotic nuclei and fission fragments. Because of the capability of selecting ions of specific atomic numbers, this set-up can also be employed in other studies, like the unknown charge distribution of the products of quasi-fission. The PAC emphasizes that the proposed experimental method is feasible.
Recommendation.
The PAC strongly recommends starting to work on the details of this proposal within the Flerov Laboratory right away.
R E C O M M E N D A T I O N S 35th meeting, PAC for Nuclear Physics, 27-27 January, 2012
New set-up of FLNR for on-line separation of reaction products by means of selective laser ionization
The PAC notes with great interest that the availability of such a facility extends the experimental possibilities of the laboratory in the field of low-energy heavy-ion physics, and, most importantly, in an unexplored region of the nuclear chart.
Recommendation.
Taking into account the relevance of such studies and the international competition on similar approaches, the PAC strongly recommends the start of construction of such a facility in 2012.
The setup project was approved by JINR's Directorate on June 6, 2012

## Slide 3: r-process and heavy neutron rich nuclei
difficult to synthesize
difficult to separate

## Slide 4: Production of new heavy nuclei in the Xe + Pb collisions

## Slide 5
IGLIS – Ion Guide Laser Ionization and Separation
Laser
beams
+
+
+
mass
separator
cyclotron
beam
SPIG
Ni filament
He
target
3-10 mg/cm2
40 kV
Time profiles of laser-ionized stable
Ni-58 from the filament
~1994
Laser-produced Ni ions recombine in a plasma created by a primary beam
>99% are neutral
We have to provide for radioactive atoms:
1. Efficient laser ionization
2. Survival of laser-produced ions in a volume around the exit hole
Weak beam, 1nA, 1ms
Strong beam, 1uA,20ms
Delay time - down to 10 ms (He)
Refractory elements - !

## Slide 6: Multistep selective laser ionization

## Slide 7
Schematic view of setup for resonance laser ionization of nuclear reaction products stopped in gas

## Slide 8: General view of GALS setup
Experimental Cabin
Experimental Cabin
Detection System
Front End
Ion Beam
Laser Lab.
Control Room

## Slide 9
 | Dye | Ti:Sa
Active Medium | > 10 different dyes | =1 Ti:sapphire crystal
condition of aggregation | liquid | solid-state
Tuning range | 540 – 850 nm | 680 – 980 nm
Power | < 15 W | < 5 W
Pulse duration | 8 ns | 50 ns
Power stability | decrease during operation | stable
Synchronization | optical delay lines | q-switch, pump power
Maintenance | renew dye solutions | ~ none
Comparison dye vs. possible Ti:Sa system
Ti:Sa
Dye
2x Ti:Sa
2x Dye
3x Ti:Sa
4x Ti:Sa
3x Dye
Dye
Ti:Sa

## Slide 10: The optimum RILIS Laser System
Nd:YAG
Dye 2
Dye 1
THG
SHG
RILIS Dye Laser System
GPS/HRS
Target &
Ion Source
l – meter
Nd:YAG
Ti:Sa 3
Ti:Sa 2
RILIS Ti:Sa Laser System
l – meter
Master clock
Delay Generator
pA – meter
Faraday cup
SHG
Narrowband Dye
Ti:Sa 1
SHG/THG/FHG

## Slide 11: The laser lab construction

## Slide 12: Laser system (delivered to JINR)
Nd:YAG laser specification (EdgeWave GmbH)
Maximal average power: 90 W and 36 W at fundamental and 2nd harmonic respectively;
Repetition rate: 10-15 kHz;
Pulse duration: 8-10 ns.
Divergence parameter of the green beam: M2 = 1.4;
Electrical power 3.6 kW including 1.6 kW for the water chiller.
Credo dye laser specification (Sirah)
Maximal average power: 20 W at fundamental wavelength, 2 W at 2nd harmonic;
Line width: 1.8 GHz
Pulse duration: ~7 ns
Remote control of wavelength with stabilization to an external laser wavelength meter.
Type | Output power Main&harmonic, W, (2nd),{3rd, 4th} | Puls frequency, Hz | Puls length, ns | Wave length, nm
Dye laser | 3, (0.3) | 104 | 10-30 | 213-850
Ti:Sapphir | 2, (0.2), {0.04} | 104 | 30-50 | 680-960
Nd-YAG | (80-100), {20-40} | 104 | 10-50 | 532
Matisse system |  |  |  | 
Ring dye | 0.8-6 | cw | cw | 540-900
Ti:Sapphir | 0.8-6.5 | cw | cw | 700-1000

## Slide 13: Ti:Sa laser system installing in the laser lab
The advantages of the TU series:
Simpler design
Superior wavelength stability over Fabry-Pérot etalon based approaches
Superior wavelength stability that's better than 0.1cm-1 (typically <0.04 cm-1 over eight hours).
Wavelength and line width are not affected by changes in temperature, and pressure
No need to re-calibrate wavelength on a daily basis
Diode pumped solid state (DPSS) laser solution vs a Dye laser solution:
No dye cells, replacement of dyes nor the need to flush and replenish any dyes at any time.
Much more stable wavelength.
Narrow linewidth diffraction pattern measured from a Photonics Industries TU Series Diode Pumped Solid-State Tunable ns Ti: Sapphire Laser

## Slide 14
A
B
C
D
Possible ionization schemes of OsI
λ1 nm (air) | Level, cm-1
238.729 | 41875.7
239.588 | 41725.6
242.426 | 41232.1
242.497 | 41225.1
247.618 | 40361.8
Resonance energy levels schemes - to be tested offline
λ1, nm | E1, cm-1 | λ2, nm | E2, cm-1 | λ3, nm
290.906 | 34365.30 | 475.216 | 55403 | 640.315
301.805 | 33124.48 | 558.066 | 51039 | 558.066
326.921 | 30591.45 | 550.933 | 48737 | 326.921
330.156 | 30279.99 | 481.596 | 51039 | 481.596
J.D. Blum et al, Anal. Chem. 1990
W.F. Calaway et al., J. Vac. Sci. Technol. 1995
http://physics.nist.gov/cgi-bin/ASD/lines1.pl
Ch. Corliss and W. Bozman, NBS Monograph 53, 1962
Schemes A and B
Schemes D and C
A: λ2< 360 nm
B: λ2 = λ1
D
C: λ3= λ2
C: λ3= λ1
IP = 68058.64 cm-1

## Slide 15: Front-end, separator and detection systems at U-400M
Design of the full on-line part of GaLS facility and allocation of production front-end, separation and detection part of system with two different tape stations in the experimental cave of cyclotron U-400M was performed.

## Slide 16
Fluka and Geant4 simulation for neutron and gamma background

## Slide 17
Cyclotron beam
Gas Cell
SPIG
Extraction electrode
Gas from purifier
Laser beams
Front end of GALS setup

## Slide 18
Exit hole diameter – 0.5mm/1mm
Stopping chamber – 4 cm in diameter
Laser ionization chamber – 1 cm in diameter
The aim: (by separating stopping and laser ionization chambers)
Increasing laser ionization efficiency at high cyclotron beam current
Increasing selectivity (collection of survival ions)
Working conditions:
cyclotron – DC
Ion collector – DC
Lasers – transverse or longitudinal
The layout of the dual chamber laser ion source gas cell

## Slide 19: From dual chamber to horn-like gas cell

## Slide 20: SIMION simulations of ion guide system
Parameters at the end of SPIG:
Mean time of flight ≈ 3000 μs
Mean longitudinal kinetic energy ≈ 0.2 eV
Efficiency ≈ 95 %
Advantage: a single 6-rod structure ion guide
through the whole front end vacuum chamber
Disadvantage: high risk that the ions get stuck
inside long SPIG due to kinetic energy losses
The length of the SPIG ≈ 630 mm
Urf (peak-to-peak) up to 500 V
Frequency = 4.7 MHz
SextuPole Ion Guide
Interaction with the buffer gas atoms modelled

## Slide 21: SIMION simulations of ion guide system
S-shaped RFQ
microRFQ
Parameters at the end of LRFQ:
Mean time of flight ≈ 650 μs
Mean longitudinal kinetic energy ≈ 10 eV
Efficiency ≈ 95-98 %
Advantage: much better TOF and efficiency
Disadvantage: much more complicated system
S-shaped RadioFrequency Quadrupole + microRFQ + Linear RFQ

## Slide 22: The Ion Guide design
P=10-1 – 10-2 mbar
L = 310 mm
Rod diameter = 18 mm
Rod distance = 18 mm
Segment length = 15 mm
= 0.4 – 0.6 MHz
Upp = 160 – 600 V
P=10-3 – 10-5 mbar
L = 96 mm
Rod diameter = 4.6 mm
Rod distance = 6 mm
= 0.5 – 0.9 MHz
Upp = 50 – 100 V
P < 10-5 mbar
L = 136 mm
Rod diameter = 10 mm
Rod distance = 10 mm
= 1.2 MHz
Upp = 600 V
wedge-type
micro RFQ

## Slide 23
The ion extraction system simulation

## Slide 24
Mass-separator
3D simulations of mass separator and beam dynamics within it were carried out. It used 3D map of the AM magnetic field calculated using OPERA code. The number of the ions was equal to 2∙104.The calculated distribution of the particles in the analyzing magnet focal plane is shown.The estimated mass resolution of mass-separator Rm = 1400.
Mass-separator specifications:
Bending radius 1 m
Bending angle 90о
Rigidity of about 0.5 Т.m.
Dipole gap 60 mm
Mass resolution 1400
Focal plane length of about 1 m,
Weight : 1800 kg

## Slide 25: Gas purifying system
SAES Pure Gas, Inc.
Rare Gas Purifier 3000 Model - PS4-MT3-R-2
Inlet Impurity | Ar – 4 slpm, He – 7 slpm
O2 | < 1 ppb
H2O | < 1 ppb
CO | < 1 ppb
CO2 | < 1 ppb
N2 | < 1 ppb
H2 | < 1 ppb
CH4 | < 1 ppb
The gas purity is a key issue for efficient running of the laser ion source. High-purity argon gas is additionally purified in a getter-based purifier to the sub-ppb level.

## Slide 26: b-decay Tape Station

## Slide 27: Preliminary result

## Slide 28: The experimental cabin subsystems of GALS setup
Main parts is ready for installing
Front end system
Gas purifying system
Mass-separator
Pump station
& vacuum system
Delivered to FLNR JINR, will be ready in beginning of 2019
Main parts is ready for installing
Detection system
Designing and development
with South Africa and Slovakia
Designing and development

## Slide 29: Working plan
 | Laser system |  |  | Front end system |  |  | Pump station |  |  | Gas purification |  |  | Separator, detection |  | 
 | preparation | mounting | commissioning | preparation | mounting | commissioning | preparation | mounting | commissioning | preparation | mounting | commissioning | preparation | mounting | commissioning
2017 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2018 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2019 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2020 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2021 | starting experiments |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 30
Main results obtained in 2017-2018.
1. Base laser equipment (TiSa and Dye lasers, beam diagnostic, doubling optics etc.) have been delivered and now is installing in the laser lab. This way the first laser part of setup will be completed and test experiments on selective resonance laser ionization will be started in the 2019 using the reference cell which will be manufactured in collaboration with our CERN and German colleagues.
2. Front-end subsystems (ion extraction system, Enzel lens, correcting dipoles etc) has been manufactured and delivered to laboratory.
3. Manufacturing of separator magnet was finished. Joint assembly of a yoke and coils of a separator and also tests has been carried out at the site of the producer. Joint assembly with vacuum chamber of separator and testing will be performed in 2019.
4. Manufacturing of the first gas cell design has been finished and gas cell soon will be ready to testing.
5. First design of tape station was developed by our colleagues from South Africa and prototype manufacturing has been performed in iThemba LABS. First testing experiments and real on-line run on gamma-spectroscopy of Yb isotopes have been performed in order to determine deformation and triaxiality in these nuclei (2018).
Summary

## Slide 31
Proposed program for the next years
2019: Off-line setup for laser spectroscopy modernization and development will be finished and extended investigation of ionization schemes elements under interest will be start.
Start of installation and testing of base production and separation part of setup will be performed. Laser beams transportation channel to experimental area will be arranged.
2020: Full installation of the main production and separation part of setup will be performed during planned U-400M modernization stop.
Detecting system consisting of tape-station, Ge, LEP and MCP detectors will be developed. Control and data accusition systems including all the electronic subsystems will be prepared. Testing experiment will start.
2021: Full-scaled experiments on production and study of properties of new heavy neutron rich nuclei at the cyclotron U400M of FLNR will start.
At target thickness 0.3 mg/cm2, ion beam of 0.1 pmA and setup efficiency of 10% we would be able to measure decay properties of 1 new isotope per day
Summary

## Slide 32: People involved in the Project
JINR: V. Zagrebaev , S. Zemlyanoy, K. Avvakumov, G. Myshinsky,
V.Zhemenik, N. Kazarinov, Z. Batsuren and others
iThemba: Robert Bark + 2 PhD students
Leuven: Yuri Kudryavtsev, P. Van Duppen, M. Huyse
CERN: Valentin Fedosseev, Bruce March
Poland: Zenon Janas, Zdzislaw Blaszczak
Jyväskylä : Juha Äystö, Iain Moore, Heikki Penttilä
GSI: Michael Block, Thomas Kühl
GANIL:Nathalie Lecesne, Herve Savajols
Mainz: Klaus Wendt, Hartmut Bake
Manchester: Jonathan Billowes, Paul Campbell
Mongolia: P. Zuzaan +
Egypt: Hosam Othman +
IS RAN Troitsk: Vyacheslav Mishin

## Slide 33
People involved into developing and discussion of this SETUP project
Thank you for your attention

## Slide 34: Production of NEW heavy nuclei in the region of N=126 (Zagrebaev & Greiner, PRL, 2008)
“blank spot”
82
82

## Slide 35: Test experiment demonstrates good agreement with our expectations (Dubna, 2012)

## Slide 36: Much higher cross sections for the production of new neutron rich nuclei were found for collisions of Pt beam with U target