## Slide 1
SECONDARY BEAMS
AND MACHINE PROTECTION
Francesco Cerutti
Joint US-CERN-Japan-Russia
International Accelerator School
on Ion Colliders
Dubna October-November 2019

## Slide 2
which ones?
Beam Loss Monitor system
validation of collision debris simulation
impact on the machine and mitigation strategies
new challenges
input from beam tracking
acknowledging the contribution of several CERN colleagues
OUTLINE

## Slide 3
SECONDARY BEAMS
Bound Free Pair Production
d > 0
ZZ+ + ZZ+ → ZZ+ + Z(Z-1)+ + e+
g → e- + e+
AZZ+ + AZZ+ → AZZ+ + (A-1)ZZ+ + n
g → AZ*
ZZ+ + ZZ+ → ZZ+ + Z(Z-2)+ + 2e+
2(g → e- + e+)
AZZ+ + AZZ+ → AZZ+ + (A-x)ZZ+ + xn
g → AZ*
magnetic rigidity relative difference
Double
Bound Free Pair Production
d >> 0
Electromagnetic Dissociation
d < 0
d << 0
x = 2,…
equivalent photon spectrum ~ Z2
virtual photon energy
ωmax = hcγ / (2πRA)

## Slide 4
208Pb–208Pb
power towards one side
d = 0.01235
[J. Jowett]
one side cross section | LHC (5 A TeV CM) [b] | FCC (40 A TeV CM) [b]
BFPP | 280 | 345
DBFPP | 0.01–0.1 | 
EMD | 215 | 280
EMD1 | 95 | 120
EMD2 | 30 | 35
Nuclear inelastic | 8 | 8
p–p | 0.08 | 0.11
d = -0.00481
LHC (6 1027 cm-2 s-1) [kW] | FCC (3 1029 cm-2 s-1) [kW]
0.15 | 70
0.055 | 25
0.9 | 260
EMD for 40Ar–40Ar @ FCC (45 A TeV CM): 2 b
for 84Kr–84Kr @ FCC (43 A TeV CM): 16 b
for 129Xe–129Xe @ FCC (42 A TeV CM): 60 b

## Slide 5
BEAM LOSS MONITORING
BLMs are used for diagnostics and machine protection (beam extraction in case of critical beam losses).
They are ionization chambers, pin diodes, diamond detectors, …
The LHC BLM system

## Slide 6
REGULAR PROTON LOSSES
~4000 BLMs
noise
floor

## Slide 7
THE COLLISION DEBRIS

## Slide 8
√s = 14 TeV p–p
150 W absorbed in the TAS absorber
650 W going through the TAS
of which
150 W absorbed in the triplet
950 W towards each (L&R) side
Instantaneous luminosity: 1034 cm-2 s-1
(i.e. 8.5 108 inelastic collisions)
right of ATLAS
cold magnets

## Slide 9
DEBRIS CAPTURE IN THE FINAL FOCUS “TRIPLET”
lost in Q1
end of the
TAS shadow
right of ATLAS
high energy spectra are depopulated by charge particle interception in the successive quadrupoles
due to magnetic field bending

## Slide 10
MARGIN TO QUENCH AND LIFETIME
round optics
142.5 μrad half crossing angle
V crossing in ATLAS (IR1)
H crossing in CMS (IR5)
x
x
different behavior reflecting the crossing plane variation for the same
magnetic configuration of the triplet (FDF in the horizontal plane for
positively charged particles coming from the IP)
- IR1 triplet (Q2a) reaches the design limit at nominal luminosity
peak dose [MGy] after 300 fb-1, relevant for triplet (i.e. coil insulator) lifetime

## Slide 11
RUN 1 (√s = 8 TeV) BENCHMARK @ ATLAS
[A. Lechner et al, Phys. Rev. AB 22 (2019) 071003]

## Slide 12
LHCb
compensator dipoles
LHCb spectrometer
outside
the ring
D
[on the horizontal plane for the outgoing beam]
F
F
D

## Slide 13
RUN 1 (√s = 8 TeV) BENCHMARK @ LHCb
[A. Lechner et al, Phys. Rev. AB 22 (2019) 071003]

## Slide 14
ATLAS MATCHING SECTION IN RUN 2 (√s = 13 TeV)
absorbing 40 W
[A. Tsinganis]
Fill #4919 (May 2016)
TCLs @ 15-35-20 sigma

## Slide 15
Fill #5401 (October 2016)
TCLs @ 15-35-20 sigma
CMS DISPERSION SUPPR. IN RUN 2 (√s = 13 TeV)
[A. Tsinganis]

## Slide 16
REGULAR ION LOSSES*
* see lecture of Michaela Schaumann this afternoon

## Slide 17
CMS DISPERSION SUPPR. IN RUN 1 (√sNN = 2.76 TeV)
σBFPP = 250 b (one side),
Lint = 4.2–6.2 μb-1 per fill, NBFPP = 1–1.5 109 per beam and fill
[A. Lechner et al, Phys. Rev. AB 22 (2019) 071003]

## Slide 18
A SUCCESSFUL QUENCH TEST
on Dec 8th, 2015
with 6.37 Z TeV beams
the MB.B11L5 main dipole quenched
at L=2.3 1027 cm-2 s-1 in CMS
from -3 mm to +0.5 mm
[J. Jowett et al, IPAC2016, TUPMW028]

## Slide 19
WHICH IMPACT ON THE MAGNET?
208Pb81+ distributions from MAD-X tracking
[C. Bahamonde Castro, A. Lechner]

## Slide 20
40% increase in peak power density
Δx = 2.21 mm
Δx = 1.5 mm
nominal aperture
real aperture
IMPERFECTION EFFECT
[C. Bahamonde Castro, A. Lechner]

## Slide 21
COPING WITH SECONDARY BEAMS
simulated in the absence of orbit bump
[A. Lechner]

## Slide 22
BY AN ORBIT BUMP
[A. Lechner]

## Slide 23
BY A COLLIMATOR
60 cm long W-alloy collimator
with a 30 sigma gap
[A. Lechner]

## Slide 24
MAGNET PROTECTION
[C. Bahamonde Castro]

## Slide 25
RADIATION TO ELECTRONICS
[C. Bahamonde Castro]

## Slide 26
MAIN RADIATION EFFECTS ON ELECTRONICS
 |  |  | relevant physical quantity the effect is scaling with
Single Event effects (Random in time) | Single Event Upset (SEU) | Memory bit flip (soft error) Temporary functional failure | High energy hadron fluence [cm-2] (but also thermal neutrons!)
 | Single Event Latchup (SEL) | Abnormal high current state Permanent/destructive if not protected | High energy hadron fluence [cm-2]
Cumulative effects (Long term) | Total Ionizing Dose (TID) | Charge build-up in oxide Threshold shift & increased leakage current Ultimately destructive | Ionizing dose [Gy]
 | Displacement damage | Atomic displacements Degradation over time Ultimately destructive | Silicon 1 MeV-equivalent neutron fluence [cm-2] {NIEL -> DPA}

## Slide 27
CUMULATIVE DAMAGE
[C. Bahamonde
Castro]

## Slide 28
SINGLE EVENT EFFECTS
[C. Bahamonde Castro]

## Slide 29
NEW CHALLENGES
one side cross section | FCC (√sNN = 40 TeV) [b] | FCC (3 1029 cm-2 s-1) [kW]
BFPP | 345 | 70
EMD1 | 120 | 25
EMD2 | 35 | 7
[J. Molson]

## Slide 30
BFPP AT FCC (70 kW)
would absorb 55 kW
tungsten alloy collimator
peaking at 5 kW/cm3
W/cm3
W/cm3
1350 W
140 W
25 W
2 W
severe, but
almost acceptable (if alone!)
[J. Hunt]

## Slide 31
EMD1 AT FCC (25 kW)
mW/cm3
15 kW more on the collimator
2450 W
630 W
150 W
15 W
leakage
due to distributed impacts
charged pions
neutrons
heavier fragments
[J. Hunt,
J. Molson]

## Slide 32
INPUT FROM BEAM (HALO) TRACKING
Machine protection calculations lie in a multi-disciplinary field, where particle dynamics in accelerators and radiation-matter interaction play together.
Energy deposition, particle fluence, monitor signals … are simulated by shower Monte Carlo codes but imply multi-turn tracking in accelerator rings which requires dedicated codes. On the other hand, the latter ones are faced with the problem of particle scattering in beam intercepting devices (like collimators).
The interface regularly goes through static loss files
giving the spatial distribution of non-elastic interactions
- which cannot be handled by tracking codes - inside the jaw material, together with the direction and energy of the beam particle being lost

## Slide 33
COUPLING TOOLS
On-line coupling is becoming also available, allowing to avoid possibly critical simplifications (approximate interaction modules in tracking codes and vice versa).
Two codes running at the same time and talking to each other through a network port, by which particles are exchanged at run-time
[P.G. Ortega, P. Hermes et al., LHC Collimation Working Group, Oct 6, 2014]
MMBLB
MARS and MAD

## Slide 34
SIMULATION CHAIN VALIDATION
IP7
TCP B1
Q5
Q4
TCP
LHC BETATRON CLEANING INSERTION
[E. Skordis]