## Slide 1: Heavy Ion collision at RHIC
Mei Bai
GSI GmbH and University Bonn

## Slide 2: Relativistic Heavy Ion Collider
RHIC seen from space

## Slide 3: Recreate the early phase of universe
To heat up nuclear matter to very high temperature/high energy densities, greater than 10 normal nuclear density to liberate the quarks and gluons

## Slide 4: RHIC: A versatile collider
RHIC
NSRL
LINAC
Booster
AGS
Tandems
STAR
6:00 o’clock
PHENIX
8:00 o’clock
10:00 o’clock
Jet Target
12:00 o’clock
RF
4:00 o’clock
(AnDY)
2:00 o’clock
Operated modes (beam energies):
Au–Au 2.5/3.8/4.6/5.8/10/14/32/65/100 GeV/u
Cu–Cu 11/31/100 GeV/u
U – U 100 GeV/u
Ru – Ru 100 GeV/u
Zr – Zr 100 GeV/u
p–p 11/31/100/250/255 GeV
He3 – Au* 100 GeV/u
d–Au* 100 GeV/u
p – Au* 100 GeV/u
Cu – Au* 100 GeV/u
(*asymmetric rigidity)
Achieved peak luminosities (100 GeV):
Au–Au 1551026 cm-2 s -1
p–p 2451030 cm-2 s -1
EBIS

## Slide 5: Facts about RHIC
Circumference
  2.5 miles/3.8km
Accelerated species
  Proton, Cu, Au, … Uranium
Energy Range
  Protons: 23 GeV – 255 GeV
  Ions: 10 GeV/u – 100 GeV/u
One of the few super-conducting collider in the world
  Operating temperature: 4K or -452oF
Collision temperature
  Heavy ions: 4 trillion Celsius
Revolution time
  ~13s
RF system and harmonics
  Injection and ramp: 28MHz, h=360
  Store: 197MHz, h=2520
S. OZAKI, The Relativistic heavy ion collider at Brookhaven

## Slide 6: Delivered Integrated Luminosity and Polarization
Nucleon-pair luminosity: luminosity calculated with nucleons of nuclei treated independently; allows comparison of luminosities of different species; appropriate quantity for comparison runs.
W. Fischer, https://www.agsrhichome.bnl.gov/RHIC/Runs/
Notes: updated

## Slide 7: Brief History of RHIC
1989: RHIC design
1991: construction started
1996: AGStRHIC transfer line commission
1997: first sextant test
1999: Engineering test, first circulating Au beam
2000: first Au-Au collision at 100 GeV/u!
2003: d-Au collision
2005: Cu-Cu collision
2002: first polarized proton collision at 100 GeV
2009: first polarized proton collision at 250 GeV
2012: first 238U92+ ~ 238U92+ collision at 96.4 GeV/u
2013: first polarized proton collision at 255 GeV
2015: first polarized proton and Au collision at 100 GeV/u

## Slide 8: RHIC Operation parameters & performance
 | Energies [GeV/u] | Bunch# | Bunch intensity | Beta* [m] | Store peak lum. [cm-2s-1] | Store avg. lum [cm-2s-1]
Au-Au | 100 | 111 | 2e9 | 0.7 | 155x1026 | 87x1026
U-U | 100 | 111 | 0.3e9 | 0.7 | 8.8x1026 | 5.6x1026
Cu-Cu | 100 | 37/35 | 4.5e9 | 1/0.9 | 2.0x1028 | 0.8x1028
Au - Au | 31.2-31.2 | 111 | 1.2e9 | 2.5 | 4.5x1026 | 3.0x1026
Zr-Zr | 100-100 | 111 | 1e9 | 0.7 | 48x1026 | 22x1026
Ru - Ru | 100-100 | 111 | 1e9 | 0.7 | 38x1026 | 21x1026
d - Au | 101.3-99.4 | 111 | 1.3e11/1.9e9 | 0.7 | 85x1028 | 50x1028
p-Au | 104-97.4 | 111 | 2.3e11/1.6e9 | 0.85/0.7 | 88x1028 | 45x1028
p-Al | 103.9-98.6 | 111 | 2.4e11/11e9 | 0.85/0.7 | 760x1028 | 380x1028
Cu-Au | 99.9-100 | 111 | 4e9/1.3e9 | 0.7 | 1.2x1028 | 1.0x1028
W. Fischer, https://www.agsrhichome.bnl.gov/RHIC/Runs/

## Slide 9: RHIC Operation: A Typical RHIC Store
Injection and Acceleration
Cogging, establish collision
STAR and PHENIX ZDC
Beam currents

## Slide 10: RHIC Operation: A Typical RHIC Store
Check injection:
bunch intensity
injection matching
…
Filling Blue ring…
Filling Yellow ring…
Acceleration…

## Slide 11: A closer look at RHIC Complex
RHIC
NSRL
LINAC
Booster
AGS
Tandems
STAR
6:00 o’clock
PHENIX
8:00 o’clock
(PHOBOS)
10:00 o’clock
Jet Target
12:00 o’clock
RF
4:00 o’clock
(BRAHMS)
2:00 o’clock
EBIS
Tandem van de Graff:
Two 15MV electrostatic accelerator. Each 24m long
able to develier 40 tpes of ions
world’s largest electrostatic accelerator
Alternating Gradient Synchrotron: one of the first synchrotron based on strong focusing principle
Booster: a circular synchrotron
Linear Accelerator: accelerator proton beam up to 200MeV
EBIS based pre-injector for heavy ions: 2MeV/u

## Slide 12: RHIC Injector Chain for Heavy ions
C. J. Gardner et al, IPAC2015 Proceeding, Richmond, VA, USA
J. Alessi, et al, Proceedings of IPAC11, New York, NY, USA
in service until 2012
provide maximum 5e9 Au31+ ions per pulse
no Uranium
Simple, modern, low maintenance
Lower operating cost
Can produce any ions (noble gases, U, He3)
Higher Au injection energy into Booster
Fast switching between species, without constraints on beam rigidity
Short transfer line to Booster (30 m)
Few-turn injection (now about 50)
No stripping needed before the Booster,
resulting in more stable beams

## Slide 13: RHIC Injector Chain for Heavy ions
C. J. Gardner et al, IPAC2015 Proceeding, Richmond, VA, USA
J. Alessi, et al, Proceedings of IPAC11, New York, NY, USA
in service until 2012
Ions | He-U
A/Q | <=6.25
Current | >1.5emA
Pulse length | 10-40us(< a few turn injection)
Rep. rate | 5Hz
EBIS output energy | 17 keV/u
RFQ output energy | 300 keV/u
Linac exit energy | 2MeV/u
Time2switch species | 1 sec

## Slide 14: RHIC Injector Chain for Heavy ions
C. J. Gardner et al, IPAC2015 Conference Proceeding, Richmond, VA, USA
EBIS bunch
length: 10 ~ 40us
intensity: upto 1.62e9 Au32+
Booster harmonic 4
cycle time: 200ms
RF capture: 8ms
RF merging: 20ms
harmonic 8 4 2
Au77+
Au32+
8 Booster loads per AGS cycle
RF gymnastics
  Injection: h=16 8 4
  adiabatic h=412
  ramp h=12

## Slide 15: Performance limitation
Figure of measure for a collider
  Peak luminosity:
  # of collisions per unit area and per unit time
  Integrated luminosity:
  total number of collision events within the duration of a store

## Slide 16: What is luminosity?
For fixed target
The event rate is given by
where is the cross section of interaction. And, is defined as luminosity
Collision of two relativistic beams
The luminosity is
The event rate of the collider is where is the interaction cross section

## Slide 17: Figure of Measure for a collider
Peak luminosity: # of collisions per unit area and per unit time
For the case of head-on collisions
Ways to increase the peak luminosity
  Increase # of particles in each beam, i.e. bunch intensity
  Increase # of bunches
  Make each bunch more bright, i.e. shrink the size of the bunch at the collision point
# of particles from
Beam 1 in collisions
# of particles from
Beam 2 in collisions
Frequency of collision
Area of collisions, i.e. the product of beam size

## Slide 18: Figure of Measure for a collider
Integrated luminosity is defined as total number of collision events within the duration of a store
The unit of integrated luminosity is the inverse of cross-section unit, and typically expressed in inverse barn (10−24cm−2). For instance, RHIC delivered about 540 pb−1 of about 4 month polarized proton operation in 2013.
In additional to the direct burn-off rate of collisions, the integrated luminosity is directly affected by
  how effective is the detector: vertex distribution, detector ramp-up time, etc
  beam emittance growth during store due to various diffusion mechanisms such as intra-beam scattering, beam-beam effect, orbital resonance, etc.
  overall percentage of time-in-store

## Slide 19: Performance limitation
Bunch intensity limit
Wolfram Fischer IPAC16-WEZA01
ultimate goal (25% more)
AGS 12g6g2 merge
EBIS, Booster 4g2g1, AGS 8g4g2 merge
scrubbing with protons
111 bunches
43 bunches
gt-jump, octupoles at transition

## Slide 20: Performance limitation: transition crossing
Highly non-linear, and non-adaibatic beam dynamics near transition energy
RHIC is the 1st superconducting accelerator for transition crossing of all ions except proton
  limited ramp rate: /s
  long jump time, ~30 - 50ms instead of a few ms
    Beam experiences longer non-adiabatic, chromatic non-linear effects, and is more vulnerable to beam loss, emittance growth etc
energy jump
jump
Beam intensity
Beam decay

## Slide 21: RHIC Transition Crossing
jump: two dedicated families of quadrupoles in each of the six RHIC sextants
  Size of the jump: in ~30 - 50 ms
1st order jump successfully commissionined during the 2004 d-Au Run with 216ns bunch spacing[C. Montag, J. Kewisch, PRST-AB, Vol. 7, 011001, 2004]
]

## Slide 22: RHIC Transition Crossing
X. Gu, ECLOUD, 2018
careful optics optimization is needed
  Proper optics setup to minimize the optics distortion due to jump
  chromaticity adjustment during the transition
    Chromaticity must flip sign before and after the transition to avoid microwave instability
X. Gu, ECLOUD, 2018

## Slide 23: RHIC Transition Crossing
Nevertheless, significant beam loss due to fast instability is still experienced when beam intensity is pushed higher
C. Montag, J. Kewisch, D. Trbojevic, PRST-AB, VOLUME 5, 084401 (2002)
Au intentisty [1e6]
Time during ramp [s]
Longitudinal Phase
Bunch #: 55

## Slide 24: RHIC Transition Crossing
Nevertheless, significant beam loss due to fast instability is still experienced when beam intensity is pushed higher
C. Montag, J. Kewisch, D. Trbojevic, PRST-AB, VOLUME 5, 084401 (2002)
Au intentisty [1e6]
Time during ramp [s]
Longitudinal Phase
Bunch #: 55
When 4 arc octupoles were engaged to provide more Landau damping

## Slide 25: RHIC Transition Crossing
Longitudinal plane often suffers quadrupole oscillation after the transition
C. Montag, J. Kewisch, PRST-AB, Vol. 7, 011001, 2004
V. Ptitsyn et al, Proceedings of Hadron Beam 2008,Nashville,Tennessee,USA
Longitudinal emittance growth, which subsequently cause trouble for the rebucketing at store with 197MHz (h=2520)

## Slide 26: RHIC Transition Crossing
Longitudinal plane often suffers quadrupole oscillation after the transition
  A dedicated RF feedback with was developed to damp the quadrupole oscillation and reserve longitudinal emittance
V. Ptitsyn et al, Proceedings of Hadron Beam 2008,Nashville,Tennessee,USA

## Slide 27: Performance limitation: e-cloud
Ion beam induced electron cloud was observed early on in RHIC operation
  Vacuum presure rise at warm region
27
J. Wei et al, Proceedings of 2005 Particle Accelerator Conference, Knoxville, Tennessee

## Slide 28
Transition Crossing
Bunch Length
Performance limitation: e-cloud
It gets much worse during transition crossing,
Vacuum pressure
X. Gu, ECLOUD, 2018

## Slide 29
Transition Crossing
Re-bucketing
E-cloud
Blue (H&V)
Yellow (V)
E-cloud Signal
Performance limitation: e-cloud
It gets much worse during transition crossing,
X. Gu, ECLOUD, 2018
Bunch Length

## Slide 30
2011 pp operation:
Vacuum
Intensity
Scrubbing used in 2007 Au-Au operation:
7 high intensity fills in about 2 h, Reduced dynamic pressure in worst location by more than 1 order of magnitude
Mitigation of e-cloud: beam scrubbing
X. Gu, ECLOUD, 2018

## Slide 31: Performance limitation: e-cloud
which in turn triggers more profound impact on the beam dynamics in the neighborhood of transition crossing
  Bunch-by-bunch beam loss was also observed during transition crossing
V. Ptitsyn et al, Proceedings of Hadron Beam 2008,Nashville,Tennessee,USA
J. Wei et al, Proceedings of 2005 Particle Accelerator Conference, Knoxville, Tennessee

## Slide 32
Au79+
p+
d+
Au79+
Cu29+
p+
Au79+
Au79+
X. Gu, ECLOUD, 2018
Mitigation of e-cloud: NEG coating
Starting from 2005, most of the warm areas were NEG coated, which significantly contributed to the increase of total beam intensity

## Slide 33: Performance limitation: IBS
Intra-beam scattering: IBS
  Couloumb interaction between charged particles
  Leads to debunching and transverse emittance growth, i.e. longer bunch length and larger transverse beam size
33
2004 no cooling

## Slide 34: Stochastic Cooling: Mitigation of IBS
More details in Bunched Beam Stochastic Cooling, M. Steck, Nov. 6

## Slide 35: Full 3D Stochastic Cooling at RHIC
longitudinal kicker (closed)
horizontal kicker (open)
horizontal and vertical pickups
longitudinal pickup
5-9 GHz, cooling times ~1 h
vertical kicker (closed)
Y h+v pickups
B h+v kickers
B h+v pickups
Y h+v kickers

## Slide 36: Status of Stochastic Cooling
M. Brennan, M. Blaskiewicz et al.
Longitudinal stochastic cooling since 2007
Black: data
Magenta: simulation
First Stochatic Cooling of Bunched Beam!

## Slide 37: First Transverse(vertical) Stochastic Cooling!
14 Jan 2010
So far stochastic cooling increased average store luminosity by factor 2
Beam size in vertical plane
M. Brennan, M. Blaskiewicz et al.

## Slide 38: 56MHz SRF cavity: Mitigation of IBS
To obtain short bunch at store for collision, it is designed to accelerate the beam with 28MHz RF cavity and rebucket the beam with 197MHz at store
Nevertheless, the bunch length at store is ~10ns, while the bucket length of the197MHz cavity is only 5.1 sec
Rebucketing requires bunch rotation, which often results
  Beam loss or mis-match
  spills particles to the neighboring buckets
During store, longitudinal emittance growth due to IBS pushes particles to the neighboring buckets due to rather limited bucket size of 197MHz

## Slide 39: 56MHz SRF cavity: Mitigation of IBS
Measured beam profile with 197MHz
Measured beam profile in 2011
Y. Luo et al, PRST AB 17, 081003, 2014

## Slide 40: 56MHz SRF cavity: Mitigation of IBS
Measured beam profile with 197MHz
6 hours into store
G. Robert-Demolaize, RHIC 2014 performance, RHIC retreat

## Slide 41: 56MHz SRF cavity: Mitigation of IBS
A 56MHz SRF cavity to provide short bunch and avoid re-bucketing RF gymnatics
A. V. Fedotov, I. Ben-Zvi, Proceedingsof PAC09,Vancouver,BC,Canada, 2009
Cavity is designed to be a quarter-wave resonator, located at RHIC IP-4

## Slide 42: 56MHz SRF cavity commissioning in 2014
Q. Wu, et al, Proceedings of SRF2015, Whistler, BC, Canada

## Slide 43: Asymmetric collision
RHIC started its asymmetric collision d-Au in 2003. Different from LHC, RHIC carries out asymmetric collision
The successful development of He3-Au in 2014 demonstrated the feasibility of local orbit path through D0. This set the path for the later-on p-Au operation with re-positioned D0 magnets
More to see lecture on Performance Highlights from the LHC, M. Schaumann, Nov. 5, afternoon
store
ramp
injection of d
store Au
mini- ramp Au just above
Injection Au
Injection porch
flattop porch

## Slide 44: RHIC Low Energy Operation
Motivation: search critical point in QCD phase diagram
Energy scan extends below nominal injection energy
main challeng: magnetic errors at low fields

## Slide 45: RHIC Low Energy Operation
Motivation: search critical point in QCD phase diagram
Energy scan extends below nominal injection energy
main challeng: magnetic errors at low fields
Desing RHIC injection

## Slide 46: RHIC Low Energy Operation: √s=7.7GeV
short stores due to limited beam lifetime
luminosity is also limited by space charge effect as well as IBS
  beam size blowup
10 minute
store
2 minute turnaround
Au Ions [e9]

## Slide 47: E-cooling for Low Energy Operation
1st success cooling heavy ions with RF accelerator based electron bunches
A.V. Fedotov et al, FIRST ELECTRON COOLING OF HADRON BEAMS USING A BUNCHED ELECTRON BEAM, NAPAC 2019

## Slide 48: E-cooling for Low Energy Operation
1st success cooling heavy ions with RF accelerator based electron bunches
A.V. Fedotov et al, FIRST ELECTRON COOLING OF HADRON BEAMS USING A BUNCHED ELECTRON BEAM, NAPAC 2019
Dmitry Kayran, et, al. Proceedings of NAPAC2019

## Slide 49: Summary
As the first high energy heavy ion collider, RHIC delivered amazing physics
  Re-recreated the conditions of the early universe
  Early universe behaved like perfect liquid
  Detected exotic anti matter and Jet quenching
The RHIC team has achieved an exceptional performance improvements with numerous techniques and upgrade measures
  Peak luminosity exceeded design by a factor of 75!
    NEG coating, e-cloud,
    3-D Stochastic cooling
    56 Mhz
  variety of collisions also exceeded expectation, in particular the asymmetric collision options
    EBIS, Improved the local orbit control and manipulation
  Collision energy
    Bunched electron cooling
Look forward to its next phase with electron beams for the electron ion collider!