## Slide 1
SIMULATIONS TOOLS:
INTERACTION WITH MATTER
Francesco Cerutti
Joint US-CERN-Japan-Russia
International Accelerator School
on Ion Colliders
Dubna October-November 2019

## Slide 2
interaction types and modeling
sources and effects
acknowledging the contribution of several CERN colleagues
OUTLINE

## Slide 3
THE MICROSCOPIC VIEW [I]
one 450 GeV proton on aluminum
high energy nuclear reaction

## Slide 4
THE MICROSCOPIC VIEW [II]
one 450 GeV proton on aluminum
hadronic shower continues until particle energy falls below pion production threshold
non-negligible fraction of initial energy goes to mass by nuclear binding breaking

## Slide 5
ELECTROMAGNETIC SHOWERS
development stops after tmax radiation lengths X0 as energy per particle reaches the critical energy Ec
shower depth increases logarithmically with initial energy E0
90% of deposited energy within ~ 1 RM
hence

## Slide 6
THE MICROSCOPIC VIEW [III]
one 450 GeV proton on aluminum

## Slide 7
THE MICROSCOPIC VIEW [IV]
one 26 GeV proton on copper
THE MACROSCOPIC VIEW: ACTIVATION

## Slide 8
THE MACROSCOPIC VIEW OF
HIGH ENERGY SHOWERS
particle fluence and energy deposition profile
100 GeV protons on lead
100 GeV protons on iron
volume-averaged particle spectra

## Slide 9
MATERIAL DEPENDENCE
energy deposition transversally integrated
[different from peak density profile, which depends on beam size]
Fe 7.9 26 1.76 15.1
for 7 TeV p

## Slide 10
In general there are two kinds of nuclear reactions:
Elastic interactions are those that do not change the internal structure of the projectile/target and do not produce new particles. Their effect is to transfer part of the projectile energy to the target (lab system), or equivalently to deflect in opposite directions target and projectile in the Centre-of-Mass system with no change in their energy. There is no threshold for elastic interactions.
Non-elastic reactions are those where new particles are produced and/or the internal structure of the projectile/target is changed (e.g. the nucleus is excited). A specific non-elastic reaction has usually an energy threshold below which it cannot occur (the exception being neutron capture).
NUCLEAR REACTIONS

## Slide 11
NON-ELASTIC HADRON-NUCLEON REACTIONS
Intermediate Energies
All reactions proceed through an intermediate state containing at least one resonance (dominance of the D(1232) resonance and of the N* resonances)
N1 + N2  N1’ + N2’ + p threshold around 290 MeV, important above 700 MeV
p + N  p’ + p” + N’ opens at 170 MeV
High Energies: Dual Parton Model/Quark Gluon String Model etc
Interacting strings (quarks held together by the gluon-gluon interaction into the form of a string). Each of the two hadrons splits into 2 colored partons  combination into 2 colorless chains  2 back-to-back jets.
Each jet is then hadronized into physical hadrons.
momentum fraction
In order to understand Hadron-Nucleus (hA) nuclear reactions, one has to understand first Hadron-Nucleon (hN) reactions, since nuclei are made up by protons and neutrons.

## Slide 12
NON-ELASTIC HADRON-NUCLEUS REACTIONS [I]
Target nucleus description (density, Fermi motion, etc)
Preequilibrium stage
with current excitation energy and exciton configuration
(non-nucleons are emitted/decayed )
Glauber-Gribov cascade with formation zone
Generalized IntraNuclear cascade
Evaporation/Fragmentation/Fission
γ de-excitation
t (s)
10-23
10-22
10-20
10-16
FLUKA PEANUT

## Slide 13
NON-ELASTIC HADRON-NUCLEUS REACTIONS [II]
i. two-chain diagram
ii. hadronization
q-q and qq-qq
pairs generation
Condition for possible re-interaction inside a nucleus:
iii. formation zone
reflecting the materialization time

## Slide 14
A BENCHMARK GLIMPSE
Differential pion and kaon production
Points: exp. data (C. Alt et al., EPJC49 (2007) 897
and T. Anticic et al. (NA49) EPJC68 (2010) 1)
Histogram: FLUKA
Inclusive fragment production
Points: exp. data (T. Enqvist, Nucl. Phys. A 686 (2001) 481)
Data
FLUKA
FLUKA after cascade
FLUKA after preeq
1 GeV/n 208Pb+p
PROTON ‒ C, PROTON
Pb ‒ PROTON

## Slide 15
NON-ELASTIC NUCLEUS-NUCLEUS REACTIONS
[L. Sihver et al, Advances in Space Research 49 (2012) 812]
[H.H. Braun et al, Phys. Rev. ST AB 17 (2014) 021006]
nuclear reaction cross section
by virtual photon absorption g + A → A’ + X
+ ElectroMagnetic Dissociation
charge changing cross section
208Pb
7 Z TeV 208Pb
nuclear
EMD
√sNN = 2.76 TeV (LHC 2011)
√sNN = 39.4 TeV (FCC)
[H.H. Braun et al, Phys. Rev. ST AB 17 (2014) 021006]

## Slide 16
158 GeV/n 208Pb on C, Al, Cu, Sn, Au, Pb
Inclusive fragment production
Red squares and blue circles: exp. data
Blue histograms: FLUKA EMD; Yellow histograms: FLUKA EMD+hadronic
(Phys. Rev. ST AB 17 (2014) 021006)
NUCLEUS-NUCLEUS PRODUCTS

## Slide 17
ENERGY LOSS
mean energy loss rate
C. Amsler et al.,
Phys. Lett. B667 (2008) 1
bremsstrahlung
ionization
20 MeV for e - on Cu
shell, Barkas, Mott corrections
effective charge for low energy high z ions
z2/b2 dependence

## Slide 18
NUCLEAR STOPPING POWER
partition function Sn/(Sn+Se) decreases with energy and increases with charge
16O in Silicon
107Ag in Gold
total kinetic

## Slide 19
DISPLACEMENTS PER ATOM
It is a “measure” of the amount of radiation damage in inorganic materials 0.3 dpa means that on average 3 atoms out of 10 have been displaced once from their site within the structural lattice
Displacement damage can be induced by all particles
produced in the hadronic cascade, including high energy photons
(through photonuclear reactions).
It is directly related to energy transfers to atomic nuclei
i.e. (restricted) Non Ionizing Energy Losses
As a result of the nuclear stopping power behavior,
NIEL and DPA are dominated by low energy heavy recoils
E particle energy Eth displacement threshold N atom density T energy transfer

## Slide 20
Heating energy deposition (integral power)
Thermal shock energy deposition (power density)
Quenching energy deposition (power density)
Deterioration energy deposition (dose), particle fluence, DPA
Oxidation, radiolysis, ozone production energy deposition
Gas production residual nuclei production
Single event effects in electronic devices high energy hadron fluence [+ neutron fluence, energy deposition (dose)]
Shielding requirements particle fluence (prompt dose equivalent)
Access limitations, radioactive waste, air activation residual dose rate and activity
Beam Loss Monitors (BLM) energy deposition
Radiation Monitors (RadMon) thermal neutron and high energy hadron fluence
Tumor cell destruction energy deposition (dose, biological dose)
EFFECTS
relevant macroscopic quantity

## Slide 21
GENERAL-PURPOSE PARTICLE TRANSPORT
MONTE CARLO CODES

## Slide 22
GEOMETRY MODELING
NEED FOR DETAILED MODELS OF ACCELERATOR COMPONENTS WITH ASSOCIATED SCORING
ELEMENT SEQUENCE AND RESPECTIVE MAGNETIC STRENGTHS
IN THE MACHINE OPTICS (TWISS) FILES

## Slide 23
THE LINE BUILDER
Profiting from roto-translation directives and replication (lattice) capabilities,
the AUTOMATIC CONSTRUCTION OF COMPLEX BEAM LINES,
including collimator settings and element displacement (BLMs), is achievable
Beam orbit
[A. Mereghetti et al., IPAC2012, WEPPD071, 2687]

## Slide 24
BEAM LOSSES
on beam intercepting devices (targets, collimators*, dumps, stoppers, stripping foils, … )
  regular
  accidental: smearing failures, injection mis-steering, asynchronous beam dump, top-off
diffused
  synchrotron radiation, beam-gas interaction, gas bremsstrahlung
debris from regular collisions at the interaction points
on unexpected obstacles (UFO, ULO, … )
* see lecture of Roderik Bruce later this morning

## Slide 25
BEAM−GAS INTERACTION
LHC (FCChh): 7 (50) TeV proton energy σ = 77 (89) mb 0.58 (0.5) A = 3.6 (3.1) 1018 s-1 1015 m-3 H2 eq. density
2.8 104 m-1s-1 ≥ 100 h
σ [m2] I [s-1] n [m-3] collision rate [m-1s-1] 1/(σ [m2] c [m/s] n [m-3]) beam lifetime [s]
nuclear reaction between the circulating hadron and an atomic nucleus of a gas molecule
LHC (FCChh): 574 (4100) TeV 208Pb energy σ = 1.9 (2.0) b 6.12 (43) mA = 4.7 (33) 1014 s-1 1015 m-3 H2 eq. density
89 (660) m-1s-1 ≤ 5 h

## Slide 26
GOING THROUGH THE EFFECT LIST

## Slide 27
BACKGROUND: ALICE [I]
LHC IR2 Long Straight Section (Left)
Residual Gas density
Fill 2736, Jun 16, 2012
Beam orbit
[A. Lechner, G. Bregliozzi, E. Leogrande, A. Di Mauro
LHC Background Study Group Meeting, Jan 28th, 2013]

## Slide 28
BACKGROUND: ALICE [II]
muons
charged pions and kaons
protons
neutrons
[R. Kwee
HL-LHC Annual Meeting 2013]

## Slide 29
proton beam on a 1 m long and 10 cm radius copper rod
160 MeV
7 TeV
LINAC4
and LHC
the macroscopic view
INTERACTION WITH ACCELERATOR MATERIAL:
ionization
electromagnetic shower

## Slide 30
3 MeV PROTON DUMP
Intensity: 65mA over 100μs
Beam size: 4.5mm σx = σy
orthogonal impact
tilting
beam
z
y
85% gain!
[C. Maglioni, V. Vlachoudis, EDMS 1182648]
graphite

## Slide 31
HIGH Z ION BEAMS
350 MeV/n 238U
two pulses
one pulse
per beam particle
dE/dz [10 MeV/mm]
1 mm
GSI S-334 experiment [courtesy of J. Lettry]
Intensity: 2.4 109 ions per pulse
Beam size: 0.85 mm FWHM
tantalum target

## Slide 32
5 TeV PROTON BUNCH ON TERTIARY COLLIMATOR [I]
Pmax 30 GPa
t = 1 ns
t = 85 ns
t = 2.8 ms
Compression Wave (red)
+ Rarefaction Wave (blue)
Compression Wave
reaches W-Cu interface
t = 3.2 ms
t = 4.2 ms
t = 5.6 ms
t = 6.6 ms
t = 3.7 ms
Compression Wave
reaches Cu-Ni Pipes
Pmax 160 MPa
Pmax 500 MPa
Pmax 2.2 GPa
Compression Wave bouncing back in W jaw
[courtesy of A. Bertarelli and his team]
shock wave propagation
Intensity: 1.3 1011 p
Beam size: 1.75 μm rad norm. emittance (0.3 mm sx and 0.19 mm sy)

## Slide 33
[courtesy of A. Bertarelli and his team]
Plastic Strain
Max 1.4%
(on Water Pipes)
Particle spray on the opposite jaw Sticking droplets?
~8 mm
Intensity: 1.3 1011 p
Beam size: 1.75 μm rad norm. emittance
(0.3 mm sx and 0.19 mm sy)
5 TeV PROTON BUNCH ON TERTIARY COLLIMATOR [II]

## Slide 34
HYDROGEN AND HELIUM GAS PRODUCTION
Spallation reactions induced by protons, neutrons, pions, … produce a variety of particles including protons (1H), deuterons (2H) , tritons (3H), 3He, and alphas (4He). The least energetic of these products (which are also the most abundant) can stop in the target assembly giving rise to a hydrogen and helium buildup.
These gases can lead to grain boundary embrittlement and accelerated swelling.
In the case of the CNGS target, for 1.4 1020 protons on target one expects about 4 1021 H atoms.
Assuming that all H atoms are desorbed from the target solid structures, this corresponds to 150 ml of atomic H at atmospheric pressure (75 ml if we assume they combined into molecules).

## Slide 35
REDOX
Ball bearings exposed
to hadronic showers in air
Ionising radiation creates radicals chemically active
PVC dehydrochlorination by X and g-rays
Cl- ions react with water droplets and create a very corrosive environment
energy deposition

## Slide 36
OZONE PRODUCTION
under the assumption of no O3 decomposition
(yielding in the  expression a neglected term kPeV/V with k decomposition constant
equal to 1.4 10-16 cm3/eV)
[NCRP Report 51, LEP Note 379]
deposited power
conversion factor

## Slide 37
ELECTRONICS FAILURES [I]
Electronics
Ventilation Units
CV,crane,
fire controls
Gy per 4.5 1019 p.o.t.
CNGS 2007 physics run, 8 1017 protons on target delivered ( 2% of a nominal CNGS year )
Single event upsets in ventilation electronics caused ventilation control failure and interruption of communication
Predicted dose levels
[in agreement with measurements]
[L. Sarchiapone, A. Ferrari]

## Slide 38
ELECTRONICS FAILURES [II]
collimator controls

## Slide 39
MAIN RADIATION EFFECTS ON ELECTRONICS
 |  |  | relevant physical quantity the effect is scaling with
Single Event effects (Random in time) | Single Event Upset (SEU) | Memory bit flip (soft error) Temporary functional failure | High energy hadron fluence [cm-2] (but also thermal neutrons!)
 | Single Event Latchup (SEL) | Abnormal high current state Permanent/destructive if not protected | High energy hadron fluence [cm-2]
Cumulative effects (Long term) | Total Ionizing Dose (TID) | Charge build-up in oxide Threshold shift & increased leakage current Ultimately destructive | Ionizing dose [Gy]
 | Displacement damage | Atomic displacements Degradation over time Ultimately destructive | Silicon 1 MeV-equivalent neutron fluence [cm-2] {NIEL -> DPA}

## Slide 40
HOW HIGH ENERGY HADRONS?
28Si(n,xa) cross section
5 MeV
>20 MeV
plus

## Slide 41
MITIGATION/PREVENTION STRATEGY
design shielding
relocate
identify forbidden regions
install radiation resistant equipment
CNGS radiation issues solved
during shutdown 2007-2008
2007
2008
< 106 heh/cm2
107  109 heh/cm2
high energy hadron fluence
per nominal CNGS year
[L. Sarchiapone, A. Ferrari]

## Slide 42
FACILITY SHIELDING DESIGN
For radiation protection purposes, depending on the aspects to be considered,
particle fluence in a given location is transformed into effective dose or ambient dose equivalent (Sv)
through the use of respective sets of conversion coefficients, which are a function of particle type and energy.
Prompt dose equivalent outside a radiation facility, reflecting the relevant radiation level in a public space during normal or accidental operation of the facility, is the quantity to minimize below acceptable limits.
top view of the ISR tunnel on the side of the n_TOF EAR-2 vertical beam line
(for neutrons from 1.6 1012 Hz 20 GeV/c protons on lead)
with default* shielding
* 80 cm thick 2m high concrete block
† triple concrete volume + two iron plates
with improved† shielding
0.5 μSv/h classification limit
[I. Bergström, V. Vlachoudis, J. Vollaire]

## Slide 43
10B (n,a)
tot
el
HADRON (NEUTRON) ATTENUATION
high energy
“disappearing” by non-elastic reactions
through dense (and cheap) materials
iron
low energy neutrons
slowed down by elastic scattering
through hydrogen-rich materials
and once thermalized
absorbed by neutron capture (n,g) or
borated polyethylene

## Slide 44
PHOTON ATTENUATION
Compton dominated
Compton dominated
Photoelectric dominated
Photoelectric dominated
Pair dominated
Pair dominated

## Slide 45
DELAYED RADIATION FROM RADIOACTIVE DECAY
Bateman equations
production
rate
growth by parent decay
decay
which are solved for a given irradiation profile at different cooling times
…
…
1h
8h
1d
7d
etc.
I, Dt
0, Dt
In, (Dt)n
yielding (specific) activities [Bq(/g)] – to be compared to legal exemption limits –
and residual dose rates [uSv/h] by the decay radiation (mainly electromagnetic)

## Slide 46
ACTIVITY BENCHMARKING
500 MeV/n 238U beam on Cu
[E. Mustafin et al., EPAC 2006, TUPLS141, 1834]

## Slide 47
RESIDUAL DOSE RATE EVOLUTION
tcool < 2 hours :
11C (b+, t1/2 = 20min)
2 hours < tcool < 2 days :
24Na (b-g, t1/2 = 15h)
[M. Brugger et al.,
Radiat. Prot. Dosim. 116 (2005) 12-15]
A benchmarking experiment at CERF: Irradiation of samples of different materials in the stray particle field created by
the interaction of a 120 GeV positively charged hadron beam in a copper target
t
current
instantaneous lumi
accumulated intensity
integrated lumi
short-lived isotopes (~ low Z)
long-lived isotopes (~ high Z)

## Slide 48
RESIDUAL DOSE RATE MAPS
SM
@ 40 cm
SM
HL-LHC final focus triplet around ATLAS and CMS 900fb-1 between Long Shutdowns
[C. Adorisio and S. Roesler,
HL-LHC TC, Sep 30, 2014]

## Slide 49
INTERVENTION PLAN
dose per action (mSv) | individual dose (mSv)
290 | 145
103 | 
48 | 427
138 | 
206 | 
206 | 
206 | 
48 | 
155 | 258
Collective Dose 1.4 mSv
4 months cooling time
team | # person | action | distance from the beam pipe | duration (minutes)
T0 | 2 | Valve investigation | 400 mm | 60
A | 1 | Jacket and cabling removal | in contact | 30
B | 2 | Pneumatic system disconnection | 400 mm | 10
B | 2 | Flanges disconnection | in contact | 20
B | 2 | Valve removal | in contact | 30
B | 2 | Valve re-installation | in contact | 30
B | 2 | Flanges reconnection | in contact | 30
B | 2 | Pneumatic system reconnection | 400 mm | 10
A | 1 | Jacket and cabling installation | in contact | 45
valve exchange in the TAS-Q1 region at 22m from the collision point
limit of 6 or 20 mSv/y depending on the worker category
with optimization threshold of 100 uSv/y and design criterion requiring not to surpass 2 mSv per intervention/year
[C. Adorisio and S. Roesler,
HL-LHC TC, Sep 30, 2014]
[work example by C. Garion]

## Slide 50
OPTIMIZATION PRINCIPLES
Material choice
  Low activation properties to reduce residual doses and minimize radioactive waste
  Avoid materials for which no radioactive waste elimination pathway exists (e.g., highly flammable metallic activated waste)
  Radiation resistant
Optimized handling
  Easy access to components that need manual intervention (e.g., valves, electrical connectors) or complex manipulation (e.g., cables)
  Provisions for fast installation/maintenance/repair, in particular, around beam loss areas (e.g., plugin systems, quick-connect flanges, remote survey, remote bake-out)
  Foresee easy dismantling of components
Limitation of installed material
  Install only components that are absolutely necessary, in particular in beam loss areas
  Reduction of radioactive waste
[C. Adorisio and S. Roesler,
R2E and Availability Workshop, Oct 16, 2014]

## Slide 51
AIR ACTIVATION
The activity of an air radioisotope (7Be, 11C, 13N, 15O, 38Cl, 39Cl, etc.) in the irradiation area
at the end of the irradiation period T is
where is the relative air exchange rate during irradiation,
i.e. the fraction of the air volume renewed per unit time
and is the saturation activity
irradiated air volume
differential fluence rate of (hadron) particles (P=p,n,p±)
production cross section
air atom density (T=12C,14N,16O,40Ar)
Amount of activity released into atmosphere all along the irradiation period
( is the time taken by the air flux to reach the release point from the irradiated area)
Amount of activity released into atmosphere after the end of the irradiation
( and as and but referring to the shutdown period)