## Slide 1: Recap of longitudinal beam dynamics. RF gymnastics
E. Shaposhnikova (CERN)
29 October 2019
Joint US-CERN-Japan-Russia School on Ion Colliders
28 October – 7 November 2019
Dubna, Russia

## Slide 2: Outline
Acceleration
Longitudinal beam dynamics
  Equations of motion
  Longitudinal phase space
RF gymnastics/manipulations
  CERN ion complex
  Bunch rotation, bunch shaping, controlled emittance blow-up, bunch splitting, momentum slip-stacking
Bibliography

## Slide 3: Acceleration

## Slide 4: Electromagnetic force
We characterize a particle by charge q = eZ and rest mass m0
The Lorentz force acting on a particle with charge q
acceleration bending (steering)
+ focusing by
  quadrupole magnets in transverse planes
  the same electro-magnetic field in longitudinal plane
  * Exceptions exist, have you heard about an RFQ?

## Slide 5: Relativistic kinematics. Reminder
Total particle energy:
rest energy E0 = m0c2
momentum p =m0 βcγ
normalised velocity β = v/c
relativistic factor
Particle energy can also be expressed as E = m0c2 + Ekin,
where Ekin = m0c2(γ -1) is kinetic energy
Acceleration provides kinetic energy to the charged particle

## Slide 6: Acceleration
Energy gain of a particle from the electric field Ez
∆E = eZEz (r,z,t)dz = eZ V, V is a potential
→ Energy and particle mass are expressed in [eV]: it is the energy which electron or proton gains in a potential of 1 Volt. Particle momentum is measured in [eV/c]
Acceleration by DC devices is limited
to ~ 20 MeV (insulation, …)
→ Use varying/oscillating field!
CERN proton accelerators (Ekin)
Linac4 160 MeV (106 eV)
PSB 2 GeV (109 eV)
PS 25 GeV
SPS 450 GeV
LHC 6.5 TeV (1012 eV)
Particle mass
electron m0 = 0.511 MeV
proton m0 = 938 MeV
ion m0 = A mu
mu = 931 MeV for nucleon
(A - atomic number)

## Slide 7: Acceleration: energy gain (1/2)
(1) Induction acceleration
This is the principle of betatron.
The first PhD project (R. Wideroe, 1927) for betatron
was rejected.
In 1928 achieved 50 keV acceleration of K+ ions with 25 kV
voltage at 1 MHz using alternating (rf) field.
The effect (called also “betatron voltage”) exists in other circular accelerators, but is small in comparison with external accelerating voltage
Rolf Wideroe (U. of Aachen)

## Slide 8: Acceleration: energy gain (2/2)
(2) Alternating electrical (rf) field Ez = E0 sinωrft = E0 sin φ(t)
Single beam passage → linear accelerator
Beam - RF field synchronism at low energy is achieved by varying the drift tube length
Multiple beam passages → circular accelerator!
Energy gain ∆E = q V T sin φ, where is a transit time factor in a gap of length g and . T describes reduction of acceleration efficiency due to finite velocity of a particle .

## Slide 9: Circular accelerator
The bending magnetic field B compensates the centrifugal force F
Magnetic rigidity of a particle with momentum p = mv = m0 cβγ is
During acceleration (increase in momentum p)
one needs to change either
ρ → cyclotron or
B → synchrotron
There are other schemes: synchrocyclotron, microtron, …
CERN PS
B - the total integrated dipole magnetic field
ρ - bending radius

## Slide 10: Cyclotron
Cyclotron:
Cyclotron frequency ωc = β c/ρ = qB/(m0 γ) decreases with energy
B and ωRF are constant
→ Synchronism: ωc = ωRF works only for β <<1 (γ ~ 1)
Synchrocyclotron: ωRF ~ 1/γ – decreases with energy (time)
Isochronous cyclotron: athimuthal varying B field
Limited to a few hundreds of MeV/u.

## Slide 11: Synchrotron. Synchronous particle
Design momentum follows the magnetic field variation
Corresponding particle has revolution period
A particle synchronised with RF frequency ωRF = h ω0 is called synchronous particle, its energy gain per turn is
where φs is synchronous phase, h harmonic number.
The acceleration rate of synchronous particle
→ No acceleration, if φs = 0 or π.
Longitudinal motion → synchrotron motion
ps = q Bρ.
Constant orbit during acceleration → B and ωRF increase synchronously.
(R – average machine radius)
and angular revolution frequency ω0 = 2π f0 = 2π/T0

## Slide 12: Synchrotron: LHC magnetic cycle
Design value 7 TeV
Operational 6.5 TeV
Magnetic field B(t) or momentum program

## Slide 13: Synchrotron: RF frequency program
The RF frequency fRF should follow the magnetic field variation due to change in revolution frequency.
Indeed
and
Since E/c = (E02 /c2 +p2)1/2 we have
Here ps(t) = q ρ B(t)
RF frequency programs in LHC
for proton and Pb ion beams
What about the corresponding RF voltage program V(t)?

## Slide 14: Longitudinal beam dynamics

## Slide 15: Non-synchronous particle. First equation of longitudinal motion
Non-synchronous particle with parameters ω, φ, p, E has small deviations ∆ω, ∆φ, ∆p, ∆E from corresponding parameters ω0, φs, ps, Es of the synchronous particle (defined earlier).
The energy gain for this particle is qV0 sinφ, where φ = φs + ∆φ
and acceleration rate
Subtracting similar equation for synchronous particle we obtain
→ This is our 1st equation of longitudinal motion

## Slide 16: Non-synchronous particle. Dispersion effects
Non-synchronous particle with momentum p = mβcγ has different velocity and also, due to the dispersion (Dx) of the ring lattice, orbit length. The latter effect is described by momentum compaction factor
The deviation in revolution frequency ω0 = βc/R
with slip factor (careful for definition!)
→ Transition energy crossing at (Qx - horizontal tune).
For a particle with δp > 0 has a longer revolution period T0 = 2π/ω0 → ”negative mass”?
(αc = = <Dx> /ρ)

## Slide 17: Second equation of particle motion
The phase of any particle relative to the RF voltage is ,
where its azimuthal position .
Then
Now, using the definition of η,
the 2nd equation of longitudinal motion is

## Slide 18: Phase equation. Small amplitude oscillations
Combining two equations of motion in conjugate variables
and assuming slow time-variation of E, ω0, η, we obtain phase equation:
For small amplitude particles with ∆φ = φ – φs < 1
(since = →
&
With frequency of linear synchrotron oscillations

## Slide 19: Small amplitude oscillations. Phase stability
For phase stability:
No acceleration:
for
for
→ Equation of a harmonic oscillator
Solutions:
=
= = -
where Ψ = – synchronous angle,
- amplitude of phase oscillations

## Slide 20: Phase equation. Large amplitude oscillations
The phase equation can be re-written as
Multiplying both sides by and integrating over t, we obtain an integral of motion
with RF potential
Phase trajectories are described by
Ꜫ
voltage
potential
φs = π
φs = π
separatrix
φs = π

## Slide 21: Hamiltonian of longitudinal motion
Using conjugate variables φ and ∆E/(hω0), the equations of longitudinal motion can be also presented as
and ,
with the Hamiltonian
where potential for a single RF system was defined as
It can be easily generalised for more RF systems (with different harmonic numbers h) and even induced voltage (collective effects).

## Slide 22: Acceleration. Separatrix
Phase stability
deceleration
Potential well for
φs = π – π/18
acceleration
Potential
∆E = 0 at extremes of potential: W’(φ) = V(φ) = 0
→ sinφ = sinφs has 2 solutions:
- φ1 = φs + 2πk (k=0, 1,... h-1) - stable fixed point
- φ2 = π – φs + 2πk – unstable fixed point
the 2nd turning point is φm defined by
W(φm) = W(φ2) = W(π - φs)
φ2 = π/18
φm
φm
φ2
φs
Example:
The separatrix separates the bound oscillations from unbound

## Slide 23: Acceleration. Transition crossing
Direction of particle motion.
Since
→ φ increases
(for
∆E < 0 if η < 0
or
∆E > 0 if η > 0
Below transition:
Above transition:
[a.u]
→ RF phase jump (π - 2φs) needed during transition crossing
Potential well
φs = π – π/18
Potential well
φs = π/18

## Slide 24: Acceleration. RF bucket
The phase-space limited by the separatrix is the RF bucket:
Bucket area [eVs] (also longitudinal acceptance):
Bucket length [rad] is φm - (π - φs)
Bucket height (energy acceptance)
with synchrotron tune
φm
φ2 =
π – φs
φs
separatrix

## Slide 25: Longitudinal phase space. Longitudinal phase space. Bucket area
No energy gain → sinφs = 0 and
W(φ) = cosφ (for ). Then
The bucket area
is reduced due to acceleration by a factor which approximately is
uncaptured
particles
Stationary case. No acceleration
Note, that A = 0 for φs = π/2.
Bucket area should be sufficient to accommodate a given bunch

## Slide 26: Longitudinal phase space. Bunch emittance
Particles usually fill some part of the bucket, a bunch
There can be up to h = ωRF/ω0 bunches in the ring
Longitudinal emittance [eVs] is the area inside the limiting phase trajectory
Here W(φL ) = W(φR).
For ions units are [eVs/charge]
∆φ
Bunch length [rad] ∆φ = φL - φR
and in [s] τ = ∆φ/(hω0)
bunch

## Slide 27: Longitudinal bunch emittance
Ratio
(no acceleration)
Phase trajectory (reminder)
For non-accelerating bucket: φL - φR = 2φb
and bunch emittance is
Short-bunch approximation
/
φb
→ Short-bunch approximation
should be used with caution
for φb > 1

## Slide 28: Adiabaticity: why it is important?
During beam acceleration, the Hamiltonian H of the system depends on time. If changes are slow enough (adiabatic), H is considered to be quasi-static.
The parameter λ changes adiabatically if where T is a period.
Applying for the synchrotron motion
Adiabatic invariant of motion (action)
→ Longitudinal bunch emittance is an invariant of motion during acceleration and RF manipulations, if parameter change is adiabatic.
During acceleration, voltage program should be designed to keep a certain filling factor (< 90%) of the bucket area for a given bunch emittance

## Slide 29: Energy loss
Even without acceleration the average energy of particles may change due to synchrotron radiation, induced voltage, electron cloud…
Energy lost by a particle per turn ∆E = U0 is compensated by the RF system
→ Bucket becomes accelerating with B = const.
→ Damping of synchrotron oscillations
Synchrotron radiation at LHC flat top:
U0 = 7 keV for protons and for 208Pb82+ ions it is
larger!
Damping time is also smaller!
→ 6.3 h for longitudinal emittance
U0 = q V sinφs
Phase trajectories of lost particles on LHC flat top
V = 16 MV, 400 MHz

## Slide 30: Synchrotron frequency
Oscillation amplitude φb [rad]
Due to non-linearity of RF voltage
all particles oscillate with different frequencies ωs = 2π fs , which depend on amplitude of oscillations.
Since
the period of synchrotron oscillations is
=
For non-accelerating bucket
K(x) is the complete elliptical integral of the 1st kind
Ts → ∞

## Slide 31: Discrete equations. Mapping/particle simulations
Discrete equations of longitudinal particle motion in (∆t, ∆E) canonical coordinates at revolution turn (n+1) with general RF system and induced voltage
Index “0” refers to design values, including reference time
These equations can be written in the form of the symplectic mapping from a point {∆t(n), ∆E(n)} to {∆t(n+1), ∆E(n+1)} preserving the phase space area.
Open-source simulation code BLonD developed in RF group at CERN (all types of particles, RF manipulations, RF loops and feedbacks): http://blond.web.cern.ch

## Slide 32: Rf Manipulations

## Slide 33: LHC ion beam at CERN
 | State of lead ion | Energy [GeV/u]
Linac3 | 27+ | 0.0042
LEIR | 54+ | 0.0722
PS | 54+ | 5.9
SPS | 82+ | 176.4
LHC | 82+ | 2759
Ions accelerated for the collider physics in LHC: Pb, Xe
More ions for the fixed-target physics in all CERN accelerators

## Slide 34: LHC ion beam production scheme
LEIR
Multi-turn injection
Adiabatic RF capture
into 2 bunches
PS
Batch expansion
Bunch splitting
Batch expansion
SPS
Multiple injections with 150 ns batch spacing
Momentum slip stacking at high energy (50 ns bunch spacing → 100 ns)
LHC
bunches
2
2
4
28 + 28
56
1256
LEIR

## Slide 35: Ion beam production at CERN
RF manipulations used for LHC ions in injector chain
  Rebunching - LEIR
  Bunch shaping (double RF operation) – LEIR
  Bunch splitting - PS
  Batch compression/expansion – PS
  Controlled emittance blow-up - PS
  Bunch rotation - SPS in future (2021)
  Fixed frequency acceleration - SPS
  Momentum slip-stacking - SPS (2021)
Even more for the proton beams…

## Slide 36: RF gymnastics for Pb ion beam in CERN PS
Batch compression
(2018)
Batch expansion.
Bunch splitting
Batch compression
(< 2015)
2 bunches at 200 ns → 4 bunches at 100 ns
2 bunches at 200 ns →
2 bunches at 100 ns
3 bunches at 100 ns → 3 bunches at 75 ns
Voltage at the next harmonic h is adiabatically increased and then the initial one is decreased. For 2 bunches in the ring, it works without intermediate steps in h.

## Slide 37: Controlled longitudinal emittance blow-up
  Some possible methods (used at CERN):
  Coloured (band-limited) phase noise (for protons during ramp in PSB, SPS and LHC, also for ions in LHC and planned in SPS)
  Deliberate bunch to bucket mismatch (in phase or energy) – the simplest but not always well controlled, used at injection and during transition crossing (SPS)
  Phase modulation of the main (in LHC during physics) or of the higher harmonic RF system (PS)

## Slide 38: Controlled emittance blow-up by band-limited noise
Noise-band frequencies
fup -- to cover bunch centre
fdown – for target emittance
Emittance blow-up in the CERN PSB.
Synchrotron frequency distribution
Similar technique is applied in SPS and also in LHC, with bunch-length feedback acting on strength of excitation.

## Slide 39: Phase error/shift
PSB - PS bunch transfer.
90 deg injection error
In hadron accelerators beam phase loop keeps bunch locked to the RF phase to avoid uncontrolled emittance blow-up
→ Large (intentional emittance blow-up at transition crossing
Average bunch length of ion beam during acceleration in SPS

## Slide 40: Voltage mismatch. Bunch rotation
Bunch matched to bucket
Mismatched → rotation
Sharp increase of RF voltage → used for bunch compression (at Ts0/4)
Less voltage needed than with adiabatic voltage increase
(after bunch rotation instead of )

## Slide 41: Bunch rotation. Jump to unstable phase
(1) Jump to unstable phase (fixed point) to stretch the bunch
(2) Jump back to stable phase and continue the rotation

## Slide 42: Fixed-frequency acceleration of ion beam in the SPS
During lead ion acceleration with constant harmonic number h, the RF frequency frf = h f0 changes from 198.51 MHz to 200.39 MHz
The tuning range of the 200 MHz TW cavities is (199.5 - 200.4) MHz
The LHC ion beam occupies only a part of the ring (6.6 μs out of 23.1 μs)
Cavity-amplifier rise time ~ 1μs
Switch to the constant harmonic number acceleration, when frf is inside the cavity bandwidth
→ Use non-integer harmonic number (D. Boussard et al., 1989): pulse cavity at the centre cavity frequency during beam passage and switch it off in the beam gap to correct the RF phase for the next beam passage

## Slide 43: Momentum slip-stacking of ion beam in the SPS
MSS is extensively used in Fermilab.
Usually performed at B0 = const
→ Change in phase or “drifting” per T0
Slip-stacking parameter:
At α = 4 the two separatrices touch.
→ Keep α > 4 to reduce perturbation.
ωRF1(t)
ωRF2(t)
Two independently controlled 200 MHz RF systems with large frequency bandwidth.
Radial displacement of two beams.

## Slide 44: Particle simulations of ion beam in the SPS. Momentum slip-stacking and bunch rotation
Should work in 2021 to obtain the design ion luminosity in HL-LHC!

## Slide 45
Bibliography
G. Dome, Theory of RF acceleration, CAS 1985, CERN 87-03
S. Y. Lee, Accelerator physics, World Scientific, 1999
LHC Design Report, CERN-2004-003, 2004
Acknowledgements
T. Argyropoulos
H. Damerau
V. Kain
D. Quartullo
F. Tecker
Thank you for your attention!

## Slide 46: Accelerators used for ions
Linear Accelerators (LINAC):
  Linac3 (CERN), ATLAS (ANL), FRIB (MSU), UNILAC (GSI),…
Cyclotrons: easy to operate and tune; used for isotope production, but limited to a few hundreds of MeV/u
  RIKEN RIBP, HRIBP (pd), TRIMF (pd), NSCL, GANIL; U400, U400M, IC100 and DC130, DC280 in JINR Dubna
  *pd – proton driver
Synchrotrons
  SIS18 @GSI; LEIR, PS, SPS, LHC @CERN; RHIC@BNL, NICA @ JINR