## Slide 1: Injection and extraction
Introductory slides:
  Kickers, septa and normalised phase-space
Injection methods
  Single-turn hadron injection
  Injection errors, filamentation and blow-up
  Multi-turn hadron injection
  Charge-exchange H- injection
  Lepton injection
Extraction methods
  Single-turn (fast) extraction
  Non-resonant and resonant multi-turn (fast) extraction
  Resonant multi-turn (slow) extraction
Verena Kain, CERN (BE-OP-SPS)
based on lectures by B. Goddard and M. Fraser

## Slide 2: Injection and extraction
An accelerator has limited dynamic range
Chain of stages needed to reach high energy
Periodic re-filling of storage rings, like LHC
External facilities and experiments:
  e.g. ISOLDE, HIRADMAT, AWAKE…
Beam transfer (into, out of, and between machines) is necessary.
CERN Accelerator Complex
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 3: Kicker magnet
I
Ferrite
B
g
B = μ0I / g
L [per unit length] = μ0w / g
dI/dt = V / L
Typically 3 kA in 1 μs rise time
w
Pulsed magnet with very fast rise time
(100 ns – few μs)
Ferrite
Conductors
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 4: Magnetic septum
Yoke
Septum coil
I
Bo = μ0I / g
Typically I 5 - 25 kA
Pulsed or DC magnet with thin (2 – 20 mm)
septum between zero field and high field region
Typically ~10x more deflection given by magnetic septa, compared to kickers
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 5: Electrostatic septum
E0
E=0
High voltage
electrode
Hollow earth
electrode
Thin wire or
foil (~0.1 mm)
High voltage
electrode
Hollow earth
electrode
Septum wires
E = V / g
Typically V = 200 kV
E = 100 kV/cm
g
DC electrostatic device with very thin septum between zero field and high field region
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 6: Normalised phase space
x(s)
x’(s)
Area = pe
Area = pe

Real phase space
Normalised phase space
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 7: Single-turn injection – same plane
Septum magnet
Kicker magnet
Septum deflects the beam onto the closed orbit at the centre of the kicker
Kicker compensates for the remaining angle
Septum and kicker either side of D quad to minimise kicker strength
F-quad
t
kicker field
intensity
injected
beam
‘boxcar’ stacking
Injected beam
Circulating beam
D-quad
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 8: Single-turn injection
Normalised phase space at centre of idealised septum
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 9: Single-turn injection
septum
Normalised phase space at centre of idealised septum
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 10: Single-turn injection
Normalised phase space at centre of idealised septum
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 11: Single-turn injection
μ/2 phase advance to kicker location
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 12: Single-turn injection
Kicker deflection places beam on central orbit:
Normalised phase space at centre of idealised kicker
kicker
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 13: Injection oscillations
kicker - Δ
For imperfect injection the beam oscillates around the central orbit,
e.g. kick error, Δ:
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 14: Injection oscillations
After 1 turn…
For imperfect injection the beam oscillates around the central orbit,
e.g. kick error, Δ:
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 15: Injection oscillations
After 2 turns…
For imperfect injection the beam oscillates around the central orbit,
e.g. kick error, Δ:
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 16: Injection oscillations
After 3 turns etc…
For imperfect injection the beam oscillates around the central orbit,
e.g. kick error, Δ:
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 17: Injection oscillations
Betatron oscillations with respect to the Closed Orbit:
Transfer line
LHC (first turn)
Horizontal
Vertical
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 18: Filamentation
Non-linear effects (e.g. higher-order field components) introduce amplitude-dependent effects into particle motion
Over many turns, a phase-space oscillation is transformed into an emittance increase
So any residual transverse oscillation will lead to an emittance blow-up through filamentation
  Chromaticity coupled with a non-zero momentum spread at injection can also cause filmentation, often termed chromatic decoherence
  “Transverse damper” systems are used to damp injection oscillations - bunch position measured by a pick-up, which is linked to a kicker
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 19: Filamentation
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 20: Filamentation
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 21: Filamentation
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 22: Filamentation
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 23: Filamentation
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 24: Filamentation
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 25: Filamentation
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 26: Filamentation
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 27: Filamentation
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 28: Filamentation
ABT Introductory Lectures – CERN Accelerator School, Constanta, Romania, 2018

## Slide 29: Filamentation
Residual transverse oscillations lead to an effective emittance blow-up through filamentation:
Injection oscillation
Reference closed orbit
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 30: Multi-turn injection
For hadrons the beam density at injection can be limited either by space charge effects or by the injector capacity
If we cannot increase charge density, we can sometimes fill the horizontal phase space to increase overall injected intensity.
  If the acceptance of the receiving machine is larger than the delivered beam emittance we can accumulate intensity
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 31: Multi-turn injection for hadrons
Septum magnet
No kicker but fast programmable bumpers
Bump amplitude decreases and a new batch injected turn-by-turn
Phase-space “painting”
Programmable closed orbit bump
Varying amplitude bump
Injected beam
(usually from a linac)
Circulating beam
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 32: Multi-turn injection for hadrons
Turn 1
Septum
Example: CERN PSB injection, high intensity beams, fractional tune Qh ≈ 0.25 Beam rotates π/2 per turn in phase space
On each turn inject a new batch and reduce the bump amplitude
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 33: Multi-turn injection for hadrons
Turn 2
Septum
Example: CERN PSB injection, high intensity beams, fractional tune Qh ≈ 0.25 Beam rotates π/2 per turn in phase space
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 34: Multi-turn injection for hadrons
Turn 3
Septum
Example: CERN PSB injection, high intensity beams, fractional tune Qh ≈ 0.25 Beam rotates π/2 per turn in phase space
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 35: Multi-turn injection for hadrons
Turn 4
Septum
Example: CERN PSB injection, high intensity beams, fractional tune Qh ≈ 0.25 Beam rotates π/2 per turn in phase space
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 36: Multi-turn injection for hadrons
Turn 5
Septum
Example: CERN PSB injection, high intensity beams, fractional tune Qh ≈ 0.25 Beam rotates π/2 per turn in phase space
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 37: Multi-turn injection for hadrons
Turn 6
Septum
Example: CERN PSB injection, high intensity beams, fractional tune Qh ≈ 0.25 Beam rotates π/2 per turn in phase space
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 38: Multi-turn injection for hadrons
Turn 7
Septum
Example: CERN PSB injection, high intensity beams, fractional tune Qh ≈ 0.25 Beam rotates π/2 per turn in phase space
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 39: Multi-turn injection for hadrons
Turn 8
Septum
Example: CERN PSB injection, high intensity beams, fractional tune Qh ≈ 0.25 Beam rotates π/2 per turn in phase space
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 40: Multi-turn injection for hadrons
Turn 9
Septum
Example: CERN PSB injection, high intensity beams, fractional tune Qh ≈ 0.25 Beam rotates π/2 per turn in phase space
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 41: Multi-turn injection for hadrons
Turn 10
Septum
Example: CERN PSB injection, high intensity beams, fractional tune Qh ≈ 0.25 Beam rotates π/2 per turn in phase space
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 42: Multi-turn injection for hadrons
Turn 11
Septum
Example: CERN PSB injection, high intensity beams, fractional tune Qh ≈ 0.25 Beam rotates π/2 per turn in phase space
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 43: Multi-turn injection for hadrons
Turn 12
Septum
Example: CERN PSB injection, high intensity beams, fractional tune Qh ≈ 0.25 Beam rotates π/2 per turn in phase space
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 44: Multi-turn injection for hadrons
Turn 13
Septum
Example: CERN PSB injection, high intensity beams, fractional tune Qh ≈ 0.25 Beam rotates π/2 per turn in phase space
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 45: Multi-turn injection for hadrons
Turn 14
Septum
Example: CERN PSB injection, high intensity beams, fractional tune Qh ≈ 0.25 Beam rotates π/2 per turn in phase space
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 46: Multi-turn injection for hadrons
Turn 15
In reality, filamentation (often space-charge driven) occurs to produce a quasi-uniform beam
Phase space has been “painted”
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 47: Charge exchange H- injection
Multi-turn injection is essential to accumulate high intensity
Disadvantages inherent in using an injection septum:
  Width of several mm reduces aperture
  Beam losses from circulating beam hitting septum:
    typically 30 – 40 % for the CERN PSB injection at 50 MeV
  Limits number of injected turns to 10 - 20
Charge-exchange injection provides elegant alternative
  Possible to “cheat” Liouville’s theorem, which says that emittance is conserved….
  Convert H- to p+ using a thin stripping foil, allowing injection into the same phase space area
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 48: Charge exchange H- injection
H- beam
Injection chicane dipoles
Circulating p+
p+
Stripping foil
H0
H-
Circulating p+
Start of injection process
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 49: Charge exchange H- injection
Circulating p+
Stripping foil
End of injection process with painting
H- beam
p+
H0
H-
Injection chicane dipoles
Displace orbit
Circulating p+
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 50: Accumulation process on foil
V. Forte, Performance of the CERN PSB at 160 MeV with H- charge exchange injection, PhD thesis – CERN and Université Blaise Pascal
Linac4 connection to the PS booster at 160 MeV:
  H- stripped to p+ with an estimated efficiency ≈98 % with C foil 200 μg.cm-2
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 51: Charge exchange H- injection
Paint uniform transverse phase space density by modifying closed orbit bump and steering injected beam
Foil thickness calculated to double-strip most ions (≈99%)
  50 MeV – 50 μg.cm-2
  800 MeV – 200 μg.cm-2 (≈ 1 μm of C!)
Carbon foils generally used – very fragile
Injection chicane reduced or switched off after injection, to avoid excessive foil heating and beam blow-up
Longitudinal phase space can also be painted turn-by-turn:
  Variation of the injected beam energy turn-by-turn (linac voltage scaled)
  Chopper system in linac to match length of injected batch to bucket
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 52: H- injection - painting
Time
x’ vs x
y’ vs y
y vs x
Note injection into same phase space area as circulating beam
≈100 turns
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 53: Lepton injection
Single-turn injection can be used as for hadrons; however, lepton motion is strongly damped (different with respect to proton or ion injection).
  Synchrotron radiation
    see Electron Beam Dynamics lectures by L. Rivkin
Can use transverse or longitudinal damping:
  Transverse - Betatron accumulation
  Longitudinal - Synchrotron accumulation
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 54: Betatron lepton injection
Beam is injected with an angle with respect to the closed orbit
Injected beam performs damped betatron oscillations about the closed orbit
Septum magnet
Closed orbit bumpers or kickers
Injected beam
Circulating
beam
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 55: Betatron lepton injection
Injected bunch performs damped betatron oscillations
In LEP at 20 GeV, the damping time was about 6’000 turns (0.6 seconds)
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 56: Synchrotron lepton injection
Septum magnet
Beam injected parallel to circulating beam, onto dispersion orbit of a particle having the same momentum offset Δp/p
Injected beam makes damped synchrotron oscillations at Qs but does not perform betatron oscillations
Closed orbit bumpers or kickers
Bumped circulating beam
xs = Dx · Δp/p0
xs
p = p0
p = p0 + Δp
Inject an off-momentum beam
Injected beam
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 57: Synchrotron lepton injection
F
E
Double batch injection possible….
Longitudinal damping time in LEP was ~3’000 turns (2x faster than transverse)
Injection 1 (turn N)
Injection 2 (turn N + Qs/2)
Stored beam
RF bucket
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 58: Synchrotron lepton injection in LEP
Synchrotron injection in LEP gave improved background for LEP experiments due to small orbit offsets in zero dispersion straight sections
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 59: Injection - summary
Several different techniques using kickers, septa and bumpers:
  Single-turn injection for hadrons
    Boxcar stacking: transfer between machines in accelerator chain
    Angle / position errors  injection oscillations
    Uncorrected errors  filamentation  emittance increase
  Multi-turn injection for hadrons
    Phase space painting to increase intensity
    H- injection allows injection into same phase space area
  Lepton injection: take advantage of damping
    Less concerned about injection precision and matching
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 60: Extraction
Different extraction techniques exist, depending on requirements
  Fast extraction: ≤1 turn
  Non-resonant (fast) multi-turn extraction: few turns
  Resonant low-loss (fast) multi-turn extraction: few turns
  Resonant multi-turn extraction: many thousands of turns
Usually higher energy than injection  stronger elements (∫B.dl)
  At high energies many kicker and septum modules may be required
  To reduce kicker and septum strength, beam can be moved near to septum by closed orbit bump
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 61: Fast single turn extraction
Septum magnet
Kicker magnet
Bumpers move circulating beam close to septum to reduce kicker strength
Kicker deflects the entire beam into the septum in a single turn
Most efficient (lowest deflection angles required) for π/2 phase advance between kicker and septum
Closed orbit bumpers
    Entire beam kicked into septum gap and extracted over a single turn
Extracted beam
F-quad
D-quad
Circulating
beam
t
kicker field
intensity
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 62: Fast single turn extraction
For transfer of beams between accelerators in an injector chain
For secondary particle production
  e.g. neutrinos, radioactive beams
Losses from transverse scraping or from particles in extraction gap:
  Fast extraction from SPS to CNGS:
Particles in SPS extraction kicker rise- and fall-time gaps
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 63: Multi-turn extraction
Some filling schemes require a beam to be injected in several turns to a larger machine…
And very commonly Fixed Target physics experiments and medical accelerators often need a quasi-continuous flux of particles…
Multi-turn extraction…
  Fast: Non-resonant and resonant multi-turn ejection (few turns) for filling
    e.g. PS to SPS at CERN for high intensity proton beams (>2.5 1013 protons)
  Slow: Resonant extraction (ms to hours) for experiments
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 64: Non-resonant multi-turn extraction
Extracted beam
Bumped circulating beam
Magnetic
septum
Fast bumper deflects the whole beam onto the septum
Beam extracted in a few turns, with the machine tune rotating the beam
Intrinsically a high-loss process: thin septum essential
Often combine thin electrostatic septa with magnetic septa
Fast closed orbit bumpers
    Beam bumped to septum; part of beam ‘shaved’ off each turn
Electrostatic septum
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 65: Non-resonant multi-turn extraction
Example system: CERN PS to SPS Fixed-Target ‘continuous transfer’.
  Accelerate beam in PS to 14 GeV/c
  Empty PS machine (2.1 μs long) in 5 turns into SPS
  Fill SPS machine (23 μs long)
  Quasi-continuous beam in SPS (2 x 1 μs gaps)
  Total intensity per PS extraction ≈ 3  1013 p+
  Total intensity in SPS ≈ 5  1013 p+
Extracted beam
beam
To the SPS
The PS
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 66: Non-resonant multi-turn extraction
CERN PS to SPS: 5-turn continuous transfer – 1st turn
Qh = 0.25
1 2 3 4 5
Bump vs. turn
1
2
3
4
5
septum
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 67: Non-resonant multi-turn extraction
CERN PS to SPS: 5-turn continuous transfer – 2nd turn
Qh = 0.25
1 2 3 4 5
Bump vs. turn
1
2
3
4
5
septum
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 68: Non-resonant multi-turn extraction
CERN PS to SPS: 5-turn continuous transfer – 3rd turn
Qh = 0.25
1 2 3 4 5
Bump vs. turn
septum
1
2
3
4
5
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 69: Non-resonant multi-turn extraction
CERN PS to SPS: 5-turn continuous transfer – 4th turn
Qh = 0.25
1 2 3 4 5
Bump vs. turn
septum
1
2
3
4
5
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 70: Non-resonant multi-turn extraction
CERN PS to SPS: 5-turn continuous transfer – 5th turn
Qh = 0.25
5
1 2 3 4 5
Bump vs. turn
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 71: Non-resonant multi-turn extraction
CERN PS to SPS: 5-turn continuous transfer
  Losses impose thin (ES) septum…
  …a second magnetic septum is needed
  Still about 15 % of beam lost in PS-SPS CT
  Difficult to get equal intensities per turn
  Different trajectories for each turn
  Different emittances for each turn
1
2
3
4
5
I
1
2
3
4
5
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 72: Resonant multi-turn (fast) extraction
Adiabatic capture of beam in stable “islands”
  Use non-linear fields (sextupoles and octupoles) to create islands of stability in phase space
  A slow (adiabatic) tune variation to cross a resonance and to drive particles into the islands (capture) with the help of transverse excitation (using damper)
  Variation of field strengths to separate the islands in phase space
Several big advantages:
  Losses reduced significantly (no particles at the septum in transverse plane)
  Phase space matching improved with respect to existing non-resonant multi-turn extraction - ‘beamlets’ have similar emittance and optical parameters
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 73: Resonant multi-turn (fast) extraction
Unperturbed beam
Increasing non-linear fields
Beam captured in stable islands
Islands separated and beam bumped across septum – extracted in 5 turns
(see Non-Linear Beam Dynamics lectures by Y. Papaphilippou)
Courtesy M. Giovannozzi: MTE Design Report, CERN-2006-011, 2006
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 74: Resonant multi-turn (fast) extraction
Septum wire
1 2 3 4 5
Bump vs. turn
Qh = 0.25
Unperturbed beam
Increasing non-linear fields
Beam captured in stable islands
Islands separated and beam bumped across septum – extracted in 5 turns
Courtesy M. Giovannozzi: MTE Design Report, CERN-2006-011, 2006
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 75: Resonant multi-turn (slow) extraction
Extracted beam
Bumped circulating beam -
particles moved across
septum by resonance
Slow bumpers move the beam near the septum
Tune adjusted close to nth order betatron resonance
Multipole magnets excited to define stable area in phase space, size depends on ΔQ = Q - Qr
Closed orbit bumpers
    Non-linear fields excite resonances that drive the beam slowly across the septum
Magnetic
septum
Electrostatic septum
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 76: Resonant multi-turn (slow) extraction
3rd order resonances – see lectures by Y. Papaphilippou
  Sextupole fields distort the circular normalised phase space particle trajectories.
  Stable area defined, delimited by unstable Fixed Points.
  Sextupole magnets arranged to produce suitable phase space orientation of the stable triangle at thin electrostatic septum
  Stable area can be reduced by…
    Increasing the sextupole strength, or…
    Fixing the sextupole strength and scanning the machine tune Qh (and therefore the resonance) through the tune spread of the beam
    Large tune spread created with RF gymnastics (large momentum spread) and large chromaticity
Rfp
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 77: Third-order resonant extraction
Particles distributed on emittance contours
ΔQ large – no phase space distortion
Septum wire
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 78: Third-order resonant extraction
Sextupole magnets produce a triangular stable area in phase space
ΔQ decreasing – phase space distortion for largest amplitudes
Septum wire
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 79: Third-order resonant extraction
Septum wire
Sextupole magnets produce a triangular stable area in phase space
ΔQ decreasing – phase space distortion for largest amplitudes
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 80: Third-order resonant extraction
Septum wire
Sextupole magnets produce a triangular stable area in phase space
ΔQ decreasing – phase space distortion for largest amplitudes
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 81: Third-order resonant extraction
Septum wire
Sextupole magnets produce a triangular stable area in phase space
ΔQ decreasing – phase space distortion for largest amplitudes
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 82: Third-order resonant extraction
Largest amplitude particle trajectories are significantly distorted
Locations of fixed points discernable at extremities of phase space triangle
Septum wire
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 83: Third-order resonant extraction
Septum wire
ΔQ small enough that largest amplitude particle trajectories are unstable
Unstable particles follow separatrix branches as they increase in amplitude
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 84: Third-order resonant extraction
Septum wire
Stable area shrinks as ΔQ becomes smaller
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 85: Third-order resonant extraction
Septum wire
Separatrix position in phase space shifts as the stable area shrinks
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 86: Third-order resonant extraction
As the stable area shrinks, the circulating beam intensity drops since particles are being continuously extracted
Septum wire
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 87: Third-order resonant extraction
Septum wire
As the stable area shrinks, the circulating beam intensity drops since particles are being continuously extracted
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 88: Third-order resonant extraction
Septum wire
As the stable area shrinks, the circulating beam intensity drops since particles are being continuously extracted
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 89: Third-order resonant extraction
Septum wire
As the stable area shrinks, the circulating beam intensity drops since particles are being continuously extracted
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 90: Third-order resonant extraction
Septum wire
As ΔQ approaches zero, the particles with very small amplitude are extracted
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 91: Third-order resonant extraction
Particle at turn 0
On resonance, sextupole kicks add-up driving particles over septum
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 92: Third-order resonant extraction
Particle at turn 1
On resonance, sextupole kicks add-up driving particles over septum
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 93: Third-order resonant extraction
Particle at turn 2
On resonance, sextupole kicks add-up driving particles over septum
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 94: Third-order resonant extraction
Particle at turn 3
On resonance, sextupole kicks add-up driving particles over septum
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 95: Third-order resonant extraction
On resonance, sextupole kicks add-up driving particles over septum
  Distance travelled in these final three turns is termed the “spiral step,” ΔXES
  Extraction bump trimmed in the machine to adjust the spiral step
Extracted beam
q
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 96: Third-order resonant extraction
On resonance, sextupole kicks add-up driving particles over septum
  Distance travelled in these final three turns is termed the “spiral step,” ΔXES
  Extraction bump trimmed in the machine to adjust the spiral step
RF gymnastics before extraction:
Extracted beam
q
momentum spread, tune
  Spill = 4.8 s
time
Schottky measurement during spill, courtesy of T. Bohl
Δϕ = π
Δϕ = -π
small Δp
rotation: large Δp
RF off
RF gymn.
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 97: Slow extraction channel: SPS
electrostatic septum (ES)
QFA
QDA
magnetic
septum (MST)
magnetic septum (MSE)
QFA
TPST
mask
extraction
bumper
To TT20
and NA
ES
circulating beam
extracted beam
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 98: Slow extracted spill quality
  Reducing DQ with main machine quadrupoles can be augmented with a ‘servo’ quadrupole, which can modulate DQ in a servo loop, acting on a measurement of the spill intensity
50 Hz
10 Hz
  A recent example of a spill at SPS to the North Area with large n x 50 Hz components and another noise source at 10 Hz
  The slow-extraction is a resonant process and it amplifies the smallest imperfections in the machine:
    e.g. spill intensity variations can be explained by ripples in the current of the quads (mains: n x 50 Hz) at the level of a few ppm!
    Injection of n x 50 Hz signals in counter-phase on dedicated quads can be used to compensate
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 99: Second-order resonant extraction
An extraction can also be made over a few hundred turns
2nd and 4th order resonances
  Octupole fields distort the regular phase space particle trajectories
  Stable area defined, delimited by two unstable Fixed Points
  Beam tune brought across a 2nd order resonance (Q → 0.5)
  Particle amplitudes quickly grow and beam is extracted in a few hundred turns
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 100: Resonant extraction separatrices
Amplitude growth for 2nd order resonance much faster than 3rd – shorter spills (≈milliseconds vs. seconds)
Used where intense pulses are required on target – e.g. neutrino production
3rd order resonant extraction
2nd order resonant extraction
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 101: Extraction - summary
Several different techniques:
  Single-turn fast extraction:
    for transfer between machines in accelerator chain, beam abort, etc.
  Non-resonant (fast) multi-turn extraction
    slice beam into equal parts for transfer between machine over a few turns.
  Resonant low-loss (fast) multi-turn extraction
    create stable islands in phase space: slice off over a few turns.
  Resonant (slow) multi-turn extraction
    create stable area in phase space  slowly drive particles into resonance  long spill over many thousand turns.
Thank you for your attention
ABT Introductory Lectures – JAS, Dubna, Russia, 2019

## Slide 102: Further reading and references
Lot’s of resources presented at the recent CAS Specialised School:
Beam Injection, Extraction and Transfer, 10-19 March 2017, Erice, Italy
https://cas.web.cern.ch/schools/erice-2017
ABT Introductory Lectures – JAS, Dubna, Russia, 2019