## Slide 1: Bunched Beam Stochastic Cooling
M. Steck, GSI Darmstadt
Joint US-CERN-Japan-Russia International Accelerator School,
JINR Dubna, Russia,
28 October - 7 November 2019

## Slide 2
x
x'
Fluctuations in Phase Space
compression of total phase space volume by reduction of locally empty phase space volume
 result is an improvement of beam quality, reduction of emittance and momentum spread
x'
x
cooling
phase space is not homogeneously filled with particles  fluctuations of local particle density
2D phase space x-x‘

## Slide 3
First cooling method which was successfully used for beam preparation
Conditions:
Betatron motion phase advance (pick-up to kicker): (n + ½) 
Signal travel time = time of flight of particle (between pick-up and kicker)
Sampling of sub-ensemble of total beam
Principle of transverse cooling:
measurement of deviation from ideal orbit
is used for correction kick (feedback)
S. van der Meer, D. Möhl, L. Thorndahl et al. (1925 – 2011) (1936-2012)
pick-up
kicker
amplifier
deviation
kick
Stochastic Cooling

## Slide 4
Stochastic Cooling
single particle betatron motion along storage ring
without (dashed) and with (full)correction kick
projection to two-dimensional horizontal phase area
kick3 (=0)
kick1
kick2

## Slide 5
Nyquist theorem: a system with a band-width f = W in frequency domain can resolve a minimum time duration T = (2W)-1
Stochastic Cooling
low pass
band pass
time domain
frequency domain

## Slide 6
For exponential damping ( ):
correction kick
(unlimited time resolution)
correction kick with bandwidth W
Nyquist  the time resolution for a system of bandwidth W is T = (2W)-1
Correction kick
correction kick
cooling rate
in time domain
Stochastic Cooling
-
-

## Slide 7
Stochastic Cooling
some refinements of cooling rate formula
noise: thermal or electronic noise adds to the beam signal
mixing: change of relative longitudinal position of particles due to momentum spread
cooling rate
M mixing factor
U noise to signal ratio
cooling heating
with wanted mixing
and unwanted mixing
(kicker to pick-up)
(pick-up to kicker)
further refinement (wanted  unwanted mixing):
maximum of cooling rate

## Slide 8
Mixing
pick-up (at s1)
pick-up
kicker
(at s2)
kicker
 half a turn from pick-up to kicker
 half a turn from kicker to pick-up
unwanted mixing (from pick-up to kicker)
wanted mixing (from kicker to pick-up)
 eff ~ 0
k-pu  0, (Tp/prms)-1  1
pick-up
kicker
mixing is determined by the ion optical functions

## Slide 9
Basic Studies of Stochastic Cooling
summary of initial stochastic cooling studies at CERN
with (anti-)protons
noise limit regime (depending on gain)
mixing limit regime
  N
particle number
cooling time
(normalized to 1 GHz bandwidth)
for highly charged ions: cooling time is significantly reduced (Q-2)

## Slide 10
Requirements Stochastic Cooling
large bandwidth (typically one octave in the GHz range)
good transfer function in gain and phase
high sensitivity (high impedance) of pick-ups and kickers
low electronic noise (cold pick-ups, low noise amplifiers)
large, but variable gain
special ion optical properties of the ring betatron phase advance between transverse pick-up and kicker small momentum slip factor (large wanted and little unwanted mixing) for Palmer cooling: large dispersion value at pick-up

## Slide 11
Stochastic Cooling Circuit
noise
energy kick:
transfer function:
T(f)
Ib(f)

## Slide 12
Stochastic Cooling Circuit
T(f)
B(f)
beam feedback
kick:
open loop gain:
results in shielding and a reduction of Schottky noise  reduction of gain

## Slide 13
Longitudinal Stochastic Cooling
1) Palmer cooling
a pick-up in a dispersive section detects the horizontal position (sensitivity to the particle longitudinal momentum)
at the kicker the correction signal derived from the position
results in an acceleration/deceleration kick which counteracts a momentum deviation
(coupling longitudinal-horizontal degree of freedom can cause heating  compensation by horizontal cooling system)

## Slide 14
Longitudinal Stochastic Cooling
transmission line:
signal delay by one turn, subtraction of the delayed signal results in a short circuit at all harmonics of the revolution frequency
notches at harmonics
of the revolution frequency
with 180º phase jump
2) Notch filter cooling
filter creates notches at the harmonics of the nominal revolution frequency
 particles are forced to circulate at the nominal frequency

## Slide 15
Longitudinal Stochastic Cooling
3) ToF cooling
simplified scheme without notches allows efficient pre-cooling
compared to notch filter cooling the delay line is open and
the 90° phase shifter is used for
differentiation of the signal
acceleration
deceleration
without phase shift
with 90° phase shift
transmission line open

## Slide 16
Fokker-Planck Equation
diffusion term
drift/cooling term
notch filter
TOF
cooling term
diffusion term
longitudinal cooling TOF and notch filter method
distribution function
coordinate
momentum deviation p/p [10-3]
equilibrium distribution ( =0) is a Gaussian
 = -
()2 =

## Slide 17
storage ring
frequency analysis
momentum slip factor 
transition energy t
ion
pick-up
signal
amplification
Schottky Diagnostics
sum signal longitudinal
difference signal transverse
measurement of momentum spread
measurement of transverse emittance
(I)n2  x
 1/f
 p/p
coasting beam case

## Slide 18
Comparison of Longitudinal Cooling Methods
Palmer cooling
Time-of-Flight cooling
Notch filter cooling
Ar18+ 400 MeV/u longitudinal momentum distribution versus time
large momentum capture range
fast cooling
good final momentum spread
drawback: horizontal heating needs to be compensated
by horizontal cooling
large momentum capture range
slower cooling
moderate final momentum spread
simple set-up
no special lattice requirement
reduced momentum capture range
good cooling rate
smallest final momentum spread
most elaborate rf hardware
issue of notch filter stability
measured at the ESR heavy ion storage ring
Schottky signal observed at 245 MHz (h=124)

## Slide 19
Electrode Structures
quarter wave pick-up universal backward coupler
transverse slotline pick-up transverse microwave slotline coupled to two microstrip lines
Faltin type structure
travelling wave coaxial waveguide with slot coupling
slotted waveguide structure travelling wave rectangular waveguide with slot coupling
electrode size matched to the frequency range typically in the range 1- 4 GHz

## Slide 20
Movable Electrodes
pioneered by the plunging system of CERN AC
more recently developed for:
cryogenic shield at 80 K
electrodes cooled to 30 K
motor drive unit
FAIR Collector Ring stochastic cooling improvement of sensitivity repetition time down to 1 s cooling during motion
open position during injection and ramping
BNL RHIC Collider operation after acceleration in the collision mode
repetition time many hours
cooling after acceleration and closing
closed for operation at the collision energy
beam opening
beam axis

## Slide 21
Stochastic Cooling RF Components
for the Collector Ring CR of FAIR
pick-up (kicker) tank
summing of signals from different pick-ups along the beam with matched delay
sum/difference of the two sides for longitudinal/transverse cooling
signal processing:
delay, sum/difference, differentiation, filtering
beam

## Slide 22
Antiproton Accumulation by Stochastic Cooling
kicker array
cryogenic microwave amplifier
microwave electronics
power amplifiers (TWTs)
momentum distribution of accumulated antiproton beam
accumulation of 8 GeV antiprotons at accumulator ring, FNAL, shut down 09/2011
a similar facility AC/AA at CERN was operated until 11/1996

## Slide 23
Bunched Beam Stochastic Cooling
main motivation: increase of luminosity in hadron colliders:
luminosity:
L =
* beam size at interaction point
cooling reduces emittance /beam size  increases luminosity
for the same beam intensity
cooling compensates beam blow-up during store due to beam-beam interaction, intrabeam scattering or space charge
bunched beams are required to have a well defined interaction point
side effect: longitudinal cooling reduces bunch length and
compensates longitudinal blow-up (reduced losses from bucket)

## Slide 24
Bunched Beam Stochastic Cooling
first successful attempt of bunched beam stochastic cooling in ICE ring (1978)
discussion of feasibility for colliders in CAS 1983 (CERN/84-15)
goal: increase luminosity in the proton-antiproton collider SPS
problem: suppress coherent signal of bunches (P  N2) in order to damp the incoherent (P  N) particle motion (cooling)
later: attempts to implement bunched beam stochastic cooling in the SPS at CERN and in the Tevatron at FNAL (  1985-1995 )
Experimental attempts were unsuccessful with protons and antiprotons due to unexpectedly high level of coherent signals.
peculiarity of bunched beam stochastic cooling: increased particle density Neff = Nb/(t  h  frev) = Nb/B
 cooling time increases proportional to 1/B
consequently larger bandwidth required for compensation

## Slide 25
Layout of cooling equipment. Transverse signal via (RHIC) fiber optics. Pickup-to-kicker delay is 2/3 turn. Longitudinal signal sent via microwave links. Delay is 1/6 turn.
RHIC Ring
The RHIC Cooling Equipment
Relativistic Heavy Ion Collider (RHIC) 2 100 GeV/u Gold 79+ ions
circumference 3834 m
bunched beam cooling of the two counter-propagating beams in RHIC
first stochastic cooling of gold bunches in 2007
M. Brennan et al.

## Slide 26
Bunched beam
  High local particle density
    1.8 x 109 ions per bunch
    5 ns bunches
  Coherent lines in the Schottky spectrum
100 GeV/n
  required kick strength ~ 2 kV kick at 5-9 GHz
Strong Intrabeam Scattering with fully stripped ions (about 1000 times larger than for protons)
Not an optimized lattice for cooling. Momentum slip factor  is too small for good mixing (about 4 turns)
Beam aperture for pickups and kickers ≥ 20 mm
Challenges of the RHIC Cooling System
transverse
longitudinal

## Slide 27
A traversal filter with 16 delays of 5.000 ns reduces the peak signal value but has passbands at 200 MHz intervals.
It is realized passively with only coax cables. So it is linear.
After this filter the signal goes into the fiber optic analog link to the surface.
This stretched pulse ultimately drives the kicker cavities to fill them between bunches
Time domain
Frequency domain
10 ns/division
Fiber optic link
Solution to the Coherent Line Problem

## Slide 28
Kickers are realized by high Q, narrow band, cavities.
  16 cavities synthesize a Fourier composition of the kick
  Cavities bandwidth matches time between bunches
  With bunch length of 5 ns the cavity frequencies are multiples of 200 MHz between 5-8 GHz for transverse and 6-9 GHz for longitudinal
  Kickers open to 80 mm clear aperture for injection and ramping
  Afterwards close to 20 mm aperture for operation
Each cavity is driven by a 40 Watt linear solid state amplifier (a broad band system would require 50 kW, rf power is expensive)
Power feed is coax cables for transverse and waveguide for longitudinal kicker cavities
RHIC Stochastic Cooling Kickers

## Slide 29
Microwave link (70 GHz carrier)
Stabilized by phase feedback from a pilot tone at 4.7 and 9.4 GHz (fast fluctuations)
Local oscillator for up and down conversion a 16 GHz
16 GHz Local Oscillator
Microwave Link from Longitudinal Pick-up to Kicker
goal: minimize signal propagation time

## Slide 30
RHIC – 3D stochastic cooling for heavy ions
longitudinal pickup
3 tanks with longitudinal (narrow band) kicker units
longitudinal kicker open for injection and ramping (left), closed during cooling (right)
horizontal and vertical pickups
70 GHz carrier with 16 GHz local oscillator

## Slide 31: RHIC Luminosity Increase
For Uranium-on-Uranium collisions the cooling increased the integrated luminosity per store by a factor of 5
The transverse emittances were reduced by x 4 with a cooling time of ½ hour
luminosity with/without stochastic cooling
beam emittance during store

## Slide 32
cross-talk between rings, signal propagation in the beam pipe from kicker of one ring to the pick-up of the other solution: operation of the cooling systems of the two rings at frequencies shifted by 100 MHz
thermal drift of system solution: regular automatic re-tuning
Specific RHIC Problems

## Slide 33
Barrier Bucket and Target in COSY
protons at 3 GeV/c captured
by a barrier bucket waveform
for particles which are captured in the barrier bucket the energy loss in the internal target is compensated
particles with large momentum deviation escape from the bucket and lose energy
 bunch with moderately increased particle density
Schottky noise frequency spectrum
no cooling
cooling
R. Stassen et al.

## Slide 34
Stochastic Cooling in COSY
Chart: PANDA Cluster-Target with Stochastic Cooling
cooling reduces the transverse emittance and results in longer lifetime and increased luminosity
particle loss due to scattering and energy loss
cooling supports and stabilizes the capture of particles in the bucket
uncooled and cooled bunch (unbunched particles cannot be observed)
stored protons at 3 GeV/c in interaction with internal hydrogen target (up to 11015cm-2)

## Slide 35
energy 400 (-550) MeV/u bandwidth 0.8 GHz (range 0.9-1.7 GHz)
p/p = 0.35 %  p/p = 0.01 % e = 10  10-6 m  e = 2  10-6 m
electrodes installed in the
ultrahigh vacuum inside magnets
combination of signals from electrodes
power amplifiers for generation of correction kicks
fast pre-cooling of hot rare isotopes
Stochastic Cooling of Rare Isotopes at ESR

## Slide 36
injection of a second batch
proposed for the accumulation of antiprotons in the HESR of FAIR
Barrier Bucket Accumulation by Stochastic Cooling
first batch
simulation by T. Katayama
a similar method was applied in the Recycler (FNAL)

## Slide 37
Proof of Principle Experiment at ESR Longitudinal Accumulation with Stochastic Cooling
kicker (differentiated signal)
circulating bunch
injected bunch
revolution time 0.5 s
beam current stored in the ESR
pick-up signal of beam structure
using a single bunch of Ar18+ at 400 MeV/u from SIS
at higher intensity and beam density heating can dominate
mitigate by variation of the system gain in the course of the cooling process

## Slide 38
Stochastic Cooling Systems
CERN, Geneva, Switzerland Intersecting Storage Ring (ISR) 1977
Initial Cooling Experiments (ICE) 1978
Antiproton Accumulator (AA) 1981
Low Energy Antiproton Ring (LEAR) 1983
Antiproton Collector (AC) 1987
Antiproton Decelerator (AD) 1999
FNAL, Chicago, USA
Test Ring 1979
Debuncher Ring 1985
Accumulator Ring 1985
Recycler Ring 1997
NAP-M, INP, Novosibirsk, Russia 1979
TARN, Tokyo, Japan 1983
ESR, GSI, Darmstadt, Germany 1997
COSY, FZJ, Jülich, Germany 1997
RHIC, BNL, Brookhaven, USA 2009
CSRe, IMP, Lanzhou, China 2016
decommissioned
in operation

## Slide 39
Optical Stochastic Cooling
applicable to electrons/positrons or very high energy hadrons
large bandwidth (up to THz) of optical system
transverse cooling by longitudinal-transverse coupling
accelerator test facility IOTA (Fermilab) is preparing a demonstration of optical stochastic cooling

## Slide 40
Coherent Electron Cooling
test experiment
proposed at RHIC (Brookhaven)
FEL Section
Helical Wigglers
Gun
Bunching
Cavities
Modulator
Section
simulations of an ion in the electron plasma

## Slide 41
Comparison of Cooling Methods
Stochastic Cooling Electron Cooling
Useful for: low intensity beams low energy
all intensities
hot (secondary) beams warm beams (pre-cooled)
high charge high charge
full 3D control bunched beams
Limitations: high intensity beams space charge effects
/problems beam quality limited recombination losses
bunched beams high energy

## Slide 42
References Stochastic Cooling
D. Möhl, Stochastic Cooling of Particle Beams, Springer Lecture Notes in Physics 866 (2013)
H. Stockhorst, T. Katayama, R. Maier, Beam Cooling at COSY and HESR, Forschungszentrum Jülich, Key Technologies Volume 120, ISBN 978-3-95806-127-9
D. Möhl, Stochastic Cooling for Beginners, CAS 1983, CERN 84-15, pp. 97-162
D. Möhl, Stochastic Cooling, CAS 85, CERN 87-03, pp. 453-533, 1987
S. van der Meer, Rev. Mod. Phys. Vol. 57, No. 3 Part 1, 1985
F. Caspers and D.Möhl, History of Stochastic Beam Cooling and its Application in Many Different Projects, Eur. Phys. J. H 36, 601-632 (2011)
D. Boussard et al., Feasibility Study of Stochastic Cooling of Bunches in the SPS; CERN/84-15 p.197
Proceedings of Biannual Workshops on Beam Cooling: e.g. COOL 2019, Novosibirsk, Russia