## Slide 1: Joint Experimental Laboratory Located at York
JELLY

## Slide 2
„
“
Science knows no country, because knowledge belongs to humanity, and is the torch which illuminates the world.
Louis Pasteur
International Facility with Partners all around the globe

## Slide 3
d - I
p
England will be the home for the first projekt of the JELLY.
The Proton-Deutoron - Ion Collider

## Slide 4
Ion Source

## Slide 5: Ion Source
H- D- Volume Ion Source
NPulse = 1.5 ∙ 1011
Energy 95 keV
Duty Cycle 4 Hz
H2 + e- (fast) → H2* + e- (slow)
H2* + e- (slow) → H- + H0
(easier Injection with Stripper)

## Slide 6
Linac

## Slide 7: Linac
Consists of 2 Parts
  Normalconducting Injector
  Normalconducting Linac
Used Technology
  4-Rod RFQ
  NC IH-Cavities
  NC CH-Cavities
f = 200 MHz βin = 0.01
Ltotal = 320 m βout = 0.7
NBunch = 1.25 ∙ 1010
0.095 MeV/u
1.5 MeV/u
10 MeV/u
400 MeV/u
4-Rod RFQ
IH-Cavities
CH-Cavities
320 m
4 m
40 m
276 m

## Slide 8: Linac - Injection
H- beam
Injection chicane dipoles
Circulating p+
p+
Stripping foil
H0
H-
Circulating p+
ABT Introductory Lectures, Verena Kain, JAS Dubna, Russia, 2019
450 mT

## Slide 9
Ring - Parameter

## Slide 10: Ring - Parameter
2 Rings
Circumfrences both 300 m
Superconducting Dipoles
1 IP
Injection at 90°
Linac

## Slide 11: Ring - Parameter
NBunch = 50
nProton = nDeutoron = 5 ∙ 1010 pB
εx(1σ) = εy(1σ) = 0.5 π mm mrad
βx* = 2 m ; βy* = 2 m
σx,y = 1 mm

## Slide 12
F O D O - Lattice
Dipole length calculated from Bρ
3 FODO Cells per arc
3.2 m of Drift space for e.g. Diagnostics, Sextupoles, etc.
Linac

## Slide 13
F O D O - Lattice
3 T/m

## Slide 14
Superconducting Magnets

## Slide 15: Superconducting Magnets
48 Dipols planned
LMagnet = 4.75 m
2 T fo the P-ring
4 T for the D-ring
38% of the rings length
(24 each ring)

## Slide 16
With the parameters
from the case study
but B = 4 T:
Cow flies now 23m high
Superconducting Magnets
(6 m for 2 T)
23 m

## Slide 17: Thanks to all of You
Special Thanks to …
  Mingxuan Chan
  Thorsten Conrad
  Georgy Filatov
  James Hunt
  Simon Lauber
  Julian List
  Fu Ma
  Tsukasa Miyajima
  Yana Samofalova
  Michaela Schaumann
  Aleksei Trifonov
  Ippei Yamada
  Takaaki Yasui

## Slide 18: Back up