## Slide 1: Proposal for the opening of a new theme «Development of the Conceptual Design of a New Advanced Neutron Source at JINR»
V. Shvetsov
50th meeting of the PAC for Condensed Matter Physics
June 17-18, 2019, JINR, Dubna, Russia

## Slide 2: Content
Historical introduction;
Research in the field of condensed matter physics in Dubna;
The IBR-2 pulsed reactor, status and prospects;
World trends in the development of the neutron sources;
Current status of the development of conceptual design of a new neutron source at JINR;
Resource requirements;
Conclusion;

## Slide 3: Historical introduction

## Slide 4: Historical introduction

## Slide 5: IBR, IBR-30, IBR-2
IBR reactor – one of the worlds first dedicated for experiments on extracted beams;
Condensed matter physics – one of the three scientific “pillars” of the Joint Institute;
First experiments on CMP at the Laboratory of Neutron Physics of JINR started in early 60-th by initiative of F.Shapiro, J.Janik and B.Buras;
Effective development of the neutron instrumentation in parallel with construction of the new neutron sources;

## Slide 6: Research in the field of condensed matter physics in Dubna

## Slide 7: Research directions and instrumentation development
High temperature superconductors;
Soft matter, gels, polymers;
Chemistry, real time experiments;
Biology, ribosome and proteins structure;
Materials science, engineering analysis, mechanical stresses;
Neutron diffraction at extreme conditions;
Small angle scattering;
Inelastic scattering spectrometers;
TOF Fourier diffractometry;
Reflectometry of polarized neutrons;
Pulsed action on the sample, synchronized with the neutron pulse;

## Slide 8: 2018 results
203 papers in referred magazines;
208 reports at the international conferences;
3 patents;
40 students participated in the research;

## Slide 9: Comparison of the effectiveness of the IBR-2 instruments with the instruments at European sources
We have about 160 neutron instruments at 13 European neutron sources, generating almost 30000 instrument days, resulting 1900 scientific papers each year;
16 instrument days/paper in Europe
At IBR-2 we have 15 instruments, operating about 2500 hours per year, that generates about 1563 instrument days, resulting about 90 scientific papers each year;
17 instrument days/paper at IBR-2

## Slide 10
FLNP JINR:
2 plenary lectures
8 invited talks
20 oral presentations
31 poster

## Slide 11: The IBR-2 pulsed reactor, status and prospects

## Slide 12: Topic was reported at the 49-th PAC meeting

## Slide 13: World trends in the development of the neutron sources

## Slide 14: Why do we need new source?
In order to preserve condensed matter physics as one of the three scientific pillars of JINR, we need a new world-class source that will replace the IBR-2 reactor after the end of its service life;
The period of ageing of the modern scientific facilities is increasing;
All developed countries are planning construction of the new neutron sources with extracted beams for neutron scattering and nuclear physics;
Thermal neutron flux density on the moderator surface (2 equivalent): average not less than 1014 n/cm2/s, peak not less than 1017 n/cm2/s

## Slide 15
2015

## Slide 16
2032 ?

## Slide 18
1. Investigations performed at neutron sources are essential components of R&D in numerous areas of science and engineering.
2. Neutron scattering is often an essential part of a broader experimental study that uses a complementary suite of tools (e.g., light sources, high-performance computers). Thus, neutron sources play a key role in overall U.S. innovation capacity.
3. The United States has lost important capability in neutron R&D in the last two decades and is no longer the world leader. The United States cannot afford to lose its remaining capacity and capability without significant detriment to the quality and quantity of science, engineering, and even medical and manufacturing processes that rely on neutron sources.
4. Reactor fuels containing HEU represent a risk for proliferation, which should be considered when planning for the future infrastructure for neutron R&D.
5. Current HEU-fueled research reactors provide unique R&D capabilities relative to other neutron sources available today. Eliminating them without developing and deploying alternative methods of producing neutrons with the same properties
(e.g., from high-density LEU-fueled reactors and/or a new generation of spallation sources) would compromise U.S. innovation capacity.
6. World-class neutron science and engineering require the comprehensive benefits of spallation facilities, research reactors, and high-performance instrumentation. While there is some overlap in the capabilities provided by spallation and reactor sources, each provides certain capabilities that cannot now be duplicated by the other type of source.

## Slide 19: Current status of the development of conceptual design of a new neutron source at JINR

## Slide 20
N. Kučerka & E.V. Lychagin: Development of the scientific case for a new source of neutrons at JINR
E. Shabalin & Yu.N. Pepelyshev: Concepts of JINR’s high-flux pulsed neutron source
V.N. Shvetsov & V.L. Aksenov: Milestones and time schedule proposal to the strategy plan of JINR
PuO2 based superbooster
Progress outline:
A superbooster (multiplying target of proton linear accelerator with periodic reactivity modulation) is being considered for the new neutron source
Feasibility study of 2 concepts (neptunium and plutonium based) has been started
Time schedule road map has been developed that establishes 6 major stages and proposes the finalization in 2035 – replacing the present source IBR-2M smoothly
Dubna Neutron Source of the Fourth Generation two options
Notes: In accordance to the 7-year plan and long-term strategic planning of JINR, the Frank Laboratory of Neutron Physics has initiated project for the realization of new JINR source of neutrons. In addition to developing the case for scientific justification, discussions are carried out regarding the type of this new source. A superbooster (multiplying target of proton linear accelerator with periodic reactivity modulation) has been concluded to be able to provide record parameters desired by physicists. Recently, the feasibility study of 2 most appealing concepts has been ordered at NIKIET, and time schedule road map has been developed that will allow a timely and smooth replacement of the present source IBR-2M.

## Slide 21: At present we have contract with NIKIET on feasibility study of the:
Pulsed reactor with mechanical modulation of reactivity, based on Np fuel;
ADS with mechanical modulation of reactivity (super booster), based on PuO2 fuel;

## Slide 22: PROJECT ROADMAP (preliminary)
Stage | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37
Concept development |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Conceptual design |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Investment justification |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
R&D |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Technical design |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Construction |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Commissioning |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 23: Basic parameters of the reactor
Parameter | Value
1 Average thermal power, MW | 15
2 Operational mode | pulsed
3 Repetition rate, Hz | 10
4 Fuel | NpN
5 Coolant | Na
6 Inlet temperature of the coolant, 0С | 290
7 Outlet temperature of the coolant, 0С | 391
8 Coolant flow through ½ of the core, kg/s | 58
9 Pressure drop across the core, Pa | 0,33·105
10 Fast neutrons flux density on the reactor vessel, 1014 n/cm2·s1 | 5,7
11 Fluence on the reactor vessel for 20 000 hours, n/cm2 | 4,1·1022

## Slide 24: General view of the reactor in the bulk concrete
IC
Shutter
Stationary reflector
Reactivity modulator
Ø 6m
Ø 2m

## Slide 25: Control
CR-3 (TiH2)
AR-2 (Ni)
EP-2 (Ni)
CR-4 (TiH2)
CR-2 (Ni)
CR-1 (Ni)
EP-1 (Ni)
AR-1 (Ni)

## Slide 26
Spectrometers – Moderators: Optimization task
The basic set of spectrometers can include 15 the most called-for instruments, with ~10 additional ones as the second stage
Spectrometers at moderators for the first stage: 2 (80-90K+300 K) – small/bi-spectral, 4 (80-90 K)– large/cold, 9 (<30K) – small/very cold
Moderator size: 8 – small (~10 x 10 cm or d=10 cm), 7 – large (~20 x 20 cm)
The optimal “Moderator – NG” distance is around L = (2  3) m
Instruments can be grouped to take a full advantage of moderators
*) from report of A. Balagurov

## Slide 27: Beam ports arrangement at the IBR-2 reactor
30 0
36 0
18 0
14 beamports

## Slide 28: Beams arrangements of ESS
*) from report of L. Zanini
42 beamports with ~6° separation

## Slide 29: Neutron fluxes at ”Neptun” neutron source
Be
reflector
Water moderators
(ambient temperature, size d120 mm, h=60 mm )
Core
arb. units: 2.25E-08 (Energy range: 0 - 0.5 eV)
arb. units: 2.89E-08 (Energy range: 0 - 0.5 eV)
~ 1014 n/cm^2/sec
arb. units: 2.86E-08 (Energy range: 0 - 0.5 eV)
The wheel of modulator

## Slide 30
The basic set of 15 neutron TOF instruments (the first stage)
Moderator
Instrument Main issue T, K Size, cm
1. Material science*) Internal stresses 300 / 80 K 10x10
2. High-resolution*) Crystal structure 300 / 80 K 10x10
3. High-intensity In situ, real-time 80 K 20x20
High-pressure Micro samples 80 K 20x20
Direct geometry-I**) General purpose 80 K 20x20
Inverse geometry Molecular systems 80 K 20x20
7. Magnetic Magnetic structure 30 K 20x20
8. Direct geometry-II***) General purpose 30 K 20x20
9. Energy dispersive Complex media 30 K 20x20
*) Fourier chopper **) Fermi chopper ***) Set of choppers
10. High-resolution General purpose 30 K 10x10
11. High-intensity-I In situ, real-time 30 K 10x10
12. High-intensity-II Micro samples 30 K 10x10
13. Horizontal plane General purpose 30 K 10x10
14. Vertical plane Liquid media 30 K 10x10
15. “White” beam General purpose 30 K 10x10
2
4
3
6
*)from report of A. Balagurov

## Slide 31
Beams – Moderators
Moderator | Amount of beams (first stage) | Temperature, K | Size, mm | Possible material
bi-spectral | 2 | Cold 80-90 K + warm 300 K (one above the other) | 100x100 + 100x100 | (Liquid methane/ethane/ pelletized mesitylene)+water
cold | 4 | 80-90K | 200 x 200 | Liquid methane/ethane/ pelletized mesitylene
very cold | 3 | <30K | 200 x 200 | Pelletized solid methane/parahydrogen/pelletized mesitylene
very cold | 6 | <30K | 100 x 100 | Pelletized solid methane/parahydrogen/pelletized mesitylene

## Slide 32
32 beamports with
10° separation:
For instruments:
4 – bi spectral
8 – large cold
8 – large very cold
8 – small cold
4- small tangential cold
2- small/tangential/cold (80K)
2- small/ tangential/ very cold (<30K)
4 – bi spectral
(300+80K)
4– small /cold
(80K)
4 – small/ cold (80K)
8 – large/ very cold (<30K)
8 – large cold (80K)
Be reflector
Water pre-moderators
Core

## Slide 33
The basic set of 15 neutron TOF instruments for the first stage +
~ 10 instruments for the second stage
Moderator
Instrument Main issue T, K Size, cm
1. Material science*) Internal stresses 300 / 80 K 10x10
2. High-resolution*) Crystal structure 300 / 80 K 10x10
3. High-intensity In situ, real-time 80 K 20x20
High-pressure Micro samples 80 K 20x20
Direct geometry-I**) General purpose 80 K 20x20
Inverse geometry Molecular systems 80 K 20x20
7. Magnetic Magnetic structure 30 K 20x20
8. Direct geometry-II***) General purpose 30 K 20x20
9. Energy dispersive Complex media 30 K 20x20
*) Fourier chopper **) Fermi chopper ***) Set of choppers
10. High-resolution General purpose 30 K 10x10
11. High-intensity-I In situ, real-time 30 K 10x10
12. High-intensity-II Micro samples 30 K 10x10
13. Horizontal plane General purpose 30 K 10x10
14. Vertical plane Liquid media 30 K 10x10
15. “White” beam General purpose 30 K 10x10
2
4
3
6
*) report A. Balagurov
4
8
8
10+2

## Slide 35: Resource requirements

## Slide 37: Conclusion

## Slide 39
Thanks a lot for your attention!