## Slide 1: Resume of video-conference of the NICA MAC ("miniMAC")
Currently, two proposals are being considered for the implementation of a polarized program at NICA:
(A) I. Koop A.Otboyev, S.Mane, P.Shatunov, Yu.Shatunov (Budker INP), Polarized colliding beams in NICA storage ring
(B) Yu.Filatov (MPTU, Moscow), A.Kovalenko (JINR), A. Kondratenko (Novosibirsk), Polarized ions in NICA complex

## Slide 2: The main tasks of proposals:
The main tasks of the magnetic optics of the accelerator complex "Nuclotron + NICA" are
to preserve ion polarization during beam acceleration at each stage,
to control the direction of polarization at the meeting point in the collider and
also to match the direction of polarization between the stages.

## Slide 3: Proposal (A): transition energy to NICA
The authors of the proposal (A) consider a single mode of operation, when the Nuclotron in the entire energy range accelerates the polarized beam to the required energy and then injects the beam into the collider NICA operated in the accumulating and colliding mode.
In accordance with this scheme, the task falls into two: preservation of polarization in the Nuclotron and control of polarization direction in the NICA collider.

## Slide 4: Proposal (A): preservation of polarization
As a result of this consideration, the authors conclude
the problem of preserving the polarization of protons in the Nuclotron can be solved using standard methods in the whole range of energies.
assuming that the beam will be injected into the collider at any necessary energy, the authors nevertheless made estimates of the resonance forces in the collider in the whole range of energies from 2 to 14 GeV.

## Slide 5: Proposal (A): control of polarization direction
First, the authors consider the transformation of a vertically polarized proton beam with a slight initial detuning from integer resonance νs = k-ε into a beam with longitudinal polarization for the frequency νs = 12 and νs = 26 by slow switching on weak solenoids 0.5-1 T · m (partial Siberian snake) and reduce detuning ε to zero.
Second, the authors make an assessment of the use of Siberian snakes to control the direction of polarization of deuterons. If for protons the magnitudes of the magnetic fields can be realistic ~ 45 T · m, then for deuterons the value BL = 165 T · m looks unrealistic.
Third, the authors estimate the parameters of the RF flipper used to control the direction of polarization. The frequency of the RF flipper must be tunable depending on the energy. The estimates of the polarization lifetime are very optimistic, about 105 seconds. The authors recommend exploring this option.

## Slide 6: Proposal (B):transition energy to NICA
The authors of proposal (B) consider two modes of operation of the accelerator complex:
the NICA collider operates in the accumulating mode with an arbitrary fixed energy, and the Nuclotron injects a polarized beam with the required energy;
the NICA itself accelerates the polarized beam to the required energy, and the injection energy from the Nuclotron is fixed.

## Slide 7: Proposal (B): “spin transparency” mode
The authors suggest
“spin transparency mode” (ST) and
compare ST with the “preferred spin mode” (PS) using strong spin-rotators.
The ST method is based on work in the vicinity of the integer spin tune resonance νs = 0 (spin converts in itself after each turn)using the weak transverse magnetic fields ~1 T · m to control the direction of polarization. However, to realize the transparent mode we need the integral field
for the protons (B||L)max=4(5÷25) Tm
and for the deuterons (B||L)max=4(15÷80) Tm
Therefore the space problems have to be solved.
However, for PS mode we need the transverse magnetic field
~30 Tm=> strong perturbation of betatron motion

## Slide 8: Resume of the NICA Machine Advisory Committee at JINR, November 15, 2018
1. First step should be done is the choice of the scheme of injection and storage of the polarized particles. Both options – fixed injection energy and acceleration in the Collider – are to be analysed and compared.
2. The spin preservation at acceleration in Nuclotron has to be analysed using numerical simulation and tested experimentally a.s.a.p.
3. Process of particle storage and bunched beam formation in the Collider was not presented properly in both proposals that is a weak point of both of them. This should be investigated.

## Slide 9: Resume of the NICA Machine Advisory Committee at JINR, November 15, 2018
4. Comparison of two proposed modes of spin preservation in the Collider – the Spin Transparency and the Spin Flipper driving the polarization direction – has to be done in details and a choice has to be made. The effect of high field solenoids on particle dynamics in the Collider rings when strong snakes are used to support spin transparency requires a detailed analysis
5. Application of the cooling methods is mandatory, however they lose efficiency with increase of the beam intensity (stochastic cooling) and particle energy (electron cooling).

## Slide 10: Resume of the NICA Machine Advisory Committee at JINR, November 15, 2018
6. Analysis of the Collider luminosity with polarized proton and deuteron beams was not considered sufficiently at this session by mutual agreement. However, it should be done in the nearest future.
7. One should consider also the idea outspoken in the Proposal (A) “to operate the coasting beams that would be an essentially advancing approach for NICA case due to the space charge and synchronization problems of the bunch –bunch collisions regime”.
Conclusion:
Both proposals show the good perspectives of the polarization program at the accelerator complex with the NICA collider.