## Slide 1
Budker Institute of Nuclear Physics
Siberian Branch of RAS
Novosibirsk
Russia
RF systems
of the NICA collider
A.Tribendis
on behalf of the JoINt Rf team

## Slide 2
Harmonic number |  | 22 | 66
Frequency | MHz | 11.513.2 | 34.438.7
Accelerating voltage (amplitude) / ring | kV | 100 | 1000
Cavities / ring |  | 4 | 8
Cavities, total |  | 8 | 16
Barrier bucket system: RF1
Frequency | kHz | 522÷587
Barrier voltage (amplitude) Pulse width Number of pulses | kV ns | 5 var, 80 max 4
Accelerating voltage (meander, amplitude) | kV | var, 0.3 max
Stations / ring |  | 1
Stations, total |  | 2
3 RF systems of the NICA Collider:
Bunch formation
Harmonic systems: RF2 RF3
T
V
Inj
Stack
t
T
t
Acceleration
Injection, accumulation and acceleration

## Slide 3
NE
NW
SW
SE
MPD
SPD
W
E
ECool
Ring 1 (bottom)
Ring 2 (top)
Vacuum Gate Valves
Groups of 1-5 RF cavities are placed between vacuum gate valves in 8 warm sections, thus forming 10 vacuum units.
Location of RF cavities in the accelerator tunnel.
1RF1
1RF1
2RF2
2RF2
2RF2
2RF2
5RF3
2RF3
4RF3
5RF3
Distribution of RF cavities along the collider is dictated by the available free spots.

## Slide 4
RF3-1E2
RF3-2E2
RF3-3E2
RF3-4E2
RF3-5E2
RF3-1AE2
RF3-2AE2
RF3-3AE2
RF3-4AE2
RF3-5AE2
RF3-1/2CE2
RF3-3/4CE2
RF3-5CE2
RF2-3E2
RF2-4E2
RF2-1E2
RF2-2E2
RF2-4AE2
RF2-1AE2
RF1PE2
RF1CE2
RF2-3CE2
RF2-4CE2
RF1DE2
RF1E2
RF2-3AE2
RF2-2AE2
NE
Radiation shielding
Radiation shielding
RF cavities in the accelerator tunnel
RF amplifiers, power supplies, control electronics etc. outside the tunnel
in the limited access area
Single vacuum unit
of 5 RF3 cavities between 2 gate valves
RF feeders & aux. cables run in the grooves under the wall
6 000
Example: Location of RF equipment in the NE sector.
A cavity does not have its own vacuum gate valves
 has to be installed air filled and evacuated / baked out in-situ in a group.

## Slide 5
RF systems: R&D and production plan.
 | RF1 | RF2 | RF3
Key part proto | 2016 – gap short 2016 – inductor module | 2017 – tuner gear box | 
Full size proto |  | 2019 | 2019
RF for NICA | 2019 – 2 pcs | 2020 – 8 pcs | 2020 – 8 pcs 2021 – 8 pcs
Key part prototypes/models
developed and tested
in 2016-17
Movable gap short
RF1 inductor module
RF2 tuner gear box

## Slide 6
RF1

## Slide 7
Vacuum
Ceramic break
Barrier bucket system RF1: the concept.
1 2 3 4 5 6 … 20
A
A
A
A
A
A
B
B
B
B
D
Sections:
D – damping (1, 2)
A – accelerating (3- 5)
B – barrier (6-20)
D
Air
Pulse generator
a
b
+V DC
a
b
= Switching PS
Switching PS is triggered by external signals thus allowing variation of the output pulse length.
The min gap between two adjacent bipolar pulses is limited to 10ns in order to ensure NO through current.
Example: barrier pulses before merging the already stored and newly injected bunches

## Slide 8
Barrier bucket system RF1: 2D.
Vac. (beam) chamber
Vac. chamber heater in thermal insulation
Inductors
Pulse generators
Agilent Vaclon Plus 300
Ion sublimation combination pump
Ceramic break
Mechanical decoupling
ellow w/rf shielding
b
b
b
While an RF system (1, 2 or 3) is off movable shorts with finger spring contacts close accelerating gaps of the cavities: SAME DESIGN FOR ALL CAVITIES!
Gap closed
Short gear box
Movable gap short
L =

## Slide 9
Amorphous magnetic alloy (82% Co)
Amet 84XB-M (www.amet.ru)
f,MHz  tg
0.5 5200 1.67
1.0 3250 1.87
Barrier bucket system RF1: inductor with pulse generators.
Pulse generator
Pulse generator
Coupling loop
(primary coil)
Coupling loop
(primary coil)
Cooling water inlet/outlet
Water cooled copper disks with magnetic core glued in between
Cooling channel as seen if end cover is transparent

## Slide 10
Barrier bucket system RF1: 3D.
Water manifolds
Max dissipated power, W
Module | /inductor | /pulse gen | /module
Barrier | 1020 | 90 | 1200
Accelerating | 680 | 60 | 800
Damping | 500 | -- | 500
Ptotal = 21.4kW / station
Ltot = 1 405 mm

## Slide 11
Barrier bucket system RF1: test assembly at BINP.
Pulse generator
Short gear box
Ceramic break
Vac. chamber not installed
Assembly of 20 inductors is spring loaded in long. direction
for thermal expansion compensation

## Slide 12
Barrier bucket system RF1: tests at BINP.
RF1E2
RF1E1
Power supply cabinets
Vac. cabinets
(vac. pump above)
(vac. pump below)

## Slide 13
Barrier bucket system RF1: test results.
20ns/
1kV/
VDC = 360V
5kV
250ns/
+400V
-400V
200V/
VDC = 125V
Rise/fall time  10ns
Accelerating meander
Barrier pulse
(rep. freq.: single shot of 4 barrier pulses)
RF1E2
To do:
1. Operation with movable barriers. 2. Slope correction.
3. Reliability run at max repetition freq. and voltages.
Notes: Injection at 3Gev/u, p Nuclotron=1.2E-4  1.21E-4 (ideal rectangular pulses) or 2E-4 (actual pulse shape)
– not essential for the injection rate 1/8s and e-cooling current Ie=1A
Stack at 3Gev/u, p=3.7E-4  3.9E-4 (ideal rectangular pulses) or 4.3E-4 (actual pulse shape)

## Slide 14
RF2&3: cavities

## Slide 15
Harmonic systems RF2 and RF3: cavities.
Dimension, mm |  | RF2 | RF3
L | Cavity length (*) | 1200 | 1000
D | Сavity ID | 490 | 490
а | Aperture ID | 100 | 100
g | Accelerating gap | 5 | 20
d |  tuner | 450 | 410
G | Tuner length | 450 | 210
s | Tuner gap | 2.54.1 | 1027
g
L
a
D
s
Tuner (4 segments)
Acc. gap
d
G
Tuner parameters | RF2 | RF3
Tuning range f, MHz | 1.7 | 4.3
Tuner stroke s, mm | 1.6 | 17
Precision δs, um (UI = 5) | 0.13 | 0.5
Sensitivity f/s, MHz/mm | 0.90÷1.60 | 0.14÷0.60
* - movable gap short not accounted
Limitations: low frequency, OD < 2(32050)mm = 540mm, min long. space available
 strongly capacitively loaded coax cavity (with large tuning range!)

## Slide 16
Harmonic systems RF2 and RF3: cavities.
Agilent Vaclon Plus 150
Ion sublimation combination pump
Agilent titanium
sublimation pump (TSP)
Movable gap short
End plate w/coax insert
Cavity cylindrical shell
Capacitive freq. tuner
Tuner gear box
Short gear box
RF3 prototype cavity

## Slide 17
Harmonic systems RF2 and RF3: cavities.
Parameter |  | RF2 | RF3 | Units
Harmonic number |  | 22 | 66 | 
Resonant frequency | f0 | 11.513.2 | 34.438.7 | MHz
Quality factor (unloaded) | Q0 | 3 4003 700 | 6 6007 200 | 
Characteristic impedance | R/Q | 18.821.7 | 5058 | Ohm
Shunt impedance | Rsh | 6580 | 330418 | kOhm
Max gap voltage | Egap | 25 | 125 | kV
Max surface field | ES max | 5.25.5 | 88.2 | MV/m
Kilpatrick limit | EKP | 5.65.9 | 7.98.2 | MV/m
Max dissipated power | Pmax | 4.8 | 24 | kW
Max power density | PS max | 0.6 | 2.8 | W/cm2
Relatively low power losses make it possible to simplify water cooling scheme
in favor of increased mechanical stability of coax inserts of the RF2 cavities
(which are longer than the RF3 cavities)

## Slide 18
Water cooling | RF2 | RF3
1. Outer shell | + | +
2. End plates | + | +
3. Inner coax | + | +
4. Coax C: flat | - | +
5. Coax C: cylinder | - | +
6. Tuner segments | - | +
7. Input coupler | + | +
1
1
2
2
2
2
5
5
3
3
3
3
6
6
7
7
7
7
4
4
Ltot = 1 660 mm
(flange-to-flange)
Ltot = 1 626 mm
(flange-to-flange)
Harmonic systems RF2 and RF3: prototype cavities.

## Slide 19
Harmonic systems RF2 and RF3: prototype cavities.
Coax inserts (front – RF3, back – RF2)
Tuners (RF2)
Cavity shell (RF2)
Cavity shell (RF3)
Cavity shell (RF3) with coax insert and tuners …
… and movable gap short

## Slide 20
RF2 cavity prototype
RF3 cavity prototype
f0 = 11.1÷13.6MHz
Q0 = 3 600 (@ 12.2MHz)
Ready for high power tests.
Test assembly at BINP Workshop.
f0 = 34.1÷39.4MHz
Q0 = 6 900 (@ 39.0MHz)
Harmonic systems RF2 and RF3: prototype cavities.
Stepping motor + piezo
Stepping motor

## Slide 21
RF2&3: power amplifiers

## Slide 22
4-transistors module
Harmonic systems RF2 and RF3: amplifiers.
Each cavity is driven by a SSA designed and produced by the Triada-TV company (Novosibirsk, Russia, www.triadatv.ru).
Amplifier | RF2 | RF3
Freq. range, MHz | 11÷13.5 | 34÷39
Max. output power, kW | 7 | 40
Mode of operation | CW | 
Gain, dB | 40 | 
Max. load VSWR at full power | 2 | 
Output | 50 Ohm 1-5/8” coax | 50 Ohm 3-1/8” coax
Cooling | DI water + air | 
Transistors: MRFX1K80H – RF Power LDMOS by NXP Semiconductors (www.nxp.com)
1.8–400MHz, 1.8kW CW, 65V, VSWR 65:1
Actual regimes: <1.0kW CW, 50V for increased reliability
Power combiners: 3dB directional couplers
Notes: LDMOS = laterally diffused metal oxide semiconductor

## Slide 23
Harmonic systems RF2 and RF3: amplifiers.
23-05-2019
21-05-2019
 | RF2 | RF3
Triada-TV | Pmax, matched | ½ Pmax, matched *)
BINP | Pmax, matched | Pmax, matched
BINP | Pmax, cavity | Pmax, cavity
Prototype amplifier acceptance tests:
*) – limited by the available 20 kW load
100 kW load
Passed
Passed
To be done
RF2
RF3

## Slide 24
Harmonic systems RF2 and RF3: amplifiers.
+ 2 more pages with logged data
Test logs
Передатчик – Работает нормально.
Transmitter – Operates properly.
40.38 kW
7.10 kW

## Slide 25
Vacuum

## Slide 26
RF1
RF2
RF2
RF2
RF2
RF3
RF3
RF3
RF3
RF3
ВЧ3
ВЧ3
ВЧ3
ВЧ3
RF1
RF2
RF2
RF2
RF2
RF3
RF3
RF3
RF3
RF3
ВЧ3
ВЧ3
NE
SW
SE
SIP300
SIP150+TSP
SIP150+TSP
SIP150+TSP
SIP150+TSP
SIP150+TSP
SIP150+TSP
SIP150+TSP
SIP150+TSP
SIP150+TSP
SIP300
SIP150+TSP
SIP150+TSP
SIP150+TSP
SIP150+TSP
SIP150+TSP
SIP150+TSP
SIP150+TSP
SIP150+TSP
SIP150+TSP
SIP150+TSP
SIP150+TSP
SIP150+TSP
SIP150+TSP
SIP150+TSP
SIP150+TSP
SIP300 – Agilent Vaclon Plus 300 ion sublimation combination pump
SIP150 – Agilent Vaclon Plus 150 ion sublimation combination pump
TSP – Agilent titanium sublimation pump
Vac. gauges: Pfeiffer IMR 430, hot cathode, 1.510-12÷ 0.7510-4 Torr
2 / group of 5 cavities, 1 / group of 1÷3 cavities
Vacuum: 310-11 Torr (tech. specs)
Vac. pumps, gauges and CF flanges for ALL cavities procured.
Notes: SIP150 610l/s N2 1380l/s H2
SIP300 720l/s N2 1580l/s H2
TSP 515l/s N2 1200l/s H2

## Slide 27
Spring loaded gasket compressed between 2 flat SS surfaces:
HTMS High Tech Metal Seals
CSE-046200-6.35M-2/2-1-S50
462
6.35
2 types of vacuum gaskets are used in the RF cavities:
spring loaded gaskets at the connections of end plates w/coax inserts-to-cavity shell (RF2, 3)
Conflat® gaskets at all other connections.
RF3 prototype cavity
Vacuum: gaskets.
Advantage: provides “smooth” rf surface, simple flange shape, UHV compatible, reusable (?).
SIP150
TSP

## Slide 28
Vacuum: test sequence.
 Prototype cavity test sequence
Partial assembly (cavity w/o movable gap short):
Pump down with turbo pump only.
Leak check, HTMS joints with special care.
Connect the SSPA, test at full gap voltage.
Complete assembly (cavity w/ movable gap short):
Perform high t vacuum baking.
Repeat step 2.
Repeat step 3 (if limited by MP in unbaked cavity).
RF2 prototype cavity under vacuum tests.
310-7 Torr
no leak <110-11 mbarl/s
Ok
Ok
A spring loaded gasket is an attractive solution (particularly for the end wall-to-cavity shell connections) but require special care and experience in designing and assembling the connections.
It is essential to test the cavity connections with HTMS gaskets ASAP.
310-11 Torr

## Slide 29
Vacuum: baking.
Baking of ALL cavities is done inside local thermal insulation (jackets) by heat tapes (wires) temporarily mounted on the cavity outer surface:
every single cavity – at BINP
group of cavities – at JINR, in-situ
RF1E2
330С
200С
300С
45hrs
6
6
Baking cycle
P, Torr
1
4
1
2
3
4
5days/
29/05/2019: 10-11 Torr
RF1E2 2.9
RF1E1 2.8
10-8
10-10

## Slide 30
RF systems: R&D and production plan.
 | RF1 | RF2 | RF3
Key parts proto | 2016 – gap short 2016 – inductor module | 2017 – tuner gear box | 
Full size proto |  | 2019 | 2019
RF for NICA | 2019 – 2 pcs | 2020 – 8 pcs | 2020 – 8 pcs 2021 – 8 pcs
RF1 for NICA –
06-07/19 reliability run at max repetition freq. and voltages
08-09/19 operation with movable barriers
10-12/19 shipment to JINR, acceptance tests (?)
RF2,3 proto –
06-09/19 high power and vacuum (incl. baking) tests
10-12/19 shipment to JINR, acceptance tests (?)
RF2,3 for NICA –
09/19 series production start
OFE copper, CF flanges and vac. pumps/gauges – received for ALL cavities
HTMS gaskets – estimated prod. time: 4 months
RF amplifiers – estimated prod. time: 12 months (f8+16 amps)

## Slide 31
Thank you!
Transferring knowledge between generations …