## Slide 1: SOLCRYS – new JINR facility for structural research at synchrotron SOLARIS
Norbert Kučerka
Frank Laboratory of Neutron Physics
at Joint Institute for Nuclear Research in Dubna

## Slide 2: Workgroup
JINR SOLARIS
Norbert Kučerka Marek Stankiewicz
Alexander I. Kuklin Maciej Kozak
Evgeniy V. Lukin Jacek Szade
Dorota Chudoba Michał Młynarczyk
and
Denis P. Kozlenko, Mikhail V. Avdeev, Andrey V. Rogachev, Pavel Yu. Apel

## Slide 3: Condensed Matter Research Fields at JINR
solid and liquid states of matter
novel functional materials & materials under extreme conditions
nanomaterials
surfaces and interfaces
polymers and soft matter
solutions and chemical reactions
engineering structures
Chart: 
source: FLNP
Chart: 
Notes: …
Due to the specific definition of the condensed matter research methodology at JINR, the experimental work is performed mostly at the laboratory of neutron physics.

## Slide 4: Advantages of Neutrons
No El. Interactions: ==> deep penetration into matter
Magnetic Moment: ==> the world smallest magnetometer
Scattering Power: ==> sensitivity to light elements
==> sensitivity to isotope exchange
Disadvantage
Low Brilliance: ==> not the method of first choice

## Slide 5: Disadvantages of X-rays
El. Interactions: ==> small penetration into matter
No Magnetic Moment: ==> low sensitivity to magnetism
Scattering Power: ==> low sensitivity to light elements
==> no sensitivity to isotope exchange
Advantage
Very High Brilliance: ==> method of the first choice

## Slide 6: Advantages
neutrons: ==> deep penetration into matter
            ==> sensitivity to magnetism, light elements and isotope exchange
X-rays: ==> very high brilliance
+ others
Chen et al. PNAS 109, 2012
X-rays
neutrons
Complementarity of Neutrons and X-rays

## Slide 7: SOLCRYS – laboratory for structural research
Materials science
- structure of crystalline materials
- semiconductors and new electronic materials
- alloys and nanocomposites
- polymers and fibers
Chemistry
- catalysis
- porous materials
Pharmacy
- drug polymorphism
- drug carriers
- gels, lotions, creams
Structural biology
- proteins and nucleic acids
- biomacromolecular solutions
Notes: The research directions are aligned well with the JINR’s scientific program in condensed matter physics. Some of the research will benefit from the complementarity of neutron and X-ray based measurements, some will achieve opportunity for further expansion, and others will help to create new competencies.

## Slide 8: SOLCRYS – beamlines proposed
MX
- Macromolecular X-ray Crystallography
BioSAXS
- Small-Angle X-ray Scattering of Bio-macromolecular solutions
PD
- Powder Diffraction in a wide range of temperature & pressure
Cryo TEM
- Cryo Transmission Electron Microscopy

## Slide 9: MX-BioSAXS-PD beamline

## Slide 10: Small Angle X-ray Scattering

## Slide 11: Powder Diffraction

## Slide 12: Cryo Transmission Electron Microscope

## Slide 13: SOLCRYS – objectives
electronic structure of different materials
using X-ray absorption spectroscopy
(topological insulators)
heavy atom diffraction of single crystals and powders
diffraction at high pressure
macromolecular crystallography
structure of bio-macromolecular assemblies
courtesy of P.Kuzhir from BSU, Minsk
Magnetoferritin
P.Kopčanský, V.I.Petrenko, et al.

## Slide 14: SOLCRYS – desires
SuperConducting Wiggler providing
X-rays at the energy up to 20keV (0.6 Å)
Front end infrastructure
Endstations:
  SAXS/WAXS
  Macromolecular crystallography
  Powder diffraction with a high pressure option

## Slide 15: SOLCRYS – desires
High pressure diffraction (ALS, Berkeley and/or NSLS, Brookhaven)
Energy > 17keV & ΔE/E~2x10-4
Focusing down to 20μm
Parameter | focus | Divergence in the focus | Flux in the focus | Energy resolution | Energy
Value | <20x20 μm | < 1 mrad | ~1011 photon/sec (>1010) | 2x10-4 | >17 keV

## Slide 16: SOLCRYS – desires
Beamline endstation compatibilities allow co-sharing by SAXS and EXAFS (MAX-lab, Lund and STM at Kurchatov Institute, Moscow)
Monochromator with a varied wavelength is applicable to methods:
  harder X-rays apply to heavy atom crystal diffraction
  dispersion mode applies to high pressure diffraction
  option to use an anomalous scattering in SAXS
Protein crystallography requires a dedicated beamline attainable by utilizing splitters (max of 3 endstations)
The need of auxiliary equipment and preparation lab (equipment and specialists)

## Slide 17: SOLCRYS – desires
User program
    beamline access
    proposal system
    exchange of specialists
    long term secondments

## Slide 18: Summary
The joint work over the concept of new beamlines at Solaris has been established
Endstation competencies have been selected
Desires and proposals for endstation parameters are being discussed
The idea of user program is included from the very beginning

## Slide 19: Thank You for Your Attention!

## Slide 20: SOLCRYS – новая установка структурных исследований на синхротроне SOLARIS
Норберт Кучерка
Лаборатория Нейтронной Физики им. И.М. Франка
Объединенный Институт Ядерных Исследований
в Дубне