## Slide 1: HIGH AIRBORNE RADIOACTIVITY IN TERRESTRIAL ENVIRONMENTS OF ARCTIC REGION Łokas E.1, Zagórski P.2, Sobota I.3, Zawierucha K.4, Pawłowski Ł.5, Singh SM.6, Ziaja W.7, Gaca P.8
1Institute of Nuclear Physics, Polish Academy of Sciences, Krakow, Poland, Edyta.Lokas@ifj.edu.pl
2Marie Curie Sklodowska University, Lublin, Poland
3Nicholas Copernicus University, Toruń, Poland
4Adam Mickiewicz University in Poznań, Poznań, Poland
5University of Wrocław, Wrocław, Poland
6Earth System Science Organisation, National Centre for Antarctic and Ocean Research, India
7Jagiellonian University in Cracow, Kraków, Poland.
8University of Southampton, Southampton, United Kingdom.

## Slide 2
GLACIAL – PROGLACIAL SYSTEM
SEA
ATMOSPHERE

## Slide 3: WHAT IS THE IMPORTANCE OF KNOWLEDGE ABOUT THE PRESENCE OF RADIONUCLIDES IN THE ARCTIC AND OTHER REGIONS?
to assess the threats to those ecosystems and to humans
identification of sources, chronology and routes of contamination in polar regions and in glacierized mountainous areas
Swiss glaciers Tschierva and
Roseg (www.gletscherarchiv.de)
1936
2005
Werenskiold glacier (Spitsbergen)

## Slide 4: Major sources of radioactive contamination in the Arctic
Athmospheric nuclear weapon tests (1945 – 1980) – global fallout
SNAP-9A accident (1964) over the Madagascar
B52 accident - Thule, Greenland (1968)
Chernobyl accident (1986 r.)
Fukushima accident (2011 r.)
Discharges from nuclear fuel reprocessing plants - Sellafield (UK) and Cap de La Hague (France)
…
238Pu/239+240Pu
Global fallout with SNAP 9A: 0.025
Chernobyl accident: 0.50
Nuclear reprocessing plant - Sellafield: 0.17 – 0.21
Nuclear reprocessing plant - La Hague: 0.26 – 0.34
239+240Pu/137Cs
Global fallout: 0.05
240Pu/239Pu
Global fallout: 0.18
Chernobyl accident: 0.40

## Slide 5
evaluate the contamination levels of airborne radionuclides (137Cs, 210Pb and Pu isotopes) in soils and cryoconites from Arctic;
identify the sources of contamination based on artificial radionuclides ratios (238Pu/239+240Pu, 239+240Pu/137Cs, 240Pu/239Pu).
IMPORTANCE OF CRYOCONITE INVESTiGATION
Current changes in the Arctic environments may result in release of cryoconite-bound contamination to ecosystems.
OBJECTIVES

## Slide 6: RESEARCH METERIAL
CRYOCONITES - accumulations of atmospheric dust on glacier surface
Cryoconite material may be washed down or melt out at glacier terminus
INITIAL SOILS from the proglacial zone of glaciers
TUNDRA SOILS

## Slide 7: STUDY AREA
Austre Brogger G.
Hans G.
Waldemar G.
Werenskiold G.
Scott G.
Soil samples
Cryoconite samples
Petunia

## Slide 8: ANALYTICAL METHODS
2.5cm
Disolved in hot acids,
purified from U, Pb tracers
Homogenization
Drying (24h, 105 °C)
Ashing (600 °C)
Measurements-low-
background gamma-
ray spectrometers
with HPGe detectors
210Pb, 137Cs
Radiochemical
procedure
Measurements:
-alpha-ray spectrometers
with Si detectors
-mass spectrometry
MC-ICP-MS Neptune
(IGS PAS Krakow)
240Pu/239Pu
238, 239+240Pu

## Slide 9: INITIAL SOILS
TUNDRA SOILS
AMAP, 1997; 2002, 2015:
137Cs: 0.4 – 2.2 kBq/m2
239+240Pu: 14 – 26 Bq/ m2
238Pu: 0.3 Bq/ m2
Inventory (Bq m-2) INITIAL SOILS |  | 
238Pu | 239+240Pu | 137Cs
6-565 | 9-946 | 180-120000
Inventory (Bq m-2) TUNDRA SOILS |  | 
0.3 – 0.4 | 15 - 30 | 300 - 1400
Łokas et al., 2014, 2016, 2017
RESULTS

## Slide 10: RESULTS
Max value for tundra soils
Max value for tundra soils
Soil from proglacial zone of a glacier (Arctic):
137Cs – 3,300 Bq/kg (max value)
Tundra soil (Arctic):
137Cs – 180 Bq/kg (max value)
Soil from proglacial zone of a glacier (Arctic):
239+240Pu –20 Bq/kg (max value)
Tundra soil (Arctic):
239+240Pu – 4.8 Bq/kg (max value)
Soil from proglacial zone of a glacier (Arctic):
210Pb – 620 Bq/kg (max value)
Tundra soil (Arctic):
210Pb – 312 Bq/kg (max value)

## Slide 11: SOURCES OF CONTAMINATION
Łokas et al., 2016, 2017

## Slide 13: CONCLUSIONS
1.The highest activity concentrations of airborne
radionuclides 137Cs, Pu isotopes and 210Pb investigated in
southern part of Spitsbergen.
2. Activity concentrations of airborne radionuclides
in cryoconite samples exeed activity concentrations
found in Arctic peats, soils and lakes and are comparable
only to the cryoconte-derived deposits of the proglacial
zones of Arctic glaciers.
3. The average activity ratios for 238Pu/239+240Pu (0.060) in cryoconites significantly exceed the mean global fallout ratio (0.025), pointing to possible contributions of 238Pu from other sources.
4. The observed enrichments in 238Pu might be associated with release of 238Pu from the upper stratosphere, where it is likely still stored after burn up of the SNAP- 9A satellite.
5. 239+240Pu/137Cs in the Arctic differ slightly from the global fallout values but these discrepancies might be caused by post-depositional mobility of 137Cs.
6. Transfer of cryoconite material from glacier surface constitutes an additional pathway for the atmospheric contaminants to downstream ecosystems.

## Slide 14
This study was supported by the National Science Center grant no. NCN 2016/21/B/ST10/02327. Samples from SE Spitsberegn were taken during the Jagiellonian University Expedition, 2016, co-financed by the Prince Albert II of Monaco Foundation.
FUNDING

## Slide 15
THANK YOU