## Slide 1: Diagnostics development for Particle Accelerators
Pavel Karataev,
John Adams Institute for Accelerator Science
To change the colours, add department name and add the relevant icon, use the master templates. RGB breakdowns of the colours can be found in the guidelines. The page background colours can also be changed there.

## Slide 2: John Adams Institute for Accelerator Science
Imperial College London
Royal Holloway, University of London
University of Oxford

## Slide 3: e-beam laser wire for linear colliders
Colliders e-/e+ high precision machines.
Two main current designs - International Linear
Collider (ILC) and Compact Linear Collider (CLIC).
Extreme focusing/charge/luminosity requirements.
Need high quality non-invasive measurements of beam size, emittance, position, charge, duration, etc.

## Slide 4: Laser-Wire for electrons

## Slide 5: KEK:ATF2 – Accelerator Test Facility
Charge | 1 – 8 x 109 e
Energy | 1.28 GeV
Beam size (LWIP) | 100 x 1 mm
Bunch | 30 ps (3.12Hz, single bunch)
Laser (532nm, Nd:YAG) | 100 mJ, 150 ps

## Slide 6: KEK:ATF2 – Accelerator Test Facility
Detector
Laser beam transport
Laserwire IP

## Slide 7: LW interaction region

## Slide 8: Laser – e-beam collision search

## Slide 9: f2 lens design
f2 lens at 50 mm focal distance
Aberration free at 532 nm
Geometrical shadow avoided

## Slide 10: Laser-Wire Layout
2zR ~ 30 – 40 mm.
Horizontal direction scan
Vertical direction
scan

## Slide 11: Horizontal and Vertical beam profiles
Horizontal
Vertical

## Slide 12: Emittance measurement
Physical beam emittance was 82.56 ± 3.04 pm rad

## Slide 13: Performance characteristics
Dynamic range: Defined by the signal to noise ratio and can be adjusted by the laser power
Resolution - determined by the laser waist (Linear Collider requires 1m, 3.4m convoluted size achieved at ATF)
Accuracy
  Aberration of the lens system (need an aberration free lens)
  Laser waist and waist position should be stabilized
  Bunch-by-bunch instability
Non-Destructive method
  Major candidate for linear collider

## Slide 14: H- Laser-wire for proton machine injectors
Large Hadron Collider injection complex
  High Luminosity upgrade
Proton beam driven neutron sources
  High intensity beam is needed for generating high flux neutrons or neutrino

## Slide 15: Direct Phase-space measurement principle

## Slide 16: H- Laser-wire principle
Courtesy to T. Hoffman

## Slide 17: Photo-detachment cross-section
J.T. Broad and W.P. Reinhardt, One- and two-electron photoejection from H-: A multichannel
j-matrix calculation. Physical Review A, 14(6):2159–2173, 1976.

## Slide 18: Laser delivery system
Courtesy to T. Hoffman

## Slide 19: H0 Diamond Strip detector
Courtesy to T. Hoffman

## Slide 20: Diamond detector signal

## Slide 21: Phase-space measurements
Slit and grid technique
Laser-wire technique

## Slide 22
Transition radiation
Appearing when a charged particle crosses a vacuum-metal interface\
Characteristic opening angle is ~1/𝛾
Emitted along the particle trajectory (FTR) and along the direction of specular reflection

## Slide 23: Resolution of OTR monitors
Castellano & Verzilov,
PRST-AB 1, 062801 (1998)
Resolution is defined by the width of the OTR Point Spread Function (PSF)

## Slide 24: ZEMAX simulations of OTR PSF
24
Dark
area
T. Aumeyr, et al.,
PRST-AB 18,
042801 (2015)
B. Bolzon, et al.,
PRST-AB 18,
082803 (2015)

## Slide 25: OTR monitor at ATF-Accelerator Test Facility built by SLAC team.
Very high resolution for an OTR monitor (~2m) predicted by the theory but only ~5.5m spot was actually measured.

## Slide 26: OTR PSF Diagnostics at ATF2

## Slide 27: OTR PSF Diagnostics at ATF2
An example of the image measured with linear polarizer and 550±20 nm
First Observation: P. Karataev, et al., Physical Review Letters 107, 174801 (2011).

## Slide 28: OTR PSF Diagnostics at ATF2
Horizontal Projection
Vertical Projection
The minimum vertical beam size measured was 0.754±0.034 μm

## Slide 29: OTR PSF Diagnostics at ATF2
Emittance measurement

## Slide 30: DIFFRACTION RADIATION
Impact parameter, h, – the shortest distance between the target and the particle trajectory
- observation wavelength
 = E/mc2 – Lorentz - factor
Diffraction radiation (DR) appears when a charged particle moves in the vicinity of a medium

## Slide 31: ODR Experiment at KEK-ATF
P. Karataev et al.

## Slide 32: ODR Experiment at KEK-ATF

## Slide 33: ODRI Emittance Measurement at FLASH facility
A. Cianchi, et al., New J. Phys. 16 (2014) 113029
OTR emittance εOTR = 2.4 ± 0.4 mm mrad
ODRI emittance εODRI = 2.3 ± 0.4 mm mrad

## Slide 34: Design of a combined OTR/ODR diagnostics station for ATF2
Beam
BPM Flange
(Beam)
BPM Flange
(Beam)
40 degrees
View Port on target (imaging)
90 degrees
View Port on target (angular)
Camera
45deg View Port
Mask Camera
45deg View Port
Target laser alignment
Mask
Actuators
Target
Actuator
Conceptual design

## Slide 35: Design of a combined OTR/ODR diagnostics station for ATF2
Optical table
30cm as Laser Wire
Target I: molecular adhesion
Target II: chemical itching

## Slide 36
UV DR measurements at ATF2

## Slide 37: Beam size and emittance measurements
Emittance 32+-5 pm rad

## Slide 38
Cherenkov radiation
R(t)
O
z(t)
Cherenkov Radiation is generated whenever the charged particle velocity is larger than the phase velocity of light

## Slide 39
Cherenkov Diffraction Radiation
Vertical polarization
gamma = 104, λ = 600 nm, b = 0.8 mm, a = 11.5 mm
Horizontal polarization

## Slide 40
Cherenkov Diffraction Radiation
Exponential decay
of the particle field

## Slide 41
Simulations of Coherent ChDR using EM simulations codes
e = 5
d = 10 cm
e = 2.1
Using MAGIC and an electron beam current modulated at a 25GHz
propagating at the vicinity of a Teflon cone
Cherenkov Diffraction Radiation

## Slide 42
Cherenkov Diffraction Radiation
Depending on the physical size radiator, smaller frequencies cannot be produced (cut-off effect as in waveguide)
Measuring beam power spectrum in 3 frequency bands

## Slide 43
Optical/IR ChDR experiment at Cornell
L
First tests of incoherent ChDR on Cornell Electron Storage Ring
ChDR
ChDR
Target
Camera
CESR Ring Circumference | 768.4m
Revolution Time | 2.563 ms
Beam Energy | 2.1 and 5.3GeV
Beam Species | e- and e+
Particles per bunch | 1.6 1010
R. Kieffer et al., “Direct Observation of Incoherent Cherenkov Diffraction Radiation in the Visible Range”, PRL 121 (2018) 054802

## Slide 44
Optical/IR ChDR experiment at Cornell
Using a 2cm long SiO2 (n=1.46) ChDR target

## Slide 45
Optical/IR ChDR experiment at Cornell
Imaging Positrons
Positron
Beam
Positron
Beam
Cherenkov Diffraction Radiation

## Slide 46
Optical/IR ChDR experiment at Cornell
Imaging Electrons
Electron
Beam
Electron
Beam
Images from e- is truncated due to the limited aperture of the current detection system
Cherenkov Diffraction Radiation

## Slide 47
Electron Beam
Positron Beam
The photons produced by electrons and positrons appear on a different zone of the image and give the possibility to high directivity beam measurements
Optical/IR ChDR experiment at Cornell

## Slide 48
Optical/IR ChDR experiment at Cornell
  Imaging conditions and Radiation power vs Impact parameter
‘Cherenkov photons yield increasing strongly for smaller impact parameter’

## Slide 49
Optical/IR ChDR experiment at Cornell
  Imaging conditions and Radiation power vs Impact parameter

## Slide 50
Optical/IR ChDR experiment at Cornell
Horizontal polarization
Vertical polarization
Positron Beam
Cherenkov
Diffraction
Radiation
‘Vertically polarized photons give the best spatial resolution (here for sy=2mm)
  Beam imaging - Polarization studies
5.3 GeV positrons - 600nm+/-10nm

## Slide 51
Optical/IR ChDR experiment at Cornell
  Beam imaging as function of impact parameter
  5.3 GeV positrons 600nm+/-10nm filter – Vertical polarizer
Measured beam size increasing for larger impact parameter
Theoretical model is being developed to investigate Line Spread Function as function of impact parameter

## Slide 52
Optical/IR ChDR experiment at Cornell
Measurements with Positrons
Simulations from PCA
Horizontal polarization
Vertical polarization
Ang. divergence: ±200urad
Angular distributions

## Slide 53
Optical/IR ChDR experiment at Cornell
Impact parameter (mm) | 1.04 | 1.33 | 1.68 | 2.02 | 2.46
FWHMexp (mrad) | 0.54 | 0.49 | 0.47 | 0.45 | 0.43
FWHMest (mrad) | 0.56 | 0.49 | 0.46 | 0.44 | 0.40
Angular distributions as function of impact parameter
  5.3 GeV positrons - 600nm+/-10nm filter – Vertical polarizer
Excellent agreement with simulations

## Slide 54
Optical ChDR experiment at KEK-ATF2
Studying the spatial resolution of ChDR at ATF2/KEK - 2018
ATF2 extraction line | 
Beam Energy | 1.25 GeV
Particles per bunch | 1.6 1010
Achievable beam size H/V (microns) | 100 / 1
Re-using and modifying the hardware used for Diffraction radiation studies
Optical system in the visible
OTR for cross calibration

## Slide 55
Optical ChDR experiment at KEK-ATF2
Vertical rms: 63.5 um
ChDR Vertical beam profile
OTR Vertical beam profile
Vertical rms is: 67.2 um

## Slide 56
Optical ChDR experiment at CLEAR in CERN
20cm long stripline in Fused Silica
CLEAR facility at CERN | 
Beam Energy | 200 MeV
Particles per bunch | 1.6 1010
Typical beam size H/V (mm) | > 0.1 / > 0.1

## Slide 57
Optical ChDR experiment at CLEAR in CERN
Beam at 3mm from
surface of the dielectric
Images taken using visible light at 600 ± 10 nm and few bunches of 500pC with a beam size of 130um sigma.
Beam size is important as transverse beam tail would generate Cherenkov radiation (as background light )

## Slide 58
Coherent ChDR experiment at CLEAR in CERN
CChDR radiator installed in the in-air test-stand
Pyramid in Teflon
Measuring in 3 bands (60-90-110GHz)
Scintillating screen on the radiator’s input face for beam tuning
Typical beam size (H/V) < 500microns
All set-up mounted on remotely controlled table to allow hor/ver centering
A. Curcio et al, Beam-based sub-THz source at the CERN Linac Electron Accelerator for Research facility, PRAB 22, 020402 (2019)
5x5cm base
45∘ output angle
∅ 1cm hole

## Slide 59
Coherent ChDR experiment at CLEAR in CERN
Comparison between CChDR and RF deflector
Larger noise for longer bunches as we measured at (too) high frequencies

## Slide 60
Coherent ChDR experiment at CLARA in Daresbury
f = 10Hz
E = 35 MeV
Longitudinal beam size was about 0.2-0.3 ps with charge ranging within 70 - 100 pC
200 microns RMS transversal bunch size

## Slide 61
Coherent ChDR experiment at CLARA in Daresbury
1 — Horizontal positioning stage
2 — Teflon (VCR) target
3 — Tip-Tilt stage
4 — Vertical positioning stage
5 — Concave mirror
6 — Mirror for TR
7 — Foil (TR) target
Both TR and ChDR scans were conducted during same accelerator run

## Slide 62
Coherent ChDR experiment at CLARA in Daresbury

## Slide 63
Coherent ChDR experiment at CLARA in Daresbury

## Slide 64
Coherent ChDR experiment at CLARA in Daresbury

## Slide 65
Coherent ChDR experiment at CLARA in Daresbury

## Slide 66
Coherent ChDR experiment at CLARA in Daresbury

## Slide 67: X-Ray Cherenkov Radiation
http://ibic2013.org/prepress/html/sessi0n.htm
WEPF36

## Slide 68: Carbon Dielectric Permittivity
−δ
η
K-edge

## Slide 69
Very short bunches emitting Coherent radiation in the visible / NIR would benefit from ChDR with very compact BPM (for centering beams in dielectric capillaries)
Dielectric wakefield acceleration
Laser wakefield acceleration
Plasma acceleration
1GeV electron in a 2mm aperture SiO2 capillary
BPM response (a.u.)
Beam offset (mm)
Experimental Plan in Diamond LS

## Slide 70
Can we measure low fluxes of particle using long radiators (optical fiber)
Study plasmonic resonance induced in thin metallic layer coated on the dielectric surface
S. Liu et al., “Surface Polariton Cherenkov Light Radiation Source”, PRL 109 (2012) 153902
Dielectric substrate
Metallic coating
Surface
plasmon
Beam
Towards a ‘monochromatic’ emission of ChDR

## Slide 71: International Network on Development of Advanced Instrumentation for Particle Accelerators
D. Alves 1, A. Aryshev6, M. Bergamaschi1, V.V. Bleko3, M. Billing5, L. Bobb7, J. Conway5, A, Curcio1, K. Fedorov2. J. Gardelle4, S.Y. Gogolev3, D. Harryman2, R.O. Jones1, R. Kieffer1, I. Kishchin8, A.S. Konkov3, P. Karataev2, A. Kubankin8, K. Lasocha1, T. Lefevre1, K. Lekomtsev2, J.S. Markova3, S. Mazzoni1, N. Mounet1, R. Nazhmudinov8, Y. Padilla Fuentes5, A.P. Potylitsyn3, J. Shanks5, D.A. Shkitov3, S. Stuchebrov3, N. Terunuma6
CERN, Geneva, Switzerland
John Adams Institute at Royal Holloway, University of London, Egham, UK
Tomsk Polytechnic University, Tomsk, Russia
CEA, France
Cornell University, Ithaca, USA
KEK, High energy Accelerator Organization, Japan
Diamond Light Source, Oxfordshire, UK
Belgorod National Research University, Belgorod, Russia