## Slide 1
BEAM TRANSFER LINE NUCLOTRON-COLLIDER
AND INJECTION INTO COLLIDER
Tuzikov A.
on behalf of JINR team

## Slide 2
Beam transfer from Nuclotron to Collider
Goals
Accumulation of required intensity of ions (with help of barrier bucket system and beam cooling systems of Collider).
Commissioning: June 2022
Ions | Au79+
Energy of ions, GeV/u | 1 ÷ 3.8
Magnetic rigidity of ions, T m | 14 ÷ 38.5
Ion number | 1∙109
Beam Parameters
NICA MAC 2020

## Slide 3
Layout
Nuclotron-Collider beam transport channel
Composition
NICA MAC 2020

## Slide 4
Pulsed magnet elements
Nuclotron-Collider beam transport channel
Magnetic element | Number | Effective length, m | Max. magnetic field (gradient), T (T/m)
Long dipole | 21 | 2 | 1.5
Short dipole | 6 | 1.2 | 1.5
Quadrupole Q10 | 22 | 0.353 | 31
Quadrupole Q15 | 6 | 0.519 | 31
Steerer | 33 | 0.466 | 0.114
Designed by SigmaPhi
NICA MAC 2020

## Slide 5
Pulsed magnet elements
Nuclotron-Collider beam transport channel
Manufactured by SigmaPhi
NICA MAC 2020

## Slide 6
Pulsed magnet elements
Nuclotron-Collider beam transport channel
Ready for delivery to JINR
JINR has prepared a temporary storage in the Collider tunnel and ready to receive the channel magnets. But... Magnetic measurements were fulfilled in quasi-static modes for one magnet of each type only.
RISKS?
NICA MAC 2020

## Slide 7
NICA MAC 2020
Status of channel equipment
Power supplies are being re-designed in order to be based on components provided by Russian vendors.
Beam diagnostics is purchased and manufactured partially. Full sets of beam diagnostics electronics, fast current transformers, beam loss monitors are ready for delivery to JINR. The first set of 6 pick-us are already delivered.
Purchasing of vacuum equipment is near completion.
Nuclotron-Collider beam transport channel

## Slide 8
Collider injection system
Beam injection
NICA MAC 2020

## Slide 9
Collider injection system
Design development is in progress
NICA MAC 2020

## Slide 10
Septum
10
Collider injection system
Length, m | 2.5
Max magnetic field, T | 0.42
Gap, mm | 35
Septum thickness, mm | 3
Pulse shape | semisinusoidal
Pulse duration, μs | ~ 10
Technical design development is in progress. The main crucial items are low-inductive feedthroughs for current pulses of order 50 kA.
New design of power supply based on semi-conducting switches is being developed.
NICA MAC 2020

## Slide 11
Collider injection system
Kicker
Length, m | 4
Max magnetic field, T | 0.1
Pulse duration, ns: rise plateau fall | 200 200 200
After-kick amplitude, plateau level | ≤1.5%
After-kick duration, ns | ≤160
Concept of the kicker and its power supplies is developed.
Concept of measures against after-kicks is developed.
Effects of after-kicks to the stack are estimated.
NICA MAC 2020

## Slide 12
Collider injection system
Kicker of beam extraction system of Booster
NICA MAC 2020
Manufactured by BINP

## Slide 13
Collider injection system
Kicker after-pulses
Suppression of after-pulses by damping circuit
NICA MAC 2020

## Slide 14
Collider injection system
Kicker subsystem
Disadvantages
Power supplies have a complicated circuit scheme.
High voltage on capacitors and other components of power supplies (up to 60 kV).
Many power supplies (8 PS per a kicker).
NICA MAC 2020
Possible alternative solutions
Suppression of a kicker after-pulse influence on a beam instead of a kicker after-pulse itself → simplification of power supplies

## Slide 15
Collider injection system
Kicker subsystem
NICA MAC 2020
Possible alternative solutions
Revision of the beam injection concept → decrease of a kicker’ angle → lower current and voltage in PS
Local closed orbit bump
Hor. acceptance of the Collider stack – 20 π∙mm∙mrad

## Slide 16
Collider injection system
Revisioned injection system (to be optimized)
Length, m | 2 ÷ 4
Max magnetic field, T | 0.05 ÷ 0.12
Pulse duration, ns: rise plateau fall | 200 200 200
NICA MAC 2020
Kicker
Powering | 1 additional PS per a pair of dipoles
Number of power supplies | 4
Max current, A | 150
Max bending angle, mrad | 1.2
Bump dipoles

## Slide 17
THANK YOU FOR ATTENTION