## Slide 1: JINR Grid Tier-1@Tier-2
N.S. Astakhov, A.S. Baginyan, S.D. Belov, A.G. Dolbilov,
A.O. Golunov, N.I. Gromova, I.S. Kadochnikov,
I.A. Kashunin, V.V. Korenkov, V.V. Mitsyn,
I.S. Pelevanyuk, S.V. Shmatov, T.А. Strizh,
V.V. Trofimov, N.N. Voitishin, V.E. Zhiltsov

## Slide 2
Entry into the Big Data era
The Worldwide LHC Computing Grid (WLCG)
Data: Outlook for HL-LHC
On a festivity dedicated to receiving the Nobel Prize for discovery of Higgs boson, CERN Director professor Rolf Dieter Heuer directly called the grid-technologies one of three pillars of success (alongside with the LHC accelerator and physical installations)
Nowadays, every large-scale project will fail without using a distributed infrastructure and Big Data Analytics for data processing
Computing in High Energy Physics and Nuclear Physics

## Slide 3: Multifunctional Information and Computing Complex (MICC) main components
JINR grid sites of WLCG/EGI: Tier-1 for CMS
Tier-2 for ALICE, ATLAS, CMS, STAR, LHCb,
BES, biomed, fermilab, compass
Cloud infrastructure
Heterogeneous(CPU + GPU)
computing cluster HybriLIT
Off-line cluster and storage system for BM@N, MPD,
SPD Storage and computing facilities for local users
Network infrastructure
Engineering infrastructure

## Slide 4
We have two WLCG Data Centers at the
JINR Laboratory of Information Technologies
Tier-1 (T1_RU_JINR) provides one of 7 dedicated real-time computing facilities for experimental data from the CMS detector at the CERN
Tier-2 (JINR-LCG2) provides one of more then 170 dedicated real-time computing facilities for experimental data from the ATLAS, ALICE, CMS, LHCb detectors, and other VO from RDIG community

## Slide 5
Network and telecommunication channels
One of the most important components of JINR and MICC providing access to resources and the possibility to work with the big data is a network infrastructure.
Local Area Network – 10Gbps, planned upgrade to 100Gbps
Wide Area Network – 2x10Gbps, 100Gbps – test mode
Upgrade WAN to 2x100Gbps planned

## Slide 6: JINR Tier-1 Connectivity Scheme
Notes: This slide shows the JINR’s Computing Center Scheme of equipment.
Here you can see the JINR Tier 1 connectivity plan with Tier0.
6

## Slide 7
Tier-1
JINR participation in Worldwide LHC Computing Grid (WLCG)
Grid Tier-1 is one of the 7 centres in the world intended for large-scale processing of experimental and event-modeling data coming from the centres of Tier-0 (CERN), as well as Tier-1 and Tier-2 of the Worldwide Computing Grid WLCG for the CMS experiment. This component is considered as a prototype of the system of processing and storage of the experimental data from the mega-project NICA as a centre of Tier-0 and Tier-1.

## Slide 8
Chart: T1_RU_JINR Logical CPU
| 2014 | 2015 | 2016 | 2017
Logical CPU | 1200 | 2400 | 3600 | 4160
Chart: T1_RU_JINR HEPSPEC06
| 2014 | 2015 | 2016 | 2017
HEPSPEC06 | 18024 | 39420 | 54072 | 63731
Chart: T1_RU_JINR Disk (TB)
| 2014 | 2015 | 2016 | 2017
Disk (TB) | 652.5 | 2567.414 | 3477.437 | 5943.7
Chart: T1_RU_JINR Tape (TB)
| 2014 | 2015 | 2016 | 2017
Tape (TB) | 0 | 5478.317 | 5478.317 | 9119.127

## Slide 9
Computing Elements (CE)
* Worker Node (WN)
Typically SuperMicro Blade
100 64-bit machines: 2 x CPU (Xeon X5675 @ 3.07GHz, 6 cores per processor); 48GB RAM, 2x1000GB SATA-II; 2x1GbE.
148 64-bit machines: 2 x CPU (Xeon E5-2680 v2 @ 2.80GHz, 10 cores per processor), 64GB RAM; 2x1000GB SATA-II; 2x1GbE.
Total: 4160 core/slots for batch.
* Software
OS: Scientific Linux release 6 x86_64.
BATCH : Torque 4.4.10 (home made)
Maui 3.3.2 (home made)
CMS Phedex
Storage Elements(SE)
Storage System: dCache
* Hardware
Typically Supermicro and DELL
1st - Disk Only:
  31 disk servers: 2 x CPU (Xeon E5-2650 @ 2.00GHz); 128GB RAM; 63TB h/w ZFS (24x3000GB NL SAS); 2x10G.
  24 disk servers: 2 x CPU (Xeon E5-2660 v3 @ 2.60GHz); 128GB RAM; 76TB ZFS (16x6000GB NL SAS); 2x10G.
  4 disk servers: 2 x CPU (Xeon E5-2650 v4 @ 2.29GHz) 128GB RAM; 150TB ZFS (24x8000GB NLSAS), 2x10G
Total space: 4.6PB
  3 head node machines: 2 x CPU (Xeon E5-2683 v3 @ 2.00GHz); 128GB RAM; 4x1000GB SAS h/w RAID10; 2x10G.
  8 KVM (Kernel-based Virtual Machine) for access protocols support.
2nd - support Mass Storage System:
  8 disk servers: 2 x CPU (Xeon X5650 @2.67GHz); 96GB RAM; 63TB h/w RAID6 (24x3000GB SATAIII); 2x10G; Qlogic Dual 8Gb FC.
  8 disk servers: 2 x CPU (E5-2640 v4 @ 2.40GHz); 128GB RAM; 70TB ZFS (16x6000GB NLSAS); 2x10G; Qlogic Dual 16Gb FC.
Total disk buffer space: 1.1 PB.
1 tape robot: IBM TS3500, 11PB
  4400xLTO Ultrium-6 data cartridges; 12xLTO Ultrium-6 tape drives FC8.
  3 head node machines: 2 x CPU (Xeon E5-2683 v3 @ 2.00GHz); 128GB RAM; 4x1000GB SAS h/w RAID10; 2x10G.
  6 KVM machines for access protocols support
* Software
  dCache-2.16
  Enstore 4.2.2 for tape robot.

## Slide 10
JINR CMS Tier-1 - 2017
The requests from the worldwide Tier’s to the JINR CMS Tier-1 for data
Tier-1 network configuration
Notes: Грид-центр уровня Tier-1 для обработки данных эксперимента CMS в рамках международного проекта WLCG (Worldwide LHC Computing Grid) является одним из 7-ми центров в мире такого уровня для CMS. В настоящий момент он содержит 3600 вычислительных ядер, 4 PB дискового хранилища, а также ленточный робот общей емкостью 5,4 PB. Центр уровня Tier-1 для CMS в ОИЯИ продемонстрировал стабильную работу в течение всего периода после его запуска в работу в полном объеме в 2015 году. В течение всего 2016 года этот центр выполнил 8 257 163 задачи, нормированное время ЦПУ составило 237 346 520 часов в единицах HEPSpec06.
На слайде представлен вклад мировых центров 1-го уровня в обработку экспериментальных данных CMS (в миллионах обработанных событий) за 2016 год (диаграмма слева). Сайт Tier-1 ОИЯИ занимает второе место в мире – за 2016 год на нем обработано 14% от общего числа событий.
На диаграмме справа показано количество событий, обработанных в ОИЯИ в центре уровня Tier-1 для CMS в июне 2016 года по разным типам потоковой обработки данных (реконструкция, моделирование, повторная обработка, анализ и т. д.).
Одной из основных функций центров уровня Tier-1 является организации архивного хранения сырых экспериментальных и моделированных данных. На нижнем рисунке слева показана нагрузка ленточного робота в течение 2016 года.
На нижнем рисунке справа представлена сетевая структура для сайта Tier-1. Средняя скорость передачи сырых данных в Tier-1 CMS ОИЯИ составляет 250-300 МБ/с, более 1 ТБ в час.
The grid center of Tier-1 level for CMS experimental data processing in frames of the international project WLCG (Worldwide LHC Computing Grid) is one of 7 centres in the world of this level for the CMS experiment. At present, it contains 3600 computing cores, 4 PB disk storage as well as a tape robot with a total capacity of 5.4 PB. The Tier-1 center for CMS at JINR has demonstrated its stable operation during the whole period after its putting into full service in 2015. Throughout 2016, this center executed 8 163 257 jobs, a normalized CPU time was 237 346 520 hours in HEPSpec06 units.
The slide shows a contribution of the world centers of the 1st level to the CMS experimental data processing (in millions processed events) for 2016 (left chart). The JINR’s site Tier-1 takes second place in the world, in 2016 it handled 14% of the total number of events.
The right chart shows the number of events processed by the JINR’s center of the Tier-1 level for CMS in June 2016 for various types of stream data processing (reconstruction, simulation, reprocessing, analysis, etc.).
One of the key functions of the Tier1 centres is an archival storage of raw experimental and simulated data. The lower figure on the left gives the load of the tape robot during 2016.
The lower right figure shows the network structure for the Tier-1 site. The average speed of the raw data transfer to Tier-1 CMS JINR is 250-300 MBps, more than 1 TB per hour.

## Slide 13
Tier1 hardware monitoring +

## Slide 14
Importance of the Tier-1 center at JINR
Creation of conditions for JINR physicists, JINR Member States, RDMS-CMS collaboration for a full-scale participation in processing and analysis of data of the CMS experiment on the Large Hadron Collider.
The invaluable experience of launching the Tier-1 center will be used for creating a system of storage and data processing of megaproject NICA and other scale projects of the JINR-participating countries.
The studies in the field of Big Data analytics assume significance for the development of the perspective directions of science and economy as well as analysis and forecasting of processes in various fields.

## Slide 15
Tier-2/CICC
JINR Grid-site (JINR-LCG2), as the Tier-1 JINR site, is fully integrated into the worldwide grid infrastructure WLCG / EGI and is a resource centre of Tier-2 in the hierarchy of data-processing centres for experiments at the Large Hadron Collider and other grid Virtual organizations. The resources of JINR Grid-site have been successfully used in the global infrastructure and in terms of reliability the JINR-LCG2 site is one of the best in the WLCG / EGI infrastructure.
This cluster also provides carrying out computations, including the parallel ones, outside the grid-environment. They are asked both by the experiments NoVA, PANDA, BES, NICA/MPD, etc. and the local users of the JINR Laboratories and Member States

## Slide 16
Chart: JINR-LCG2 Physical CPU
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
Physical CPU | 350 | 803 | 1291 | 1210 | 1234 | 1244 | 1244 | 1840
Chart: JINR-LCG2 Logical CPU
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
Logical CPU | 1132 | 1606 | 2582 | 2420 | 2468 | 2568 | 2568 | 3760
Chart: JINR-LCG2 HEPSPEC06
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
HEPSPEC06 | 10389 | 16110 | 25889 | 24264 | 24745 | 25537 | 25537 | 47891
Chart: JINR-LCG2 Disk (TB)
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
Disk (TB) | 587.597 | 610.39 | 1168.494 | 1170.104 | 1455.837 | 1455.964 | 1551.179 | 1554.573

## Slide 17
Computing Elements (CE)
* Worker Node (WN)
Typically SuperMicro Blade, SuperMicroTwin2,
Dell FX
  100 64-bit machines: 2 x CPU (Xeon X5675 @ 3.07GHz, 6 cores per processor); 48GB RAM, 2x1000GB SATA-II; 2x1GbE.
  148 64-bit machines: 2 x CPU (Xeon E5-2680 v2 @ 2.80GHz, 10 cores per processor), 64GB RAM; 2x1000GB SATA-II; 2x1GbE.
  249 machines, 2 x CPU Xeon, 4-14 cores per CPU, E54XX, X65XX, X56XX, ES-26XX v3/4, 2-4GB RAM per core
Total: 3640 core/slots for batch.
* Software
OS: Scientific Linux release 6 x86_64.
BATCH: Torque 4.2.10 (home made)
Maui 3.3.2 (home made)
CMS Phedex
ALICE VObox
Storage Elements(SE)
Storage System: dCache
* Hardware
Typically Supermicro and DELL
1st - Disk for ATLAS & CMS
  24 disk servers: 2 x CPU 24GB RAM, 24 SATA h/w RAID6, 43-63TB
  4 disk servers: 2 x CPU (Xeon E5-2660 v3 @ 2.60GHz); 128GB RAM; 76TB ZFS (16x6000GB NL SAS); 2x10G
Total space: 1332ТB
  2 head node machines: 2 x CPU (Xeon E5-2683 v3 @ 2.00GHz); 128GB RAM; 4x1000GB SAS h/w RAID10; 2x10G.
  7 KVM (Kernel-based Virtual Machine) for access protocols support.
2nd – Disk for ALICE, EOS + XROOTD cluster
  12 disk servers: 2 x CPU 24GB RAM, 24 SATA h/w RAID6, 10-63TB
  2 disk servers: 2 x CPU (Xeon E5-2660 v3 @ 2.60GHz); 128GB RAM; 76TB ZFS (16x6000GB)
Total space: 587ТB.
  2 head node machines: 2 x CPU (Xeon E5-2683 v3 @ 2.00GHz); 128GB RAM; 4x1000GB SAS h/w RAID10; 2x10G.
  4 KVM machines for access protocols support
3-rd Disk for some EGI VОs & local users
  12 disk servers Core2 Duo CPU E8400, 4GB RAM, 12 x SATA h/w RAID6, 8TB
  1 disk server 2 x CPU 24GB RAM, 24 SATA h/w RAID6, 63TB
Total space: 147TB
* Software
  dCache-2.16
  EOS aquamarine
  XROOTD 3

## Slide 18
Experiments
BM@N,
MPD,
CMS,
ATLAS,
ALICE,
LHCb,
COMPASS,
PANDA,
CBM,
STAR,
NOvA,
BESIII,
DIRAC,
OPERA
NEMO
Mu2e,
NUCLON,
HONE,
FUSION
BIOMED
Tier2 & CICC
Tier-1 and Tier-2:
JINR in Worldwide LHC Computing Grid
CPU work HS06 Ноurs by JINR Labs and group. 2017
2017
2017

## Slide 20
Tier2 hardware monitoring +

## Slide 21
development of the CMS Tier-1 center according to the schedule foreseen within RDMS CMS collaboration framework
upgrade of the outdated compute element (CE) and of the data storage element (SE), as well as new additions according to the existing schedule of the Grid JINR Tier-2 site, which provides support to the virtual organizations (VOs) concerning the JINR participation in the LHC experiments (ATLAS, ALICE, CMS, LHCb), FAIR (CBM, PANDA), other VOs within large-scale international collaborations with the JINR groups, and the sequential computing tasks of non-grid JINR users
The further development in accordance with the JINR Seven-Year Plan of development for 2017-2023:
 | 2017 | 2018 | 2019
Processor power of computing core / kHS06 | 3700/59,2 (37%) | 4700/75,2 (27%) | 6000/96,0 (74%)
Disc storages (TB) | 2970 (10%) | 3400 (14%) | 5000 (26%)

## Slide 22
Thank you for your attention!