## Slide 1: The development of Online Event Display using the ATLAS TDAQ for the NICA experiments
28 September 2017
NEC’2017: XXVI International Symposium
on Nuclear Electronics & Computing
K. Gertsenberger, M. Mineev
Joint Institute for Nuclear Research
on behalf of the MPD&BM@N collaboration

## Slide 2
Nuclotron based Ion Collider fAcility
Beams: from to
Collision energy: = 4 – 11 Gev = 1 – 6 AGev
Luminosity: (Au), (p)
Fixed target experiment: BM@N (2017)
2 interaction points: MPD (2020) & SPD
Online Event Display for the NICA experiments

## Slide 3
BM@N physics program:
strange/multi-strange hyperon and hypernuclei production at the threshold
hadron femtoscopy
short range correlations
event-by event fluctuations
in-medium modifications of strange & vector mesons in dense nuclear matter…
MPD and BM@N experiments at NICA
MPD physics program:
study of hot and dense baryonic matter at the energy range of max baryonic density
particle yields and spectra (π, K, p, ΛΞ ,Ω…)
femtoscopy involving π, K, p, Λ
collective flow for identified hadron species
electromagnetic probes (electrons, gammas)
di-Lepton precise study, Charm, Exotics…
Online Event Display for the NICA experiments

## Slide 4: Event Display in the modern experiments
CMS (IGUANA)
ALICE (AliEVE)
ATLAS (Atlantis)
Online Event Display for the NICA experiments

## Slide 5: Purposes of Event Display
design / offline stage = offline event display:
model and algorithm checking and debugging for developers
data reconstruction and analysis visualization for a better understanding of the detector and event structure
demonstration and presentation of works
run / online stage = online event display:
online visual presentation of the selective events during the experiment run – monitoring system
visual control and debugging of current events
Online Event Display for the NICA experiments

## Slide 6: Event Display for the NICA experiments
is the same part of BmnRoot and MpdRoot environments which developed for event simulation, reconstruction and physical analysis of particle collisions in MPD and collisions with a fixed target registered by BM@N, and based on ROOT and FairRoot frameworks
uses Event Visualization Environment (EVE package):
included in the ROOT environment
graphically presents the events
by means of ROOT GUI and OpenGL
oriented on physical objects
visualization, such as raw data, clusters,
hits and tracks
Online Event Display for the NICA experiments

## Slide 7: Event Display (views and projections)
Online Event Display for the NICA experiments
The Event Display can show/hide setup geometry, simulated and reconstructed data: points, hits, tracks, calorimeter towers, select event to display, select particles with definite PDG codes, set energy range and many other visualization options.

## Slide 8: Simulation data for offline Event Display
reconstruction
run_reco.C
simulation
run_sim.C
evetest.root
UrQMD,
QGSM, Pythia…
dst.root
Geant 3/4
detector geometry, MC data
reco data
visualization
eventdisplay.C
event
generator
Online Event Display for the NICA experiments
Au-Au

## Slide 9: BM@N Event Display (MC and reco. points)
Au-Au Elab = 4 GeV
Online Event Display for the NICA experiments
Au-Au

## Slide 10: MPD Event display (MC and reco. tracks)
Au-Au √sNN = 7 GeV
Online Event Display for the NICA experiments
Event Display for simulated MPD event data:
MC tracks and EMC+FHCAL towers
Event Display for reconstructed data:
TPC KalmanTracks
Au-Au
Au-Au

## Slide 11: Experimental data for offline Event Display
visualization
eventdisplay.C
dst.root
digits.root
raw (binary) data
in MPD format
digitizer
raw_run.data
tracking
clustering
hits and tracks
reconstruction
detector
geometry
Online Event Display for the NICA experiments
C-C
Unified Database

## Slide 12: Purposes of Event Display
design / offline stage = offline event display:
model and algorithm checking and debugging for developers
data reconstruction and analysis visualization for a better understanding of the detector and event structure
demonstration and presentation of works
run / online stage = online event display:
online visual presentation of the selective events during the experiment run – monitoring system
visual control and debugging of current events
Online Event Display for the NICA experiments

## Slide 13: NICA DAQ Data Flow (Event Monitor)
matched from “MPD Data Acquisition System TDR”, MPD DAQ Collaboration
￼
￼
Database
FLP
First Level
Processor
Data Check Flow Control Formatting
DRE
EvM
Event
Monitor
TDS
Transient Data Storage
PDS
Permanent Data Storage
EvB
Event
Builder
Buffering
Sorting
Distribution
On-line
Processing
DAQ
LDC
Off-line
Processing
Rootifier
ROOT Format
Mapping
Alignment
REC
Event
Reconstruction
PA
Physics
Analysis
ATLAS TDAQ components
FT REC
Fast Event
Reconstruction
HLT
High Level
L3 Trigger
RQ
Raw Data
Quality
Check
HIST
Online
Histograms
distributed cluster
13

## Slide 14: ATLAS TDAQ system
Online Event Display for the NICA experiments

## Slide 15: ATLAS TDAQ Online Monitoring
ATLAS TDAQ Online System:
specifies the required configuration, including program parameters
provides transfers between programs, deliver by subscription or request and save, if necessary, error messages and other requested information
consistently starts and shutdowns the entire run system
stores all required detector and run parameters
monitors the correctness of system operations
restarts, if possible, malfunctioning parts of the system
monitors the quality of incoming data
Online Event Display for the NICA experiments

## Slide 16: TDAQ for Online Event Display
ATLAS TDAQ Online Components
Raw Event Builder
Histogram Presenter
Displays
Data Quality Monitoring
Analysis
Monitoring Data Archiving
Archiving
Archive Browser
first prototype was developed
in LIT JINR cloud
Web Monitoring
Event Display
Information Monitors
Online Event Display for the NICA experiments

## Slide 17: Remote monitoring with Online Event Display
EvB
Event
Builder
TDS
Transient Data Storage
BmnRoot
BmnRoot
Inter Process Communication
Event Monitoring Service
BM@N DAQ system
start_sampling
Event Provider
Event Consumer
Online Event Display for the NICA experiments
Event Monitor
stop_sampling
add_event
select
next_event
Event Accumulator
Event Iterator
Event Distributor
1000
Event Sampler

## Slide 18: Experimental data for Online Event Display
Online Event Display
(GEM hits and tracks in run #1220)
digits
digitizer
fast
tracking
fast
clustering
tracks
Unified Database
BM@N geometry
run 1986
TDAQ
EMS
DAQ storage
raw *.data
digits
hits
Online Event Display for the NICA experiments
C-C

## Slide 19: Conclusions
The EVE package of the ROOT environment was chosen for the Event Display to show detector geometries, simulated and reconstructed data.
Event Display classes and macro were developed for graphical presentations of the NICA experiments in offline as well as online mode and integrated into the BmnRoot and MpdRoot software.
ATLAS TDAQ components are used to transfer raw event data outside the DAQ system to visualize the NICA experiments on another machine with powerful graphic card. It can also be used for online histogramming and Web monitoring.
The Online Event Display was tested with raw data files from the DAQ storage system.
It is planned to use the Online Event Display for visual presentation of the selective BM@N events during the future experiment runs.
Online Event Display for the NICA experiments

## Slide 20
Thank you for your attention!
More information: mpd.jinr.ru
email: gertsen@jinr.ru
Online Event Display for the NICA experiments
28 September 2017
NEC’2017: XXVI International Symposium
on Nuclear Electronics & Computing