## Slide 1
ECal Module Production in China
Chendi Shen
Department of Engineering Physics, Tsinghua University
VI-th Collaboration Meeting of the MPD Experiment at the NICA Facility
October 28-30, 2020

## Slide 2
1
  Mass Production Plan
2
  Module Production in THU
3
  Beam Test and Calibration
4
  Summary
Contents

## Slide 3
1
  Mass Production Plan
2
  Module Production in THU
3
  Beam Test and Calibration
4
  Summary
Contents

## Slide 4
The Multi Purpose Detector (MPD) is one of the detectors at NICA collider, which is optimized for the study on properties of hot and dense matter in heavy-ion collisions and, in particular, the search for a manifestation of possible deconfinement and/or chiral symmetry restoration phase transitions, critical end-point and mixed quark-hadron phase.
Experiments
with fixed targets
bld. 205
NUCLOTRON 0.6-4.5 GeV/u
PS and
LU-20 (5MeV/u)
Accelertor complex LHEP
existing
In preparation
Collider NICA
(√sNN = 4-11 GeV, C=503 m)
KRION-6T+HILac (3MeV/u)
Booster
(600 MeV/u)
MultiPurpose
Detector - MPD
SPD
MPD
BM@N
Transfer lines
1
  NICA/MPD

## Slide 5
MPD: Multi-Purpose Detector
Central Detector
ECal
4π spectrometer capable
Total charged particle multiplicity : 1000+
Beams from р to Au
L : 1027 (Au), 1032 (р)[см-2с-1]
√ SNN : 4-11 GeV
High Luminosity : 6 kHz
1
  NICA/MPD
Notes: 左图为mpd中心探测器的完整结构，有图蓝色部分为电磁量能器，mpd探测器的具体性能特点列举如下。

## Slide 6
1 tower
1 module
1 half-sector
Barrel ECal ~ 38400 ECal towers
1
  MPD ECal Production

## Slide 7
Hardware:
1) Construction of 8 sectors ECal prototype. Energy resolution is 5%/E, spatial resolution is 5mm
2) Production of FEE PCB
3) R&D on fast readout electronics, time resolution is less than 150ps
Software and simulation
Budget: 4.8M USD
Schedule: 2020.6-2024.5
Institutes: Tsinghua University, Shandong University, Fudan University, University of South China, Huzhou University
1
  China MOST MPD ECal project

## Slide 8
Tsinghua University (60%)
Shandong University (20%)
Fudan University (10%)
University of South China (10%)
Beijing
Qingdao
Shanghai
Hengyang
1
  Production in China

## Slide 9
8 sectors=16 half sectors=768 modules=12288 towers
1
2
3
4
5
6
7
8
Modules produced in each institutes
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | Total
THU |  |  |  | 76 | 96 | 96 | 96 | 96 | 460
SDU |  | 38 | 96 | 20 |  |  |  |  | 154
FDU | 19 | 58 |  |  |  |  |  |  | 77
USC | 77 |  |  |  |  |  |  |  | 77
1
  Production in China
In the first stage (2020-2022), 8 sectors will be produced in China

## Slide 10
Four institutions have discussed and unified the process flow of ECal module production
same material
same standard
same procedure
same QA and QC
1
  Production in China

## Slide 11
 | 2020.10 | 2020.11 | 2020.12 | 2021.01 | 2021.02 | 2021.03
Lead painting |  |  |  |  |  | 
Steel wire & nut production |  |  |  |  |  | 
Aluminum plate production |  |  |  |  |  | 
Tooling production |  |  |  |  |  | 
WLSF purchase |  |  |  |  |  | 
CNC purchase |  |  |  |  |  | 
Scintillator and plastic shipment |  |  |  |  |  | 
Tower assembly |  |  |  |  |  | 
Tower pressurization |  |  |  |  |  | 
Tower milling |  |  |  |  |  | 
Tower gluing |  |  |  |  |  | 
Half-module milling |  |  |  |  |  | 
Module gluing |  |  |  |  |  | 
WLSF milling & painting |  |  |  |  |  | 
WLSF insertion & gluing |  |  |  |  |  | 
Module wrapping |  |  |  |  |  | 
Module test |  |  |  |  |  | 

## Slide 12: Storage allocation of ECal data
1
  Database
A notebook
QR Code
Notes: The data backup will be stored on our Tsinghua University server, the first is the total folder
Its subdirectories are sectors of eight different regions
Next are modules of the same model and different numbers. Our plan is to make 24 modules in each region by March.

## Slide 13: Tower Information ——Four parameters
？
？
？Assembly time
？Length
？Number of layers
Cosmic ray test results | Waveform / Wave data / Peak / Integral
X-ray test results | Waveform / Wave data / Peak / Integral
1
  Database
Notes: 3.Since the cosmic ray test takes too long, we will randomly sample for testing. But we will test each tower in the X-ray test.

## Slide 14: Module Information ——Seven parameters
？
？
？
？
？
？Assembly time
？
1
  Database
Cosmic ray test results | Waveform / Wave data / Peak / Integral
X-ray test results | Waveform / Wave data / Peak / Integral
Notes: 2.The length of the four edges, the thickness of the top and bottom, and the assembly time.
We want to add the X-ray test results, but regarding whether X-ray can play a role in quality inspection, we are now conducting relevant experiments.

## Slide 15
1
  Mass Production Plan
2
  Module Production in THU
3
  Beam Test and Calibration
4
  Summary
Contents

## Slide 16
2
  Production Site (THU)
THU
NUCTECH
NUCTECH Company
The company is ~80km away from Tsinghua University. This is very convenient for testing and transportation of modules

## Slide 17
Assembling area
(two floors)
Gate
Gate
Cutting area
(3 milling machine or more)
2
  Production Site
400m2 in total
Notes: The lower left corner is the model diagram of the NICA，MPD

## Slide 18
Up to now, two modules have been produced in THU, the angle of which is the smallest.
After measurement, the size of the module has met the design requirements. This means that THU has fully mastered the process flow of Module production.
Next, the performance of the two prototypes will be tested after getting the electronics.
Produced in 2020
2
  Module Production in THU

## Slide 19
Step1. Powder painting on the whole lead (large area).
Step2. Cutting lead into a circle with a width of 5cm.
Step3. Punching with automatic machine.
Thickness uniformity is very good by this method.
2
  Lead painting & cutting
Notes: 1.Assembling a tower by using 220 alternating layers of lead and scintillator plates in the mold, pulled together with one loops of a steel string. Strings are ﬁxed by the two tension screws.
2.Sixteen towers are pressed with a special machine.
3.Sixteen towers are cut at a small angle and bonded into one module with two rows (each row consists of 8 towers).
4.The end of ﬁbers are glued in bunches and connected with SiPM separately.
5. Cut and polished the ﬁbers, connecting the PCB plate with SiPM detector and wrapped with shading paper

## Slide 20
Assemble a tower in 20 min.
Fully automatic.
Completed the assembly of 32 towers within 2 days
MPD-ECal tower automatic assembly robot
2
  Automatic tower assembly

## Slide 21
Half-module milling
Pre-pressure
Adjust length
Pressure transmission
Tower milling
Half-module gluing
2
  process flow of module production (1)
Photo taken in 2020

## Slide 22
finished
Module gluing
WLSF cutting (A bundle)
Fiber insertion & gluing
WLSF milling (diamond cutter)
Photo taken in 2020
2
  process flow of module production (2)
WLSF painting

## Slide 23
1
  Mass Production Plan
2
  Module Production in THU
3
  Beam Test and Calibration
4
  Summary
Contents

## Slide 24
Beam test set up
Position & Energy scanning
Time
DESY, Electron beams.
Spatial resolution
Energy resolution
Time resolution
Energy linearity
3
  Beam test
Notes: On August 2018, two prototype modules of the ECal, each consisting of 16 towers, were taken to the DESY for beam test in Hamburg, Germany. The two prototypes modules named THU ECal 01 and 02 were installed on the x, y-moving table.
The experimental set up of this beam time，The two ECal prototype positioned in the x, y-moving table which can be remotely controlled in control room with a precision of 0.4 mm. One of a trigger of the experimental setup used the coincidence of 2 scintillator counters – C one, C two. The other used the LED and illuminating fiber as a monitoring system to monitor the stability of the entire test. Amplitude information obtained by SiPM conversion of light was measured by 32-bit charge sensitive ADC modules 076D-3170 over 16ns gate. The high voltage system which controlled by the switch provided high voltage for the different plug-ins of the entire experiment. The final data is collected on the computer through the switch.
Each tower of the prototype was defined with a number(1-16, 49-64).
Eight columns were scanned along the x-axis direction, and each position was scanned every 5 mm for a total of 264 position points, each time at the center of each column, for the purpose of correction.
.
Lateral energy scanning, longitudinal energy scanning of energy from 1.0 to 5.0 GeV for tower 51 and tower 05 and step Length: 0.2 GeV
time information scanning were performed.
We use the time scan results of dubna. After the slewing correction of this function, we can see that the relationship of time & amplitude becomes irrelevant.
The final time resolution. 212ps, less than the required 1ns.
The spatial resolution is around 4.7 mm @1.6GeV by using Center of Gravity (COG) algorithm
The energy resolution of the two is finally obtained, one is 4% and the other is 4.5%, all of them Less than the required 5%

## Slide 25: Convolutional Neural Network
Neural network and machine learning are powerful tools for solving non-linear problems.
In 1998, CMS ECal has tried the fully-connected neural networks. Results are similar to the COG(Center of Gravity algorithm).
A more general and powerful convolutional neural network(CNN) was designed, train and validate the network with recently developed hardware and technologies.
Convolutional
neural network
(CNN):
Energy resolution is obtained after with CNN.
3
  Beam test
Notes: We also implement a new reconstruction method based on the neural network and machine learning. The neural network and machine learning are powerful tools for solving non-linear problems in all kinds of the field. As early as 1998, CMS has tried to apply fully-connected neural networks to the reconstruction algorithm of its ECal., However, due to the simple structure of the network and the difficulty of the training, the performance of this new method is just as good as the traditional charge center of gravity. We designed a more general and powerful convolutional neural network(CNN), train and validate the network with recently developed hardware and technologies.
The performance is indeed better than the center of gravity. This plot shows the structure of the CNN, it consits of an input layer, which is the largest tower and its 8 nearest neighbors, an output layer which is the estimated position, and 3 convolutional layers and fully connected layers. The goal of the CNN layers is to extract the information from the input data and estimate for the output.
CNN works better than the traditional method.

## Slide 26: Cut the Energy Spread of accelerator– 5%
Etest: test value
  The mean of the spectrum
Etrue : truth value
  Energy spread 5%
Tower 05: 4.93% < 5%
Tower 51: 4.69% < 5%
@1GeV
P(EtestEtrue)>P(Etest)P(Etrue)
3
  Beam test
Notes: We define the mean value of the energy distribution obtained by the traditional method as E test, and the 5% energy broadening as E true, and it is a Gaussian distribution that is positively correlated with the energy resolution.
Therefore, in the energy resolution obtained by the traditional method, I deconvolved a Gaussian distribution with a sigma of 5%. After the cut of this step, the subsequent energy resolution is obtained. The energy resolution is 4.93% and 4.69% at 1GeV.

## Slide 27
Select examples of cosmic rays that completely pass through the tower
Measure the cosmic spectra
fast test method. This method can calibrate 3 modules at the same time
3
  Cosmic ray Calibration
2D readout MRPC
for Tracking
40cm x 40cm

## Slide 28
Voltage of Output signal
3
  X ray test
Tower
Fixed irradiation range
Test speed is very fast, 30s/tower
Detected the tower with obvious abnormal light output
X Ray Tower Scan

## Slide 29
1
  Mass Production Plan
2
  Module Production in THU
3
  Beam Test and Calibration
4
  Summary
Contents

## Slide 30: Summary
Chinese group has completely mastered the production process of MPD-ECal.
THU has produced 2 modules at the end of October 2020.
Preparations for mass production have started, and mass production will officially start in November 2020.
The module test system is under construction.
There are still some issues to be confirmed
  Connection method of electronic board?
  How to fix the module into the basket?

## Slide 31
Thanks for your attention
Chendi Shen
Department of Engineering Physics, Tsinghua University