## Slide 1: Measurements of spectators with Forward Hadron Calorimeter in MPD/NICA experiment
A.Ivashkin
(Institute for Nuclear Research RAS, Moscow)
The Conference "RFBR Grants for NICA"
20-23 October 2020
This work was supported by RFBR according to the research project No 18-02-40065

## Slide 2
RFBR grant tasks
Detector tasks:
Physic’s tasks:
Software for FHCal readout.
Signal processing.
FHCal modules characterization.
Software for energy calibration.
FHCal centrality trigger.
Detector Control System.
Simulation and software for study of spectators matter.
Geometry of ion collisions:
event plane,
centrality.
Properties of spectators:
energy depositions,
scattering angles.
All tasks are associated with the FHCal performance, data quality and physic’s performance.
FHCal is unique detector dedicated for the measurements of spectators at MPD/NICA

## Slide 3: Spectators in ion collisions.
Reaction plane:
plane of b and Z (beam).
spectators
Spectators are effective tool in the measurements of centrality and the reaction plane of collisions.
Spectators are sensitive to the fragmentation models.
Can spectators be an additional probe of the fireball?
Spectators – non-interacting projectile nuclear fragments.

## Slide 4: Detector tasks
Software for FHCal readout.
Signal processing.
FHCal modules characterization.
Software for energy calibration.
FHCal centrality trigger.
Detector Control System.

## Slide 5
FHCal
Two arms of hadron calorimeter at opposite sides in forward regions.
At the distance 3.2 meters from the interaction point.
Available acceptance corresponds to pseudorapidity 2.0< <5.0
FHCAL consists of 2x44 modules.
~1x1 m2 each part.
Beam hole 15x15 cm2.
Lead/scintillator sampling calorimeter.
Longitudinal segmentation;
Light readout- WLS-fibers;
7 sections/photodetectors in each module.
FHCal as a dedicated detector of spectators in MPD
FHCal modules

## Slide 6
FHCal features
Event plane
Spectator spot
Since FHCal has a beam hole, most of the bound spectators escape in this hole.
Mainly, free spectators (protons and neutrons) deposit energy in FHCal.
FHCal detects the energy of spectators;
FHCal detects the space distribution of the spectators;
FHCal detects the produced particles in forward region.
Pions
Protons + neutrons
Fragments
FHCal acceptance

## Slide 7
FHCal signal processing
The readout electronics: FPGA based 64 channel ADC64 board, 62.5MS/s (AFI Electronics, JINR).
Shape of digitized signal.
MPPC: new type
S14160-3010PS
size – 3x3 mm2;
pixel -10x10 µm2;
PDE~18%.
noise
Good signal
Bad signal
Fit function:
Prony method of fit

## Slide 8
FHCal modules characterization with cosmic muons
Tasks:
Tests of different SiPM’s;
Tests of FEE;
Development of methods of the energy calibration;
Control of the light yield of the modules;
Energy threshold for the FHCal trigger.
MPPC: S14160-3010PS
pixel -10x10 µm2;
PDE~18%;
G~1.8x105.
MPPC: S12572-010P
pixel -10x10 µm2;
PDE~12%;
G~105.
New MPPC type
Previous MPPC type
Response of FHCal modules to cosmic muons with different types of MPPC.
Raw spectrum
Corrected to pass length in scintillators.

## Slide 9
Calibration and light yield of FHCal modules
Light yield depends on WLS-fiber length.
Average light yield for MIP’s in longitudinal sections.
New MPPC type
Clear amplitude spectra from cosmic muons allow the energy calibration in self-triggering mode (without external muon trigger).
This is due to high light yield in the longitudinal sections in modules.
~5 MeV
Light drops for ~40% for 1m fiber.

## Slide 10: FHCal in trigger
FFD Trigger Efficiency
Problem: FFD trigger efficiency drops for peripheral collisions.
Is it possible to arrange minimum bias trigger?
FHCal detects the energies practically from all events, including the most peripheral ones.
Detected events – if the energy deposition in each central module exceeds 5 MeV.
5 MeV in each central module
In peripheral collision the energies are mainly deposited in central modules.

## Slide 11: FHCal in trigger - 2
5 MeV is rather reasonable threshold for a single FHCal module with new photodiodes.
Spectrum from cosmic muons.
Dependence of trigger efficiency on the energy threshold and on the number of modules.
Events with energy deposition in each central module > 5 MeV.
Total trigger efficiency ~97.7%.

## Slide 12
Detector Control System for FHCal
Control of HV at photodetectors (MPPC’s);
Temperature control of photodetectors;
Compensation of temperature drift of MPPC gain;
Monitoring of MPPC gain with stabilized light source.
Hardware:
System Module (HV sys. Co.)
Software:
Test version (full functionality) is ready.
New (advanced) python version in development.
  Proxy mode: let other software read FHCal transparently
  Provide TANGO bindings
  Faster operation with multiple System Modules
LAN
FEE
Database
FHCal New Slow Control (proxy)
General Slow Control
System Module
System Module
FEE
FEE
FEE
FEE
FEE
RS485

## Slide 13: Physic’s tasks
Simulation and software for study of spectators matter.
Geometry of ion collisions:
event plane,
centrality.
Properties of spectators:
energy depositions,
scattering angles.

## Slide 14: Fragmentation models/generators
Non-spectator’s contributions
DCM-SMM
LA-QGSM
Depending on fragmentation model, simulated energy deposition in FHCal can be quite different.
LA-QGSM: S. G. Mashnik, K. K. Gudima, R. E. Prael, A. J. Sierk, M. I. Baznat, N. V. Mokhov, CEM03.03 and LAQGSM03.03 Event Generators for the MCNP6, MCNPX, and MARS15 Transport Codes,
arxiv:0805.0751 [nucl-th] (2008)
DCM-SMM: M. Baznat, A. Botvina, G. Musulmanbekov, V. Toneev & V. Zhezher Monte-Carlo Generator of Heavy Ion Collisions DCM-SMM, Phys. Part. Nuclei Lett. 17, 303–324 (2020). https://doi.org/10.1134/S1547477120030024
For DCM-SMM, the maximum energy deposition in FHCal is about 30% less due to the larger number of intermediate fragments (effect of beam hole).
A few models must be compared!

## Slide 15: Reconstruction of the event plane with spectators
Detection of all types of the spectators (protons, neutrons) for both colliding nuclei would ensure the outstanding ~200 angular resolution of the event plane!
spectators
Event plane in first FHCal part:
Event plane in both FHCal parts:
(LA-QGSM)
(DCM-SMM)
Resolution: difference between true reaction plane and reconstructed event plane.
From energy and space distribution of spectators one can determine the event plane as an experimental estimate of the reaction plane.
Ei , (xi ,yi) – energy and coordinates of i-module.

## Slide 16: Resolution of the event plane for only charged particles
The best resolution of event plane is about 300-400 in case of charged spectators only.
For all charged particles (including pions) the resolution is 600 and larger.
It is a factor of 3 and more worse comparing to FHCal option.
Only charged spectators (protons and fragments)
All charged particles (including pions)
Weight wi=1.
The resolution degradation is due to the fact that protons and pions have an opposite signs of v1 flow.
Detection of energies of all spectators ensures the best angular resolution.
Hadron calorimeter is the best option!

## Slide 17
Energy deposition in FHCal can not resolve the central and peripheral events.
Centrality. Problem with beam hole in FHCAL.
New observables are needful to resolve ambiguity in energy deposition of the central and peripheral events.
The space information about the spectator hit points can be used additionally to the detected energy.
One can construct a few such observables.
Bound fragments have small transverse (Fermi) momentum and escape into beam hole.
LA-QGSM
For hermetical calorimeter the energy deposition of spectators has monotonic dependence on impact parameter.
It is not true in real situation.

## Slide 18: (, ) observables in FHCal for the centrality measurement
LA-QGSM
Each color bin is 10% fractions of the total number of events.
GeV]
GeV]
Each color bin is 10% fractions of the total number of events.
DCM-SMM
GeV]
GeV]
Each color bin is 10% fractions of the total number of events.
Impact parameter [fm]
counts
DCM-SMM
18
Transverse energy:
Longitudinal energy:
For DCM-SMM model the identification of central events is not suitable.
New approaches are needed!
interaction point

## Slide 19
Single event
In this method the space energy distribution in FHCal modules is used.
The histogram is fitted by a symmetrical cone (linear approximation).
Weight of each bin is proportional of the energy deposited in corresponding FHCal module.
E [GeV]
E [MeV]
Energy distribution in FHCal modules
Centrality: 2D-fit of energy distributions (linear approach)
Fitted event
Initially we have experimental energy deposition Edep in FHCal.
After linear fit we have:
Efit is reconstructed energy (volume of cone);
Emax – maximum energy in central bin (in FHCal hole);
Radius is defined by the scattering angle of spectators.
central events
peripheral events
LA-QGSM
Energy deposition vs maximum energy in FHCal center
This correlation can be used for the centrality determination.

## Slide 20
E_max [a.u]
Energy deposition vs maximum energy in FHCal center
Centrality resolution for Edep vs Emax
DCM-SMM
LA-QGSM
E_max [a.u]
Edep [a.u]
Edep [a.u]
DCM-SMM
Each color bin is 10% fractions of the total number of events.
The accuracy of centrality determination depends on fragmentation model.
Real data can be quite different!

## Slide 21
Scattering angles of spectators
Impact parameter [fm]
Impact parameter [fm]
Full event
(pion contamination)
Interaction point
E [MeV]
2θ
Interaction point
Can spectator’s scattering angle be sensitive to the fireball?
Radius of spectator’s spot is provided by fit.
Scattering angle [deg]
Scattering angle [deg]
LA-QGSM model
Free spectators (protons&neutrons)
According to the models, the size of the spectator’s spot (scattering angle) depends on the impact parameter. It reflects the spectator’s transverse momenta obtained from fireball.
Can it be used to probe the fireball properties?

## Slide 22
Reconstruction of energy of spectators
E_fit is a volume of a cone
E [MeV]
DCM-SMM
A. O. Svetlichnyi and I. A. Pshenichnov,
Formation of Free and Bound Spectator Nucleons in Hadronic Interactions between Relativistic Nuclei, Bulletin of the Russian Academy of Sciences: Physics, 2020, Vol. 84, No. 8, pp. 911–91
Energy depositions in FHCal strongly depends on the composition of the free and bound spectators.
Most of bound spectators escape in beam hole, while free spectators deposit energy in FHCal.
Subtracting the pion energy contribution from the FHCal full energy one can obtain the energy of spectators which is sensitive to the fragmentation model.
LA-QGSM
Composition of free and bound spectators depends on centrality and can be used for the centrality determination.

## Slide 23
Publication activity
A. Ivashkin, D. Finogeev, M. Golubeva et al., Compact segmented hadron calorimeter for detection of low energy spectators at MPD/NICA facility, Nuclear Inst. and Methods in Physics Research, A (2019), https://doi.org/10.1016/j.nima.2019.05.081.
Nikolay Karpushkin, Fedor Guber, and Alexander Ivashkin, Application of the Prony least squares method for fitting signal waveforms measured by sampling ADC, AIP Conference Proceedings 2163, 030006 (2019); https://doi.org/10.1063/1.5130092
Alexander O. Strizhak, and Alexander P. Ivashkin, Test of modules for Forward Hadron
Calorimeter at MPD/NICA facility, AIP Conference Proceedings 2163, 030013 (2019);
https://doi.org/10.1063/1.5130099
A. Ivashkin, D. Finogeev, M. Golubeva et al., Determination of geometry of heavy ion collisions with
forward hadron calorimeter (FHCal) at MPD/NICA, EPJ Web of Conferences 204, 0 (2019);
https://doi.org/10.1051/epjconf /201920407002
A. Ivashkin, M. Golubeva, F.Guber et al., Amplitude parameters of modules for hadron calorimeter
at MPD/NICA, Journal of Instrumentation, Volume 15, June 2020
https://doi.org/10.1088/1748-0221/15/06/C06044

## Slide 24
Future plans:
Further development of FHCal readout;
Integration of FHCal to MPD setup;
Implementation of FHCal calibration procedure in MPDRoot environment;
Development of methods for collision centrality determination;
Search for new observables to characterize the properties of spectators;
Subtraction of the energy contributions in FHCal from non-spectator particles;
Test and comparisons of different fragmentation models.

## Slide 25
Thank you!